## Slide 1
Kévin PEPITONE
2nd International Magnet Test Stand Workshop Brookhaven National Laboratory, 8-9 May 2018
Quench detection and DAQ systems

## Slide 2: Outline
FREIA
  Presentation of Gersemi
  Magnets to be tested at FREIA
Equipment connected to the magnets
  General layout
Magnets protections
  Magnet protection
  Detailed layout, PotAim cards, Safety matrix
Acquisition systems
  DAQ
  DDM
  Software

## Slide 3
FREIA
Gersemi

## Slide 4: FREIA – Gersemi
What we want
What we have
Gersemi - FREIA
Cluster D - CERN

## Slide 5: FREIA – Gersemi
Delivered later this month
Reheater
Liquifier
Dewar
Bottle
ValveBox
Cryostat
Diameter: 1.1 m
Total length: 3.2 m
Length below the lambda plate: 2.65 m
Gersemi is a cryogenic test station, using a vertical cryostat and a powering circuit up to 2x2 kA, with EE based on fast switches and dump resistor
Delivered

## Slide 6: FREIA – Magnets to test
Kevin Pepitone (FREIA)

## Slide 7: FREIA – Magnets to test
Kevin Pepitone (FREIA)

## Slide 8
Equipment connected to the magnets

## Slide 9: Equipment – Layout

## Slide 10
Magnet protection

## Slide 11: Magnet protection – Introduction
A quench happens when the superconductor goes from superconductive state to resistive state
To detect a quench, we use Vtaps on the magnets and electronics to trigger the power converters, energy extraction, quench heaters and acquisition systems
Direct voltage:
Vsum = (V1 + V2 + V3 + V4)
Differential voltage:
Vdiff(1-2) = (V1- V2 ) Vdiff(3-4) = (V3- V4 )
Vdiff(1,2-3,4) = (V1+ V2 )-(V3+ V4 )
Current derivative:
Vres = V1+ V2-(L1+L2)dI/dt
Vdiff(1-2) = (V1- V2 )
Vthreshold
tValidation
Adjustable delay
Fixed delay
Notes: Vtaps are symmetrically installed on the magnet, the signal used to protect the magnet is the difference of two voltages.
By measuring differentially, the common mode signal (e.g. inductive voltage during current injection) is mostly suppressed so that only resistive voltage remains in the resulting signal.
In case of a differential protection method, a non-symmetric quench is characterized by a continuous rise (or fall) of the voltage. In case of symmetric quench the resistance may grow in both voltages and never reach the threshold. This symmetric case is typically protected for a magnet with four identical parts by measuring multiple differential coils (i.e. (1+2)-(3+4)).
In case a magnet has only two identical parts or even only one single coil, the current derivative method may be needed. If a symmetric quench occur as shown in Figure 4 we’ll be able to detect this by subtracting the inductive voltage to the total voltage of the magnet but not with the Vdiff.

## Slide 12: Equipment – Detailed layout
The total number of signals is 12
A double aperture quadrupole
Signal higher than the threshold for a time longer than the validation time

## Slide 13: Equipment – PotAim cards
PotAim v3
PotAim VT
Notes: When a current ramp is applied to superconducting magnets made of Nb3Sn, voltage spikes of hundreds of millivolts called flux jumps appear at relatively low currents. To avoid tripping the protection during magnet tests, an adaptive voltage threshold in function of the magnet current will be required
If the absolute value of the voltage surpasses the detection threshold and remains above threshold during the validation time, a quench is detected and a Quench Detection Signal is issued

## Slide 14
Acquisition systems

## Slide 15: Acquisition systems - Settings

## Slide 16: Acquisition systems - NI DAQ
PXIe-1082: Chassis
4 hybrid slots, 2 PXI Express slots, 1 PXI Express system timing slot
High performance - up to 2 GB/s per slot dedicated bandwidth and 8 GB/s system bandwidth
Compatibility with PXI, PXI Express, CompactPCI, and CompactPCI Express modules
PXI-8840: CPU
2.6 GHz quad-core Intel i7-5700EQ or 2.7 GHz dual-core Intel i5-4400E
4 GB (1 x 4 GB DIMM) single-channel 1600 MHz DDR3 RAM standard, 8 GB maximum
2 Gigabit Ethernet, 2 USB 3.0, 4 USB 2.0, ExpressCard (optional), and other peripherals
PXIe-6365: I/O card
144 analog inputs, 2 MS/s 1-channel, 1 MS/s multichannel; 16-bit resolution, ±10 V
2 analog outputs, 2.86 MS/s, 16-bit resolution, ±10 V
24 digital I/O lines (8 hardware-timed up to 10 MHz)
Four 32-bit counter/timers for PWM, encoder, frequency, event counting, and more
Analog and digital triggering and advanced timing with NI-STC3 technology
PXIe-6358: I/O card
16 simultaneous analog inputs at 1.25 MS/s/ch with 16-bit resolution; 20 MS/s total AI throughput
Four analog outputs, 3.33 MS/s, 16-bit resolution, ±10 V
48 digital I/O lines (32 hardware-timed up to 10 MHz)
Four 32-bit counter/timers for PWM, encoder, frequency, event counting, and more
Analog and digital triggering and advanced timing with NI-STC3 technology

## Slide 17: Acquisition system - Gersemi acquisition system
DAQ (16 bits) | HF | MF | LF
Maximum number of channels to be recorded | 16 | 16 | 72
Maximum differential input voltage | 1 kVdc | 1 kVdc | 1 kVdc
Acquisition frequency | 5 - 200 kHz | 1 - 5 kHz | 1 kHz
Bandwidth of the system | 600 Hz |  | 
Noise (Ripple) | 100 µVrms |  | 
Range of selectable gain per signal | 0.01 - 40 |  | 
Range of selectable thresholds per signal | 0 – 9990 mV |  | 
Range of selectable delays per signal | 0 – 999 ms |  | 
For standard tests, duration 1 & 2 (HF) are for few hundreds of milliseconds whereas duration 3 & 4 can be few tens of seconds in total.
Data through LF individual channels are recorded in archiving mode, every 10 minutes synchronised or not, or every second on threshold exceeding.
The trigger defines the zero time reference (for data synchronisation).

## Slide 18: Acquisition systems - Settings
 |  |  |  |  |  | Nominal |  | Gain | Daq |  | Voltage |  | Securite |  | DAQ
 |  |  |  |  |  | channel |  |  | Setting |  | Span |  | Seuil | Del. | Analysis Group
 |  |  |  |  |  | attribution |  |  |  |  |  |  | [mV] | [mS] | 
 |  |  |  |  |  | External Trigger |  | - |  | 1 | 20 V |  | - | - | 1
 |  |  |  |  |  |  | Daq name | Real Gain | Daq | HF |  |  |  |  | 
 |  |  |  |  |  |  |  |  | Setting |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | ( x 10-3 ) |  |  |  |  |  | 
Crate | Card | Chan. | Woertz entrée |  |  |  |  |  |  |  |  |  |  |  | 
No | No | No | n1 | n2 | n3 |  |  |  | 1 / Gain |  |  |  |  |  | 
1 | 1 | A | 1 | 3 | 2 | Diff-total | Dif_tot | 5 | 0.200 | 26 | 20 V | 2000 | 400 | 50 | 6
1 |  | B | 4 | 6 | 5 | Vsum low gain | Vtotal | 0.012 | 83.333 | 27 | 20 V |  |  | 50 | 3
1 | 2 | A | 7 | 9 | 8 | VGas LA | VGLA | 40 | 0.025 | 28 | 20 V | 3200 | 80 | 500 | 32
1 |  | B | 10 | 12 | 11 | VGas LB | VGLB | 40 | 0.025 | 29 | 20 V | 3200 | 80 | 500 | 32
1 | 3 | A | 13 | 15 | 14 | Diff-lg | Dif_lg | 0.6 | 1.667 | 30 | 20 V |  |  | 10 | 6
1 |  | B | 16 | 18 | 17 | Vsum | Vsum | 1.2 | 0.833 | 31 | 20 V | 7200 | 6000 | 10 | 3
1 | 4 | A | 19 | 21 | 20 | VConn LA | VCONLA | 40 | 0.025 | 32 | 20 V | 400 | 10 | 8 | 32
1 |  | B | 22 | 24 | 23 | VConn LB | VCONLB | 40 | 0.025 | 33 | 20 V | 400 | 10 | 8 | 32
1 | 5 | A | 25 | 27 | 26 | Vcable LA | VCABLA | 40 | 0.025 | 34 | 20 V | 400 | 10 | 8 | 32
1 |  | B | 28 | 30 | 29 | Vcable LB | VCABLB | 40 | 0.025 | 35 | 20 V | 400 | 10 | 8 | 32
1 | 6 | A | 31 | 33 | 32 | Diff CR3403-CR1202 | Diff_CR3403_CR1202 | 5 | 0.200 | 36 | 20 V | 750 | 150 | 50 | 6
1 |  | B | 34 | 36 | 35 | Diff CR1201-CR3402 | Diff_CR1201_CR3402 | 5 | 0.200 | 37 | 20 V | 750 | 150 | 50 | 6
1 | 7 | A | 37 | 39 | 38 | CR3403 Splice Upper | CR3403_Sp_Up | 40 | 0.025 | 38 | 20 V | 200 | 5 | 8 | 32
1 |  | B | 40 | 42 | 41 | CR3403 Splice Lower | CR3403_Sp_Low | 40 | 0.025 | 39 | 20 V | 200 | 5 | 8 | 32
1 | 8 | A | 43 | 45 | 44 | CR1202 Splice Upper | CR1202_Sp_Up | 40 | 0.025 | 40 | 20 V | 200 | 5 | 8 | 32
1 |  | B | 46 | 48 | 47 | CR1202 Splice Lower | CR1202_Sp_Low | 40 | 0.025 | 41 | 20 V | 200 | 5 | 8 | 32
1 | 9 | A | 49 | 51 | 50 | CR1201 Splice Upper | CR1201_Sp_Low | 40 | 0.025 | 42 | 20 V | 200 | 5 | 8 | 32
1 |  | B | 52 | 54 | 53 | CR1201 Splice Lower | CR1201_Sp_Up | 40 | 0.025 | 43 | 20 V | 200 | 5 | 8 | 32
1 | 10 | A | 55 | 57 | 56 | CR3402 Splice Upper | CR3402_Sp_Low | 40 | 0.025 | 44 | 20 V | 200 | 5 | 8 | 32
1 |  | B | 58 | 60 | 59 | CR3402 Splice Lower | CR3402_Sp_Up | 40 | 0.025 | 45 | 20 V | 200 | 5 | 8 | 32
DAQ Analysis Group | 
Trigger | 1
Current | 2
Voltage sum | 3
Quench Detection | 4
Safety | 5
Voltage Diff | 6
Direct Voltage (horizontal benches) | 7
Quench Antena | 8
Cold Mass Temp | 9
Pressure Sensor | 10
Quench Heater Voltage | 11
Quench Heater Current | 12
Instrum Temp | 13
Voltage Diff Aux Magnet (horizontal benches) | 14
Direct Voltage Aux Magnet (horizontal benches) | 15
T Coil | 16
IAP and diode voltage (horizontal benches) | 17
Direct Voltage Aux Magnet (horizontal benches CD) | 18
Direct Voltage Aux Magnet (horizontal benches EF) | 19
Coil 1 Direct voltage | 20
Coil 2 Direct voltage | 21
Coil 3 Direct voltage | 22
Coil 4 Direct voltage | 23
Coil 5 Direct voltage | 24
Coil 6 Direct voltage | 25
Coil 7 Direct voltage | 26
Coil 8 Direct voltage | 27
Coil 9 Direct voltage | 28
Coil 10 Direct voltage | 29
Spot Heater | 30
Cliq | 31
Connection | 32
Magnetic Measurment | 33

## Slide 19: Acquisition systems - Results
Quench detected by the matrix
=> Triggers fired
Look at the differential voltages to find where is the quench
Find the segment(s) where the quench occurs

## Slide 20: Acquisition systems - Settings

## Slide 21: Acquisition systems - NI DMM
PXIe-1075: Chassis
8 hybrid slots, 8 PXI Express slots, 1 PXI Express system timing slot
791 W total power
Compatibility with PXI, PXI Express, CompactPCI, and CompactPCI Express modules
High performance - up to 1 GB/s per-slot dedicated bandwidth and 4 GB/s system bandwidth
PXIe-8821: CPU
2.6 GHz Intel Core i3-4110E dual-core processor
Up to 2 GB/s system bandwidth and 500 MB/s slot bandwidth (four Gen2 x1 PCI Express links)
2 GB 1600 MHz DDR3L RAM standard, 8 GB maximum
1x DP v1.2, 1x GbE, 2x USB 2.0, 2x USB 3.0, 1 RS-232 ports
PXIe-6341: I/O card
16 analog inputs, 500 kS/s, 16-bit resolution, ±10 V
Two analog outputs, 900 kS/s, 16-bit resolution, ±10 V
24 digital I/O lines (8 hardware-timed up to 1 MHz)
Four 32-bit counter/timers for PWM, encoder, frequency, event counting, and more
Advanced timing and triggering with NI-STC3 timing and synchronization technology
PXIe-4081: ADC
The most accurate 7½-digit DMM
Voltage measurements from ±10 nV to 1000 VDC (700 VAC)
8 DC current ranges with sensitivity down to 1 pA
Resistance measurements from 10 µΩ to 5 GΩ
±500 VDC/Vrms common-mode isolation
1.8 MS/s isolated, 1000 V waveform acquisition
Delivered later this year

## Slide 22: Acquisition systems - Results
“Plateau” -> Splices measurements
Ramp Rate -> Inductances measurements
Quench

## Slide 23
Conclusions

## Slide 24: Conclusions
Magnet protection
  Define the needs:
  How many Vtaps ?
  How many PotAim cards ?
  Energy extraction ?
  Quench Heaters ?
  Dump resistor / IGBTs ?
  Connect the magnet:
  Differential voltage
  Current derivative
  Adjust the PotAim cards and Matrix parameters:
  Threshold
  Validation time
  Delay
Acquisition system
  Define the needs:
  How many Vtaps ?
  How many HF, MF, LF channels ?
  DAQ and DMM:
  Chassis
  CPU
  Cards
  Software:
  Data analysis

## Slide 25
Thank you for your attention
Thank you to my colleagues at Uppsala University and at CERN helping me to learn more about the SC magnets
Special thanks to D. Turi and J. Villena for the pictures
Questions