## Slide 1: Helium Release from SC Link to UR
Thomas Otto, PSO
Nora Grada, PSSO
Contributions from: A. Ballarino, K. Brodzinski, S. Claudet, A. Devred, V. Parma, P. Retz, R. v. Weelderen
HL-LHC TCC, 22. 2. 2018

## Slide 2: Cold Powering layout (schematic)
DSH
Q1
Q2
Q3
D1
DFH
DFX
Current Leads
Power Converter

## Slide 3: Failure Modes leading to Helium evaporation
DSH (SC Link)
Q1
Q2
Q3
D1
DFH
DFX
Current Leads
Power Converter
MCI 3: Short / Arc
MCI 2:
Short / Arc
Heater failure
MCI 4:
Loss of Insulation vacuum
MCI 1: Short / Arc
MCI 1:
Quench
MCI 1
Rupture
MCI 3: Short / Arc

## Slide 4: SC Link Options
Different sources give different values for Helium content in SC Link – I use conservative values
Free volume of SC link approx. 1 m3
SC link with MgB2 cable
  25 kg Helium gas at p=1.3 bar and T =4.5 – 15 K
  Active shield (V ≈ 1.5 m3, T ≈ 40 K): +2 kg Helium
  Passive shield (MLI only) optional
  DFX two-phase cryostat
SC Link with Nb-Ti cable
  140 kg supercritical Helium at p = 3-4 bar and T = 4.5 K
  Active shield as for MgB2 link: +2 kg
  DFX’ one phase cryostat

## Slide 5: UR Gallery – Accessible during Operation
R=2900 mm
Volume of the gallery (300 m long)
Vfree ≈ 6000 m3 (25 % occupancy)
Ventilation:
mixing by Air handling units
Fresh air in UR : 10000 m3/h
(1 exchange every 40 minutes)
Smoke extraction system:
18000 m3/h, can be directed in one particular sector

## Slide 6: MCI 1: Quench or Short in IT
Helium (p = 17 bar / T = 20 K) passes though ruptured plug
Mass- and Heat Flow depends on rupture size:
Full evacuation by DFX Safety Device to LHC Tunnel
< 200 kg, 17 bar, 20 K

## Slide 7: MCI 2: Overheating or Short in DFX
Helium evaporation in DFX
MgB2 may quench – resistive heating leads to full loss of Helium in SC Link => MCI 4a / 4b

## Slide 8: MCI 3: Internal short or arc
Consequence: rupture of cryostat to insulation vacuum
  Size of the hole determines flow to insulation vacuum and release mass flow to tunnel
  Bottom line: the full contents of the cryostat (and active shield) will be released, as in the LIV event.
  From the point of view of Helium release, similar to MCI 4a/4b, only the dynamics may change

## Slide 9: MCI 4: Loss of Insulation Vacuum in SC Link
Cryostat surface 25 m2, 10 layer MLI
Heat load from LIV (0.6 W cm-2): 150 kW
Initial Mass Flow through SC Link Safety Device*:
  MCI 4a: MgB2 SC link: 2 kg s-1
  MCI 4b: Nb-Ti SC link: 4.5 Kg s-1
  * Estimated with CERN Kryolize Software

## Slide 10: MCI 4a: Time evolution after LIV
“Sizing of pressure relief devices for 60 m semi-flexible cryostats”*
Illustrated option is MgB2 link with active shield
    * S. Giannelli, TE-MSC-SCD, EDMS 1722630

## Slide 11: Helium Behaviour after release
Well-mixed He-air zone
MgB2 link: c(O2) = 20.5 %
Nb-Ti link: c(O2) = 18.2 %
Ventilation
Turbulent Zone
He - Air mixture
Extension of the turbulent zone ?
Time until “”homogeneous” mixture
These variables depend on the mass flow, the total amount released and the dimension of the tunnel. Two known cases:
Experimental and simulated He spill tests in LHC, 125 kg at at 0.1, 0.25 and 1.0 Kg s-1
Simulated release from SPS CC, 15 kg in very short time

## Slide 12: MCI 4a – Comparison with SPS CC Test
Small Helium Mass (15 kg vs. 27 kg)
Rapid release, quickly ceasing
Oxygen conc. (%)
Turbulent phase – low O2 concentration at spill location +/- 5, for 5 sec.
Numerical calculation: R. van Weelderen, F. Aabid, TE-CRG

## Slide 13: MCI 4b: LIV in Nb-Ti cryostat
Reminder:
  140 kg He in cryostat, +2 kg in active shield
  4.5 kg s-1 initial flow, total release within 1 minute (?)
  800 m3 Helium gas at NTP
  At the release location, a turbulent mixing zone with c(O2) << 18 % and low temperature will persist for the release location
  Size of turbulent zone ?
  Helium will warm up be mixed by AHU
  Time until mixing
  After turbulence has ceased, c(O2) close to alarm value of ODH detection

## Slide 14: Conclusion
MCI 1: IT Quench and ruptured cryogenic plug
  DFX safety device shall be sized to release all helium in underground
MCI 2: heater fault or short in DFX
  Quench of MgB2 cable, full evaporation => MCI 4a / 4b
MCI 3: internal short or arc in SC link
  Full evaporation => MCI 4a / 4b
MCI 4: Loss of insulation vacuum in SC Link
  4a, MgB2 link: release of up to 25 kg of He in UR: Similar to SPS CC test, short and limited turbulent zone
  4b, Nb-Ti link: release of 140 kg He in UR: Size and duration of the turbulent zone: need to evaluate helium behaviour after release

## Slide 15: Homework
WP 6a:
  Terminate design of SC Link
  Define Helium content and its thermodynamic state in cryostat (and shield)
  Dimension safety devices to protect SC Link, DFX and DFH from overpressure
  Determine proper dynamics of Helium outflow
PSO
  Model helium behaviour (mixing, purging) after release with consideration of the ventilation
  Decide on ventilation options in case of He release: use smoke extraction, stop AHUs to allow stratification …
PSO with WP 9:
  Analyse cryoplant and QXL