## Slide 1: Optics in HL-LHC IR4 for BE-BI
BE-BI

## Slide 2: IR4 layout (not to scale)
HEL.B2
HEL.B1
BGI.B2
BGI.B1
BGV.B2
BGV.B2
BGV.B2
EO/BPM
EO/BPM
BSRT/I
BSRT/I
B2
B1
BQSV/H
BPL
BQSV/H
BQSV/H
BQSV/H
BPL
WS.B2
WS.B1
existing
HL fixed position
HL position tbd

## Slide 3: Requirements on optics
Device/ instrument | Position (from IP4) and constraints | Phase advance | Beta/beam size | Injection/flattop optics
BGI | ~ -63m (B1) | N/A | as large as possible | *
BGI for HL | one on each side – opposite beam from BSRT. (BGI B1 on L, BGI B2 on R) | N/A | as large as possible | *
BGV now | ~ -220m (B2) | N/A | as large as possible | *
BGV for HL | 1 on B2. Baseline location for HL between Q6 and Q7. Could also consider Q5 to Q6 but more crowded. | N/A | as large as possible circular beam | constant beam size throughout the cycle would be an advantage
BSRT – BSRI | ~ ±59m | 90° from crabs and -180°from IP in IP1/5 | as large as possible | *
E/O BPM | Where phase advance (Q5-Q6 easier to integrate) | 90° from crabs and -180°from IP in IP1/5 |  | -
HEL | ~ +40m (B1), -40m (B2) | N/A | as large as possible circular beam | constant beam size throughout the cycle would be an advantage
Schottky BPM BQSV & BQSH | ~ 115.3, 174.1m (B1) ~ 114, 176m (B2) | N/A | as large as possible | Orbit must be in the centre throughout the cycle*
Tune BPM BPL | ~ 138, 149, 172.7m (B1) ~ -175, -116.8m (B2) | N/A | as large as possible | *
WS | ~ ±85m | N/A | as large as possible | *
* change in beta between injection and flattop (if not too large) should be ok, to be evaluated depending on proposed optics. Beta must then be measured throughout the full cycle.

## Slide 4: Conclusions
An increase in the beta functions in IR4 has a positive effect on all the profile monitors :
  Reducing the measurements errors: WS, BGV, Orbit and Tune
  Allowing “meaningful” (not dominated by corrections) measurements at 7 TeV: BSRT, BGI.
It makes electron beam more stable: HEL
It is no longer necessary to keep same beta, as long as measured throughout cycle.
Beta functions should not be excessively high (>400 m) at the D3; it compromises interferometry measurements at injection energy.