## Slide 1
Mar. 11, 2019
D. Ratner, E. Cropp, J. Duris, A. Edelen, C. Emma, K. Kabra, D. Kennedy, T. J. Lane, S. Li, T. Maxwell,
P. Musumeci, X. Ren, G. Stupakov, J. Wu, X. Zhang
SLAC National Accelerator Laboratory
ACAT 2019
Machine Learning for an X-ray Laser

## Slide 3: Motivation
Why build an FEL?
Shock waves in extreme conditions
Structural biology
Suga et al.
Photosystem II
Milathianaki et al.
Si
Cu powder
diffraction
Ekeberg et al.,
Single particle imaging (Mimivirus)

## Slide 4: Molecular Movies: Pump-probe scans
Slide courtesy M. Minitti

## Slide 5: Molecular Movies: Pump-probe scans
Slide courtesy M. Minitti
UV
X-rays

## Slide 6: Overview
ML for an X-ray Laser
SLAC is working (to various degrees) on:
Machine Tuning: Online optimization of the accelerator
Data Analysis: Computer vision for screens, inverse problems
Novel methods: Ghost imaging, fluctuation analysis
Surrogate modeling: machine design, tuning, user support
Prognostics: Anomaly/breakout detection to avoid/recover from beam faults.
In-the-loop data acquisition: adaptively change experimental parameters during acquisition with Reinforcement learning
User-side: edge-ML for detectors, domain science applications

## Slide 7: Overview
ML for an X-ray Laser
SLAC is working (to various degrees) on:
Machine Tuning: Online optimization of the accelerator
Data Analysis: Computer vision for screens, inverse problems
Novel methods: Ghost imaging, fluctuation analysis
Surrogate modeling: machine design, tuning, user support
Prognostics: Anomaly/breakout detection to avoid/recover from beam faults.
In-the-loop data acquisition: adaptively change experimental parameters during acquisition with Reinforcement learning
User-side: edge-ML for detectors, domain science applications

## Slide 8
Optimization
Online tuning:
XFELs are instabilities  very sensitive to initial conditions
In total 500 hours/year, single task of quad tuning half of that
Ocelot
Automate (e.g. simplex)

## Slide 9: Optimization: Bayesian optimization
Acquisition point
Joe Duris
Acquisition
function
Ground truth
Posterior
Model-based optimization
Gradient optimizer
Advantage 1: Balance “exploitation vs. exploration”
 Find global maximum
Bayesian optimizer

## Slide 10: Optimization: Bayesian optimization
Gaussian process: instance based learning method
Kernel function:
x1
x2
x3
x*
Joe Duris
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
Measured
Modeled
FEL vs quads (i.e. strong focusing)
Quad 1
Quad 1
Quad 2

## Slide 11: Optimization: Bayesian optimization
Gaussian process: instance based learning method
Kernel function:
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
ρ = 0.7
ρ = 0
Groundtruth
GP model,
no correlation
GP model,
w/ correlation
Joe Duris

## Slide 12: Optimization: Bayesian optimization
Joe Duris
Model-based optimization
Example 2: tuning quadrupoles from pure noise
Example 1: Fast tuneup in high dimensions
Upshot:  Faster tuning (factor of 4 vs. simplex)
 More robust tuning (e.g. tune from noise)

## Slide 13: Data Analysis: Pulse reconstruction
Maxwell, Timothy J., et al. International Society for Optics and Photonics, 2014.
Spectrum
Users want:
High resolution X-ray power profile shot-by-shot
Full (phase and amplitude) reconstruction of X-ray pulses
How can we measure femtosecond X-rays?
Power (W)
Time (fs)
After lasing
Before lasing
e- energy (g)
e- energy (g)
Electron phase space

## Slide 14: Data Analysis: Pulse reconstruction
Computer vision
Stanford CS231n
D. Mendez
Aphex34 https://commons.wikimedia.org/w/index.php?curid=45679374

## Slide 15: Data Analysis: Pulse reconstruction
Experiment
Training Set
Genesis Simulation
GAN
Feed Training Data
Data Augmentation
CNN
The generative adversarial network (GAN) generates labeled images
 Augment training for CNN or other data-hungry algorithms
Convolutional neural network (CNN) recovers X-ray power with smaller errors than current state-of-art
Power Prediction from with Vision-based Neural Network
Unlabeled data
Labeled Training Set
XTCAV provides best record of X-ray power profile
Problem: Can only measure one image at a time
Alternative: Use computer vision on only lasing-ON image!
X. Ren

## Slide 16: Data Analysis: Pulse reconstruction
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Guess
Field
F(t),F(w)
…
106-109 times
Pulse #1
Pulse #n
X. Zhang
Solve inverse problem w/ NN  1010 speedup!

## Slide 17: Data Analysis: Pulse reconstruction
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Guess
Field
F(t),F(w)
Measure Power
Measure Spectral power
Hidden layers
Output
Input
Guess
Field
F(t),F(w)
…
106-109 times
Pulse #1
Pulse #n
Only solve once!
X. Zhang

## Slide 18: Data Analysis: Pulse reconstruction
groundtruth
prediction
groundtruth
prediction
Amplitude
Phase
Time (fs)
Full beam reconstruction
Measure amplitude of power/spectrum: can I recover phase?
Measure Power
Measure Spectral power
Hidden layers
Output
Input
Guess
Field
F(t),F(w)
Time (fs)
Only solve once!
amplitude
X. Zhang

## Slide 19: Data Analysis: Ghost imaging
Ghost Imaging / Single Pixel Camera
Riddle: How can I take a picture with a spectrometer?
Answer: Have a friend with a flashlight

## Slide 20: Data Analysis: Ghost imaging
target
B = [ 5037,
4783,
4891, … ]
Random patterns
Radiation, A
Ghost Imaging / Single Pixel Camera
=
B
A
x
target reconstruction
Bucket measures total transmission
Philosophy: don’t average out fluctuations… use fluctuations to probe your sample!
 “Compressive ghost imaging” leverages the ML toolbox.
Siqi Li

## Slide 21: Data Analysis: Ghost Imaging
Ghost imaging in the time domain
Pump X-ray
Time
Sample, CO
System (CO) evolves after absorbing X-ray, changing electron energies
Array of buckets (B)
Incident radiation (A)
target
A. Picon
Delay (fsec)
Electron energy (eV)
Target (x)
Probe X-ray
e-
t
“Pump-probe” scan of delay, t

## Slide 22: Conclusion
Additional applications not discussed:
Surrogate modeling: machine design, tuning, user support
Prognostics: Anomaly/breakout detection to avoid/recover from beam faults.
In-the-loop data acquisition: adaptively change experimental parameters during acquisition
User-side: edge-ML for detectors, domain science applications…
And thanks to collaborators:
E. Cropp, J. Duris, A. Edelen, C. Emma, K. Kabra,
D. Kennedy, T. J. Lane, S. Li, T. Maxwell,
P. Musumeci, X. Ren, G. Stupakov, J. Wu, X. Zhang
Thanks for Listening!

## Slide 23: Conclusion

## Slide 24: Data Analysis: Ghost Imaging
Passive measurement of photocathode’s quantum efficiency
Ghost imaging with electrons
Cathode laser
Cathode
target
Total Charge

## Slide 25: Data Analysis: Ghost Imaging
Passive measurement of photocathode’s quantum efficiency
Ghost imaging with electrons
Cathode laser
Cathode
target
Total Charge
Reconstructed QE

## Slide 26: Surrogate Models: FEL simulations
Simulation ~1000 cpu-sec
GAN: ~0.001 gpu-sec
Generative adversarial networks (GANs)
X. Ren
e- energy
“Physics”
GAN
Notes: Genesis simulations provide users very accurate prediction of X-ray pulses for preparing for shifts and testing analysis methods. However, each simulation takes ~1000s of CPU-seconds. For users who require large numbers of examples, e.g.crystallography or statistical methods like ghost imaging, Genesis is too slow.
Generative adversarial networks (GANs) use two networks: the “discriminator” tries to identify if an example is real (i.e. Genesis), or fake (i.e. the “generator”). The generator tries to fool the discriminator. As the two networks fight, the generator makes more and more realistic examples. Images at right show a generated fake XTCAV image (upper right) and the associated X-ray profile (lower right, green). The blue curve is what the old XTCAV algorithm would have estimated from the fake example, showing that the generated example is reasonable.

## Slide 27: Surrogate Models: Accelerator models
J. Qiang
measurement
simulation
High fidelity physics simulations are remarkable:
…but also slow. (e.g. hours on NERSC)
How can we best support design of a new machine?
LCLS-II simulations, Y. Ding
LCLS microbunching instability

## Slide 28: Surrogate Models: Accelerator models
Emma, Edelen, et al. in preparation
Predict XTCAV image from other diagnostic output or upstream machine settings to create a non-destructive virtual diagnostic
Simulation + neural network results match well for FACET-II (see left)
Small study with LCLS machine data and XTCAV images (scan of L1S phase and BC2 peak current at 13.4 GeV)

## Slide 29: Gaussian Process Optimizer
Gaussian process: instance based learning method
Covariance function:
observations
new point
prior mean
new point to predict
taken from M. Ebner, GP for Regression

## Slide 30: Gaussian Process Optimizer
Gaussian process: instance based learning method
observations
new point
prior mean
new point to predict
Prediction of new point:
Variance of new point:
Covariance function:
taken from M. Ebner, GP for Regression

## Slide 31: Gaussian Process Optimizer
Gaussian process: instance based learning method
observations
new point
prior mean
new point to predict
Acquisition function:
Covariance function: