## Slide 1: 10 g scanning
Andrey Alexandrov

## Slide 2: Prerequisites
Ready by October 2018
Scan in 2 months
No time for R&Ds
Deploy all the resources
Optimize for better speed

## Slide 3: Resources
Japan:
  PTS-2 - preselection, 7 g/year
  PTS-3 - preselection, 15 g/year
Napoli:
  Mic6 – plasmon analysis, ~1 min/event -> ~1500 ev./day
  Mic4 – used for R&D -> convert for preselection, 7 g/y
  Mic1 – not in use -> convert for preselection, 7 g/y
LNGS:
  Have 1 microscope convertible for preselection, 7 g/y
Total:
  5 microscopes for pre-selection ~43 g/y
  1 for plasmon analysis, ~1.5k ev./day

## Slide 4: Scanning speed optimization
Current conditions:
  Preselection: 43 g/y => 10 g in 3 months
  Plasmon analysis: 1.5k ev/day (actual ~750 ev/day)
    2 months => max 90k preselected events
    Fog level ~0.1 => preselection selectivity should be ~10-4
    Current selectivity: ~10-2
Possibilities for preselection speed increase:
  Try with the new (critical) illumination system
    Stronger illumination => higher FPS => higher speed
  Increase pixel size to 50-60 nm/pixel (like in Japan)
    28 -> 56 nm/pix => 4x field of view => ~4x faster
  Move to blue light?
    Same conditions as in Japan
Possibilities for Plasmon analysis speed increase:
  Time-limiting factor: volume scan around the prediction
  Increase Z-position accuracy => less volume to scan