## Slide 1: CMS DAQ-2 Shifter Tutorial
Hannes Sakulin, CERN/EP-CMD
On behalf of the CMS DAQ group

## Slide 2: DAQ2 Tutorial Outline
Part 1: Your tasks as a DAQ shifter
Part 2: Overview of the DAQ-2 system
  Change from DAQ-1 to DAQ-2
  DAQ-2 hardware and data flow from the detector to storage / Tier 0
  Flow control
  Software
Part 3: Controlling data taking through Run Control
Part 4: DAQ monitoring tools

## Slide 3: Part 1: Your tasks as a DAQ shifter

## Slide 4: Context
DAQ shifts take place at the CMS Control Room at Point 5 of the LHC in Cessy, France
Three shifts: 7-15, 15-23, 23-7
Five shifters
  Shift leader: manage operations in line with daily plan, monitor data taking, communicate with LHC, safety
  DCS shifter: slow control, access, safety
  DAQ shifter: control, monitor & troubleshoot data taking
  Trigger shifter: monitoring of the L1 trigger
  DQM shifter: monitoring of data quality
  (the latter three shifts may get cancelled under certain circumstances)

## Slide 5
Main DAQ responsibilities:
  Monitor the DAQ
    Make sure the DAQ is running smoothly and that CMS is collecting high quality data!
    This means:
      Monitoring all stages of the DAQ from FEDs -> data sent to Tier 0.
        Data rate, dead time, back-pressure, CPU usage, problems
      Interfacing with the shift crew
  Control data taking as the Shift Leader requests
    Start / stop runs
    Take in / out sub-detectors, FEDs
    Manual re-syncs, hard resets, control random rate
  Troubleshoot the DAQ in case of problems
    But don’t hesitate to call the DAQ DOC (x76600) when you are stuck!
  Document your shift: use the ELOG!
Your responsibilities as a DAQ Shifter

## Slide 6: Your responsibilities as a DAQ Shifter
You are the main responsible for efficient data taking of CMS
  The CMS efficiency will depend to a high degree on your abilities
  As a consequence you need to
    Read and learn the necessary procedures
    Keep yourself up-to-date
      The run environment will evolve in time
      Procedures will change
      Monitoring systems will change
    This means you have to dedicate some time outside of your shift period to study the online DAQ system and how to operate it.

## Slide 7: Your responsibilities as a DAQ Shifter
During your shift you have to communicate continuously with the shift leader and other shifters/DOCs in order to keep running efficiently
  You are needed since the job CANNOT be done by a computer program or a robot !
  Since you are the key person which starts and stops the run, you also should be the key person to overcome or work around problems. This means:
    You should be able to localize where the problem is
      In the central DAQ, or in a subsystem, or in the computing infrastructure
    You must communicate efficiently to the relevant experts and the shift leader in the control room
    You are involved in suggesting workarounds where you can
    You are co-responsible to solve problems in the DAQ and online system
      This often means to efficiently communicate to the expert on call
      You must be precise & concise when reporting problems on the phone

## Slide 8: Your responsibilities as a DAQ Shifter
Be active! Do not just wait for instructions
  This will increase the data taking efficiency.
  If you think time is being wasted, talk to the shift-leader.
  If you think a specific sub-system is blocking for too long the data taking talk to the shift leader.
    You as a cDAQ shifter probably have the best feeling which subsystem is blocking data-taking.
  When you are active, you learn more about the other systems, too. This makes shifting much more fun, and is a good thing for CMS!
But always: Do nothing without informing the shift leader
  In particular when subsystem experts contact you directly: Always involve the shift leader that he/she knows what is going on!
  Always make sure that either you or the shift leader have contacted the relevant sub-system expert (DOC) before deciding to remove subsystems or FEDs from the run

## Slide 9: E-Log
Document your shift in the e-log
  Your entries are essential to make CMS run efficiently. The e-log is a primary source of information for improving the system. With your entries in the e-log you are part of the team which tries to improve the online system to achieve “smooth operation”.
There should be an e-log window already open. Logout the old shifter and log in yourself as soon as you start your shift
  Use the Subsystems>DAQ>DAQ area – there is a link to it in the shifters guide
Please “submit” comments in a timely manner
  That way people offsite can monitor what’s going on
    Many short entries are preferable to one long log entry at the end of your shift!
Document any issues that come up or observations you have about the DAQ, e.g.
  If you have to constantly restart or resync a subdetector, If the DAQ goes into error at any time, anything that seems funny or you don’t understand
  Make sure to copy / paste any error messages that are relevant
    From hotspot / RCMS / handsaw / etc.
  Add context information to the errors
Give a meaningful & correct subject to your log message
    E.g.: “Run blocked due to HCAL FED 1122 sending events out of sequence” (instead of “DAQ crashed”)

## Slide 10: Shift Bulletin Board
Before each shift check the Shift Bulletin Board
  This Twiki page contains
    Procedures
    Settings (e.g. sub-system RUN Keys, FEDs that are out for a period of time)
    Known problems (and workarounds)
    (temporary) instructions
  If you do not fully understand, check with the previous shifter or the DAQ on-call at the beginning of your shift
You must keep the Shift Bulletin Board up-to-date
  The next shifter will rely on it

## Slide 11: General Rules and Policies
Security (computing):
  Never write down passwords in public places where other people have access to (files in your home account, paper on your desk, etc)
  Do not give the passwords to other people
    It is the on-call experts which give the relevant information to the shifters

## Slide 12: General Rules and Policies
Take your work seriously:
  If you have time (during a long smooth run in the night):
    Of course you may check your email on your portable
    Of course you may write an email
    You SHOULD eat and drink something during your shift...
  BUT : You must continuously watch the screens to check that the data taking proceeds as it should.
It is unacceptable that the run stops due to some problem and you do not realize this for 5 minutes.
Shifting is real work, and unfortunately not always exciting or breath-taking...
If you manage to do efficiently other work during your shift, then you do not take the shifting seriously !

## Slide 13: General Rules and Policies
In case you are in trouble:
  FIRST INFORM THE SHIFT LEADER
    Tell him/her what you suggest to do next. (Sometimes he/she does not know what to do...)
You cannot get a run going and beam is there or imminent
  You have serious doubts that the data is taken correctly and/or there is a problem in the central DAQ
  CALL THE DAQ ON-CALL EXPERT AT ANY TIME
  The experts are there to help you at any time. (This is why they do not need to do other shifts)
If you have a problem or question which you are sure is NOT critical to efficient data taking
  Document your problem in e-log
  Call the expert at any time during the day/morning/evening.
  The experts are also there in order to make you more expert!!

## Slide 14: Your shift outline
Arrive 15 minutes early!
  Discuss with previous shifter any problems / issues / requests
  Read through the shift bulletin board and make sure you understand it
  Log into the Elog and begin documenting your shift
If a run is ongoing, check all the monitoring screens
  Is the data flowing ok?
  Do you understand the trigger rate? Is the trigger correct?
Follow any requests from the shift leader
  Never include / remove subdetectors or FEDs without talking to the shift leader
When you have time, take a tour of both the central control room and the subdetector room
  Introduce yourself to your fellow shifters!
If questions/problems do not hesitate to call the DAQ DOC (x76600)

## Slide 15: Documentation and Resources
DAQ shifter bulletin board: read before every shift.
DAQ shifter hypernews: subscribe to this! All DAQ shift related announcements are sent here
DAQ ELOG: Link to DAQ area of the ELOG
DAQ Shift Tutorial: link to slides from shift tutorial
Glossary of DAQ Terms: definition of all the DAQ acroynyms.
Expert on call: link to DAQ DOC area of shift tool
Expert List: link to list of DAQ and HLT experts
DAQ shift schedule: link to DAQ shifters area of shift tool
P5 shuttle: link to shuttle schedule
DAQ2 shifters guide twiki page
  https://twiki.cern.ch/twiki/bin/view/CMS/ShiftPourNuls2014
The leftbar of the DAQ2 shifters guide has many valuable links:
Shifter bookmarks : http://cmsdaqweb/daqpro/ShifterBookmarks.html
Questions about shifts: cms-daqshift-office@cern.ch

## Slide 16: Part 2: The central DAQ system

## Slide 17: The Central DAQ during Run-1 DAQ-1

## Slide 18: CMS DAQ for LHC Run-1
Level-1 Trigger accepting 100 kHz
Custom electronics
Event size up to 1MB
DAQ: 100 GB/s bandwidth
up to 1.2 GB/s
to storage
99.6 % cDAQ availability
(2010-2013 physics runs)
2-stage event builder Myrinet
Gigabit Ethernet
High-Level Trigger working on full events 13000 cores
~500 Hz accept rate
Only 2 trigger levels in CMS
Bunch crossing rate 40 MHz nominal
Myrinet
1 Gb/s Ethernet

## Slide 19: Why build a new DAQ?

## Slide 20: LHC plans
13 TeV center-of-mass energy
40 MHz (25 ns ) operation
targeting 40 fb-1 / year
higher pile-up
Plan for startup after LS1 (2015)
LHC run-2 pile-up scenarios
(*) LHC will perform luminosity leveling to limit pile-up to 50
(*)
(*)
CMS event size
(Run-1 subsystems)
nvtx = PU * 0.7

## Slide 21: New or upgraded detectors in CMS
Several detectors / online-systems being upgraded to cope with higher luminosity
Increase of event size
Readout electronics of upgraded systems based on µTCA
Optical SLINK-express
4 Gb/s or 10 Gb/s - retransmit
2014: New Trigger Control and Distribution System
2014: Stage-1 calorimeter trigger upgrade
2014/15: new HCAL readout electronics
2016: Full trigger upgrade
2017: New pixel detector and readout electronics
SLINK-64 copper cable
400 MB/s
SLINK sender mezzanine
plugged onto VME electronics
640 Legacy Links: SLINK-64
(600 after pixel upgrade)
+ 50 new Links: SLINK-express
(170 after pixel upgrade)
Frontend- Readout Link
Myrinet NIC
SLINK express sender = IP-core
µTCA electronics
Frontend- Readout Optical Link
Fragment size 1..4 kB
Fragment size 2..8 kB
“AMC-13” card used by many subsystems

## Slide 22: Other reasons to upgrade
Ageing hardware
  Most PCs of Run-1 system at end of life cycle
  NICs of Run-1 based on PCI-X
New technologies
  Myrinet widely used when DAQ-1 was designed
  Today Ethernet and Infiniband dominate the Top-500 supercomputers
Top500.org share by Interconnect family
Infiniband
DAQ1 TDR (2002)
Myrinet
1 Gb/s Ethernet
10 Gb/s Ethernet
2014

## Slide 23
100 kHz
L1 rate
Event size up to 1MB
100 GB/s
max. 1.2 GB/s to storage
13000 core filter farm
Event size up to 2MB
(large margin)
~ 3 GB/s to storage
16000+ core filter farm
200 GB/s
100 kHz
L1 rate
CMS DAQ 1
CMS DAQ 2
10/40 Gb/s Ethernet
56 Gb/s Infiniband
Myrinet
1 Gb/s Ethernet

## Slide 24: The Central DAQ during Run-2 DAQ-2

## Slide 25
fat tree: can route to other switches
Core Event Builder: 56 Gb/s FDR Infiniband
Clos network
10 Gb/s TCP/IP links from FPGA
Optical readout link SLINK express
Event Filter
attached by 1/10/40 Gb/s Ethernet
Storage:
Cluster file system
Legacy readout link SLINK-64
Frontend Readout Optical Links
Data Concentrator: Individual 10/40 Gb/s Ethernet switches

## Slide 26: Frontend-Readout Optical Link
10 Gb/s simplified TCP/IP from an FPGA
PCI-x
TCP/IP in principle difficult to implement in an FPGA …
10 GbE
switch
PC running standard TCP/IP Linux stack

## Slide 27: Frontend-Readout Optical Link
10 Gb/s simplified TCP/IP from an FPGA
PCI-x
10 GbE
switch
PC running standard TCP/IP Linux stack
Simplified unidirectional TCP/IP only needs 3 states
x
x
x
x
x
x
x
x
x

## Slide 28: New in 2017: FEROL 40 board
4x 10 Gb/s SLINK Express in
40 Gb/s (4x 10 Gb/s) TCP/IP to DAQ
uTCA standard
Used to read out Pixel Upgrade

## Slide 29: Data concentrator
48 Frontend Readout Optical Links (FEROLs)
per data concentrator switch
Individual 10/40 Gb/s Ethernet switches
Mellanox MSX1024
48 x 10 Gb/s in
6 x 40 Gb/s out
patch panels
Readout Unit (RU) PCs
links to fat tree

## Slide 30: DAQ-1: FRL/Myrinet
DAQ-2: FRL/FEROL 10 Gb/s Ethernet
Switchover completed

## Slide 31
Data concentrator patch panels
and switches

## Slide 32: Core Event Builder
6 Tb/s per direction
3.5 Tb/s
108x72 Event Builder – 56 Gb/s FDR Infiniband Clos network (108x108 IOs)
6 spine switches
12 leaf switches
Inputs and outputs mixed on leafs to better utilize leaf-to-spine connections
Infiniband
reliable in hardware at link level (no heavy software stack needed)
supports credit-based flow control
switches do not need to buffer
can construct large network from smaller switches
cost effective

## Slide 33
Infiniband Clos network

## Slide 34: Core event builder performance tuning
40 Gb/s Ethernet
  Linux stack with performance tuning
56 Gb/s Infiniband
  Software based on Infiniband Verbs API
  All data transport by RDMA
In both cases:
  Multiple threads for data reception and writing
  CPU affinities tuned
    threads
    memory pools
    interrupts
dual 8-core E5 2670
dual 8-core E5 2670
Non-Uniform Memory Access (NUMA)

## Slide 35: Filter Farm
Infiniband
Appliance
(=BU and its FUs)

## Slide 36: HLT farm, DAQ2
 | 2012 extension of DAQ-1 Dell Power Edge c6220 | HLT PC 2015 Megware S2600KP | HLT PC 2016 Action S2600KP | HLT PC 2018 Maguay
Form factor | 4 motherboards in 2U box | 4 motherboards in 2U box | 4 motherboards in 2U box | 4 motherboards in 2U box
CPUs per mother-board | 2x 8-core Intel Xeon E5-2670 Sandy Bridge, 2.6 GHz, hyper threading, 32 GB RAM | 2x 12-core Intel Xeon E5-2680v3 Haswell, 2.6 GHz, hyper threading, 64 GB RAM | 2x 14-core Intel Xeon E5-2680v4 Broadwell, 2.5 GHz, hyperthreading, 64 GB RAM | 2x 16-core Intel Xeon Gold 6130 Skylake, 2.1 GHz, hyperthreading, 92 GB RAM
#boxes | 64 (=256 motherboards) | 90 (=360 motherboards) | 81 (=324 montherboards) | 100 (=400 motherboards)
#cores | 4096 | 8640 | 9072 | 12800
Data link | 2x 1Gb/s | 1x 10 Gb/s, 1x 1Gb/s | 1x 10 Gb/s, 1x 1Gb/s | 1x 10 Gb/s, 1x 1Gb/s
2012 64x
2015 90x
Total 2018: 31k cores on 1100 motherboards
2016 81x
Cloud / Spare
2018
100 x

## Slide 37: HLT farm, DAQ2
Total 2018: 31k cores on 1100 motherboards

## Slide 38: File based Filter Farm Data Flow
BUs build full events and write them to RAM disk
Several FU machines per BU run CMSSW processes to reconstruct / filter the events
  CMSSW input/output is file based
  BU-FU data transfer uses file systems as a protocol
  8-16 FUs mount ram disk via NFSv4 over the BU-FU network :
    40 to 10 Gbit Ethernet (1 Gbit on legacy FU)
The output files of the CMSSW processes are merged by the Micro-Merger on the FU and written back to a hard disk on the BU over NFS.
BU-FU Appliance
FUs
Notes: 13:00

## Slide 39: Merging
File-Based Filter Farm produces output files
  After micro-merging on FU: 1100 files x 10 streams per lumi section (23s) scattered over hard disks on 72 BUs
  To be merged to 1 file per stream and lumi section in a central place
Merging is done by a Global File System (Lustre)
  Micro-merging on FU
  Mini-Merging on BU
  Macro-merging on dedicated merger nodes
Lustre
DQM
BU
~ 4.5 GB/s write
+ ~ 4.5 GB/s read
Notes: 15:00

## Slide 40: Mini-Merge step
BU1
BU2
BU64
Single output file in the cluster file system
One file per event filter PC on hard disk of Builder Unit
…
merger
2 TB hard disk
Mini-Merge step
  Merger process on BU reads data from all FUs in the appliance
  Data are written directly from the BUs to a single output file per stream in the global file system
    Exception: DQM streams: One file per BU in the global file system

## Slide 41: Macro-Merge step and Transfer System
Macro-Merge step
  Single output file in Lustre is checked and resized
  Exception: DQM streams
    Output files per BU are read from Lustre and written to single output
      Cut on size (2 GB) and timeout of 15s to ensure DQM data gets to DQM in time
    Histograms are added
Transfer
  Merged data are then transferred from Lustre to Tier 0 or to consumers (e.g. DQM/Event Display) at pt.5
Lustre
DQM
BU
~ 4.5 GB/s write
+ ~ 4.5 GB/s read

## Slide 42
fat tree: can route to other switches
Core Event Builder: 56 Gb/s FDR Infiniband
Clos network
10 Gb/s TCP/IP links from FPGA
Optical readout link SLINK express
Event Filter
attached by 1/10/40 Gb/s Ethernet
Storage:
Cluster file system
Legacy readout link SLINK-64
Frontend Readout Optical Links
Data Concentrator: Individual 10/40 Gb/s Ethernet switches

## Slide 43: Flow control
The entire DAQ from detector to storage is loss-less
If cDAQ cannot handle the data throughput, back-pressure is propagated all the way back to the FED
  Bandwidth limitation in any part of CDAQ
  CPU limitation in the filter farm
  A failure / crash
Buffers in the FED may fill up
  If too much data is coming from the detector
    Backgrounds, noise, high trigger rate, wrong settings
  Or if the FED is back-pressured by CDAQ
In this case the FED throttles the trigger
  Through the Trigger Throttling System (TTS) A tree of Fast Merging Modules (FMMs)

## Slide 44: Trigger, TCDS + flow control
Each FED sends a TTS signal
    Possible sTTS signals: Busy, Warning, OutOfSync, Error, Disconnected, Ready
FEDs are grouped into partitions
FMMs (Fast Merging Modules) merge sTTS signals from FEDs in each partition
Merged signals sent to TCDS (Trigger Control and Distribution System) which reacts according to the signal
  i.e. blocks triggers from Global Trigger for all states except Ready
Special cases of TTS signals that are only seen by TCDS (not by the FMMs):
  For tracker partitions also the emulated APV state is an input to the partition controller
  New uTCA FEDs send their TTS status through the TTC Partition Interface to TCDS
TCDS
Global Trigger
Physics triggers
Physics
+calibration +random triggers
DAQ
back- pressure
FRL/ FEROL

## Slide 45: Software

## Slide 46
L1 trigger electronics
Sub-det DAQ electronics
Central DAQ electronics
Low voltage High voltage
Gas, Magnet
Front-end Electronics
data
control
data
…
XDAQ Online Software
The online software
XDAQ Application
XDAQ Framework – C++, XML, SOAP
XDAQ applications control hardware and data flow
XDAQ is the framework of CMS online software It provides Hardware Access, Transport Protocols, Services etc.
data
Central DAQ Event Builder
High Level Trigger Farm & Storage

## Slide 47
…
Function Manager Node in the Run Control Tree defines a State Machine & parameters
User function managers dynamically loaded into the web application
Run Control System – Java, Web Technologies
Defines the control structure
HTML, CSS, JavaScript, AJAX
GUI in a web browser
Run Control Web Application Apache Tomcat Servlet Container
Java Server Pages, Tag Libraries,
Web Services (WSDL, Axis, SOAP)
L1 trigger electronics
Sub-det DAQ electronics
Central DAQ electronics
Low voltage High voltage
Gas, Magnet
Front-end Electronics
data
control
data
…
XDAQ Online Software
Level-0
DAQ
Trigger
ECAL
Tracker
…
DCS
Trigger Supervisor
Run Control System
…
DQM
The online software
Central DAQ Event Builder
High Level Trigger Farm & Storage
CMSSW
CMSSW
CMSSW
HLTD
merger
transfer

## Slide 48
L1 trigger electronics
Sub-det DAQ electronics
Central DAQ electronics
Central DAQ Event Builder
Low voltage High voltage
Gas, Magnet
Front-end Electronics
data
control
data
Tracker
ECAL
Detector Control System
…
…
…
XDAQ Online Software
TRG
DAQ
Monitor collectors
…
XDAQ monitoring
& alarming
Live Access Servers
Level-0
DAQ
Trigger
ECAL
Tracker
…
DCS
Trigger Supervisor
Run Control System
…
DQM
errors alarms
monitor clients
YOU (as DAQ shifter)
DCS Shifter
The online software
WinCC OA (Siemens ETM)
SMI++ (CERN)
High Level Trigger Farm & Storage
CMSSW
CMSSW
CMSSW
HLTD
ES
tribe
Elastic search
F3 mon
merger
transfer
ES

## Slide 49: File-based Filter Farm Software
FFF on appliances is controlled by a service (hltd), asynchronous to Run Control
hltd is running on BUs and FUs and responsible for:
  Detecting a new run (run directory in ramdisk appears)
  CMSSW runs as standard cmsRun jobs, process input files
  Output bookkeeping and copying merged data files to BU
Monitoring
  Using elasticsearch (a search engine)
  Data is indexed, searching for specific information is available in near-realtime
  Running on central ES server clusters
  Insertion of information by hltd or merger services
    CPU usage, event processing statistics, merging completion, logs (more details later in F3Mon description)
injection
Notes: 13:00

## Slide 50: How Run Control starts up a sub-system: Run Control + XDAQ system structure configurable
Job Control Service
Resource Service Database
XML
XML
Control structure
  Function Managers to load (URL)
  Parameters
  Child nodes
Configuration of XDAQ Executives (XML)
  libraries to be loaded
  applications (e.g. builder unit, filter unit) & parameters
  network connections
  collaborating applications
Resource Service API
Load configuration
High-level tools
Run Control
start & configure
applications
configurations
Store configuration

## Slide 51: Level-0 interaction
Level-0
L1-Trigger
Central DAQ
PIX
TRK
ECAL
DQM
CSC
…
Configuration DBs
Online Monitoring
Detector Control
LHC
EVB
FB
LHC + HV state
Resource Service
L1 Trg
Equipment
HLT
Run Info
Session
Logs
Run Mode
DAQ shifter Control room
FED
FEC
On-Call Expert
…
Data Quality Monitoring
FED Builder
Event Builder
GCM
sub-detectors

## Slide 52: RCMS: Registration and Keys
Sub-system configurations need to be “registered” with the Global Configuration Map Database. This is done by the DAQ on-call expert or sub-system experts
The Level-0 Function Manager queries the DB
  to know what configuration to start for a subsystem
    Important: when a new configuration is registered you need to destroy (red recycle) the corresponding FM
  to know what RUN KEYS are available for a subsystem
    You can parameterize a subsystem’s configuration by selecting a run key (unless the key is are selected by a CMS Run Mode)

## Slide 53: Part 3: Controlling data taking through Run Control

## Slide 54: Create FM Level Zero
RCMS workflow to create the FM Level Zero
  Log into RCMS as toppro (http://cmsrc-top.cms:10000/rcms)
  Configuration Chooser: Path: PublicGlobal/LevelZeroFMwithAutomator
  Press on “Create”
    At this point the Level 0 Function Manager is created in the tomcat.

## Slide 55: 1. RCMS interface
    This is your main interface to DAQ management. This is the window where you will configure the CMS running mode, start / stop runs, remove / add subdetectors and FEDs, and look for errors.

## Slide 56: 1. RCMS interface
Main activity (start / stop / TTCResync etc)
Subdetector status (Running, Configured, Error, etc)
Subdetector Configuration Keys
Subdetector recycle/reconfigure & commander buttons
Additional info from subdetectors (could be errors)

## Slide 57: 1. RCMS interface
Slow Control (DCS / LHC) information (when available)
Information (and settings) for Trigger keys, Clock source, TCDS

## Slide 58: Managing the run: start / stop runs
Main activity (start / stop / TTCResync etc)
Subdetector status (Running, Configured, Error, etc)
Subdetector Configuration Keys
Subdetector recycle/commander buttons
Additional info from subdetectors (could be errors)

## Slide 59: Simplified state diagram for run control
In green are commands, in black are states reached after command is executed
Note that “Error” state can happen during any step
Only valid commands in each state are enabled in the Run Control screen
Paused
Halted
Error
Running
Configured
Faulty/Error
Initialize
Configure
reConfigure
Stop
Pause
Resume
Start
Halt
Destroy
Re-configure = (Halt) + Configure
Re-cycle = Destroy + Initialize

## Slide 60: Full state diagram for run control
In green are commands, in black are states reached after command is executed
Note that “Error” state can happen during any step

## Slide 61: Starting / Stopping runs
In general, you will use the buttons in the main activity area
  Here the initialize / configure / start / stop buttons will address all subdetectors in the run
    There is an order in which the commands must be sent to subdetectors, and the order is built into the L0 function manager
It is possible also to use the “commander” and / or “recycle” buttons below the subdetector
  Sends commands only to one subdetector
  If this command requires subsequent action on another subdetector, then there will be a flashing message next to the subdetector that requires action
    E.g. if you add a subdetector into the run when the TCDS or DAQ (or both) is already configured, a flashing message next to the TCDS / DAQ will tell you to reconfigure it
  Recycle/Reconfigure buttons
    There are two: “red” recycle and “green” reconfigure
    Red recycle destroys the subdetector function manager and restarts it, ending in the “halted” state. You can do this from any state, you must do this from the “error” state
    Green reconfigure reconfigures the subdetector only. You can do this either from the “halted” or “configured” state

## Slide 62: Adding / removing subsystems and/or FEDs
FED & TTS button
Subdetector recycle/commander buttons
To add / remove FEDs or subsystems, click on the FED & TTS button
The window on the next slide will pop up
To remove an entire subsystem, you can also choose the “Destroy and Out” command from the commander pull down menu

## Slide 63: Adding / removing subsystems and/or FEDs
Following is pictures / more in depth information

## Slide 64: Adding / removing subsystems and/or FEDs
FED groups help to differentiate between subsystems within a partition

## Slide 65: Sub-Systems Control Panel
The Sub-Systems panel contains:
  All the subsystems included in the Global Run
  State of each subsystem
  Applied Run Key for each subsystem
  Run Key selector
  Commander for each subsystem:
    The pull down menu allows to send command directly to the subsystem
    Red re-cycle button allows to destroy the subsystem software and bring it to halted state.
    Green re-cycle button allows to (re-)configure the subsystem software.

## Slide 66: FM L0 built-in cross-checks
  Indicate sub-systems to re-configure if :
    A parameter is changed in the GUI
    A sub-system / FED is added/removed
    External parameters change
  Enforce correct order of re-configuration
  Enforce procedure to follow if LHC clock stability changes

## Slide 67: Access Control
Subsystems are created by the Level-0 in a locked state and the subsystem RCMS GUIs may be attached for read access but may not command the subsystem or set parameters.
If a subsystem-expert needs to access the sub-system through their RCMS GUI, you may unlock the subsystem by clicking on the lock icon. You should lock the subsystem again after the intervention is finished.
If a subsystem was created by a GUI or by a different Level-0, the central Level-0 may not be able to command this subsystem. In order to control the subsystem from the central Level-0, the subsystem must be destroyed from where it was created.
Destroy Backdoor (this applies for any Function Manager, whether it belongs to a subsystem or it is the Level-0 itself): If things went wrong and you cannot destroy a Function Manager in any regular way.

## Slide 68: Run and Trigger mode selection
Select CMS Run Mode other than MANUAL
All keys defined by CMS Run Mode
including (some) sub-system RUN KEYs
Tick to auto-select CMS Run Mode
Based on LHC mode (Only available if connection to DCS is working)

## Slide 69: You may sometimes need: Manual RUN MODE
Select CMS Run Mode is MANUAL
L1 and HLT keys defined by L1/HLT mode
Select L1/HLT Mode
Select clock source
( Select primary/secondary TCDS system – not yet available)
Attention: You also need to select sub-system run keys manually

## Slide 70: You may rarely need: Manual L1/HLT MODE
Select CMS Run Mode is MANUAL
L1 Keys defined by trigger shifter
L1/HLT Mode is MANUAL
Select clock source
( Select primary/secondary TCDS system – not yet available)
Choose HLT key and HLT SW Architecture
Attention: You also need to select sub-system run keys manually

## Slide 71
Monitoring Services
XDAQ Online Software
Detector Control System
…
…
Subs n
Subs 1
…
Run Control System
errors alarms
monitor clients
DAQ Operator
DCS Operator
L1 trigger electronics
Sub-det DAQ electronics
Central DAQ electronics
Central DAQ Event Builder
Low voltage High voltage
Gas, Magnet
Front-end Electronics
data
control
data
File based Filter Farm & Storage
Trigger Control and Distribution System
LHC
HV status, LHC state
Level-0 Function Manager
Automator Function Manager
HLT, merge & transfer control
Config DBs
DCS
SM
Gd
SE
Conf
Ind.
Automator
DAQ Expert

## Slide 72: Level-0 Automator
Start a run from any state
Stop a run then re-start
Taking into account all cross-checks (except sanity checks)
Taking into account scheduled actions
Attempting to recover from failures (2 retries, currently)
Schedule “at-fault” is for future automatic down-time splitting

## Slide 73: Level-0 Automator
When to use what button
  If we are not “Running”
    “Start Run” will start a new run ( “Recover Run” will do the same thing)
  If we are “Running”
    “Recover Run” will stop, then start a new run (“Start Run” has no effect)
When to use the automator
  To start a run
    First set all settings (Subsystems & FEDs in/out, run mode etc. )
    Then let the automator re-configure / re-cycle subsystems as necessary and start a new run
  To recover from a problem (if you know the appropriate recovery action)
    Select the recovery action in the Schedule
    Let the automator stop the run, re-configure / re-cycle subsystems as necessary and start a new run
  To apply changed settings such as a new run mode or trigger key
    Just click “Recover Run” while a run is going
    The automator stops the run, recycles/ reconfigures subsystems as requested by indicators and starts again

## Slide 74: Level-0 timeline
Shows history of subsystem states and all manual and automatic actions taken

## Slide 75: Level-0 timeline
Tool tips give information about the reasons for action

## Slide 76: Level-0 timeline
Tool tips give information about the reasons for action … and their outcome

## Slide 77: Tooltips for errors

## Slide 78: Going back to analyze problems

## Slide 79: FM L0 Links Panel
Save
Save the configuration parameters of the Level Zero GUI.
Refresh
Refresh the Level Zero page.
Detach
Disconnect the Level Zero GUI from the Level Zero FM.
Destroy
Kill all Function Managers and XDAQs started by them

## Slide 80
Automation: Automatic reaction to
LHC beam/machine mode and DCS high voltage state

## Slide 81
Monitoring Services
XDAQ Online Software
Detector Control System
…
…
Subs n
Subs 1
…
Run Control System
errors alarms
monitor clients
DAQ Operator
DCS Operator
L1 trigger electronics
Sub-det DAQ electronics
Central DAQ electronics
Central DAQ Event Builder
Low voltage High voltage
Gas, Magnet
Front-end Electronics
data
control
data
File based Filter Farm & Storage
Trigger Control and Distribution System
LHC
HV status, LHC state
Level-0 Function Manager
Automator Function Manager
HLT, merge & transfer control
Config DBs
DCS
SM
Gd
SE
Conf
Ind.
Automator
DAQ Expert

## Slide 82: DAQ actions on LHC and DCS state changes
Extensive automation in the Detector Control System (DCS)
  Automatic handshake with the LHC
  Automatic ramping of high voltages (HV) driven by LHC machine and beam mode
Some DAQ settings depend on the LHC and DCS states
  Suppress tracker payload while HV is off (noise)
  Reduce pixel gain while HV is off
  Mask sensitive channels while LHC ramps …
Automatic new run sections driven by asynchronous state notifications from DCS/LHC
Level-0
DAQ
Tracker
…
DCS
Tracker
ECAL
Detector Control System
DCS
Run Control System
…
PSX
LHC
PVSS SOAP eXchange
XDAQ service

## Slide 83: Automatic actions driven by the LHC …
LHC dipole current
…
ramp start Mask
sensitive trigger
channels
ramp done Unmask
sensitive trigger
channels
Tracker HV on
Enable payload (Tk) raise gains (Pixel)
DCS ramps up tracker HV
DCS ramps down tracker HV
Tracker HV off
Disable payload (Tk) reduce gains (Pixel)
Automatic actions in DAQ (“PerformingDCSPauseResume” state)
…
Special run with circulating beam
ADJUST
STABLE BEAMS
STABLE BEAMS
section 1
section 1
section 2
section 1
2
Start run at FLAT TOP. The rest is automatic.
DCS ramps up pixelHV
DCS ramps down pixelHV
3
Collisions run

## Slide 84
Automatic recovery from Soft Errors

## Slide 85: Automatic soft error recovery
With higher instantaneous luminosity in 2011 more and more frequent “soft errors” causing the run to get stuck
  Proportional to integrated luminosity
  Believed to be due to single event upsets
Recovery procedure
  Stop run (30 sec)
  Re-configure a sub- detector (2-3 min)
  Start new run (20 sec)
One Single Event Upset (needing recovery) every 73 pb-1
Single-event upsets in the electronics of the Si-Pixel detector. Proportional to integrated luminosity.
  3-10 min down-time

## Slide 86: Automatic soft error recovery
…
From 2012, new automatic recovery procedure in top-level control node
  Sub-system detects soft error and signals by changing its state to RunningSoftErrorDetected
  Top-level control node invokes recovery procedure
    Pause Triggers (TCDS)
    Invoke newly defined selective recovery transition on requesting detector (FixSoftError)
    In parallel perform preventive recovery of other detectors
    Resynchronize
    Resume
Function Manager
  12 seconds down-time
At least 46 hours of down-time avoided in 2012

## Slide 87: Other special states
RunningDegraded
  Subsystems may change into RunningDegraded state if data taking is still continuing, but there is a problem requiring the attention of the shift crew
  The subsystem message panel should contain a message describing the problem
  Discuss with the shift leader how to proceed and check with the corresponding DOC if the message is not 100% clear.
RunBlocked
  The DAQ and Level-0 may change into the RunBlocked state if the DAQ received corrupted data from a subdetector
    It is possible to (Force-)Stop the run from RunBlocked state.

## Slide 88: Part 4: Monitoring tools