## Slide 1
Monitoring of the DAQ2 system
  Remi Mommsen, FNAL
  Andre Holzner, UCSD

## Slide 2: Monitoring tools
RCMS/LVL0 interface
  Has been covered by Hannes
aDAQMon
  Overview screen to see at a glance the CMS running configuration and rates.
DAQView
  Most comprehensive monitoring tool for issues with data flow. Here you can monitor the data from FEDs to BUs.
DAQ Expert application
  automatic detection of error conditions and displaying of instructions how to get the run going again
  replacement of the DAQ doctor
Elastic Search / Filter Farm monitoring (HLT, File Merging & Transfers)
  Shows state of HLT processing. Important monitor of file-based filter farm (FFF).
CPM controller
  Central Partition Manager for the TCDS system. Good place to see rates, state of detector inputs, etc.
HotSpot
  Central display for sentinel messages for errors from all processes.
Handsaw
  Scrolling display of error messages

## Slide 3: aDAQmon – DAQ Status Display
HLT Output Streams
  http://cmsonline.cern.ch/daqStatusSCX/DAQstatusGre.html
Data taking history
DAQ flow
DAQ sub-system configuration
Status bar gives a quick overview of the DAQ
HLT activity

## Slide 4
Main systems (LHC, DCS,...) status
FED-RU data stream
FED RU configuration
Box color:
Sub-Sys ID
FED IN
FED OUT
RU bandwidth plot
BU bandwidth plot
# Ev. in BU
BU RAM disk %
BU OUT disk %
DAQ Sub-Sys configuration
Event storage summary
RU/BU box color:
Application state
RU/BU box RED frame:
flash data not updated

## Slide 5
DAQView

## Slide 6: DAQView http://daq-expert.cms/daq2view-react/
Status & navigation
FED Builder FEROL/FMM
Event Builder RU/EVM
FFF Appliances
BU & FU
Background turns red when EvB is Enabled & no data is flowing

## Slide 7: DAQView - Navigation
Stop refreshing page
Switch pages between FEDbuilder, FFF, and all
Current run
Duration and start time of run
Last update of page must be current!
If this is stale, call the oncall expert
go back/forth in time
go to a specific point in time
get a link for current view (useful to paste to ELOG)
switch to DAQExpert for this point in time
current Level0 FM state and time when state was reached
DAQ subsystem state
LHC states
DAQ configuration
(blacklist version etc.)

## Slide 8: DAQView – Global TTS
dead time in clock cycles with actual bunch crossings
total dead time in %
Trigger throttling system (dead time from subsystems)
in ‘FB+DT Table’ view
dead time in all clock cycles
dead time from trigger rules
(can come from trigger microbursts)
resonant trigger veto
(e.g. 11 kHz zero bias triggers)
backpressure from DAQ
triggers lost due to calibration
sequence

## Slide 9: DAQView – FED builder
TTC partition name & no.
Current TTS state of partition P: TTS state from TCDS
F: TTS state from FMM
A: APVE emulator TTS state
%warning, %busy in TTS partition
FEROL PC (link to hyperdaq page)
FED information (see next page)
min/max # fragments received by FEROL. Highlighted in yellow if different to trigger.
Min is only displayed if not equal to max.
FED builder name
Confused? Try the table help button!
screenshot still from classic DAQView, appearance is slightly different in current DAQ2View
DAQ2View allows sorting columns

## Slide 10: DAQView – FEROL and FMM
Entries are of form
  FRL_geoslot: FEDSourceID or
  FRL_geoslot: FEDSourceID1, FEDSourceID2 or
  FEDSourceID
    For a pseudo-FED (=TTS link only, but no data is read out by DAQ)
Additional info may be displayed next to the FEDSourceID (from left to right)
  Percentage of time during which FED was in Warning ( ) or Busy ( ) during the last 3 seconds (if non-zero)
  Current state of TTS if other than Ready
  FEDSourceID (expected) 601
    Grey if FRL input not enabled (FMM not enabled in case of pseudo-FED)
    Highlighted in color of current TTS state if other than Ready
  Percentage of time with DAQ backpressure during last update interval (5s) if non-zero
    < is meant to be an arrow, not an inequality
  Warnings
    Received source ID different to expected
    FED or SLINK CRC errors
    Number of fragments received by FRL if no data is flowing and this FRL is lagging “behind”
uTCA FEDs (FED id >= 1024) do not have an FMM
  Busy/warning in column ‘P’ DAQView
Use this to judge whether a FED is creating dead-time because of a FED problem or because of DAQ-backpressure
W:9.9%
B:0.2%
W
<6.9%
#FCRC=69
9605

## Slide 11: DAQView – RU/EVM Information
EVM/RU host
(link to hyperdaq page)
First row is TCDS / EVM
Rate (kHz)
# fragments built by RU/EVM since start of run
# incomplete fragments >> 1 indicates a problem on the RU
Throughput (MB/s)
Super-fragment size (kB)
# events currently in RU
>>1 indicates problem in IB
# requests by BU normal EVM >> 1 && RUs < 10
Each row is one FEDbuilder
Shaded values mean FEDbuilder is not in readout
screenshot still from classic DAQView, appearance is slightly different in current DAQ2View
DAQ2View allows sorting columns

## Slide 12: DAQView – FFF/BU
BU host
(link to hyperdaq page)
Rate per BU (kHz)
Throughput (MB/s)
Event size (kB)
Confused? Try the table help button!
Events built since start of run
# events being built
in this moment
Resource information (see next page)
# files written
# LS for which there is a file
Current LS number
each line is one appliance
# LS queued on output disk on FUs
# LS queued for FUs
BU state
output
bandwidth

## Slide 13: DAQView – BU Resources
BUs have use a fixed number of requests (20 in the current configuration)
  Each request corresponds to multiple events (32 in the current configuration)
The number of active requests may vary during a run
  Load balancing between independent appliances
  Backpressure mechanism if FFF/HLT cannot keep up
A request is sent to the EVM (#req. sent) when all events of the request have been handled
  If #req sent > 0, the BU is able to accept new events
When the BU got at least one fragment for the request, the request is ‘used’ (#req. used)
  The more request are used, the busier is the BU (either building events or waiting for data)
Resources can be blocked (#req. blocked)
  RAM disk becomes full
  Not enough FU CPU cores are available to process data
  FU processing lags behind
Requests have a priority depending on the load of the BU appliance
  BUs with lower priority number get events first

## Slide 14: DAQView – Running, or not?
LVL0: DAQ is running
No, rate is 0 kHz
None of the HF FEDs has sent any events
No fragments in RU
Many events requested
No data flow as HF has not sent any data  Talk to HCAL expert
screenshot still from classic DAQView, appearance is slightly different in current DAQ2View

## Slide 15: DAQView – Who Blocks the Run?
ECAL is 100% in Warning
Rate is 0 kHz
FED 602 is in warning and last event is 9605
There’s backpressure from DAQ
RU waits for data from FED 59
FED 59 has not sent any data
FED 59 is the culprit  Talk to Tracker expert
screenshot still from classic DAQView, appearance is slightly different in current DAQ2View

## Slide 16: DAQView – DAQ backpressure
ECAL is 50% in Warning
There’s backpressure from DAQ
Very few events requested by BUs
Some BUs have Failed
Resources blocked
Many FUs are stale
Data queued on HLT output
FFF output bandwidth is too high  HLT is accepting too many events  Check with trigger shifter for high L1 rates or call HLT DOC
The rate is 10 kHz
Data queued for HLT
DAQ FM goes into ‘Running Degraded’ when BUs fail
After massive failures on the FFF/HLT, DAQ oncall has to be called
screenshot still from classic DAQView, appearance is slightly different in current DAQ2View

## Slide 17: DAQ Expert
Automatic detection of problems in the event builder
  and instructions to fix the problem
Web application
Two main components:
  Dashboard
    current status/problem and instructions how to fix it
    recent problems
    recent sound messages and state changes
  Browser
    timeline of error conditions and other information
    mainly for DAQ DOC
Replaces the Run I DAQ Doctor
Core logic: classic ‘flow chart’ (see backup slides)
  https://twiki.cern.ch/twiki/pub/CMS/ShiftNews/DAQStuck5.pdf
  however not maintained anymore, conditions and solutions were and will be added to the DAQExpert
DAQExpert has been used throughout 2017, your feedback is welcome !
the first place to look at when triggers stop unexpectedly !

## Slide 18: DAQ expert
introduction/documentation at: http://daq-expert.cern.ch/

## Slide 19: DAQ Expert dashboard
http://daq-expert.cms/nm/dashboard.jsp
overall status (nothing to worry about at the moment)
recent problems and proposed solutions
all recent events (includes state changes and sound messages)

## Slide 20: DAQ Expert dashboard
overall status: there is a problem now which you need to solve !
problem is currently active
follow these steps to fix the problem
symptoms

## Slide 21: DAQ Expert dashboard demo
Example walkthrough: http://daq-expert.cern.ch/dashboard-demo.html
shows:
  normal (‘happy’) state
  an event that generates a sound in the control room
  an event that generates spoken text in the control room
  a problem without known solution (i.e. no recovery suggestions)
  a new problem which is considered more important than the currently active problem (problems overlapping in time)
have a look at this in your browser after the tutorial !

## Slide 22: DAQ Expert browser
FC = flow chart case
1 event in the time range shown
time axis
(scroll to zoom in/out, pan to move)
total events collected in run
LHC and CMS DAQ
state changes etc.
downtime / problems
readout rate
Confused? Try the help button!

## Slide 23: DAQ Expert browser
click on it for further details

## Slide 24: DAQ Expert browser

## Slide 25
F3 Mon

## Slide 26: File-based Filter Farm (FFF/F3)
Filter Units (FUs) run the CMSSW processes selecting events for permanent storage
  Each FU runs multiple, multi-threaded CMSSW instances
  Accepted events are written to the local disk
The Storage and Transfer System aggregates files (event data, DQM histograms & metadata)
  Micro-merger on each FU aggregates the data from all processes on the FU
  Mini-merger on the BU aggregates the data from all FUs
  Macro-merger(s) aggregate the data from all BUs
  Data are aggregated per stream and luminosity section
  DQM data might suffer delays when merging is lagging behind
Error stream contains events which crashed the CMSSW process
  Backtrace is available from F3 mon (see next slide)
  CMSSW processes are restarted after a crash a few times, after that they are “quarantined”
    DAQ oncall needs to clean up the FFF when this happens
  If there is a low rate of crashes, the HLT DOC should be notified

## Slide 27: F3 Mon http://es-cdaq.cms/f3mon
  Animated introduction available at http://cmsdaqfff/prod/doc/presentation/
List of recent runs
Access old runs
Active run
Errors from HLT
Time chart of HLT activity
Confused? Try the guide!
Stream rates vs LS
Stream names (click to hide them)
Completeness of data
Error events!
Both boxes must be green

## Slide 28: F3 Mon – Bad Situation
Merging incomplete (color is not green)
Huge rate
Many alerts
>5GB/s output
FFF output bandwidth is too high  HLT is accepting too many events  Check with trigger shifter for high L1 rates or call HLT DOC

## Slide 29: F3 Mon – Alerts Panel
Click here to open alerts panel

## Slide 30: Storage Manager Page 1 https://cmsonline.cern.ch/webcenter/portal/cmsonline/pages_common/storagemanager
Gives an overview of the data transfer to tier 0 for recent runs
  Number of files, sizes and event rates per stream
  Totals per run
Check that files are injected, transferred and checked
  Suspicious values are color coded
  in case of problems: make an elog entry and send an email to cms-storagemanager-alerting@cern.ch

## Slide 31
Central Partition Manager

## Slide 32: TCDS
Combines the pre-LS1:
  Trigger Control System (TCS) The conductor of all CMS triggering and data-taking
  Trigger Timing and Control (TTC) The distributor of clock, L1As, and synchronisation signals
  Trigger Throttling System (TTS) The feedback of readiness states from FEDs to TCS
Many-legged creature:
  The ‘head’ is the Central Partition Manager (controlled by central DAQ)
  Many different legs (i.e., partitions) across the different subsystems (controlled by the subsystems)

## Slide 33
TCDSCentral http://tcds-control-central.cms:2000/urn:xdaq-application:lid=100

## Slide 34
TTC machine interface applications
Provide the connection between the LHC RF and timing signals and CMS.
TCDSCentral http://tcds-control-central.cms:2000/urn:xdaq-application:lid=100

## Slide 35: TCDSCentral http://tcds-control-central.cms:2000/urn:xdaq-application:lid=100
Central Partition Manager (CPM)
Drives CMS. Controls triggers, calibration sequence, timing and synchronisation, …
This application should tell you what and how many triggers are flowing,
or why not.

## Slide 36: CPMController http://tcds-control-cpm-pri.cms:2050/urn:xdaq-application:lid=100

## Slide 37: CPMController http://tcds-control-cpm-pri.cms:2050/urn:xdaq-application:lid=100
Running state shows if triggers are flowing or why not:
Stopped
Running
Blocked by TTS
Blocked by DAQ backpressure
etc.
TTS and trigger blockers tab

## Slide 38: CPMController http://tcds-control-cpm-pri.cms:2050/urn:xdaq-application:lid=100
This tab shows:
What rate of triggers are flowing, per type
What rate of triggers are being suppressed, per type
What the deadtime is, per source
How much time each partition spends in TTS not-READY (at the bottom)
Rates and deadtimes tab
Dead times are shown twice
Averaged over all bunch crossings
Averaged over bunch crossings where collisions happen (BeamActive)

## Slide 39: CPMController http://tcds-control-cpm-pri.cms:2050/urn:xdaq-application:lid=100
Click here to change the random trigger rate
Input Sources

## Slide 40: HotSpot https://xdaq.web.cern.ch/xdaq/xmas/14/hotspot/hotspot.swf
Make sure that it updates (pulsates)
Check regularly for Errors or Fatal by clicking on corresponding button

## Slide 41: HotSpot
Click on error
Analyze the error and take appropriate action
You can use HTML to copy it into the elog
Acknowledge understood errors

## Slide 42: Handsaw
Running in a terminal on the shifter console
  You need an account in the online cluster to start it
Scrolling display of error messages from DAQ
  All messages (and more) are in HotSpot or LVL0
  Handsaw is often quicker to find the most relevant message

## Slide 43: What to do if it does not work
Don’t panic! Keep cool.
  Not always easy, especially during stable beams
  Think before clicking!
  GUIs are sometimes slow in reacting. Be patient…
Look at what the DAQ expert application suggests
  suggestions are a superset of the ‘DAQ stuck’ flow chart
Look for error messages (LVL0, HotSpot, Handsaw)
Look at DAQView for anything suspicious
  Figure out what subsystem is causing problems
  Be aware that one subsystem might get backpressure from DAQ due to other issues
Talk to the shift leader and other shifters
  They might be aware of problems affecting DAQ
  E.g. if a subsystem lost power, DAQ will go into error (you might be the first to realize it!)
If you are unsure or stuck, do not hesitate to call the DAQ oncall anytime (76600)

## Slide 44: Happy Shifting…
Thank you for your attention