## Slide 1: Interfacing Geant4/Garfield++ and Geant4/Degrad A step by step introduction
RD51 collaboration meeting Munich
19.06.2018
Carlos Azevedo, I3N - Physics Department, University of Aveiro
Lennert de Keukeleere, IKS KU Leuven
Dorothea Pfeiffer, European Spallation Source ERIC

## Slide 2: Interface paper
Contains model verification and source examples, submitted to NIM A: https://arxiv.org/abs/1806.05880

## Slide 3: Task division between Geant4 and Garfield++/Degrad

## Slide 4: Geant4/Garfield++ interface
Geant4 and Garfield++ are used in the same user C++ program
Garfield++ includes are added to the CMakeList.txt file
User program is linked against Geant4 and Garfield++ libraries

## Slide 5: Geant4 parameters: Lower production cut and lowest electron energy
Lower production cut: Minimum energy transfer required to produce a new particle. If the transferred energy is lower than the lower production cut, the energy is merely recorded as being deposited in the step.
Lowest electron energy limit: Energy threshold below which an electron is not tracked anymore. If the kinetic energy of an electron falls below the lowest electron energy limit value during a step, the full energy deposition independently of material is enforced.
PAI model: Mean number of electron-ion pairs produced by
10 keV electron in a very large
volume of He/isoButane 70/30.
Variance of electron-ion pair
distribution

## Slide 6: Physics list: SetCuts()
Lower production cut and lowest electron energy have to be set in SetCut() method of physics list
If PAI model is used, parameters are of crucial importance to create enough electron-ion pairs
Deposited energy is not influenced!
Correct values depend on the gas mixture
Paper gives guidelines how to determine the correct values

## Slide 7: Case A: Geant4 only for creation of electron-ion pairs

## Slide 8: Performance of different options for creation of electron-ion pairs
Comparison of simulation times for 105 1 GeV electrons in 1 cm of Ar/CO2 70/30
Most efficient way of interfacing is to use Geant4 PAI model in conjunction with the Heed PAI model

## Slide 9: Case B – D: Heed responsible for creation of electron-ion pairs
Geant4 has parametrization feature
G4VFastSimulationModels can be used as alternative to the Geant4 physics
Definition of a gas region in which the Garfield FastSimulationModel is used

## Slide 10: Case B – D: Heed responsible for creation of electron-ion pairs
Parameterisation has to be added to physics list
G4VFastSimulation-ManagerProcess has to be defined to trigger the FastSimulationModel
For charged particles, PAI model has to be activated as extra EM model

## Slide 11: Definition of FastSimulationModel

## Slide 12: Definition of FastSimulationModel: IsApplicable()
The FastSimulationModel is applicable for certain particle types

## Slide 13: Definition of FastSimulationModel: ModelTrigger()
The FastSimulationModel is triggered at each step for certain particle energies

## Slide 14: Definition of FastSimulationModel: DoIt()
The primary particle in Geant4 is killed
Heed track is created

## Slide 15: Definition of FastSimulationModel: DoIt()
For electrons, Heed TransportDeltaElectron is used
The produced conduction electrons are retrieved
For charged particles, Heed NewTrack is used
First the clusters, and then the conduction electrons are retrieved

## Slide 16: Definition of FastSimulationModel: DoIt()
For photons, Heed TransportPhoton() is used
The produced conduction electrons are retrieved
With the conduction electrons, the Garfield++ simulation (drift, avalanches, signal creation) is continued as needed

## Slide 17: Geant4/Degrad interface: Electroluminescence example
As before, a FastSimulationModel is defined and attached to a gas region
The model is applicable for electrons with Ekin > 7 eV, produced via the photo-electric effect in Geant4
Degrad is a Fortran program, the easiest way to execute it is to just run it using the system function
The Degrad input cards are fed to Degrad using a pipe

## Slide 18: Geant4/Degrad interface: Electroluminescence example
Degrad write the position and time of the thermalized electrons to a text file
Text file is looped through in Geant4
If position of electron is inside the gas volume (in Degrad the volume is indefinite, hence the check), new secondary electrons are created in Geant4

## Slide 19: Garfield++ FastSimulationModel: Electroluminescence example
Garfield++ FastSimulationModel is valid for electrons with Ekin < 7 eV (these electrons were just created in the Degrad FastSimulationModel)
AvalancheMicroscopic is used to create an electron avalanche
Callback function is written to access the excitation levels
Time and position of excitations are stored

## Slide 20: Garfield++ FastSimulationModel: Electroluminescence example
At the stored excitation positions, optical photons are produced in Geant4 as secondary particles in the DoIt() method of the FastSimulationModel

## Slide 21: Conclusions
Geant4/Garfield++ and Geant4/Degrad interface works
Depending on the use case, different ways exist to interface the Monte Carlo programs
Paper under review at NIM A
During work on paper, bugs in Heed C++ implementation detected and corrected
Possibility to create a Heed like physics process in Geant4 should be investigated Geant4 collaboration to further facilitate the simulations