## Slide 1: Modification of the shielded beam screen design & misalignment analysis
M. Morrone, C. Garion
TE/VSC
HL-LHC TCC, 8th March 2018

## Slide 2
Concept
Behaviour during quench
Main modifications of the beam screens due to CLIQ
Misalignment effects of the beam screen in the cold bore
Conclusions
Outline

## Slide 3
Concept
Cold bore (CB) at 1.9 K:
4 mm thick tube in 316LN
Tungsten alloy blocks:
Chemical composition: 95% W, ~3.5% Ni, ~ 1.5% Cu
Mechanically connected to the beam screen tube: positioned with pins and titanium elastic rings
Heat load: 15-25 W/m
40 cm long
Cooling tube:
Outer Diameter: 10 or 16 mm
Laser welded on the beam screen tube
Beam screen tube (BS) at 60-75 K:
Perforated tube (~2%) in High Mn High N stainless steel (1740 l/s/m (H2 at 50K))
Internal copper layer (75 mm) for impedance
a-C coating (as a baseline) for e- cloud mitigation
Laser treatments under investigation
Elastic supporting system:
Low heat leak to the cold bore
tube at 1.9K. Ceramic ball with
titanium spring
Thermal links:
In copper
Connected to the absorbers and the cooling tubes or beam screen tube

## Slide 4
The study has been presented in the TE-TM dated 31.8.2017 (https://indico.cern.ch/event/659350/).
Behaviour during a magnet quench
Quench heaters vs CLIQ
Lorentz forces driven by GG’ product
Lorentz forces acting on the beam screen are pointing toward the cold bore
Lorentz forces are maximum after 50 ÷ 60 ms.
P2
P1
P3
P4
Expected forces in red
Courtesy of S. Izquierdo Bermudez & E. Ravaioli
P2
P1
P3
P4
has opposite sign in the first phase of the CLIQ discharge!
Therefore, opposite forces are expected in the same component.
Magnet gradient decay with quench heaters
Current decay with CLIQ discharge
Specific Lorentz forces reads:
Courtesy of E. Todesco

## Slide 5
Main modifications of the Q1 beam screen
New pin (2 per W block) + reinforcement plates
Old design
New design

## Slide 6
New pin (2 per W block)
Old design
New design
Main modifications of the Q2x-Q3-D1 beam screens

## Slide 7
Misalignment effects of the beam screen in the cold bore
0
@ 5 ms
Reaction torque of the BS fixed at one end during the CLIQ discharge
magnification
x 6000
@ 85 ms
Maximum V.M. stress on the fixed end of the BS due to the 1 mm offset .
Variation of the forces in the W blocks due to 1 mm offset on the x-axis of the BS
in comparison with the nominal case at 5 ms.
y
x
1 m
Twist angle: 0.01°
Variation of the forces in the W blocks due to 1.4 mm offset at 45 ° of the BS
in comparison with the nominal case at 5 ms.
y
x
0
The misalignment effects are negligible
at the fixed point of the beam screen.

## Slide 8
Conclusions
The cost estimate for the beam screen
modification is 250 kCHF, which includes:
  raw material;
  machining and assembly of additional pins;
  reinforcement plates;
  elastic rings;
  drawing updates.
No impact neither on schedule
nor on the performance is expected:
  no impact on aperture;
  no impact on field quality;
  non significant impact on shielding efficiency.
No impact on the beam screen fixed point
due to a misalignment of the beam screen
in the cold bore.

## Slide 9
Thank you for your attention

## Slide 10
Backup slides

## Slide 11
Behaviour during a magnet quench
Impact of CLIQ
Integrated forces induced in half W block
Phase 1: Most critical!!
1
Torque
Tangential force
2
3
component | Q1 |  | Q2 | 
 | Torque [N m/W block] | Tangential force [N/W block] | Torque [N m/W block] | Tangential force [N/ W block]
Cold bore | 250 | 3400 | 250 | 3400
Heat absorber | 280 | 4200 | 150 | 2200
Octagonal pipe | 80 | 1600 | 230 | 3800
1
2
4
Phase 4: Less severe than without CLIQ
E.g. Fy for the tungsten block: Q1NO CLIQ ~230 [N/mm] > Q1CLIQ ~200 [N/mm]
Phase 2: Less severe than phase 1
Integrated forces induced in half W block
Force distribution
Deformation during the first phase
3
4

## Slide 12
Impact of CLIQ
NO CLIQ
CLIQ
The pin becomes a structural component!
 New solution needs to be found!

## Slide 13
Proposed solution
16 mm
4 mm

## Slide 14
Q1 beam screen during the CLIQ discharge
P506 Elastic limit 1350 MPa
(RED AREAS)

## Slide 15
Proposed Q1 beam screen during the CLIQ discharge_v2
P506 Elastic limit 1350 MPa
(RED AREAS)

## Slide 16
Proposed Q1 beam screen during the CLIQ discharge_v2
P506 Elastic limit 1350 MPa
(RED AREAS)

## Slide 17
Beam screen extremities and interconnections
Layout
0/90° cut
+/-45° cut
More compact components (transversally)
Longer absorber at the beam screen extremities
Update of the interconnection module design
*BPM model provided by WP 13

## Slide 18
Old pins

## Slide 19
Old W blocks

## Slide 20
New pins

## Slide 21
New W blocks

## Slide 22
Details of the proposed beam screen design

## Slide 23
Supporting system