## Slide 2: 75 ns Bunch Spacing Studies with Xenon
LIU-PS Beam Dynamics Working Group
08/03/2018
S. Albright, H. Damerau, A. Lasheen
Many thanks to H. Bartosik, S. Energico, M. Morvillo

## Slide 3
Introduction and Motivation
50 ns bunch spacing with lead from PS
  Demonstrated with 2 bunches in 2016 (MD Days 2017)
  Requires additional wide-band RF system to produce 4 bunches
  Not considered immediate priority
75 ns bunch spacing as back-up option
  3 bunches possible with existing hardware
  Recover partial performance without slip-stacking in SPS
  Beam tests with xenon at end of 2017 run
Scaling from xenon to lead?
Beam studies with lead this year

## Slide 4
Detuned 20 MHz cavity
Detuned 80 MHz cavity
75 ns, 3 bunch scheme for ions
Inject 3 bunches from LEIR
Accelerate on h = 24 to intermediate flat-top
Batch expansion step h = 24  21
Accelerate on h= 21 to flat-top
Batch compression step h = 21  28
Re-bunching h = 28  169
10 MHz RF system
Simulation
Flat-top
h = 169
h = 21
h = 28
Intermediate flat-top
h = 24
h = 21

## Slide 5
Injection

## Slide 6
Single bunch transfer LEIR-PS possible at several harmonics
The PS circumference is 8 times the one of LEIR  hPS = 8 hLEIR
Transfer of 2 bunches: hLEIR = 2 hPS = 16
Transfer of 3 bunches: hLEIR = 3 hPS = 24
Handshake LEIR-PS with standard RF trains at hPS = 1, 8 and 16
No hardware modification required thanks to programmable multi-harmonic sources (MHS)
LEIR-PS transfer of 3 bunches
Time [ns]
Time [ns]
~1 ms
DE [MeV]

## Slide 7
Longitudinally matched injection
Energy matching to be improved
Bunch still well captured by beam phase loop
Correct energy matching LEIR-PS for studies in 2018
`
LEIR-PS transfer of 3 bunches
Time [ns]
1 ms
~1 ms
Glitch when closing phase loop
Glitch when closing phase loop
Dfh=24
Phase loop switched to beam signal
Phase error [a.u.]

## Slide 8
Acceleration and intermediate flat-top

## Slide 9
The upper frequency limit of the main 10 MHz cavities excludes acceleration to the flat-top on h = 24
Highest possible harmonic compatible with frev = 473.13 kHz (129Xe39+) and 472.64 kHz (208Pb54+) at flat-top is h = 21
Single batch expansion step h = 24  21
Simple compared to RF manipulations for nominal 100 ns beam
Acceleration and intermediate flat-top
Break-up after transition
No issue expected at intermediate flat-top
Beam break-up after transition crossing for large density
Cured by emittance blow-up in PS from ~3 eVs to ~5.2 eVs (matched)
gtr

## Slide 10
Flat-top

## Slide 11
Moving the main RF harmonic from h = 21  28
Bunch spacing changes from 100 ns to 75 ns
Detuned 20 MHz cavity, slightly below the h = 28 proton frequency
Asymmetric voltages capabilities: 20 kV at h = 28, up to 200 kV at h = 21
Compromise: 80 kV (4 cavities) to 20 kV
Manipulation too fast towards the  Non-linear voltage programs
Batch compression
h = 21  28, linear in 100 ms
Normalized phase space

## Slide 12
Non-linear voltage programs to define motion of bucket centers
Sinusoidal motion of outer buckets  continuous in f and df/dt
Significantly improved adiabaticity
Optimized voltage programs
Phase of outer bucket
Non-linear voltage
Linear
Voltage prgrams
h = 28
h = 169
h = 21

## Slide 13
Duration of batch compression
100 ms
80 ms
60 ms
40 ms
20 ms
10 ms
No further improvement with longer manipulation  kept 100 ms

## Slide 14
Only 20 kV at h = 28 available for handover to h = 169 (80 MHz)
Sensitive: can be adjusted in phase such that bunches just fit
Expect higher population of satellite bunches than with nominal beam
May become critical with lead beams for LHC
Re-bucketing to 80 MHz
h = 28  169 (left bunch)
h = 28  169 (satellites)

## Slide 15
Extraction synchronization (coarse and fine) work correctly
Beam phase loop at h = 21 kept until extraction
Issues to switch phase loop from h = 21 to h = 169
Understand h = 21 phase loop asymmetry during flat-top batch compression
Check h = 169 phase loop or ejection jitter when keeping phase loop at h = 21
Towards extraction
Bunches at extraction
Loop signals at flat-top
DR
Dfh=21
500 ms
Synchronization: h = 1/9

## Slide 16
Studies with lead

## Slide 17
Scaling from 129Xe39+ to 208Pb54+
  Synchrotron frequency fs,Pb/fs,Xe  0.9
  Bucket filling factor (el/Ab)Pb/ (el/Ab)Xe  1.0
Lower flat-top field for xenon in 2017
  80 ms longer flat top than normally with lead
  Shorten intermediate flat-top and extend flat-top, duty cycle limit?
Longitudinally xenon and lead expected to behave similarly
Feasibility of 75 ns with lead?
BLonD simulation 129Xe39+
208Pb54+ case
el = 6.5 eVs
el = 10.4 eVs

## Slide 18
Summary

## Slide 19
Summary
Proof-of-principle demonstration of 3 bunches spaced by 75 ns with xenon in 2017
  Transfer of 3 bunches into h = 24 buckets
  Simple batch expansion at intermediate flat-top
  Beam break-up at transition crossing, fixed with blow-up
  Requires 2nd 20 MHz cavity for h = 21  28 compression
  Phases during re-bucketing h = 28  169 very sensitive
  Good longitudinal beam quality at PS extraction (4s  4 ns)
Studies with lead in 2018
    Similar longitudinal behaviour of lead and xenon expected at PS flat-top
    Extension of flat-top by ~80 ms required for lead
    Schedule PS studies with lead during 2nd half of May?
    Feedback on beam quality from SPS needed

## Slide 20
THANK YOU FOR YOUR ATTENTION!