## Slide 1
FRESCA 2 Safety equipment sizing
FRESCA2 Final Design Review, 21.03.2018 CERN, CH
J. Polinski

## Slide 2: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 3: Burst disc + SV set pressure strategy
Gauge pressure
Absolut pressure
PS = MAWP = 2.9 bar g = BD set press.+10%
BD set press. = PS/1.1 = 2.636 bar g
Maximum pressure = 1.1 MAWP = 3.19 bar g
BD set press.-10 % = 2.373 bar g
Pressure margin 0.2 bar
BD opening area
4.19 bar a
PS = MAWP = 3.9 bar a
Max press. when SV is open = (SV set press +5%) x 1.1 = 2.173
SV set press +5% = 1.975 bar g
SV set press = 1.881 bar g
SV set press – 5% = 1.787 bar g
SV opening area
Operating press. = 0.3 bar g
Min. press. for closing the SV
(SV set press – 5%) – 10% = 1.608 bar g

## Slide 4: Standards
Determination of the required Safety Equipment (SE) capacity (input data to EN ISO 4126-1 calculations) is done in accordance to EN13648-3
The SE sizing is done in accordance with EN ISO 4126-1

## Slide 5: Heat loads
The heat flux W with atmospheric air to He vessel is assumed as:
  W = 6 kW/m2 if the surface is covered with 10 layers of MLI or if helium has the contact with foam insulation below the vessel led
  W = 60 kW/m2 if the surface is covered with 3 layers of MLI or is not covered with the MLI
Cable sample quench – negligible
HFM magnet quench – see next slides

## Slide 6: Determination of the required SEs capacity EN13648-3

## Slide 7: Determination of the required SEs capacity EN13648-3
Chart: SV pset = 3.9 bar abs
| 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3000000000000096 | 5.4000000000000101 | 5.5000000000000098 | 5.6000000000000103 | 5.7000000000000099 | 5.8000000000000096 | 5.9000000000000101 | 6.0000000000000098 | 6.1000000000000103 | 6.2000000000000099 | 6.3000000000000096 | 6.4000000000000101 | 6.5000000000000098 | 6.6000000000000103 | 6.7000000000000099 | 6.8000000000000096 | 6.9000000000000101 | 7.0000000000000098 | 7.1000000000000103 | 7.2000000000000197 | 7.3000000000000203 | 7.4000000000000199 | 7.5000000000000204 | 7.6000000000000201 | 7.7000000000000197 | 7.8000000000000203 | 7.9000000000000199 | 8.0000000000000195 | 8.1000000000000192 | 8.2000000000000206 | 8.3000000000000203 | 8.4000000000000199 | 8.5000000000000195 | 8.6000000000000192 | 8.7000000000000206 | 8.8000000000000203 | 8.9000000000000199 | 9.0000000000000302 | 9.1000000000000298 | 9.2000000000000295 | 9.3000000000000291 | 9.4000000000000306 | 9.5000000000000302 | 9.6000000000000298 | 9.7000000000000295 | 9.8000000000000291 | 9.9000000000000306 | 10
 | 2.2447e-06 | 2.3156e-06 | 2.3922e-06 | 2.4754e-06 | 2.5662e-06 | 2.6659e-06 | 2.7761e-06 | 2.899e-06 | 3.0372e-06 | 3.1942e-06 | 3.3745e-06 | 3.5839e-06 | 3.8297e-06 | 4.1203e-06 | 4.4626e-06 | 4.8542e-06 | 5.2666e-06 | 5.6413e-06 | 5.9323e-06 | 6.1378e-06 | 6.2734e-06 | 6.353e-06 | 6.3887e-06 | 6.3913e-06 | 6.3699e-06 | 6.3318e-06 | 6.2824e-06 | 6.2257e-06 | 6.1646e-06 | 6.1009e-06 | 6.036e-06 | 5.971e-06 | 5.9063e-06 | 5.8425e-06 | 5.7799e-06 | 5.7186e-06 | 5.6588e-06 | 5.6005e-06 | 5.5437e-06 | 5.4885e-06 | 5.4349e-06 | 5.3827e-06 | 5.332e-06 | 5.2827e-06 | 5.2348e-06 | 5.1882e-06 | 5.143e-06 | 5.0989e-06 | 5.056e-06 | 5.0143e-06 | 4.9737e-06 | 4.9341e-06 | 4.8955e-06 | 4.8579e-06 | 4.8213e-06 | 4.7855e-06 | 4.7506e-06 | 4.7165e-06
= max @ T= 6.5 K

## Slide 8: The SEs sizing - EN ISO 4126-1

## Slide 9: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 10: Outer Cryostat He vessel SV – heat flux calculations
pset = 1.88 bar g = 2.88 bar abs, Trelief – 5.8K
Insulation heat flux – foam insulation below vacuum vessel led : Wins = 0.978 m2 × 6 kW/m2 = 5 868 W

## Slide 11: HFM magnet quench - heat loads
Assumptions:
  HFM temperature after quench – THFM
  HFM area – AHFM=6.85 m2
  He relieving temperature 6.5K
Calcualtions
WHFM=AHFM ×290 ×(THFM-6.5)0.92
for THFM = 80 K WHFM= 104 343 W

## Slide 12: Outer Cryostat He vessel SV capacity calculations

## Slide 13: Outer Cryostat He vessel SV capacity calculations
- critical flow

## Slide 14: Outer Cryostat He vessel SV capacity calculations

## Slide 15: Outer Cryostat He vessel SV capacity calculations

## Slide 16: Outer Cryostat He vessel SV capacity calculations
5 kW
35 K
Value estimated from HFM commissioning tests data
Calculated HFM structure temperature after the quench

## Slide 17: Outer Cryostat He vessel SV capacity calculations
5 kW
35 K
Value estimated from HFM commissioning tests data
Calculated HFM structure temperature after the quench
Finally decided as the baseline

## Slide 18: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 19: Outer Cryostat He vessel BD – heat flux calculations
External vacuum vessel failure
  10 layer Insulated area – 17.07m2
  Foam insulation – 0.978 m2
  Total heat flux –18.05 x 6 kW/m2 = 24.05 kW
Internal vacuum vessel failure
  10 layer Insulated area – 0 m2
  Uninsulated area – 3.818 m2
  Foam insulation – 0.978 m2
  Total heat flux – 3.818 m2 x 60 kW/m2 + 0.978 m2 x 6 kW/m2 = 234.9kW

## Slide 20: Outer Cryostat He vessel BD – heat flux calculations
For vacuum vessel break + HFM quench (80K), d0=118mm
For vacuum vessel break, no HFM quench d0=98 mm
Final selection of the BD for OC: d0=120 mm

## Slide 21: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 22: Outer Cryostat lambda valve – heat flux calculations
External vacuum vessel failure (area under lambda plate)
  10 layer Insulated area – 12.157 m2
  Uninsulated area (cryostat top flange) – 0 m2
  Total heat flux – (17.07 + 10 x 0)m2 x 6 kW/m2 = 72.95 kW
Internal vacuum vessel failure (area under lambda plate)
  10 layer Insulated area – 0 m2
  Uninsulated area – 0.673 m2
  Uninsulated area (cryostat top flange) – 0 m2
  Total heat flux – 0.673 m2 x 60 kW/m2 = 40.38 kW
HFM quench – 103.31 kW

## Slide 23: Outer Cryostat lambda valve capacity calculations
D
=0.304

## Slide 24: Outer Cryostat lambda valve capacity calculations

## Slide 25: Outer Cryostat lambda valve size

## Slide 26: Outer Cryostat lambda valve size
Chart: Dp, bar
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.15 | 0.2
d_lambda valve | 216.1324 | 181.6709 | 164.0903 | 152.6391 | 144.2956 | 137.8065 | 132.5385 | 128.13 | 124.3559 | 121.0677 | 109.1369 | 101.3071

## Slide 27: Outer Cryostat lambda valve size
For Q_HFM(T=80K) d0= 121 mm
For Q_HFM=0 d0= 78 mm
Final size d0= 120 mm

## Slide 28: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 29: Outer Cryostat vacuum vessel lift plate
Sized for the d=38 mm pipe break
He flow outflow area is equal to the broken pipe cross section area
He pressure in the vessel = 3.9 bar a
Max pressure in Vacuum Vessel – 1.5 bar a
He mass outflow to vacuum vessel qm=4.74 kg/s
Temperature of the He at lift plate – to be determined

## Slide 30: Outer Cryostat vacuum vessel lift plate
Temperature of the He at lift plate
Chart: OC He Vessel higth, m
Vac Vessel
300K
Thermal shield
77K
He vessel
No heat flux
He flow in VV

## Slide 31: Outer Cryostat vacuum vessel lift plate
Chart: He temperature at lift plate, K
| 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
 | 121.6903 | 131.0533 | 138.6778 | 145.186 | 150.9046 | 156.0293 | 160.6883 | 164.9707
Finally selected with some safety margin an in view of the available space

## Slide 32: FRESCA 2 Safety Equipment
Outer Cryostat
  He vessel Safety Valve – for HFM quench
  He vessel Burst Disc – for vacuum vessel failure + HFM quench
  Lambda Valve - for vacuum vessel failure + HFM quench
  Vacuum vessel lift plate
  L-L heat exchanger
Inner Cryostat
  He vessel Burst Disc – for vacuum vessel failure + SC transformer quench
  Lambda Valve - for vacuum vessel failure
  Vacuum vessel lift plate
  L-L heat exchanger

## Slide 33: OC L-L HX hydraulic loop BD size calculation
The inner cryostat L-L HX hydraulic loop is compose of the manifold and pumping line
All surfaces are covered with 10 layers of MLI
The total area of the hydraulic loop is 0.413 m2
Heat flux to the loop is 0.413 m2 x 6 kW = 2 477 W
BD required capacity

## Slide 34: OC L-L HX hydraulic loop BD capacity calculations

## Slide 35: OC L-L HX hydraulic loop BD size calculations

## Slide 36: Outer Cryostat safety equipment summary
He vessel Safety Valve – d0 = 46 mm
He vessel Burst Disc – d0 = 120 mm
Lambda Valve - d0 = 120 mm
Vacuum vessel lift plate - d0 = 130 mm
L-L heat exchanger - d0 = 10 mm

## Slide 37: Inner Cryostat safety equipment summary
He vessel Burst Disc – d0 = 25 mm
Lambda Valve - d0 = 32 mm
Vacuum vessel lift plate - d0 = 130 mm
L-L heat exchanger - d0 = 10 mm