## Slide 2: Proton EDM hardware challenges
J. Borburgh
with valuable input from M. Atanasov, M. Barnes, C. Carli, L. Jorat, M. Lamont, A. Prost, V. Senaj, N. Voumard

## Slide 3: Outline
Baseline lattice
Bends
Quadrupoles
Injection devices, septa and fast deflectors
Conclusion

## Slide 4: Baseline lattice
Arc cell
Drifts before and after bend 0.8 m (used for experiments and/or correctors/skew quad/sextupole/BPM )
2 bends of 4.16 m
Drift between bends 0.1 m
Quad 0.4 m
Total cell length: 10.417 m
Beam
Protons
700.74 MeV/c
232.8 MeV

## Slide 5: Physical length vs Effective length
SPS ZS septa: 3000 mm active length and 3378 mm device length; spacing > 870 mm
LEP ZL: 4000 mm active length; 4500 mm device length; spacing > 650 mm
Note: Additional space would be needed for vacuum valves in case plug-in systems would be adopted to reduce down time in case of exchange due to failure

## Slide 6: Bend requirements
Total number of bends: 80
Lphysical: 4.1585 m
Leff: 3.7985 m
Gap width: 30 mm
Deflection angle: 78.54 mrad
Egap: 8.655 MV/m
Vper polarity: ±130 kV
Electrode height: 200 mm [1]
Cylindrical electrodes [1]
Vacuum: 10-11 mbar [1]
Field homogeneity: 1 ppm on Ø20 mm [2]
Power supply stability < 1.10-4 [2]
Magnetic leak field: <10-11 T [3]

## Slide 7: Bend challenges
Feasibility of 1 ppm field homogeneity tbc.
Electrode profile needed to achieve required homogeneity causes higher fields on electrodes → need to reduce the average field assumed for the beam.
E field high for use of Ti. Alternatives (TiN coated Al)?

## Slide 8: Bend challenges
Non // plates induce skew quadrupolar effect → need to estimate achievable electrode precision to estimate requirements for skew quads in lattice.
Does magnetic leak field requirement exclude use of stainless steel?
To study if Al or Ti qualify as alternative construction materials.
Assume bends at room temperature: bake out needed to obtain required vacuum.
Assume all bends powered in // to reduce systematics, HV conditioning prior to operation needs to be studied.

## Slide 9
0.4 m Quad
Assuming purely hyperbolic electrodes
Central radius
Rounded edges with
Electrode length , flange-to flange 401mm
Vacuum tank

## Slide 10: Quadrupoles
Field strength depends on strong or weak focussing lattice.
Aperture (w x h): 30 x 200 mm2
k = 50 MV/m2 (strong focussing), assuming Leff = 0.4 m
Lph= 400 mm → Leff = 246 mm → k = 81 MV/m2
Knowing that →
Epole-tip: 8.1 MV/m
Epole-wings: >20 MV/m

## Slide 11: Quadrupoles
Field strength depends on strong or weak focussing lattice.
Aperture (w x h): 30 x 200 mm2
k = 50 MV/m2 (strong focussing), assuming Leff = 0.4 m
Lph= 400 mm → Leff = 246 mm → k = 81 MV/m2
Knowing that →
  U ≤ ±100 kV + R = 0.1 m → k < 20 MV/m2 , Epole= 2MV/m
  Lph= 0.8 m → Leff = 646 mm → k = 30.8 MV/m2, Epole= 3.1 MV/m,
  U=100 kV, k = 81MV/m2, Lph= 0.4 m →R = 50 mm, Epole= 4.1 MV/m

## Slide 12: Quad challenges
Field homogeneity dominated by end fields. Could be mitigated to some extend [4]. Need to determine minimum quad length that can achieve requirements
HV feedthrough integration challenging for short quads.
Alignment precision tbd, but assumed to be critical.
Cryo quad makes alignment/positioning more complex, but industrial solutions may exist [5], using flexure guides and piezo actuators.
Main quads to be powered in 4 families; conditioning to be studied.
Courtesy WWW.JPE.NL

## Slide 13: Injection straights
Uses most of LSS
P+
Injection septum
Fast deflector
3500 mm
3000 mm
4750 mm

## Slide 14: Injection devices
 | Injection septum | Fast deflector
L physical [m] | 3.5 | 3.0
Active length [m] | 3.0 | 2.5
Deflection angle [mrad] | 57.34 | 10
Gap width [mm] | 30* | 42.5**
Field [MV/m] | 8.0 | 1.674
Radius of curvature electrodes [m] | 52.32 | -
Nominal electrode voltage [kV] | - 240 | ± 35.6
Trise and Tfall (2‰ - 998‰) [µs] | DC | 1.0
Capacitance per electrode (to gnd) [pF] | ~ 660 | < 500
* Assuming curved or segmented septum and electrode
** Assuming parallel electrodes

## Slide 15: Segmented septum, fast deflector examples
Segmented septum MedAustron
Fast deflector at CERN in ELENA

## Slide 16: Open issues injection devices
Segmented foil septum v.s. curved wire septum
Feasibility of Fast Deflector pulse generator:
  rise and fall time feasibility to be validated
  voltage switch: not easily done using off the shelf switches (for example Behlke refreshes their switches at regular intervals even when switched off, and the electrodes wouldn’t remain grounded).
  Switches need to be located close to fast deflectors (0.5 m). Feasibility and reliability in the radiation to be studied.
  HV feedthroughs need development, not commercially available.
Alternative: stripline kicker(s)
  replacing fast deflector would reduce voltages to 30 kV (-20%) on plates, but at cost of added complexity.
  replacing the septum with a stripline kicker is not feasible.

## Slide 17: Conclusion
Electrode material will determine max. field strength, hence size of elements.
Quad field strength to be quantified and feasibility of precision requirement to be determined.
Lattice needs updating with:
  Longer quads
  Skew quads
  Trim quads
  Sextupoles
  Vertical correctors
  Present circumference seems optimistic
Conditioning strategy for quads and bends to be studied.
Injection equipment feasible in principle.
  Fast deflector rise and fall time requirement to be validated.
Use of stainless steel for construction desirable, but compatibility with magnetic leak field requirements tbc.

## Slide 18: References
M. Lamont, “EDM strage ring – siting at CERN”, CERN EDM WG meeting, 1 June 2017
Y. Semertzidis, “All-electric versus combined field storage ring”, EDM kick-off meeting, CERN,13-14 March 2017
Reference to leak field level
R. Baartman, “Quadrupole shapes”, Phys. Rev. ST – Accel. Beams 15, 074002 (2012)
www.janssenprecisionengineering.com

## Slide 19: Back-up slides

## Slide 20: Bend

## Slide 21: Fast deflector

## Slide 22: Electrostatic injection septum