## Slide 1: Enhancement of the Resonance Ionization Laser Ion Source (RILIS) at ISOLDE - Setting up a complementary all solid-state laser system
Sebastian Rothe
Gentner Day 2009

## Slide 2
Introduction
  Myself
  ISOLDE
  Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 3
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 4
...02/2009
Diploma thesis at Uni Mainz: Resonance ionisation spectroscopy on Si
Construction and specification of a Cr:forsterite laser (Cr:Fo)
Integration into existing laser system of Ti:sapphire lasers (Ti:Sa)
Resonance ionisation spectroscopy (RIS) on Si & Sc
Developments on the Frequency Conversion Unit
  Installation at JYFL/Jyväskylä, Finaland
05-06/2009
Research visit to TRIUMF/Vancouver, Canada
Installation of Cr:Fo at TRILIS (TRIUMF Resonance Laser Ion Source)
08/2009
CERN/ISOLDE User
09/2009
Start of Ph.D. at CERN in ISOLDE/RILIS team (EN-STI/LP)
About myself

## Slide 5
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 6
ISOLDE Introduction
ISOLDE is an isotope production facility
Intensity 1011 down to 1 ions/s
Isotope range 6He to 232Ra (Z: 2-88, N:4-144)
Half lifes 10 ms to stable
Up to now >800 isotopes of 70 elements have been produced at ISOLDE
Of the 3100 known isotopes, 256 are stable. Only 83 radioactive isotopes are found in nature.
Energy range 10-6 eV (10 mK) to 3 MeV/u
- Trapped in ISOLTRAP or WITCH
- Post accelerated by REX-ISOLDE

## Slide 7
Production
Ionization / Extraction
Effusion
Ionization
Isotope Separation
Q/A
Post acceleration
or to Experiment:
ISOLTRAP
(Examples)
ISOLDE Introduction - The ISOL process

## Slide 8
Protons
HRS Target
GPS Target
Control Room
Magnets
Experiments
ISOLDE Introduction - Overview
Laser Cabin

## Slide 9
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 10
Resonance ionization: Stepwise resonant excitation of atoms and final ionization
Z – selective & very efficient
Atom source
Atoms
Laser beams
Ion optics
Experiment
Ions
Mass separation
Ground state
Rydberg
AI
IP
Excited states
Z selection
R I L I S
RILIS (Z)
Resonance Ionization Laser Ion Source - RILIS
Mass selection
GPS or HRS
+ Mass separation (Q/A)
= Isotope selection

## Slide 11
Dye lasers pumped by frequency doubled Nd:YAG (Edgewave), 10kHz
Wavelength tuning range:
Fundamental (w) 540 - 850 nm (8 W)
2nd harmonic (2w) 210 - 425 nm (2 W)
3rd harmonic (3w) 213 - 265 nm (.15W)
RILIS operation per year: >> 2000 h
Time needed for elment change: 2 - 3 days
Current Status of RILIS Dye Lasers
Problem

## Slide 12
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 13
2 Pump lasers
Nd:YAG, Photonics Industries, 532 nm, 60 W at 10 kHz
2 Frequency Conversion Units
1 W 2nd harmonic 350 - 470 nm (blue)
0.2W 3rd , 4th harmonic 205 - 315 nm (UV)
3 Solid state Ti:sapphire lasers
Design adapted from University of Mainz
Wavelength tuning range:
3-5W Fundamental 690 - 980 nm (red - IR)
Solution: Installation af a second laser system : Solid State Ti:Sa Lasers

## Slide 14
Ti:Sa Laser System at University of Mainz
UMz RISIKO
Mass separator
FCU
Ti:Sa 1
Wide tuning Ti:Sa
Ti:Sa 2
Cr:Fo
Test Chamber MABU
(Mz Atomic Beam Unit)
Pump laser 1064 nm
Pump laser 532 nm
Pump laser 532 nm
Development laser system at University of Mainz
copies at TRIUMF, ORNL, JYFL, CERN & GANIL (under construction)

## Slide 15
off-line
TRILIS
FURIOS
IGISOL, Jyväskylä
gas cell
rep. rate ~10 kHz
ti:sa laser
TRILIS
TRIUMF, Vancouver
hot cavity
rep. rate 10 kHz
ti:sa laser
ORNL
Oak Ridge (off-line)
hot cavity
rep. rate ~10 kHz
ti:sa laser
LISOL
Louvain-la-Neuve
gas cell
rep. rate <200Hz
dye laser
RISIKO
Mainz (off-line)
hot cavity
rep. rate ~10 kHz
ti:sa laser
TIARA
Takasaki
hot cavity
rep. rate 300Hz
dye laser
Laser Ion Sources World-Wide
GISELE
GANIL, Caen
rep. rate ~10 kHz
ti:sa laser
ISOLDE, Geneva
hot cavity
rep. rate ~10 kHz
dye + ti:sa laser
RILIS

## Slide 16
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 17
Dye
Ti:Sa
2x Dye
3x Dye
2x Ti:Sa
3x Ti:Sa
Dye Laser vs. Ti:Sa Laser – Tuning ranges
Dye: Green to Red + UV
Ti:Sa: Near IR + Blue

## Slide 18
Green: successfully tested
Blue: known to be accessible (scheme known but not yet tested )
Dye Laser vs. Ti:Sa Laser – Periodic Table of Accessible Elements
Dye laser
46 elements tested
Ti:Sa laser
35 elements tested

## Slide 19
Green: successfully tested
Blue: known to be accessible / scheme developed not yet tested
Dye
Ti:Sa
2x Dye
3x Dye
2x Ti:Sa
3x Ti:Sa
Dye Laser & Ti:Sa Laser – Periodic Table of Accessible Elements
Combined
54 elements tested

## Slide 20
 | Dye | Ti:Sa | Both
Active Medium | > 10 different dyes | Ti doped sapphire crystal | 
Tuning range | 540 – 850 nm | 680 – 980 nm | 540 – 980 nm
Power | Up to 8 W | 3- 5 W | 
Power stability | Decreases during operation | Stable | 
Switch elements | 2-3 Days | 1 Day | 4 hours
Maintenance | renew dye solutions if decomposed | ~ none | 
Schemes developed | 46 | 35 | 54
Dye Laser & Ti:Sa Laser – Pros and Cons
Having two independent laser systems reduces switching time between elements daramatically.

## Slide 21
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 22
October
    first parts are delivered (Crystals, Q-Switches, BiFi)
November
    Pump lasers arrive
    first parts of Ti:Sa are in mechanical workshop in Mainz
December
    Delivery of resonator mirrors and etalons
January
    Prototype of new Ti:Sa is ready to be tested
Winter
    Lasersystem is complete and ready to be tested
Spring
    First off-line laser ions
    Step-wise installation at RILIS laser cabin
First on-line laser ions
Duo-RILIS: two laser systems available for operation with a possibility of quick switch from one element to another
Combination of Dye + Ti:Sa for one ionization scheme
2009
2010
2011
Roadmap of RILIS upgrade

## Slide 23
Introduction
  Myself
  ISOLDE
  RILIS Laser Ion Source
The new Laser System
  Facts
  Comparison of established Dye and new Ti:Sa
Agenda
Summary
Outline

## Slide 24
Summary
For selective production of Isotopes one needs a Laser Ion Source
To speed up switching between elements, a second laser system is needed
The new system will be a Mainz-Type solid-state Ti:Sapphire system
First parts arrived
Ti:Sa & Dye complement one another

## Slide 25: Acknowledgements
Larissa
KTH – Royal Institute of Technology &
Knuth and Alice Wallenberg Foundation
Stockholm, Sweden
CERN, EN department
University of Mainz, Working group LARISSA
Mainz, Germany
BMBF – Bundesministerium für Bildung und Forschung

## Slide 26
Thank you.