## Slide 1
FCC week 2018
Block-coil 16T Design
for the FCC
E. Rochepault, M. Segreti,
on behalf of C. Pes, M. Durante, C. Lorin
With contributions of the EuroCirCol collaboration
10/04/2018
The European Circular Energy-Frontier Collider Study (EuroCirCol) project has received funding from the European Union's Horizon 2020 research and innovation programme under grant No 654305. The information herein only reflects the views of its authors and the European Commission is not responsible for any use that may be made of the information.

## Slide 2: Evolution of the Design
FCC week 2017:
204 mm interbeam
750 yoke diameter
63 mm Al shell
Review Oct. 2017:
194 mm interbeam
570 mm yoke diameter
100 mm Al shell
Today:
204 mm interbeam
570 yoke diameter
67 mm Al shell +
20 mm SS shell
v5ari204
MT2017
v1ari204
C. Lorin, “Electromagnetic design of the block coil option”, FCC week 2017
C. Lorin, “Block-coil electromagnetic design”, ECC review 2017

## Slide 3: 2D Magnetic Design – main parameters
Parameter | Value | Unit
Inom | 10.123 | kA
Nturns | 5+10+21+22 | -
Bore thickness | 1.9 (1.4 + 0.5) | mm
Mid-plane shim | 2.28 | mm
Conductor area | 138 | cm2
Estimated weight* | 7.90 | kt
Yoke diameter | 570 | mm
Bcenter | 16.00 | T
Bpeak | 16.75 | T
Load-line margin | 13.75 | %
Diff. inductance | 49.1 | mH/m
*Area x 4668 dipoles x 14.1m x 8.7 t/m3
5
5
21
21
10
10
22
22
High Field “HF” cables
Low Field “LF” cables

## Slide 4: 2D Magnetic Design – Harmonics
Operation | Case | b2 | b3 | b5 | b7 | b91
Injection (3.3 TeV) | without P. C. | 5.2 | -3.2 | -4.9 | -1.7 | 
 | P. C. only | 0 | -25.5 | -2.1 | -5.7 | -2.5
 | with P. C. | 5.2 | -28.9 | -7.0 | -7.4 | 
 | Max. target2 | - | 60 | - | - | -
Collision | negligible P. C. | -37.48 | 0.49 | -1.96 | -2.43 | -1.59
 | Max. target2 | 50 | 4 | 3 | 3 | 3
Without persistent currents (geometric + saturation):
S. Izquierdo Bermudez, “Field Quality Table Update for EuroCirCol 16 T designs”, FCC-hh magnet-beam dynamics coordination meeting 03, 2017
Persistent currents P.C.:
1Other harmonics <1 unit
2Absolute value

## Slide 5: 3D Magnetic Design – 2 options
Compact:
Coil ends to the shortest
Room in the spacers for internal joints
Minimum conductor length
Are the harmonics still within spec?
Is the peak field still in the straight section ?
Long:
Extension of coil ends
Compensation of the b3 in the ends
What impact on the lengths? (conductor, coil ends)
What impact on the peak field?
Lstraight section = Liron

## Slide 6: 3D Magnetic Design – Harmonics
Compact:
Long:
Design | b2 | b3 | b5 | b7 | b9
2D | -37.48 | 0.49 | -1.96 | -2.43 | -1.59
3D, Compact ends | -39.03 | -4.59 | -2.37 | -2.47 | -1.58
3D, Long ends | -39.41 | 0.08 | -2.41 | -2.51 | -1.58
3D compact + compensation | -38.95 | -2.70 | -1.90 | -2.29 | -1.57
2D compensation | -37.40 | 2.39 | -1.48 | -2.43 | -1.59
At collision
Magnetic length 14 m

## Slide 7: Compensation of b3 in 2d
Midplane shim 2.35 mm  2.28 mm
b3 in the straight section (2d): 0.49 units  2.39 units
b3 integrated -4.59 units  -2.70 units
Slightly lower other harmonics
Slightly higher margin
2.28 mm
v5ari204

## Slide 8: 3D Magnetic Design – Peak Field
Lss
Lcoil
Lmag
Lcoil end
Peak field in the center (z = 0) = 16.6 T for both cases
at the beginning of the coil ends ~16 T
Peak field in the pole tip ~15 T
With Lss = Liron = 1 m
1.
2.
3.
1.
2.
3.
Compact:
Long:
Bpeak center – Bpeak ends = ΔBpeak > 0.6 T
Additional operational margin in the ends

## Slide 9: 3D Magnetic Design – Summary
Parameter | Compact | Compact compensated | Long | Unit
b3 integrated | -4.59 | -2.70 | 0.08 | units
Bpeak1, z=0 | 16.6 | 16.6 | 16.6 | T
Bpeak2, bend | 15.9 | 15.9 | 16.0 | T
Bpeak3, tip | 15.0 | 15.0 | 15.2 | T
Lstraight section | 500 | 500 | 500 | mm (half length)
Liron | 500 | 500 | 500 | mm (half length)
Lcoil | 722 | 722 | 813 | mm (half length)
Lmag | 642 | 642 | 678 | mm (half length)
Lcoil end = Lcoil - Lmag | 80 | 80 | 135 | mm (per end)
1.
2.
3.
Lss
Lcoil
Lmag
Lcoil end
Nominal:
Short ends
Low harmonics
Margin (ΔBpeak > 0.6 T)

## Slide 10: 2D Mechanical Design – Model
Geometry:
  Interbeam distance = 204 mm
  Outer yoke Ø = 570 mm
  67 mm Al shell + 20 mm SS shell
ECC Coil properties (293K/4.2K):
  Ex = 25 GPa / 27.5 GPa
  Ey = 30 GPa / 33 GPa
Pre-load:
  Bladders without SS shell
  2 Horizontal + 2 Vertical keys
  Imposed displacement on SS shell bottom = -0.2 mm (260 MPa tension)
Contacts:
  Bonded: inside the coils, with the poles
  Separation allowed with 0.2 friction: between the coils, with the structure
Yoke
Al Shell
SS Shell
59 MPa
2x0.72 mm
40 MPa
0.10 mm

## Slide 11: 2D Mechanical Design – Coil-Pole contact
LEFT coil
RIGHT coil
Pre-load: interference tuned
Operation at 16 T: contact pressure >0
0 MPa
0 MPa

## Slide 12: 2D Mechanical Design – Coil Peak Stress
σX
σ Von Mises
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
-148 MPa
-181 MPa
-199 MPa
137 MPa
160 MPa
177 MPa
Criteria:
<150 MPa
<200 MPa
<200 MPa

## Slide 13: 2D Mechanical Design – Structure
σ Von Mises
σ Von Mises
84 MPa
369 MPa
489 MPa
622 MPa
870 MPa
1125 MPa
Criteria:
<350 MPa
<1050 MPa
<1050 MPa
Criteria:
<800 MPa
<1650 MPa
<1650 MPa
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
Ti Poles
Stainless steel Y-pusher

## Slide 14: 2D Mechanical Design – Structure
σθ
Stress distribution
Stress distribution
σθ
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
Al Shell
298 MPa
155 MPa
276 MPa
Criteria:
<350 MPa
<1050 MPa
<1050 MPa
Criteria:
<480 MPa
<690 MPa
<690 MPa
Stainless steel shell
257 MPa
227 MPa
248 MPa

## Slide 15: 2D Mechanical Design – Structure
Sigma I:
pure tension
93 MPa
136 MPa
σ Von Mises
Criteria:
<230 MPa
<720 MPa
<720 MPa
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
Iron Y-pad
523 MPa
468 MPa
196 MPa
93 MPa
136 MPa
<380 MPa
<380 MPa

## Slide 16: 2D Mechanical Design – Structure
Stress distribution
145 MPa
188 MPa
Sigma I:
pure tension
σ Von Mises
Criteria:
<230 MPa
<720 MPa
<720 MPa
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
Iron X-pad
<380 MPa
<380 MPa
303 MPa locally
461 MPa
482 MPa

## Slide 17: 2D Mechanical Design – Structure
Stress distribution
285 MPa
344 MPa
486 MPa
631 MPa
716 MPa
Stress distribution
Sigma I:
pure tension
σ Von Mises
Criteria:
Room-temperature pre-load
Cool-down to 1.9K
Operation at 16 T
Iron Y-pad
<380 MPa
<380 MPa
<230 MPa
<720 MPa
<720 MPa

## Slide 18: Conclusion
2d magnetic design:
  16 T at 14 % of LL margin at 1.9 K
  At collision: b3 and higher orders < 3 units (absolute value)
  b2 ~ -40 units
  At injection: b3 ~ -30 units
   block-coil more favorable than other designs
  b5 and higher orders < 10 units
3d magnetic design:
  Compact ends
  Similar values for integrated harmonics
  Additional margin in coil ends (ΔBpeak > 0.6 T)
2d mechanical design:
  Coil stress < criteria
  Iron X-Pad + Yoke: locally > criterion at warm
  Other components: stress < criteria

## Slide 19: Outlooks
Short-term future (2018-2019)
Coil end design to be validated by a 3D mechanical study
  Compact ends favorable for:
    Limited number of parts
    Easier pre-load because of aligned blocks
    EM Forces more balanced between the blocks
Protection:
  To be updated by protection team
   should stay below the limits (minor modifications wrt previous designs)
Mid-term future (~2022)
F2D2: a block-coil short model dipole toward FCC
 See presentation « The CEA 16T model for the FCC », E. Rochepault

## Slide 20
Backup Slides

## Slide 21: Conductor parameters
Parameter | Values |  | Unit
Strand diameter | 1.1 | 0.7 | mm
Number of strands | 21 | 34 | adim
Unreacted width | 12.47 | 12.47 | mm
Unreacted thickness | 1.94 | 1.23 | mm
Reacted width | 12.6 | 12.6 | mm
Reacted thickness | 2.00 | 1.27 | mm
Copper/non-Copper ratio | 0.8 | 2.0 | adim
Insulation thickness | 0.15 | 0.15 | mm
Bare cable compaction | 11.8 | 12.0 | %
Packing factor | 85.4 | 88.2 | %
Transposition pitch | 93 | 93 | mm
J. Fleiter: Rutherford cable design approach and experience at CERN (here)
C. Lorin,
Oct 17 review

## Slide 22
3D magnetic design
Assumptions:
  Return ends – 1000 mm straight section
  Hardway bend : Rmin = 450 mm in upper layer (w = 12.6 mm)
    Strain 13.8 mm/m (HD2: 30.6 mm/m HD3: 12.4 mm/m Fresca2: 15.3 mm/m)
  Coil-to-aperture y-direction: 5 mm
  Double pancake end
Fresca2 : w ~ 21 mm
R ~ 700 mm
LHC MB : w ~ 16 mm
5 mm

## Slide 23: 3D Harmonics
Ex: -10 units on a short length
Ib3 = [ -10 units x 0.68x2 -0.8 units x (14.069-0.68x2) ] / 14.069
= -1.69 units

## Slide 24: 2D Mechanical designs
Interbeam distance = 204 mm
Øext iron yoke = 570 mm
Total Øext = 740 mm
65 + 20 mm thick shells
 2 x 0.67 mm 
 | σX max | σ Von Mises max
Keys + SS shell | -170 | 149
Cool-down | -205 | 188
Energization 16 T | -188 | 178
v3ari204
Interbeam distance = 204 mm
Øext iron yoke = 570 mm
Total Øext = 740 mm
65 + 20 mm thick shells
1.51mm 
 | σX max | σ Von Mises max
Keys + SS shell | -135 | 123
Cool-down | -184 | 170
Energization 16 T | -214 | 186
v4ari204
Interbeam distance = 204 mm
Øext iron yoke = 570 mm
Total Øext = 744 mm
67 + 20 mm thick shells
 2 x 0.72 mm 
 | σX max | σ Von Mises max
Keys + SS shell | -148 | 137
Cool-down | -181 | 160
Energization 16 T | -199 | 177
v4ari204

## Slide 25
Material properties (Davide 3rd FCC week)
  Coil maximum stress
    @ 4.2 K: 200 MPa
    @ 300 K: 150 MPa
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Al 7075 | 480 | 690
SS 316 LN | 350 | 1050
NITRONIC 40 | 350 | 1240
Ferromagnetic iron | 230 | 720*
Ti 6Al 4V | 800 | 1650
*Ferromagnetic iron @ 4.2 K stress < 380 MPa in tension (1st principal stress)
Material | E [GPa] |  | pr | (L4.3K-L293K)/L293K
 | 293 K | 4.3 K | 293K/4.3K | 293 K -> 4.3K
Coil | EX = 25 EY = 30 GXY = 21 | EX = 27.5 EY = 33 GXY = 21 | 0.3 | X = 3.36e-3 Y = 3.08e-3
StSt | 193 | 210 | 0.28 | 2.84e-3
Iron | 213 | 224 | 0.28 | 1.97e-3
Aluminum | 70 | 79 | 0.34 | 4.2e-3
Titanium | 115 | 126.5 | 0.3 | 1.74e-3
Nitronic 40 | 210 | 225 | 0.28 | 2.6e-3

## Slide 26: 2D Mechanical Design – Structure
Component | Material | Pre-load | 1.9 K | 16 T | Crit. 293K | Crit 1.9 K
Poles | Ti6Al4V | 622 | 870 | 1125 | 800 | 1650
Y-Pusher | Stainless steel | 84 | 369 | 489 | 350 | 1050
Y-Pad | Iron | 196 | 468 | 423 | 230 | 720
X-Pad | Iron | 303 | 461 | 482 | 230 | 720
Yokes | Iron | 486 | 631 | 716 | 230 | 720
Al shell | Al | 155 | 275 | 289 | 480 | 690
SS shell | Stainless steel | 260 | 230 | 250 | 350 | 1050
Von Mises [MPa]
Within spec
At spec or localized
Outside spec