## Slide 1
Linear vs non-linear beam-beam kick
Dima El Khechen
Acknowledgements: K. Oide

## Slide 2
OUTLINE
 Reminder
Trials and failures: Correction of residual dispersion/xy coupling
Artificial damping/excitation
Non-linear beam-beam kick (Ohmi san,s code) vs linear kick

## Slide 3
Reminder
Beamstrahlung simulations done in SAD with beam-beam element at IP
XY coupling established by vertical misalignments of sextupoles
Beam-beam simulations: larger emittance than design values
No beam-beam: A blow-up of emittance from 2.7 pm to 5 pm
Why? : Residual dispersions/xy couplings
175 GeV
45.6 GeV

## Slide 4
Reminder
Beamstrahlung simulations done in SAD with beam-beam element at IP
XY coupling established by vertical misalignments of sextupoles
Beam-beam simulations: larger emittance than design values
No beam-beam: A blow-up of emittance from 2.7 pm to 5 pm
Why? : Residual dispersions/xy couplings
= 5 pm

## Slide 5
Corrections
Corrections done locally
Variation of skew quadrupole components of few sextupoles upstream/downstream of the location to be corrected
IP
FRF
IP
FRF
IP
FRF
IP
FRF

## Slide 6
Corrections
Corrections done locally
Variation of skew quadrupole components of few sextupoles upstream/downstream of the location to be corrected

## Slide 7
Artificial excitation/damping
Instead of vertical misalignments, perform artificial excitation/damping as: Xf=Xi *(1-dmpr) +GaussRandom(), where X=(x,px,y,py,z,pz)
Energy spread
NO beam-beam element
@ 45.6 GeV

## Slide 8
Artificial excitation/damping
Instead of vertical misalignments, perform artificial excitation/damping as: Xf=Xi *(1-dmpr) +GaussRandom(), where X=(x,px,y,py,z,pz)
Energy spread
NO beam-beam element
@ 175 GeV

## Slide 9
Beam-beam w/ beamstrahlung
Perform beam-beam simulations with artificial noise
At 45.6 GeV, the emittance shows a slight increase than the design value (1 pm)
The beam size is also slightly larger than the design value w/ beamstrahlung
Different update schemes of the strong beam gave same results (Tobias)
Perform excitation/damping at different places not only at the beam initialisation
Is it a dynamic effect?

## Slide 10
Dynamic effects
Lattice simulations:
The beam-beam focusing can be presented by a thin quadrupole at the IP
Where the KL= ( the beam-beam focusing)
Tracking in the presence of a thin quadrupole shows a dynamics emittance effect
Beamstrahlung seems to have an effect on the vertical emittance
Dynamic Emittance from lattice simulations, with vertical misalignments of the sextupoles:
@45.6 GeV  =(0.27 nm, 1 pm)  =(0.264 nm, 1 pm)
@175 GeV  =(1.34 nm, 2.7 pm)  =(1.85 nm, 3.85 pm)
@ 45.6 GeV

## Slide 11
Dynamic effects @ 175 GeV

## Slide 12
Conclusions
Sextupole misalignments are not corrected yet
Simulations with artificial excitation/damping were performed
Linear and non-linear beam beam kicks were compared
Dynamic effects seem to exist.
Corrections need to be done and simulations should be verified with corrected dispersions and xy couplings

## Slide 13
BACK UP

## Slide 14
The beam-beam parameter
where is the beam-beam interaction strength
 ; where
Consider half ring tunes (since we have 2 IPs) :
=(0.569, 0.61) ,  (𝛽x0, 𝛽y0)= (0.15 m, 0.8 mm) , (𝛽x, 𝛽y)= (0.143 m, 0.525 mm) @ 45.6 GeV
=(0.553, 0.59),  (𝛽x0, 𝛽y0)= (1 m, 2 mm) , (𝛽x, 𝛽y)= (0.49 m, 1.12 mm)  @ 175 GeV
=(0.553, 0.59),  (𝛽x0, 𝛽y0)= (1 m, 2 mm) , (𝛽x, 𝛽y)= (0.49 m, 1.14 mm)  @ 182.5 GeV