## Slide 1: Radioactive ion beam R&D with SPIRAL 1
P. Delahaye for the Upgrade SPIRAL 1 team
Beamlab meeting, ISOLDE
3rd of April 2018
SPIRAL 1 Upgrade

## Slide 2: SPIRAL upgrade in a nutshell
Extending the number of elements produced by the ISOL method at SPIRAL
1+ ionisation: VADIS from ISOLDE
  1+ beams from metallic elements with Tfusion <2000°C
Conversion from 1+ to n+: Phoenix booster
  Almost chemistry independant, charge breeding times from 10 to ~200ms

## Slide 3: FEBIAD source
Already 7 new elements
Na, Mg, Al, P, Cl, Cu, Fe
+ many more to come
ISOLDE VADIS
1+ beams from metallic
elements with Tfusion <2000°C
Day 1 beams from FEBIAD TIS test results with 36Ar@95AMeV at nominal power at SPIRAL 1
2014- 2015: reliability tests
Failing BeO insulators exchanged
High voltage discharges at extraction fixed
More than 3 weeks running with stable efficiencies
2011 -2013 - Different tests at SIRA and SPIRAL 1
Coupling of the SPIRAL 1 targets with the VADIS
Dilatation problems are fixed
Ion source sliding against its axis
oven attached to container
Record temperature of 2400°C attained
Dec. 2013: tests at nominal power at SPIRAL 1
O. Bajeat et al, NIM B 317(2013)411
P. Chauveau et al, NIM B 376(2016)35
Notes: Fonctionnement pendant plus de 3 semaines avec efficacités stables

## Slide 4: FEBIAD source - status
2 ion target ion sources
1 in assembly
1 conditioned on the SPIRAL 1 test bench
Intensity increase to be confirmed on long term
*Yield estimates use conservative efficiencies*
A
Chart: 
| 4 | 20 | 36 | 76 | 132 | 222
MK5 ISOLDE | 0.37 | 7.8 | 11 | 19
VADIS ISOLDE | 1.4 | 6.7 | 26 | 38 | 47 | 62
VADIS GANIL | 1.7 | 8 | 14
MK5 ALTO | 20 | 9 | 22
IRENA ALTO | 26 | 15 | 30
Ref: L. Penescu et al, Rev. Sci. Instrum. 81, P. Chauveau et al, NIM B 376, S. Essabaa et al NIM A 317
Ionisation efficiency measurements
h%
He Ne Ar Kr Xe Rn
Using a calibrated leak with gas injection: h= I1+/Igaz
Latest @ GANIL
With Xe injection
?
?
Energy profile measurement
Charge breeding efficiency depends on dE
Simulations: M. Herbane, LPC Caen
sE~1.5eV
Notes: Interrogation sur les efficacités – eficcacité des taux cnservateurs – insister sur hors ligne, conditionnement

## Slide 5: Phoenix ECR charge breeder
Former ISOLDE ECR charge breeder
Upgraded with new Al plasma chamber, UHV vacuum,2 RF ports and gas injection, injection triplet, mobile injection and puller electrodes
Tested at LPSC in summer 2015
1+
High efficiencies with stable beams
Rare gases and alkalis
With contributions from
L. Maunoury et al, Rev Sci Instrum. 87(2016)02B508

## Slide 6: Phoenix ECR charge breeder
Back to efficiencies measured in 2015 at LPSC
Possible optimizations with higher B field at injection, as shown with LPSC CB are still possible
Noble gases
Alkaline elements
Notes: Ronds et diamants

## Slide 7
Upgraded magnetic field configuration: does not work for us!

## Slide 8: Overall schedule
SPIRAL 2 week 11/2016
RIB second semester of 2017
Presentation M. Dubois

## Slide 9: Organisation of the target and ion source R&D
Different developments
Testing production with new primary beam on C target
New Target or … new ion source
GANISOL
ISOL beams for GANIL
Evaluation in
reviews after each PAC meeting
Direction + TISS developpers + 4 external physicists (T. Stora, M. Assié, B. Blank, N. Orr)
List of priorities - from Review 2016/07
Test of new beams with C targets
1) 30P and 25Al from 40Ca fragmentation
2) 56Ni, 48Cr from fragmentation of 58Ni. For 56Ni: 56Co contamination to evaluate.
3) Beams (79Se, 60Fe, 67As) from 86Kr fragmentation.
Development of new targets
1) Nb for production of high intensities for beams with 30<Z<40
1) ex aequo Fusion evaporation targets (N=Z nuclei)
All science driven (LoIs)

## Slide 10: Radioactive ion beam commissioning
Accepted experiments:
Resonant proton elastic scattering on 17F and 2-proton emission from excited states in 18Ne, G. F. Grinyer et al (E750)
17F was observed as BeF molecule with dissociating BeO insulator
F atomic beams in principle well produced with FEBIAD sources
Optimization of 17F production from 20Ne fragmentation using the FEBIAD, directly followed by the experiment
Direct isospin mixing measurement in Coulomb excitation of an 38mK isomeric beam from SPIRAL1, G.De France et al (E737)
38mK from 58Ni fragmentation ok but not from transfer reaction with 36Ar
Population of the isomeric state depends on the reaction mechanism!
Testing 38mK from 40Ca fragmentation
2018 – run 1
R&D for future beams - Beamlab activities:
- Priorities from GANISOL review 2016/7/4
Preparing the MUGAST campaign – 2019/2020
From 40Ca fragmentation: test of of production of 25Al and 30P (LoI De Séréville et al)
  Trying the formation of hydride molecules
Test of production of 56Ni from the fragmentation of 58Ni (LoI Assié et al)
  Stripping to get rid of 56Co and 56Fe
Notes: Tentative dates for the radioactive ion beam commissioning March 2018
First experiments could then be in the end of first semester 2018 maybe after the tests

## Slide 11: Beyond commissioning…
To longer term: 2018-…
From day 1 beams…
ISOLDE FEBIAD + Graphite targets
New targets:
Fragmentation targets
  Nb target design is ongoing
  Others under study (SiC, Al2O3, CaO…)
Fusion evaporation targets
  thin Ni target (PhD thesis V. Kuchi)
+ ion source developments
Collaborations within EURISOL/Beamlab within ENSAR2
Fragmentation targets
Fusion - evaporation targets
Notes: For nuclear safety reasons (no Iodine filter at SPIRAL 1), the highest Z material that can be used for fragmentation is Nb.

## Slide 12: Fusion evaporation targets
Ongoing developments
To be tested at SPIRAL at the earliest in 2020
Fusion evaporation target ion source development
neutron deficient isotopes such as 74Rb, 114Cs, N=Z for DESIR
List of priorities from the GANISOL review 2016, July 4th
ECS fusion evaporation V. Kuchi, P. Jardin
fragmentation
Fusion evaporation
Collaboration with IPN Orsay – first test possible in 2019 with the Tandem
Offline test 2017-2018
Ionisation efficiency and rapidity measurement
Online test at ALTO earliest 2019
Online test at SPIRAL earliest 2020

## Slide 13: Fusion evaporation targets
Ongoing developments
To be tested at SPIRAL at the earliest in 2020
Fusion evaporation target ion source development
neutron deficient isotopes such as 74Rb, 114Cs, N=Z for DESIR
Ongoing measurement of emissivity of target foils
ANR ‘TULIP’ (Target Ion Source for Short-Lived Ion Production) has been submitted
List of priorities from the GANISOL review 2016, July 4th
Collaboration with IPN Orsay – first test possible in 2019 with the Tandem
Offline test 2017-2018
Ionisation efficiency and rapidity measurement
Online test at ALTO earliest 2019
Online test at SPIRAL earliest 2020
Test setup
Measurement of emissivity
with a 2 wavelength pyrometer

## Slide 14: Conclusion
SPIRAL 1 upgrade status
  The FEBIAD source has been thoroughly tested and is ready for on-line operation
    >3 weeks operation has been proven possible
    Stable efficiencies, some improvements possible (?)
  The SPIRAL 1 charge breeder has been installed in the beam lines and confirm performances shown in LPSC
    Efficiencies and charge breeding times are ok
    Optimized magnetic configuration gives higher efficiencies at LPSC, but not at GANIL
  Documentation for internal safety authorization is being prepared
    Should be completed these days!
  The RIB commissioning is planned in beginning of run 1
    Production test for accepted experiments: 17F, 38mK
    Production tests for future experiments: 56Ni, 25Al and 30P
    First experiment 17F@ACTAR
  Ongoing R&D for fusion evaporation target

## Slide 15: SPIRAL upgrade team
E. Lienard
G. Ban
X. Fléchard
D. Durand
O. Bajeat
M. Babo
P. Chauveau (now CSNSM)
C. Couratin (now IKS leuven)
M. Dubois (chef de projet)
P. Delahaye (resp. scientifique)
M. Fadil
R. Frigot
S. Hormigos
P. Jardin
P. Lecomte
N. Lecesne
L. Maunoury
B. Osmond
V. Toivanen (postdoc)
E. Traykov (now IPHC)
J. C. Thomas
…
GANISOL
ISOL beams for GANIL
T. Stora
C. Seiffert
F. Wenander
L. Penescu
J. Angot
T. Lamy
R. Vondrasek
Acknowledgements to