## Slide 1
Results to be obtained from test beam
-1- general illumination of detector with e.g. few GeV muon beam to get more data on alignment, pulse height uniformity and resolution, effective time resolution, position resolution, calibration procedure etc... check performance of detector with baby-MIND electronics.
-2- obtain a sample of converted gammas to study the two track separation and the e/gamma PID ability of the device.
Need magnets – Essential for e and e cross-sections
-3- test performance of Baby-MIND electronics in 0.2 T magnetic field could be done separately but may as well do it if we can.
-4- exposure to {p + e+ } and {- e- } in momentum (0.5 to 3 GeV/c ) to measure energy loss and time resolution. Try to acquire a sample of stopping pions and muons of both signs to study response to stopping particles and required dynamic range
Joint operation with TOF would be very useful
-5- exposure to + and - beams to observe a number of elastic scattering events e.g.
+ p  + p (kinematically constrained reaction!) and higher energy events with many tracks (multi track separation)

## Slide 2
Aim is to make use of the June-July period.
possibility to run also in 22 August – 19 September
period parasitically to TPC and EnuBET

## Slide 3
beam Cherenkov
converter
copper or lead
tracking chamber
do we have one?
Helium or low pressure bag
(if possible)
dipole
magnet
scintillator hodoscope
MNP17 B=0.2-1T
superFGD
prototype
superFGD prototype:
52x22x8 cm3
MDX
Possible layout
TOF

## Slide 4
A. Longhin

## Slide 5
BHZ3 ~2.66 m long.
~14m

## Slide 6
Alex Korzenev

## Slide 7
we located two magnets
-- one MDX type for the production of the gamma beam (I explained that in my presentation at the workshop in November 2017). There are several of those available so it should not be a problem.
-- one for the immersion of the detector in magnetic field (0 to 0.96T) MNP17 The aperture height is 30 cm, the length 52 cm and the width is quite large. So it would work very well to immerse a prototype of e.g. 50x20x10cm (10k cubes and 1700 channels).
We have made the request to the SPS coordinator for the use of this magnet.
This would allow investigation of
-- momentum reconstruction and
-- e/gamma separation
vs magnetic field
It is urgent to check the availability of this magnet in June-July period!

## Slide 8
A Photon beam in T9 area
Principle
e- beam
Cu radiator
MDX magnet
0.51 T.m
hodoscope
(measures electron momentum
 photon energy)
 beam
A. Blondel, L. Gatignon
may need a position detector
best is probably
around 2 GeV/c e-
for 200-800 MeV
photons
(should be simulated)

## Slide 10
x-y view
x-z view
MNP17 magnet
(laid with B vertical normally
… horizontal possibility?)

## Slide 11
x-y view
MNP17 magnet
(laid with B vertical normally
… horizontal possibility?)
question is there a few bolting
holes on the surface of the magnet pole
or somewhere else on the magnet,
to design the support?

## Slide 12
x-z view
Cables
electronics
Cables
SFGD
electronics
Cables
electronics
Cables
SFGD
electronics
Cables
electronics
Cables
SFGD
electronics

## Slide 13
x-z view
SFGD
electronics
Cables
electronics
Cables
Cables
Cables
SFGD
electronics
Cables
electronics
Cables
Cables
Cables
SFGD
electronics
Cables
electronics
Cables
Cables
Cables

## Slide 14
x-z view

## Slide 15
example of set-up from last year using a magnet,
and with another detector test upstream,
there is 2.9m free space in front of the magnet

## Slide 17
Detector shape
Especially for the photon conversions in magnetic field it is better to have a deeper
and thinner detector
beam
52
8
22

## Slide 18
photon beam
B

## Slide 19
electron beam
B

## Slide 20
pion beam
+
+
p
we can also get a nice sample of low energy protons from + p  + p

## Slide 21
proton beam
+
Or simply study stopping protons for momenta 500-800 MeV/c

## Slide 22
Chart: 
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 125 | 150 | 160 | 200 | 225 | 250 | 275 | 294.81953290000001
range vs kinetic Energy | 0.185 | 0.257 | 0.432 | 0.647 | 0.9 | 1.19 | 1.51 | 1.87 | 2.268 | 3.639 | 4.153 | 4.706 | 5.284 | 5.889 | 6.515 | 7.183 | 7.87 | 11.7 | 16.1 | 18.02 | 26.5 | 32.4 | 38.7 | 45.5 | 51.05
range vs momentum | 0.185 | 0.257 | 0.432 | 0.647 | 0.9 | 1.19 | 1.51 | 1.87 | 2.268 | 3.639 | 4.153 | 4.706 | 5.284 | 5.889 | 6.515 | 7.183 | 7.87 | 11.7 | 16.1 | 18.02 | 26.5 | 32.4 | 38.7 | 45.5 | 51.05
Range vs Momentum of protons in Polystyrene
Maximum energy deposition in a single cell: ~30-45 MeV (22 MIPs = 880 pixels)
Range of 500 MeV/c protons : 12cm
Range of 800 MeV/c protons : 50cm
https://physics.nist.gov/PhysRefData/Star/Text/PSTAR.html

## Slide 23
Maximum energy deposition in a single cell: ~30-45 MeV (22 MIPs = 880 p.e.)
this means that the MPPCs need much more than 900 pixels. 1600 possibly OK
Because of scintillator saturation (Birk’s law) the single cell signal
might be further saturated (down to ~600 p.e.?) still 1600 pixels needed, as their might be
more than one evaporation proton at vertex.
This is not an effect that is well understood, test beam data will be very useful.
Range of 500 MeV/c protons : 11cm
Range of 800 MeV/c protons : 51cm
The lowest beam momentum of the beam is 500 MeV/c,
Thus we can essentially explore all the detector with settings from 500 to 800 MeV/c
However 500 MeV/c pions or muons will not stop in the detector unless they interact
Inelastic multi-prong interactions will also be interesting to collect.
Comments

## Slide 24
2017 EnuBET test set-up
The silicon beam chambers
provide 50 micron resolution
useful for TPC/SFGD?

## Slide 25
From Baby-MIND electronics to SuperFGD electronics
For test beam in summer 2018
8x22x52 cubes (cm3) is being prepared @ INR 1736 channels. FANTASTIC!
we have begun production of 13 x 96 channels + 7x 96 spare channels from Baby-MIND
 aim at full instrumentation of SuperFGD prototype for June-July test beam.
layout the electronics outside MNP17 magnet
Plan test of the effect of magnetic field and the timing resolution (see below)
DAQ will be that of Baby-MIND. Work already started to include TOF. (Korzenev)
Towards SuperFGD (a first look)
-- SuperFGD is inside the magnet surrounded by TPCs
material budget should small, avoid copper and cables
 try geometry of electronics directly set on detector surface.
 re-routing of (hopefully mostly) same electronics on different layout.
-- 2’000’000 cubes and 60’000 channels
 thermal issues and communication issues (getting data out)
-- mechanical design, cooling system and communication system must be integrated
-- 2kG magnetic field must be tested
-- may need to improve timing resolution (establish after summer test)
A few weeks will be necessary to define full set of questions and required extra manpower;
collaboration welcome; test beam results will be important!