## Slide 1: IR magnets and MDI integration
A.Bogomyagkov, A.Krasnov, E.Levichev, S.Pivovarov, S.Sinyatkin
Budker Institute of Nuclear Physics, Novosibirsk, Russia

## Slide 2: Initial conditions and constrains
Full crossing angle 30 mrad.
First (defocusing) quad QC1 is placed in L*= 2.2 m from the IP.
Set of magnets (QC1, QC2, A-sol, screening sol, correctors) in a cryostat which has to occupy 100 mrad cone.
Lumical at 1m to 1.25 m in not symmetrical space covering +140 mrad and -100 mrad.
IP vacuum chamber with 30 mm inner diameter increasing with distance.
A BPM (at each tube) before the cryostat.
Remote vacuum flanges.
Bellows before the cryostat.

## Slide 3: MDI scheme
Very schematical example from KEK.
IP
Cooled IP Be tube
Flange and Be tube cooling inlet
Cooled Y-chamber, HOM absorber, SR masks
BPM module
Remote flange
Bellow
Cryostat
Cryostat wall thickness

## Slide 4: Cryostat “wall” thickness (KEK)
58 mm
50 mm
37 mm
According to BINP experts (~50 SC wigglers), a minimum cryostat “wall” thickness is ~30-50 mm, which corresponds well to the KEK example drawing.
Inner SS wall 6(5) mm
Outer SS wall 15 (5) mm
10 (3) mm vacuum
10 (7) mm superinsulation
Cu screen 4 (2) mm
In total: ~45 (22) mm

## Slide 5: February MDI meeting at CERN
140 mr
100 mr
Lumical
HOM abs.
Cryostat is in the 100 mrad cone with 50 mm wall
Anti-sol by Mike
Anti-sol by Sergey
Mike’s design
Sergey’s design
Neither Mike’s no Sergey’s (old) design fits the cryostat
QC1
Anti-sol

## Slide 6: February MDI meeting at CERN
Between remote flanges
Qs
ScS
CS
HOM Absorber
LumiCal
Remote flange
Two bellows
NEG pump, custom design

## Slide 7: Koratzinos design, (February)

## Slide 8: Remote flange prototype
Flange outer dimensions:
Length 71.5 mm
Flange 2*radius(2*43)+ distance between beams
At s=1619 mm
Flange outer size
Receiving part
1619*0.03+86=134.57 mm
Incoming part
134.57+6=140.57 mm

## Slide 9: Current IR design
Present designs does not fit the 100-mrad-cone with the cryostat.
Having the flange inside the cryostat, how to fit mechanical transmission of the flange?
Reduction of antisolenoid diameter is not possible, because it will degrade the vertical emittance due to the strong horizontal field at the beam’s orbit.
Stray field from large diameter antisolenoid needs a large gap before the first quadrupole.
Even if we increase 100 mrad cone to 140 mrad, still there are problems with accommodation of HOM absorber, flanges, bellows, BPMs, NEG pump (needs to be activated by heating to 400C).

## Slide 10: New design of the cryostat tip (preliminary)
Lumical
Individual antisolenoids for each beam shifted closer to QC1 and covered by common screening solenoid ( –2 T).
HOM abs. + NEG pump
BPM
Remote flange
Bellows
Cryostat, 100 mrad, 22-50 mm “wall” thickness
Antisolenoid x 2
Screening sol

## Slide 11: Compact single beam solenoid
Individual anti-solenoid for each beam covered by common screen-solenoid ( –2 T) shifted closer to QC1.

## Slide 12: Overall size
500

## Slide 13: 3D views
Lumical
HOM abs NEG pump
BPM
Flange
100 mrad cone
Anti-sol
QC1
QC1 cryostat
QC2 cryostat

## Slide 14: 3D views
QC2 cryostat
QC1 cryostat
100 mrad cone

## Slide 15: 3D views

## Slide 16: 3D views without comments

## Slide 17: Assembling with remote control flanges I

## Slide 18: Assembling with remote control flanges II

## Slide 19: Assembling “on a table” I
500
500

## Slide 20: Assembling “on a table” II

## Slide 21: 3D views without comments