## Slide 1
DAB-based Ring fast BCTs – BA3
2 integrators (21ns effective integration time) in tandem
2 acquisition modes:
  REPETETIVE:
  Total Intensity averaged @ 20 Hz – published at the end of the cycle
  Bunch-by-bunch intensity averaged @ 20 Hz – published at the end of the cycle
  TURN_BY_TURN:
  Turn-by-turn (max 500) intensity for tracking instabilities at injection – published at the end of the cycle
Calibration a la BCTFI
Settings a la BCTFI
Expert settings to treat undershoots in SW

## Slide 2
SFTPRO cycle with DAB (BA3) and VFC (ECA5)
DAB - LBW
DAB - HBW
VFC

## Slide 3
SFTPRO cycle with DAB (BA3) and VFC (ECA5) - Zoom
OP never trusted the measurement in BA3
DAB - LBW
VFC
DAB - HBW

## Slide 4
VFC-based Ring fast BCTs – ECA5
Automatic gain selection – possibility to lock to a specific one
Numerous algorithms implemented in firmware for:
  Zero-suppression
  Baseline
    Minimum
    Abort gap
    Variable
  Peak finding
  …

## Slide 5
VFC-based Ring fast BCTs – ECA5
Total Intensity averaged @ 50 Hz – published at the end of the cycle
Bunch-by-bunch intensity averaged @ 50 Hz – published at the end of the cycle
Beam filling pattern @ 50 Hz – published at the end of the cycle
Turn-by-turn (max 1023) intensity for tracking instabilities at injection – published when data ready
Total Intensity @ the basic period
Total Intensity @ the flat-top (not available for every cycle due to missing timings) – published at the end of the cycle
Bunch-by-bunch Intensity @ the flat-top (not available for every cycle due to missing timings) – published at the end of the cycle
Down sampled bunch intensities for logging (@ the basic period)

## Slide 6
Free running buffers cause misalignment (1st IRQ never at the same time)
This is an issue for MDs (reported by Simone)
Total Intensity averaged at 50 Hz

## Slide 7
Raw ADC in 16 bits otherwise too big
Rarely overflows
Bunch Intensity averaged at 50 Hz
adc
# of charges

## Slide 8
1023 Turn-by-turn measurement
Total intensity measurement
adc
adc
time
20 ms Injection Warning
Configurable delay in ms
Unfreeze buffers
IRQ
# of turns
Injection
Turn-by-turn Intensity

## Slide 9
1023 Turn-by-turn measurement
Total intensity measurement
adc
adc
Due to the free running nature of the acquisition, injection is moving around!
Turn-by-turn Intensity
time
20 ms Injection Warning
Configurable delay in ms
Unfreeze buffers
IRQ
# of turns
Injection

## Slide 10
Average of the 50 Hz measurements
Not available for every cycle
Flat-Top total and bunch-by-bunch Intensity

## Slide 11
Total Intensity averaged @ 50 Hz
Bunch-by-bunch intensities averaged @50 Hz – averaged @ basic period
Intensity @ flat-top
Logging

## Slide 12
5th degree polynomial while we use linear correction
3 types of factors per beam type – non PPM
  Single bunch
  25 ns
  200MHz
Setting to choose which type to use PPM
Scaling Factors

## Slide 13
36 PPM Settings!
Difficult names as kept register names
Description available for most of them…
Guru Settings PPM

## Slide 14
Conclusions
VFC gives very nice results
Free-running nature of acquisition is an issue for SPS measurements
Too many capabilities… Too many settings!
No calibration (yet)