## Slide 1: n_TOF commissioning
INTC-P-249
Spokespersons: J.L.Tain, V.Vlachoudis
Contactperson: V.Vlachoudis
16-17th Nov 2009
for the n_TOF collaboration

## Slide 2: New Target – Refurbished Facility
Pb mono-block (60cm L40cm)
Forced water cooling
Chemically controlled water
Oxygen/Corrosion control
Separate moderator from cooling
  Al container
  3 Al-windows with air-gap
Defocused proton beam
New Ventilation system
Air-tight primary zone with a 40Pa depression

## Slide 3: Proposed measurements
Neutron fluence
Neutron beam profile
Neutron energy resolution function
Neutron energy versus time-of-flight relation
Scattered in-beam -ray background
Scattered neutron background
Off-beam background
Needed to obtain cross sections
The neutronics of the new target is different, therefore there is a need to characterize carefully the beam and backgrounds in order to fulfill our goal of obtaining accurate data:
Needed to control systematic errors
Detected counts as a function of ToF
Cross section as a function of energy

## Slide 4: Requested beam time
General start-up: 1.01017 p
Neutron fluence: (*) 1.61018 p
Beam profile: -
Resolution Function: (*) 5.01017 p
In-beam -ray background: (*) 4.01016 p
Scattered n background: 2.11017 p
Off-beam background: -
Total: 2.451018 p
(*) assuming: normal water / borated water

## Slide 5: Proposed Experimental Apparatus
Beam characteristics:
Neutron fluence: PTB Fission Chamber 235U, 238U FIC 235U, 238U uMegas: 235U & 10B SiLi, Gold foils
Spatial distribution: Medipix with LiF & polyethylene X-Y mMegas with 10B
Resolution function: C6D6 with 54,56Fe, 32S
Background: CR-39, TLD, BaF2 and C6D6
Cooling station:
Monitor Performance
Control O2 level
PTB FC
X
uMegas
Quad Medipix
C6D6
TAC

## Slide 6: Commissioning Diary
18.05.2009 Scheduled beam on n_TOF target
Delayed due to PS problems
26.05.2009 Medipix run. Problem on readout of the beam transformer. No reliable proton information.
01.06.2009 X-Y mMegas Beam profile measurements Alignment issues with the detectors
Possible alignment problem on 2nd collimator
09.06.2009 Beam transformer readout problem solved
15.06.2009 Resolution function
22.07.2009 Fluence measurements with PTB chamber
13.08.2009 Fe/Ni proposal
…
09.11.2009 Scattered neutron background in TAC
16.11.2009 Experimental alignment of the second collimator

## Slide 7: Experimental Area

## Slide 8: Beam profile results
Comparison X-Y Micromegas data vs. simulation for the New Target
Projection of a cut around the mean value of the 2D distribution of X and Y
  +/- 2.5 mm in simulated data
  +/- 2.8 mm for X-Y Micromegas data
Experimental @ S-Ex position
Simulated @ 184.5 m
Full coverage from thermal to 1 MeV

## Slide 11: Resolution Function
The direct comparison with data from 2002 do not indicate a significant change in the Resolution Function. The detailed analysis from high energy 56Fe resonances and simulations remains to be done.
Use 2 C6D6 detectors
2g samples enriched 54Fe, 56Fe
Also 32S (513, 819keV)
Expected:
103 counts in weakest resonance
25% worsen on the tail. Effect to be seen after resonance analysis with SAMMY
The C6D6 were placed upstream to reduce the in-beam gamma background → Statistics were lower
PRELIMINARY

## Slide 12: Neutron Fluence measurements
The shape and intensity of the neutron fluence at n_TOF has been characterized by means of five different measurements:
 | Reaction | Shape | Intensity
PTB | 235U(n,f) | Yes | Yes
mMegas | 235U(n,f) & 10B(n,a) | Yes | ~
SiMon | 6Li(n,t) | Yes (En<keV) | ~
TAC | 197Au(n,g) | No | Yes (@4.9 eV)
Activation | 197Au(n,g)198Au(b) | No | Yes (@4.9 eV)
The shape of the neutron fluence is crucial for all capture measurements, which are normalized to a saturated resonance at a given energy.

## Slide 13: Neutron fluence
A combination of all detectors provided the neutron fluence spectrum&intensity
All detectors agree within 4-5%
Neutron fluence is lower by 20-28% than expectations → Consistent with a possible 2nd collimator tilt by -2mm.
PRELIMINARY

## Slide 14: Comparison with old target
Neutron fluence is comparable with the previous target apart from more pronounced the aluminum resonances
Deeper Al dips (En>30 keV)
PRELIMINARY

## Slide 15: Summary
Setup
Problems in reading the transformers
Problems in alignment of detectors
Beam Profile
Protons: uMegas 1×1018 + Medipix 6×1016 p
Horizontal plane: Very good agreement with the expectations
Vertical plane: Agreement assuming a tilted second collimator by -2mm
Neutron fluence
Protons: PTB 1×1018 p
20-25% lower than the expectations → collimator misalignment/tilt
Resolution function + Energy-Time relation
Protons: 4×1017p (+exploiting the statistics from Fe/Ni proposal)
No significant change with the past
Analysis still on progress

## Slide 16: On-going / future measurements
2009: ongoing
Sample scattered neutron background in TAC
Cross-check 2nd collimator alignment experimentally
2010: planned
Borated water circuit operating in two modes 0% 10B-content or fully saturated ~1% 10B Measure:
  Neutron fluence
  Resolution
  Reduction effect of in-beam g-rays