## Slide 1: CI updates

## Slide 2: Chamber repair
Returned yesterday
Initial vacuum test
  After 12 hour pumping, reaching to 10-8 mbar
  No obvious leaking
  Might have outgassing
Chamber | Pressure
Nozzle chamber | 3.6e-8 mbar
Skimmer chamber | 3.6e-8 mbar
Interaction | 6.2 e-8 mbar
Dumping | 2.3e-8 mbar

## Slide 3: Alignment
Installed the reflecting mirror
Currently using the alternative designed nozzle.
Laser-nozzle-mirror is aligned.
Skimmers is waiting to reinstall
mirror
Camera

## Slide 4: Faraday cup design
Based on previous faraday cup
On a DN63 to Dn40 reducer flange
DN40 feedthrough
High voltage plates
Cup
Collecting pin
36 mm
opening
20 mm

## Slide 5: Electron Gun
Arrived this week
Installed in the old setup
Wait some modification of the old faraday cup then close the chamber to pump
Vacuum gauge
Port aligner
gun

## Slide 6: Next
Install skimmers and align them with current reference laser.
Machining Faraday cup for the new setup.
Curry out experiments with new electron gun in the old setup.
  Integration time
  Gas density using the gauge