## Slide 1: Brief PS status 20 April 2018
Frank Tecker, on behalf of PS operations and supervisor team

## Slide 2: PS Beams Overview
Operational Beam Status: | 
LHCPROBE | Operational
LHCINDIV | Operational
LHC25#12b | Available at nominal intensity (1.3 · 1011 ppb)
LHC25#72b | Available at nominal intensity (1.3 · 1011 ppb)
LHC25#12b_BCMS | Available at nominal intensity (1.3 · 1011 ppb)
LHC25#48b_BCMS | Available at nominal intensity (1.3 · 1011 ppb)
LHC50#36b | Not set up
LHC100#18b_Split_1_4GeV | Not set up
LHC25#56b_8b4e | Not set up
LHC25#32b_BCS_8b4e | Not set up
LHC_ION_Early_Pb54 | Longitudinal preparation without beam completed. Should be able to take beam
ILHC100#2b | Not set up
ILHC100#4b | Not set up
SFTPRO-MTE | Available, intensity limit: 1.8 · 1013 ppp (today @ 830 ·1010)
EAST_North | Operational
EAST_IRRAD-CHARM | Operational
EAST_Irrad_Probe | Not set up
TOF | Available up to 8 · 1012 ppp (today @ 770 ·1010)
AD | Available at 1.4 · 1013 ppp (today @ 1 · 1013)

## Slide 3: PS
Parallel MDs started this week
Dedicated MD for transfer line matching PSB -> PS
  Had to be rescheduled on LHC request on the fly for the morning (instead afternoon)
  Magnets recabled, Beam steering with ~95% transmission in the line
  Losses at injection, later attributed to the PS internal dump
  Measurement with PS horizontal SEMGRIDS, kick response
Faults
  Timing repeater failure delayed the startup after dedicated MD on Wednesday by ~3 hours
    Difficult to diagnose: Beam loss, consequence of MD suspected, Internal dump found blocking, transition problems, extraction bump not pulsing
  EAST area T10 QDE01 magnet issue, current limits physics to 5 GeV/c (instead of 6)
  Several problems from the Booster, temperature interlock on quadrupole, now solved