## Slide 1: 3YP: UFOs in the large hadron collider
Collection Group: Isobel Patterson, James Rudkin, Thomas Yates, Chloe Adams-Pickford
Supervised by: Alexander Korsunsky and Daniel Eakins

## Slide 2: Contents
Defining the project scope: objectives, technical review, initial design ideas and final design criteria
Overview of the proposed solution
Detailed view of key components: generating and calculating air flow, filter, connector modules
Evaluation of design: comparisons with literature and simulation
Areas for further development

## Slide 3: Project Definition
To develop a method or device to collect particles from within the Large Hadron Collider (LHC) at CERN

## Slide 4: Motives
What is the problem?
Why is the problem important to solve?

## Slide 5: Technical Review: UFOs
Assumptions on nature of UFOs
  Diameter ranging from 1-100µm
  Uncharged
  Spherical
  Metallic, ceramic or organic (solid at room temperature)

## Slide 6: Design Criteria
Collected particles must be representative of the Unidentified Falling Objects (UFOs)
Must not interfere with the operation of the LHC
Must not produce further contamination – if possible use materials that are not used in the LHC to allow easy identification

## Slide 7: Overview of Proposed Solution
4

## Slide 8: Overview of Proposed Solution
4

## Slide 9: Detailed view: Air flow calculations
Assumptions:
Perfectly spherical
Properties of gold
Apply vertical equilibrium:
Free body diagram of the forces on a sphere in a linear velocity profile (Modified from Hayden et al (2003))

## Slide 10: Detailed view: Air flow calculation (2)
Experimental data of minimum pick-up velocity from Hayden et al (2003) along with derived equation as a function of particle diameter.

## Slide 11: Detailed view: Connector module
Purpose: to join the sample segment of cold bore tube to a filter
Criteria:
Connect to cold bore tube with diameter of 50mm
Connect to filter with inlet tube of diameter 8.5mm
Fits into space made available from removal of plug-in modules
Fabricated from a material not present in the LHC (to minimise production of further debris)
Minimise mass and cost where possible
Material capable of withstanding the applied force from air flow

## Slide 12: Overview of Proposed Solution
4

## Slide 13: Detailed view: Connector module (2)

## Slide 14: Overview of Proposed Solution
4

## Slide 15: Detailed view: Filter
Criteria:
Collect particles
Withstand pressure drop
Diameter approx 6mm

## Slide 16: Detailed view: Filter (Pressure Drop)

## Slide 17: Filter: Pressure Drop Evaluation

## Slide 18: Filter: selection
HEPA
Whatman HEPA-Vent filter
A = 16cm2
2.38 bar, 4.1 bar

## Slide 19: Overview of Proposed Solution
4

## Slide 20: Detailed view: Overall Requirements

## Slide 21: Detailed view: Air cylinder, inlet pipes
Air inlet – flexible hosing (PVC)
  Positives for non-lab applications
  Significant limitations due to ‘rule of thumb’ calculations
Exhaust – removed
Cylinder
  Late change of gas
  Synthetic air selected
Valve
  Limited information on valves included
  Recommendation of diaphragm valve
Opportunity for integration with other systems?

## Slide 22: Overview of Proposed Solution
4

## Slide 23: Solidworks Simulation of Air Flow
Plots comparing theory and calculation for pressure and velocity from ‘VALIDATION EXAMPLES SOLIDWORKS’ FLOW’SIMULATION 2017’

## Slide 24: Pressure drop
The simulated/calculated pressure distribution along the 16m cold bore section.

## Slide 25: Velocity and streamlines
Figure 4.4H. The velocity profile along the cold bore and beam screen. Offset to be along the pumping slots. Also showing the velocity streamlines.

## Slide 26: Post-Collection Particle Analysis Scanning electron microscopes with energy dispersive X-ray spectroscopy
A diagram showing the X ray emission from an atom.
Courtesy of: ‘Generation of X-Rays in the SEM specimen’
A SEM image (left) of HVAC filter with particulates and corresponding EDS spectrum
Courtesy of: Nanoscience Instruments
Other potential Method: Solvent bath and centrifugation
A diagram showing the separating of particles in a solvent through centrifugation.
Courtesy of: Sofroniou 2012

## Slide 27: Evaluation of Design
Assumptions
Testing and Iteration
Simulation

## Slide 28: Areas for further development
Comparisons – before and after
Targeted post-collection analysis
Multiple filtration options

## Slide 29: Thank you for your time Any questions?

## Slide 30: References?