## Slide 2
Statistic
Notes: In the us 38% of all men and women are diagnosed with cancer at some point during their lifetime (https://www.cancer.gov/about-cancer/understanding/statistics)
2

## Slide 3
Beams for Cancer Treatment
Johanna Pitters
31/07/2018
Summer Camp Lecture
Notes: 3

## Slide 6
https://www.mun.ca/biology/desmid/brian/BIOL2060/BIOL2060-24/CB24.html
What is cancer?
Notes: Cancer= malignant cells that devide in an uncontrolled way
Primary tumor, spread through circulatory system, invade new locations
Early diagnostic is key to success
6

## Slide 7
Dose-Response-Curve
Treatment: higher response from cancer cells than normal, healthy tissue
Harm to healthy tissue may induce unwanted side effects
tumor
healthy tissue
Notes: 7

## Slide 8
Treatment methods
Chemotherapy
(Systemic therapy)
Notes: 8

## Slide 9
Treatment methods
Surgery
Chemotherapy
(Systemic therapy)
Notes: 9

## Slide 10
Treatment methods
Radioisotope + Linker + Carrier
Receptor
Surgery
Chemotherapy
(Systemic therapy)
Radiopharmaceuticals
(Targeted therapy)
Production of radioisotopes
at CERN Medicis facility
Notes: 10

## Slide 11
Treatment methods
Radioisotope + Linker + Carrier
Receptor
https://www.treatmesothelioma.org/treatment/complementary/immunotherapy/
Surgery
Chemotherapy
(Systemic therapy)
Radiopharmaceuticals
(Targeted therapy)
Immunotherapy
Notes: 11

## Slide 12
Treatment methods
Radioisotope + Linker + Carrier
Receptor
https://www.treatmesothelioma.org/treatment/complementary/immunotherapy/
Surgery
Chemotherapy
(Systemic therapy)
Radiopharmaceuticals
(Targeted therapy)
Immunotherapy
External beam irradiation
Notes: 12

## Slide 13
Cell damage through
ionizing radiation
Chemical stage:
-> chemical bonds break
-> formation of free radicals
Biological stage:
cell cycle stops while cell attempts to repair
Physical stage:
Excitation and Ionization

## Slide 14
Cell damage through
ionizing radiation
Chemical stage:
-> chemical bonds break
-> formation of free radicals
Biological stage:
cell cycle stops while cell attempts to repair
Irreversible DNA damage
-> Apoptosis
Physical stage:
Excitation and Ionization

## Slide 15
http://radioactivityci2010.pbworks.com/w/page/30525316/Fast%20Neutron%20Therapy
low ionization density
high ionization density
Cell damage through
ionizing radiation
More likely to cause severe DNA damage
e.g. through double- strand breaks
http://radioactivityci2010.pbworks.com/w/page/30525316/Fast%20Neutron%20Therapy

## Slide 16
Dose
Dose Equivalent dose Effective dose
Energy deposited in tissue
Gy [J/kg] Sv [J/kg] Sv [J/kg]
Damage to organ
weighted: tissue
Photons (1)
Electrons (1)
Protons (2)
Heavy ions (20)
Neutrons
...
CIRT 73.6 GyE
16 fractions IMPT
Damage to tissue
weighted: radiation

## Slide 17
External Beam Irradiation
www.particlezoo.net
electron
photon
How do they deposit energy in the tissue?
Where do they deposit energy in the tissue?
carbon ion
proton

## Slide 18
Electrons
http://www.sfowler.com/investigations/Mail%20Irradiation.htm
Relative Dose [%]
Energy loss:
- Inelastic scattering -> excitation, ionization
- Radiative stopping → ‘bremsstrahlung’ (goes up with electron energy and Z)
Scattering through collisions
-> broadening of the beam
Nucleus

## Slide 19
Electrons
LINAC – linear accelerator

## Slide 20
Electrons
LINAC – linear accelerator
Proton LINAC

## Slide 21
http://tulectures.web.cern.ch/TULECTURES/Folien/06_Linearbeschleuniger_MB.pdf
Electrons
Electron LINAC
4 – 25 MeV electrons

## Slide 22
http://tulectures.web.cern.ch/TULECTURES/Folien/06_Linearbeschleuniger_MB.pdf
Electrons
Collimator
for transverse beam shaping

## Slide 23
http://tulectures.web.cern.ch/TULECTURES/Folien/06_Linearbeschleuniger_MB.pdf
Electrons
Gantry allows for irradiation from all angles

## Slide 24
Photons
Intensity of photons decreases exponentially with penetration depth
www.radsafemedical.com
Interaction with matter through:

## Slide 25
Photons
Intensity of photons decreases exponentially with penetration depth
www.radsafemedical.com
Photoeletric Effect
Compton Scattering
Electron
Z
Pair Production
Positron
Interaction with matter through:

## Slide 26
Photons
Intensity of photons decreases exponentially with penetration depth
www.radsafemedical.com
Photoeletric Effect
Compton Scattering
Electron
Z
Pair Production
Positron
Interaction with matter through:

## Slide 27
Photons
Depth in water [cm]
Dose [%]
https://www.uniklinik-freiburg.de/roentgen/live/lehre/kursplan/strahlentherapie.pdf
Dose build-up
Most of the biological effect comes from secondary electrons
Dose buid-up as electrons tend to move in forward direction
Intensity of photons decreases exponentially with penetration depth
Interaction with matter through:
Photoelectric effect
Compton scattering
Pair production

## Slide 28
Photons
Production of photons from
bremsstrahlung of electrons on target
Energy loss:
- Inelastic scattering -> excitation, ionization
- Radiative stopping → ‘bremsstrahlung’ (goes up with electron energy and Z)
Scattering through collisions
-> broadening of the beam
Nucleus
Electrons

## Slide 29
Protons
DOI=10.3389/fonc.2015.00150
Excitation and ionization
of target electrons
Ion approaches Bohr-velocity
Viscous drag ~v

## Slide 30
Protons
DOI: 10.2174/1872210509999141222224121
Protons stop!
Protons lose most of their energy towards the end of their track!
Bragg peak

## Slide 31
Protons
Bragg peak
Photons
Protons
+ healthy tissue can be spared
+ very precise dose deposition

## Slide 32
Protons
Beam delivery:
SOB – Spread-out Bragg peak
Tumor divided in slices, each slice
at a certain depth irradiated with
corresponding energy

## Slide 33
Protons
DOI: 10.1088/0034-4885/79/9/096702

## Slide 34
Protons
DOI: 10.1088/0034-4885/79/9/096702
Cyclotron

## Slide 35
DOI: 10.1088/0034-4885/79/9/096702
Protons
http://discovermagazine.com/2014/oct/14-precision-vs-profits
IBA proton gantry
100 t

## Slide 36
Protons
DOI: 10.1088/0034-4885/79/9/096702
http://www.medicalexpo.com/prod/iba/product-101137-666281.html
Gantry treatment room

## Slide 37
Carbon Ions
http://radioactivityci2010.pbworks.com/w/page/30525316/Fast%20Neutron%20Therapy
proton track
carbon ion track
High density ionization:
→ High biological effectiveness
→ DNA double-strand breaks
→ Radioresistant tumors

## Slide 38
Carbon Ions
http://radioactivityci2010.pbworks.com/w/page/30525316/Fast%20Neutron%20Therapy
proton track
carbon ion track
High density ionization:
→ High biological effectiveness
→ DNA double-strand breaks
→ Radioresistant tumors

## Slide 39
Carbon Ions
High density ionization:
→ High biological effectiveness
→ DNA double-strand breaks
→ Radioresistant tumors

## Slide 40
Radiotherapy and Oncology 95 (2010) 3–22
http://flab.phys.nagoya-u.ac.jp/workshop/2008/emws03docs/s09_Toshito.pdf
Carbon Ions
target fragmentation
projectile fragmentation
Projectile fragments can travel beyond the Bragg peak
→ fragmentation tail
projectile
target atom

## Slide 41
Carbon Ions
4 treatment lines
3 treatment rooms
2 ECR sources
Synchrotron
25m diameter
7 MeV/u LINAC
Synchrotron for
protons and carbon ions
World-wide
only 10 centers

## Slide 42
Carbon Ions

## Slide 43
Carbon Ions
HIT carbon ion gantry
450 t of rotating parts

## Slide 44
Carbon Ions
HIMAC, Japan

## Slide 45
Carbon Ions
‘compact’
superconducting
gantry
HIMAC, Japan

## Slide 46
Carbon Ions
‘compact’
superconducting
gantry
HIMAC, Japan

## Slide 47
Proton and Carbon Centers world-wide
Durante M, Orecchia R, Loeffler JS, 2017
60 Proton Centers
10 Carbon Ion Centers
More than
120 Centres
expected for 2022

## Slide 48
Summary: Dose-depth profile
http://www.wikiwand.com/en/Electron_therapy

## Slide 49
Summary: Dose-depth profile
http://www.wikiwand.com/en/Electron_therapy

## Slide 50
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | 
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | 
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | 
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | 
5 | Chondrosarcoma, tumor on scull base, radioresistant | 
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 51
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | 
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | 
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | 
5 | Chondrosarcoma, tumor on scull base, radioresistant | 
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 52
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | 
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | 
5 | Chondrosarcoma, tumor on scull base, radioresistant | 
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 53
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | A
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | 
5 | Chondrosarcoma, tumor on scull base, radioresistant | 
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 54
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | A
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | E
5 | Chondrosarcoma, tumor on scull base, radioresistant | 
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 55
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | A
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | E
5 | Chondrosarcoma, tumor on scull base, radioresistant | G
6 | inoperable liver tumor, skin should be spared as far as possible | 
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 56
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | A
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | E
5 | Chondrosarcoma, tumor on scull base, radioresistant | G
6 | inoperable liver tumor, skin should be spared as far as possible | D
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | 
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 57
Your turn!
Which treatment would you suggest for these patients?
# | Patient | 
1 | well localized brain tumor close to brain stem at 10 cm depth | F
2 | widespread bronchial carcinoma (lung cancer) at 10 cm depth, heart should be spared | C
3 | tumor on chest wall, healthy heart muscle starts at 2.5 cm depth | A
4 | Aderhautmelanom (tumor of the eye), healthy eye tissue and optic nerve must not be irradiated! | E
5 | Chondrosarcoma, tumor on scull base, radioresistant | G
6 | inoperable liver tumor, skin should be spared as far as possible | D
7 | skin cancer, reaching 3 cm deep, critical organ at 5 cm depth | B
# | Treatment
A | 5 MeV electrons
B | 9 MeV electrons
C | Photons
D | Photons
E | 60 MeV protons
F | 115 MeV protons
G | Carbon ions

## Slide 58
Beam delivery
3D scanning:
Tumor divided in voxels
→ Z: energy slice
→ XY: raster scanning
M. Pullia 2018 – Ions for cancer therapy, Workshop Archamps
Additional challenge:
patient movements
→ beam gating
→ on-line imaging?

## Slide 59
Video
S. Rossi The CNAO experience, talk at Archamp Ion Workshop
Medical physicists
CIRT 73.6 GyE
16 fractions IMPT
Medical doctor
-> marks boundaries
-> dose
Procedure

## Slide 60
Ideas for the future – smaller, cheaper, faster
TULIP - TUrning LInac around Patient
LINAC-based:
+ compact
+ fast energy change
+ shorter treatment time

## Slide 61
CABOTO
CArbon BOoster for Therapy in Oncology
Ideas for the future

## Slide 62
Spare slides on PET imaging in hadron therapy
Notes: 62

## Slide 63
p
p
target fragmentation
1H
Fiedler et al., in Ion Beam Therapy, Springer-Verlag Berlin Heidelberg 2012
Notes: 63

## Slide 64
p
p
12C
target fragmentation
1H
projectile fragmentation
12C
Fiedler et al., in Ion Beam Therapy, Springer-Verlag Berlin Heidelberg 2012
Notes: 64

## Slide 65
target fragmentation
projectile fragmentation
1H
12C
Fiedler et al., in Ion Beam Therapy, Springer-Verlag Berlin Heidelberg 2012
Positron
Emission
Tomography
+ therapy control
+ dose verification
biological washout
low intensities
PET scanning in hadron therapy
Notes: 65

## Slide 66
Notes: 66

## Slide 67
e+
11C
11B
Notes: 67

## Slide 68
e-
e+
Notes: 68

## Slide 69
Notes: 69

## Slide 70
P E T
Notes: 70

## Slide 71
12C
Notes: 71

## Slide 72
11C
Notes: 72

## Slide 73
11C aided hadron therapy
11C primary beam
increased β+ activity
maximum at Bragg peak
-> PET imaging for dose
verification
Dose
β+ activity
Dose
β+ activity
R. S. Augusto et al., NIM B376 (2016) 374-378
12C
11C

## Slide 74
Depth in Water [mm]
Relative Dose [%]