## Slide 1: Improved concept of the Nelium Turbo-Brayton cycle for the FCC-hh beam screen cooling
FCC Week 2019, Brussels // 26.06.2019
Technical University Dresden // Bitzer Chair Of Refrigeration, Cryogenics And Compressor Technology
Sofiya Savelyeva, Steffen Klöppel, Christoph Haberstroh, Hans Quack
EASITrain – European Advanced Superconductivity Innovation and Training. This Marie Sklodowska-Curie Action (MSCA) Innovative Training Networks (ITN) has received funding from the European Union’s H2020 Framework Programme under Grant Agreement no. 764879

## Slide 2: Outline
Cycle requirements & former baseline
Limiting factors
Comparison of cycle arrangements
New baseline
Upper heat exchanger design
Natural Nelium mixture

## Slide 3: Baseline cryogenic cycle
Cooling power requirements:
680 kW for beam screens cooling (60 to 40 K)
270 kW for Helium cycle pre-cooling (300 to 40 K)
Key components:
multi-stage centrifugal compressor (~10 MW range)
turbo-expander ~700 kW → power recovery in compressor
Considered Nelium composition: 33 vol. % of neon
Nelium Turbo-Brayton cycle: former baseline cycle layout
Image courtesy: MAN Diesel and Turbo
Image courtesy: SKF

## Slide 4: Limiting factors
1. Turbo-compressor design
Design inputs: first cycle baseline parameters
Design limitations:
maximal impeller diameter,
rotor dynamics,
shaft length, etc.
Currently developed 1-tandem design:
up to 40 vol. % He;
total compressor isentropic efficiency: ~73 %
Chart: Helium content (vol.)
| 0 | 0.4 | 0.4 | 0.6 | 0.6 | 0.75 | 0.75 | 0.9 | 0.9 | 0.98 | 0.98 | 1
 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7
Poster session (25.06.19 15:30):
- M. Podeur, D. Vogt, “Optimisation of a multi-stage turbocompressor architecture operating with a neon-helium gas mixture”;
- M. Podeur, D. Vogt, S. Savelyeva, S. Kloeppel, Ch. Haberstroh, H. Quack, “Test rig for the experimental evaluation of turbo-compressor impeller designs for light gases”
Number of required compressor casings depending on the helium content
(M. Podeur, University of Stuttgart; MAN)

## Slide 5: Limiting factors
Chart: Theoretical relative gas mass compared to a pure helium cycle (excluding the buffer)
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1
Total | 9.1957 | 6.4918 | 4.5504 | 3.0814 | 1.9313 | 1
Neon | 9.1957 | 6.1851 | 4.019 | 2.3748 | 1.0769 | 0
Helium | 0 | 0.30671 | 0.53146 | 0.70658 | 0.8544 | 1
2. System size and gas mass
Chart: Neon mass fraction
| 1 | 0.99 | 0.95 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.30000000000000004 | 0.19999999999999996 | 9.9999999999999978E-2 | 0
 | 0 | 0.048456 | 0.2097 | 0.35904 | 0.55759 | 0.68361 | 0.77069 | 0.83448 | 0.88321 | 0.92165 | 0.95275 | 0.97844 | 1
Chart: Relative heat exchanger sizes
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1
K3 | 2.6426 | 2.1013 | 1.717 | 1.4263 | 1.1956 | 1
Example:
67 vol. % helium - 240 kg of gas
30 vol. % helium - 510 kg of gas

## Slide 6: Compared cycle arrangements
Cycle A (baseline)
Cycle B
Cycle C

## Slide 7: Compared cycle arrangements
 2 inner heat exchangers |  reduced pressure ratio |  reduced pressure ratio
 |  easier pressure control |  higher volumetric flow to the second compressor casing
 |  |  reduced pressure ratio of pre-cooling turbine compared to cycle B
 higher pressure ratio |  additional heat exchanger |  additional heat exchanger
 |  high speed of the pre-cooling turbine (high pressure ratio) | 
Chosen arrangement
Cycle A (baseline)
Cycle B
Cycle C

## Slide 8: Compared cycle arrangements
Chart: Required pressure ratio depending on the gas mixture composition
| 0.7 | 0.6 | 0.5 | 0.4 | 0.30000000000000004
Cycle C | 5.422 | 5.4876 | 5.5681 | 5.6648 | 5.7574
Cycle A | 5.779 | 5.8399 | 5.916 | 6.0192 | 6.136
Cycle C - > new baseline
Advantages:
Reduced pressure ratio
Higher volumetric flow on the inlet of the second casing
Thus, for 40 % helium:
Cicle A:
Cycle C: (var)
Increase helium content up to 60 vol. % He
- 1 compressor impeller → +4..5 % to the total compresor ηs↑
or

## Slide 9: Upper heat exchanger design
Reduction of the heat exchanger cross-section area and the cold box diameter
IHX1
IHX2
New baseline cycle flow diagram

## Slide 10: Cold box size
Upper heat exchanger (IHX1+IHX2):
L x W x H: ~4.7 x 1.3 x 1.2 m
↓
Within maximal industrially possible size: 8 x 1.5 x 3.4 m
Cold box:
Length: 5.6…6 m;
Diameter: 3.6..3.8 m
↓
Transportable
Upper heat exchanger
Cold box cross section
IHX 1 + IHX2 – upper heat exchanger,
IHX3 – inner heat exchanger,
LHX – load heat exchanger

## Slide 11: Improved cycle concept
Chart: Total isentropic power of the compressor depending on the NTU value of the IHX1
| 15 | 16 | 17 | 18 | 20
 | 7552.9691 | 7544.8989 | 7538.5294 | 7539.7851 | 7565.9914
NTU of the upper heat exchanger reduced from 40 to 30;
Optimal NTU of IHX1: 17...18
Case study (under progress): matching the turbo-compressor middle pressure with the cycle parameters
Estimated total power for the chosen case: ~9.7 MW
New baseline cycle flow diagram
Chart: Total isentropic power of the compressor depending on the middle pressure (for NTU1=18)
| 11 | 12 | 13 | 14 | 15 | 16 | 16.440000000000001 | 17 | 18 | 19
 | 8102.4749 | 7888.8128 | 7736.8134 | 7632.587 | 7568.6192 | 7542.5813 | 7539.7851 | 7542.929 | 7570.282 | 7621.3098

## Slide 12: Improved cycle concept
 Possible chillers implementation
Poster session (25.06.19 15:30):
H. Quack, F. Holdener, S. Savelyeva, S. Kloeppel, C. Haberstroh
“Cooling of the refrigerant with chilled water before the inlet of the compressor”
 Preliminary check of the turbines design:
↓
no limitations observed
New baseline cycle flow diagram
 | Power, kW | D, m | N, rpm | Ns
MT | 789 | 0.18 | 23000 | 0.57
PCT | 362 | 0.10 | 54000 | 0.61

## Slide 13: Natural Nelium concept
Corresponds to the neon-helium ratio in the air:
Natural Nelium: 68.8 % Ne, 23.4 % He, 7.8 % H2 (3…8 %)
Economically advantageous
Current target composition: 60 % neon, 40 % helium → cheaper helium can be added
Crude nelium mixture production flow diagram
Hydrogen presence in the mixture: good thermophysical properties
Problem: instability of composition

## Slide 14: Next steps
Case study for the turbo-compressor and cycle parameters matching
Transient operation modes for the improved cycle
Detailed cool-down investigation using the improved cycle
Further study of the Natural Nelium concept

## Slide 15: Thank you for your attention!
EASITrain – European Advanced Superconductivity Innovation and Training. This Marie Sklodowska-Curie Action (MSCA) Innovative Training Networks (ITN) has received funding from the European Union’s H2020 Framework Programme under Grant Agreement no. 764879
Improved concept of the Nelium Turbo-Brayton cycle for the FCC-hh beam screen cooling
S. Savelyeva, S. Klöppel, Ch. Haberstroh, H. Quack