## Slide 1: The SACLA C-band Linac
June 25, 2019, Brussels
Future Circular Collider Conference (FCC week 2019)
Takahiro Inagaki, Takao Asaka, Chikara Kondo, Hirokazu Maesaka,
Takashi Ohshima, Tatsuyuki Sakurai, and Hitoshi Tanaka
RIKEN SPring-8 center
JASRI / SPring-8
RIKEN SPring-8 Center

## Slide 2: Outline
Introduction
  X-ray free electron laser SACLA
  C-band main accelerator
Component design and performance
  Acceleration structure
  RF pulse compressor
  Klystron & pulse modulator
  Timing and low-level RF system
Operational status at SACLA
  History and statistics
  Accelerating gradient
  Fault rate
Consideration of FCC-ee injector
Summary

## Slide 3: World’s leading photon source facilities in Japan
SPring-8 (1997~)
8 GeV storage ring
56 hard-X & soft-X beamlines
SACLA (2011~)
X-ray free electron laser
New SUBARU (1998~)
1.5 GeV storage ring
owned by Univ. of Hyogo pref.
700 m
Beam injection from SACLA (2018~, commissioning)
1 km ring
Low emittance ring
SPring-8-II (202X~)

## Slide 4: X-ray free electron laser SACLA
Short facility size (700 m)
  Low emittance (< 1 mm mrad) E-gun
  High peak current (> 10 kA) by 3 BCs
  High gradient (35 MV/m) C-band structure
  Short period (18 mm) in-vacuum undulator
Stable XFEL generation
  CeB6 thermionic cathode E-gun
  Stable (V/V < 10ppm) klystron modulator
  Stable (t < 100 fs) Low-level RF system
Parameter | BL3, BL2 | BL1
Beam energy | 6 – 8 GeV | ~ 0.8 GeV
Bunch length | ~ 10 fs | < 1ps
Peak current | > 10 kA | 300 A
Photon energy | 4 - 20 keV | 20~150 eV
Pulse energy | > 500 J | ~ 100 J
Pulse rep. rate | 60 pps | 60 pps
~ 0.8 GeV
~ 10 keV XFEL
~ 100 eV Soft-X, FEL
4 ~ 8 GeV
8 GeV
1.3 GeV
0.4 GeV
40 MeV
500 kV
E-gun
C-band
Undulator

## Slide 5: Why we use C-band ?
High accelerating gradient
  High accel. gradient 35-42 MV/m
  Copper surface field ~ 100 MV/m
  Achievable with present technology
Practical cavity size & accuracy
  Beam aperture >12 mm
  Alignment accuracy ~ 0.1 mm
  Wakefield effect is acceptable.
Normal conducting RF
  No cryogenic system.
  Repetition rate (60 pps) is suitable for experiments (CCD frame rate).
Components are available
  Initially developed at KEK for the linear collider project in 1990s.
C-band accelerator in tunnel
f=5.712 GHz
Klystron gallery

## Slide 6: C-band (5.712 GHz) RF system
Klystron HV
-330 kV
Klystron beam
290 A
2.5s
Klystron output
40 MW
Pulse compressed
160 MW
4.5s
Typical waveform
Key features
High RF field
  Accel. structure
  Pulse comp.
Stability
(100ppm, 0.2 deg.)
  Klystron
  Modulator
  Low-level RF
T. Inagaki, PR-AB 17 080702 (2014)

## Slide 7: Outline
Introduction
  X-ray free electron laser SACLA
  C-band main accelerator
Component design and performance
  Acceleration structure
  RF pulse compressor
  Klystron & pulse modulator
  Timing and low-level RF system
Operational status at SACLA
  History and statistics
  Accelerating gradient
  Fault rate
Consideration of FCC-ee injector
Summary

## Slide 8: Acceleration structure
 | Choke-mode | High gradient
Structure type | Quasi-CG | Quasi-CG
RF mode | TM01 - 3/4 | TM01 - 2/3
Accelerator length | 1.79 m | 1.77 m
Iris aperture (2a) | 13.6 ~ 17.3 mm | 12.1 ~ 15.9 mm
Atten. param () | 0.53 | 0.54
Filling time | 300 ns | 270 ns
Quality factor | 10.300 | 8,900
Shunt impedance | 54 M/m | 64 M/m
Accel. gradient | 35-39 MV/m | 42 MV/m
Choke filter
SiC
absorber
Disk
Ellipsoidal shape
Two types of traveling wave structure
8GeV linac (2011-): Choke-mode-type, 128 tubes
potential of multi-bunch (~30) operation
but….no practical operation of multi-bunch mode
800MeV linac (2014-): High gradient type, 10 tubes
mitigate surface field for higher gradient, low cost
Choke-mode type structure
T. Inagaki, PR-AB 17 080702 (2014)
High gradient type structure
T. Sakurai, PR-AB 20 042003 (2017)
Curvature ratio
Electric field ratio
10% reduction

## Slide 9: Fabrication of the structure
Copper
  Oxigen free copper (OFC), class-1
  hot iso-static pressing (HIP)
Machining
  High precision lathe, without lubricant oil
  No electrochemical polishing, no rinsing
Assembly
  Assembly in the clean room
  RF measurement to check the cavity
  Vacuum brazing with silver solder
Inspection
  RF characteristics (reflection, attenuation, …)
  Physical dimension, straightness
  Vacuum leak check
  Out gas measurement
Shipping
Machining
Assembly
Brazing
Straightness
measurement

## Slide 10: Quality of the acceleration structure for SACLA
Frequency
57120.2 MHz
Phase error
< 1 degree
Quality factor >10,000
Straightness <0.2 mm
Finally adjusted by water temperature
During the mass-production, MHI modified the cavity design and brazing process.
Finally they produced 128 structures with excellent quality

## Slide 11: RF pulse compressor (SLED)
3dB coupler
Mode converter
WG  cylinder
Cavity RF mode | TE0,1,15
Q0 | 185 k
 | 9 ~ 9.5
VSWR | <1.05
Tuner
Diaphram structure
differential screw
Compress RF pulse 2.5 s  0.5 s
Multiply peak RF power 40 MW  160 MW (average of 300 ns filling time)
SLED type: pair of high-Q (TE mode) cavity + 3dB coupler
Frequency tuning
  Precise tuner 500 kHz/turn
  Temperature controlled by cooling water
RF monitor
(dir. coupler)

## Slide 12: Klystron & modulator
50 MW pulse klystron (Canon E37212)
  Power efficiency ~ 43%, gain ~ 53dB
Pulse modulator
  -370 kV, 330 A, 5 s pulse in 60 pps.
  Pulse Forming Network (PFN) type
  Thyratron switch (jitter < 1ns)
  Insulation-oil filled, for high reliability
  Steel tank for perfect noise shielding
Ultra-precise HV charger
  Combination of two inverter modules
  Main charger (35 kW) charged to 99.9%.
  Sub charger (1 kW) precisely regulate capacitor voltage to the target value.
 | Stability (rms)
PFN capacitor volt. | 7 ppm
Klystron cathode volt. | 24 ppm
Klystron RF amplitude | 92 ppm
Klystron RF phase | 0.03 degree
Klystron
Modulator
HV charger

## Slide 13: Timing and low-level RF system
Timing distribution (RF & trigger)
  Phase-stabilized optical fiber
  Water cooled duct.
  Fiber length feedback control
  using Michelson interferometry method.
Low-level RF system
  IQ-modulator & IQ-demodulator
  VME 16-bit, 238 MHz DAC & ADC
  VME Time delay unit
  Low-noise DC power supply
  Series regulator (no switching noise)
  Large noise filter at DC line.
  Water cooled cabinet
  Temperature stabilized within ~0.1 K.
Y. Otake, PR-AB 19 022001 (2016)
T. Ohshima, NIMA 820, 65-74 (2016)
Optical fiber & duct
Low level RF
Water cooled
cabinet
Driver amplifier
Measured stability
requirement

## Slide 14: Outline
Introduction
  X-ray free electron laser SACLA
  C-band main accelerator
Component design and performance
  Acceleration structure
  RF pulse compressor
  Klystron & pulse modulator
  Timing and low-level RF system
Operational status at SACLA
  History and statistics
  Accelerating gradient
  Fault rate
Consideration of FCC-ee injector
Summary

## Slide 15: Operation status of SACLA
History
2011 Commissioning, first lasing.
2012 BL3 user experiments.
2015 BL1 commissioning.
2017 BL2 & BL3 multi-beamline operation.
2018 SPring-8 beam injection.
Statistics (FY 2018) | BL2 and BL3 Hard-X FEL | BL1 EUV FEL
Accel. operation | 6,281 hours | 
User experiments | 5,046 hours | 1,224 hours
Laser availability | 97% | 94%
MTBF | 56 hours | 190 hours
BL2 7.0 keV, 30 Hz
BL3 9.4 keV, 30 Hz

## Slide 16: Acceleration gradient of C-band accelerator
 | Beam energy | RF units | Structure type | Accel. gradient
8GeV linac | 6 ~ 8.5 GeV | 64 | Choke-mode-type | 35~39 MV/m
800MeV linac | 250 ~ 800 MeV | 8 | High-gradient-type | ~ 42 MV/m
Operational gradient for SACLA 8 GeV linac
Beam energy measurement
at SACLA 800MeV linac
147 MV / 3.5 m = 42 MV/m

## Slide 17: Fault rate of C-band accelerator (Jan~Apr. 2019)
Average
0.67 times /day
RF arcing (45%)
Klystron HV arcing (13%)
Thyratron pre-trigger (42%)
 | 8 GeV linac | 800 MeV linac
Average fault rate per unit | 0.67 times/day | 1.32 times/day
Fault rate of accelerator | 1.8 times/hour | 0.27 times/hour
Mean time before failure (MTBF) | 30~60 minutes | 3 hours
8 GeV linac 64 units, ~35 MV/m
800 MeV linac
5 units, ~42 MV/m
Average
1.32 times /day

## Slide 18: Outline
Introduction
  X-ray free electron laser SACLA
  C-band main accelerator
Component design and performance
  Acceleration structure
  RF pulse compressor
  Klystron & pulse modulator
  Timing and low-level RF system
Operational status at SACLA
  History and statistics
  Accelerating gradient
  Fault rate
Consideration of FCC-ee injector
Summary

## Slide 19: Consideration of FCC-ee injector
Acceleration gradient ~35 MV/m
  14 GeV / 35 MV/m = 400 m
Repetition rate: 200 Hz
  We tested up to 120 Hz.
  Klystron, modulator cooling capacity.
  Fault rate should be considered.
2 bunch operation is not tested at SACLA.
Hardware cost ~ 2M-Euro /1unit (125 MeV)
without building, infrastructure, and cabling
(from SACLA construction in 2006-2010.)
Copied from “S. Ogur, et. al.,
Proc. of eeFACT2018”

## Slide 20: Summary
In SACLA, the C-band RF system constantly operate with 35-42 MV/m in 60 pps repetition rate.
The fault rate (MTBF 30~60 min.) is acceptable level of the operation.
XFEL requires high RF stability (100 ppm, 0.2 degree for C-band RF).
We achieved the required stability based on….
  Precise HV charging of klystron modulator
  Precise timing distribution system and low-level RF system.
C-band RF system has been well established at SACLA.
Recently C-band RF system was also adopted as an injector linac of a new 3 GeV light source in Japan-Tohoku (2019-2023).
We hope to be widely used C-band RF system for new accelerator facilities.

## Slide 21: Backup slides

## Slide 22: Beam energy vs. fault rate
User run 2014-2015, 30 pps
Frequent operation at 10 keV
7.8 GeV (35 MV/m), K=2.1

## Slide 23: Beam arrival time stability
Measured by a cavity-BPM at the end of undulator.
The measured value includes the instability of the BPM system and the master timing distribution system.
Jitter
=82 fs
of 4.8 GHz
Drift
< 580 fs
of 4.8 GHz
From
Y. Otake, PR-AB 19 022001 (2016)

## Slide 24: Multi-XFEL beamline operation
High quality & stable electron beam
  300 pC, >10 kA, 10 fs, several mm*mrad
  Energy stability E/E ~ 10-4
Precise kicker magnet
  Switching 300 A with 10 ppm stability
New dog-leg optics
  Pair of double-bend achromat cancels CSR induced horizontal kick
Independent control of electron beam
  Pulse-by-pulse control of C-band RF
    RF phase and trigger timing
  Different energy and bunch profile
Kicker magnet
T.Hara, PR-AB 21 040701 (2018)
C. Kondo, RSI 89, 064704 (2018)
Kicker pulsar

## Slide 25: 50 MW pulse klystron
Solenoid focus high power klystron
Suppliers (compatible)
  Canon Electron Tube & Device
  Mitsubishi Electric
Operating C-band klystrons: 71
Replaced since 2011: 11
Klystron gallery at SACLA
Number of replaced klystrons
 | Nominal operation
Output RF power | 50 MW
Power efficiency | 43%
Gain | 53 dB
Cathode voltage | -370 kV
Beam current | 330 A
RF pulse width | 2.5 s
Pulse repetition | 60 pps