## Slide 2
Energy deposition in the Betatron Cleaning Insertion of HE-LHC machine
M. Varasteh and F. Cerutti
Tracking input from BE-ABP:
M. Crouch, J. Molson, R. Bruce, A. Mereghetti
Acknowledgments: C. Bahamonde, M.I. Besana, E. Skordis, other colleagues in BMI & FLU
FUTURE CIRCULAR COLLIDER CONFERENCE 2019
Brussels, Belgium

## Slide 3
M. Varasteh
Outline
Challenges for the HE-LHC collimation system
Power density on the collimators and warm magnets
Energy deposition in the cold section, IR7
Impact of the dog-leg removal

## Slide 4
As the first stage, the same collimation design as LHC machine is used
Vertical halo scenario was studied
Considering high loss scenario of 0.2h beam life time (BLT)
 | unit | FCC-hh | HE-LHC | HL-LHC | LHC
center-of-mass energy | TeV | 100 | 27 | 14 | 14
arc dipole field | T | 16 | 16 | 8.33 | 8.33
bunch population [1011] | ppb | 1 | 2.2 | 2.2 | 1.15
number of bunches |  | 10600 | 2808 | 2760 | 2808
stored beam energy | GJ | 8.4 | 1.4 | 0.7 | 0.36
total power loss for 12 min BLT | MW | 11.8 | 1.9 | 0.95 | 0.5
Main challenge is due to the restrictions caused by the geometry of the existing Tunnel
M. Varasteh
25/06/2019
FCC Conference 2019 - BRUSSELS, BELGIUM
4
Parameters / challenges

## Slide 5
8 warm dipoles (MBW)
24 warm quadrupoles (MQW)
Beam-Beam separation (bbs):
  204 mm in the arc
  (194 mm for LHC)
  224 mm within the doglegs
  (same as LHC)
3 Passive absorbers (TCAP)
(1 m, 20 cm, 60 cm)
 | HE-LHC | LHC | Comments
MBW | 3.4 m | 3.4 m | different return coils
MQW | 3.5 m | 3.1 m | different length
Collimators |  |  | the same
MQTLH/I | 1.3 m | 1.3 m | different bbs, beam screen, material
MCBCH/V | 0.9 m | 0.9 m | different bbs, beam screen, material
MQ7 | 3.5 m | 3.1 m | different length, material
MBWs
TCPs
TCAP
TCSG
MQWs
MQTLs
MCBC
MQ7
TCLA
MCBW
M. Varasteh
HE-LHC IR7, warm section
about 30 m longer w.r.t. LHC
Collimators | Length (cm) | Aperture (σ) | Material | Number
Primary | 60 | 6.7 | CFC | 3
Secondary | 100 | 9.1 | CFC | 11
Active absorbers | 100 | 11.5 | tungsten | 5

## Slide 6
x-y-z resolution: 0.2cm, 1cm, and 5cm
Horizontal;
Skew;
M. Varasteh
Horizontal and Skew primary collimators
most loaded primary collimator
Total power (kW) | 
Vertical | 3.7
Horizontal | 29.5
Skew | 53.1

## Slide 7
the maximum is on the metallic support! New design with thicker jaws is mandatory…
x-y-z resolution: 0.2cm, 1cm, and 10cm
Total power (kW) | 
Secondary Collimators | 
TCSG.A6L | 56.1
TCSG.B5L | 12.6
TCSG.A5L | 37.3
TCSG.D4L | 6.9
TCSG.B4L | 3.7
TCSG.A4L | 4.9
TCSG.A4R | 5.3
TCSG.B5R | 0.5
TCSG.D5R | 1.2
TCSG.E5R | 1.9
TCSG.6R | 0.2
For LHC at 6.5TeV, the max load is about 15 kW
most loaded secondary collimator (1st TCSG)
M. Varasteh
Secondary collimators
jaw

## Slide 8
X (cm)
Y (cm)
Magnetic field (T)
(MBW)
X (cm)
Y (cm)
Magnetic field (T)
(MQW)
HE-LHC
LHC
M. Varasteh
Warm dipole’s return coil (MBW)
Magnetic field map in FLUKA simulation

## Slide 9
Maximum power per unit length  55 kW/m
(bulk is below 14 kW/m)
Total power (kW) over warm dipoles | 
MBW.B6L | 66.36
MBW.A6L | 53.57
M. Varasteh
Warm dipoles
Two MBWs downstream the TCPs take more than 99% of the total power on the warm dipoles!
at LHC the maximum is about 22 kW

## Slide 10
moving away from the beam pipe, a factor of 10 less dose on the return coil…
**considering 1e16 proton lost per year**
0.25cm, 0.25cm, 5cm (x-y-z resolution)
Dose along the coil (per year)
In total, the coil insulator can stand about 30 MGy
MBW.B6L’s front face
M. Varasteh
Coils in the most loaded warm dipole

## Slide 11
Total power (kW) | 
MQWVF5L | 95.1
MQWVE5L | 39.0
MQWVD5L | 31.1
MQWVC5L | 26.8
MQWVB5L | 23.5
MQWVA5L | 21.1
≈ 4 MGy
On the coils
Material dose limits is 50 MGy for the coils and 10 MGy for the spacers!
*At LHC, internal shield is used
M. Varasteh
Warm quadrupoles (MQWs)

## Slide 12
Chart: 
| TCP & TCS jaws | MBW | MQW | TCAP | Beam pipe | Tunnel | Other elements | Missing energy | AIR | Cables
 | 0.1168 | 0.065 | 0.2 | 0.118 | 0.092 | 0.3045 | 0.0858 | 0.02 | 0.005 | 0.018
Chart: 
| TCP & TCS jaws | MBW | MQW | TCAP | Beam pipe | Tunnel | Other elements | Missing energy | AIR | Cables
 | 0.1 | 0.085 | 0.095 | 0.13 | 0.086 | 0.331 | 0.094 | 0.065 | 0.005 | 0.009
HE-LHC @ 13.5 TeV
LHC @ 7 TeV
M. Varasteh
Power fraction on different elements at IR7

## Slide 13
Values are for the 12 min BLT !
With two collimators (TCLDs) in the cold section, before MQ8 and MQ10, the maximum peak power density is about 5 mW/cc
Beam1
r-φ-z resolution: 1.86cm, 2⁰, 10cm
(three radial bins of 1.86cm)
M. Varasteh
Cold section

## Slide 14
204mm bbs
(no dogleg) 
224mm bbs
(nominal dogleg) 
244mm bbs
(larger dogleg) 
Dump plane
M. Varasteh
Impact of the dogleg removal - I

## Slide 15
NEUTRONs (nominal dogleg)
NEUTRONs (no dogleg)
1 Proton
7 Photon
8 Neutron
9 ANeutron
13 Pion+
14 Pion-
M. Varasteh
Impact of the dogleg removal - II

## Slide 16
Total power (W) |  | 
beam separation in warm section | MQ7 | MBA8
204mm (no dogleg) | 7.1 | 419.3
224mm (nominal) | 5.9 | 12.7
244mm (larger dogleg) | 4.8 | 12.1
(r-φ-z resolution: 1.86cm, 2⁰, 10cm)
M. Varasteh
Impact of the dogleg removal - III
If no dogleg:
First cold dipole (MB.A8R7)
*
 | w/o dogleg | dogleg
PHOTON | 4E-3 | 4E-5
NEUTRON | 3E-4 | -
(per proton lost)

## Slide 17
  The maximum power collected by a collimator is below 60 kW (for 0.2h BLT)
  For the first TCSG, the max power density is NOT on the Jaw! A new design would address the issue…
  Thanks to the TCLD collimators, Energy deposition in the cold section is NOT hazardous
  No apparent showstopper was seen
  Dogleg removal results in a dramatically higher impact of the neutral particles in the first cold dipole
M. Varasteh
Messages from FLUKA simulation of HE-LHC machine

## Slide 18
Mohammad Varasteh
CERN / EN-STI-BMI
m.varasteh cern.ch

## Slide 19
Backup Slides

## Slide 20
M. Varasteh
NEUTRONs
PHOTONs
PROTONs
PIONs

## Slide 21
ELEMENTS | HE-LHC | LHC
TCP & TCS jaws | 11.7% | 10%
MBW | 6.5% | 8.5%
MQW | 20.0% | 9.5%
TCAP | 11.8% | 13%
Beam pipe | 9.2% | 8.6%
Tunnel | 30.5% | 33.1%
Other elements | 8.6% | 9.4%
Missing energy | 2.0% | 6.5%
AIR | 0.5% | 0.5%
Cables | 1.8% | 0.9%
Active absorbers | Total power (kW)
TCLA.A6R (CLAA6R1i & j) | 3.0
TCLA.B6R (CLAB6R1i & j) | 0.3
TCLA.C6R (CLAC6R1i & j) | 0.1
TCLA.D6R (CLAD6R1i & j) | 0.1
TCLA.A7R (CLAD6R1i & j) | 0.03
Passive absorbers | 
TCAPA.6L (CAPA6L1) | 59.8
TCAPB.6L (CAPB6L1) | 8.0
TCAPC.6L (CAPC6L1) | 150.3
MAX !
In front of most exposed MQW
M. Varasteh
 | w/o dogleg | dogleg
PHOTON | 48088 | 1085
NEUTRON | 3187 | -
MBA8