## Slide 2: Update on R2E and Heat Load Simulations
J. R. Hunt, F. Cerutti, A. Infantino:
EN/STI-BMI and the Infrastructure and Operations Working Group
FCC Week 2019
Thursday, 27th June

## Slide 3: Contents
Introduction
Simulation & Updates
Power load on beam screen and magnets
Radiation levels on electronics
Conclusions

## Slide 4: Introduction
FCC-hh arc cell beam-gas interaction
  Impact of secondary showers on magnets and electronics.
Beam lifetime, , considering losses due to nuclear scattering with residual gas:
  Where:
  nuclear scattering cross section (86.4 mb),
  molecular gas density
  -> Gives ng = 1×1015 atoms/m3
Update on previous work carried out by A. Infantino
  FCC week 2017: “FLUKA Montecarlo modelling of the FCC arc cell: radiation environment and energy deposition due to beam-gas interactions”
  FCC week 2018: “Radiation environment assessment in the FCChh and FCCee machines”

## Slide 5
xAxis = 0.1zAxis
z
x
FLUKA Model
x
y
z
FCC-hh arc FODO cell
Lattice based on latest optics, MAD-X TWISS file (R. Martin)
214 m in length
Top View
MB1
MB2
MB3
MB4
MB5
MB6
MB7
MB8
MB9
MB10
MB11
MB12
MB x 6 x 2
L = 14.2 m
  θ = 1.3 mrad
MQ1
MQ1
MQ x 2
L = 6.4 m
Simulation Parameters:
  >200,000 primaries per beam
  Boundary condition
  CPU Time ~120 – 130 seconds per primary

## Slide 6
Dipole
Dipole
No active pumping in interconnect leads to spike in residual gas density here
Gas Profile
Average gas density unchanged (1e9 atoms/cm3)
Shorter photon absorber (previously absorbing ~x2 more power than now which led to higher outgassing.)
Optimised interconnect region geometry, increasing the conductance of the region.
Old
New
Beam Screen
New scheme for dealing with synchrotron radiation effects
Better vacuum quality and lower electron cloud density
I. Bellafont: “Study on the beam induced vacuum effects in the FCC-hh beam vacuum chamber”, this conference, Wednesday, 8:30 am
Updates
Perforated baffle, enlarged
(periodic)
Cooling channel
Primary
chamber
Sawtooth surface
Secondary chamber

## Slide 7: Lattice Element Updates
RCoil = 8.1 cm
RCM = 45 cm
RCM = 37 cm
RCoil = 8.1 cm
 |  | Previous Radius [cm] | Updated Radius [cm]
MB | Cold mass | 45 | 37
MQ | Cold mass | 32.37 | 24.87
MB | Coil | 8.1 | 8.1
MQ | Coil | 5.672 | 5.922
Additional increase in beam – beam separation: 20 -> 25 cm

## Slide 8
Energy Deposition on Coils
Power density: steady state losses
(as opposed to transient losses)

## Slide 9
Energy Deposition on Coils
Centre of ring
Beam
Power density [mW cm-3]

## Slide 10
Secondary Trajectories
xAxis = 0.1*zAxis
MB1
MB2
xAxis = 0.01*zAxis
MB1
MB2
Top View
xAxis = 0.01*zAxis
MB1
MB2

## Slide 11
Secondary Trajectories
Neutral particles
xAxis = 0.01*zAxis
MB1
MB2

## Slide 12
Secondary Trajectories
Split into inner- and outer- ring scoring
xAxis = 0.01*zAxis
MB1
MB2
Positive x towards outside of ring
x

## Slide 13
Secondary Trajectories
D1
D2
D3
D4
D5
D6
Q1
beam
Periodic lattice
Periodic lattice

## Slide 14
Secondary Trajectories
Q1
beam
D6
D7
D8
D5
Periodic lattice

## Slide 15
Secondary Trajectories
beam
D5
D7
D8
Q1
D6

## Slide 16: Energy deposition on coils
D1
D2
D3
D4
D5
D6
Q1
Comparison with previous study
beam

## Slide 17: Energy deposition on coils
D1
D2
D3
D4
D5
D6
Q1
beam

## Slide 18: Energy deposition on coils
D1
D2
D3
D4
D5
D6
Q1
beam
Peak power density
in coils:
1.6 mW/cm3
Corresponding to a dose of: 4.1 MGy y-1
Pessimistic gas density, 200x density achieved currently in LHC
Notes: power = 1.64 # mW/cm^3
density = 7.954 #g/cm^3
densityKg = density/1000
timeScale = 1e7 # seconds
dose = power/densityKg * timeScale
print dose/1e6, "MGy y-1"

## Slide 19: Power Per Element (Cold Mass)
Updated design of beam screen provides less shielding for coils and cold mass:
  Each beam screen now absorbing ~5% of power loss density as opposed to 16% previously.
  86% absorbed by cold mass, 73% previously.
Average losses along arc cell: 414 mW/m (2 beams)
Maximum heat load on most impacted dipole is 476 mW/m on cold mass (2 beams)
Two Beams Power per Element [W]
Beam 1
Beam 2
Element | Beam Screen | Cold Mass
MB1 | 0.140 | 5.52
MB2 | 0.212 | 6.51
MB3 | 0.164 | 5.84
MB4 | 0.162 | 5.87
MB5 | 0.161 | 6.76
MB6 | 0.160 | 5.67
MQ1 | 0.113 | 2.13
MB7 | 0.131 | 5.28
MB8 | 0.211 | 6.41
MB9 | 0.160 | 5.68
MB10 | 0.159 | 5.71
MB11 | 0.157 | 6.57
MB12 | 0.156 | 5.36
MQ1 | 0.121 | 2.14
(Current per beam: 0.5 A)

## Slide 20: Radiation to Electronics
Scoring mesh in location of power converters/electronics
  Direct comparison with previous results
Normalised to 107 s
  ~1 year beam operation
Total ionizing dose
  Cumulative effects, long-term radiation damage
High-energy hadron fluence (HEH):
  proportional to number of single event upsets (SEUs)

## Slide 21
Dose on Electronics
Q1
beam
D7
D5
D9
D6
D8
158 Gy yr-1
Maximum:
341 Gy yr-1
Maximum:
244 Gy yr-1
Dose mostly photons & electrons, easily blocked by cold mass

## Slide 22: Longitudinal Plots Dose
Average Dose [Gy y-1]
Beam
MB
MQ
MB
MB
MB
Beam
For R2E it is important to consider 2 simultaneous beams

## Slide 23
Dose on Electronics:
Combined Beams
Q1
beam
D7
D5
D6
D8
Maximum:
400 Gy yr-1
beam
Based on pessimistic gas density, 200x lower density achieved currently in LHC

## Slide 24
R2E impact - HEH
Q1
beam
D7
D5
D9
D6
D8
Neutron dominated
Some increase due to reduced radius of cold mass in dipoles and quadrupoles

## Slide 25
R2E impact - HEH
Q1
beam
D7
D5
D6
D8
beam
Again, based on pessimistic gas density, 200x density achieved currently in LHC

## Slide 26: Summary
New beam screen design has impacted energy deposition on coils and cold mass
  Now only 5% on beam screen with 86% on cold mass
  Higher peak power density 1.6 mW/cm3 on coils
R2E outcome: an increase in radiation to electronics under beamline
  Maximum dose: 400 Gy yr-1
  Maximum high energy hadron fluence: 1.2e11 cm-2 yr-1
  However, the gas density used ~200x greater than achieved currently in the LHC

## Slide 27: Thanks for listening james.hunt@cern.ch
Special thanks to
I. Bellafont