## Slide 1: Alternatives
D. Schulte

## Slide 2: Injector Complex Layout in CDR
The same complex is used for electrons and positron
The current baseline has important changes compared to the CDR to consolidate the design
See today’s presentations

## Slide 3: Simplified Current Concept
Rational
  Chose damping ring energy (E1 = 1.54 GeV)
  Chose injection energy into pre-booster (E3 = 6 GeV)
  Then define energy at target (E2 = E3 – E1 = 4.46 GeV)
+1.54 GeV
+1.54 GeV
+2.92 GeV
PL1
PL2
CL
E1 = 1.54 GeV
E2 = 4.46 GeV
E3 = 6 GeV
E1 = 1.54 GeV

## Slide 4: CDR Specifications
Current [1011 s-1] | 69 | 28 | 8.9 | 0.6
Max current [1011 s-1] | 85 | 38 | 19 | 14
In CLIC each main linac 915 x 1011 s-1 ( 50 Hz)

## Slide 5: New Parameters

## Slide 6: Alternatives
A number of alternatives can be considered for the injector complex
To make complex more robust
Reduce cost
Some example options are:
Inject directly into booster
Consider using bunch trains
Consider doubling the number of bunches for electrons
…

## Slide 7: Example: Electron Filling
For electrons, can reach beam emittances with gun
  Hence just pass through the linacs
Need power for more bunches in PL 2 and CL
  RF must be dimensioned for 2-3 times the electron pulse charge
Electron filling time could be (much) shorter than positron filling time
  Provided we upgrade PL 1
CL
PL 1
PL 2
1.54 GeV
1.54 GeV
2.92 GeV
Positron mode
Electron mode
Alt. mode

## Slide 8: Generic Layout
Break into functional pieces
Leave parameters flexible
  Baseline choice right now is to have no HEL1
  HEL2 is considered as alternative
Other configurations can be envisaged
  But would lead to far today
E0
e-gun
E1
E2+E1
E1
E5
D=E1
D=E2-E1
D=E1
D=E3-E2-E1
D=E4-E3
D=E5-E4
E2
e+prod
E3
E4
PL 1
PL 2
CL
HEL 1
HEL 2
PBR synch
FEB synch
e+ damping ring

## Slide 9: RF Design
In current baseline all RF is S-band
  Except for HEL2, which is C-band
But need actual RF design of each linac
  RF structures, pulse compressors etc.
Each linac has its own requirements
  Emittances
    CL needs to transport large emittance beam from target
    PL2 only sees small emittance beams
  Currents
    PL2 has a higher current during positron production
      Electron and positron beam
    Similar for CL
      Positron beam from target and positron beam toward collider
  Might want to consider RF frequency choices
E0
e-gun
E1
E2+E1
E1
E5
D=E1
D=E2-E1
D=E1
D=E3-E2-E1
D=E4-E3
D=E5-E4
E2
e+prod
E3
E4
PL 1
PL 2
CL
HEL 1
HEL 2
PBR synch
FEB synch
e+ damping ring

## Slide 10: Energy Choices
What are the best choices of the different energies?
  Need to understand each system well enough to be able to properly perform the trade-off
    E.g. what is the best RF frequency and gradient in each system?
    E.g. E4 depends on the final booster and on the high-energy linac
  Efficiency of positron production depends on E2
  With the baseline scheme currents in different linacs are different
Note other configurations could also be considered, e.g. to have a CL dedicated to the positrons after production only
E0
e-gun
E1
E2+E1
E1
E5
D=E1
D=E2-E1
D=E1
D=E3-E2-E1
D=E4-E3
D=E5-E4
E2
e+prod
E3
E4
PL 1
PL 2
CL
HEL 1
HEL 2
PBR synch
FEB synch
e+ damping ring

## Slide 11: Top-up Flexibility
Do we need to control the charge of the circulating collider bunches?
  I would guess, yes.
  Non-colliding bunches need to be treated differently
  Bunches might lose particles at different rates
  Different schemes could be envisaged
    Control of top-up bunch charge, e.g. at gun level
    Sparing given bunches from top-up for one round
    Both will produce additional constraints
How flexible do we need to be with the filling pattern?
How do we transfer?
  All bunches in one go?
  Otherwise, how do we deal with the current small difference in booster and collider circumference?

## Slide 12: Bunch Trains
Accelerating bunch trains allow to increase the RF-to-beam efficiency
typically requires increase of RF energy per pulse
but one accelerate much more charge per pulse
This allows a faster filling of the pre-booster or booster
Likely can reduce 50 ns spacing in linacs
certainly by damping the structures but maybe even without
Could aim for 15 to 20 ns bunch spacing to produce (pre-) booster patter right away
Number of bunches per pulse depends on RF frequency and trade-off with pulse compressor
Typically can expect O(10) bunches per pulse
Can also use bunch trains to reduce the charge per bunch
roughly the same charge per pulse (slight increase required)
this allows smaller aperture structures (higher frequency or smaller a/lambda), which can be more efficient and can reach higher gradients
could consider more bunches in booster than in collider and do more than one round of top-up

## Slide 13: How to Move Forward?
Develop an optimized injector layout (linacs, rings, energies, etc.)
  Matching the performance requirements of FCC-ee at all working points
  ~40 to ~200 GeV injection energy into collider in top-up mode.
  Provision of some flexibility for filling patterns (e.g. lifetime of individual bunches)
  Fast-filling will be most critical requirement for current
  Most stringent requirements in patterns/intensity/flux at Z (45 GeV).
Form a collaboration for this purpose

## Slide 14: FCC-ee Injector Workpackages
E0
e-gun
E1
E2+E1
E1
E5
D=E1
D=E2-E1
D=E1
D=E3-E2-E1
D=E4-E3
D=E5-E4
E2
e+prod
E3
E4
PL 1
PL 2
CL
HEL 1
HEL 2
PBR synch
FEB synch
e+ damping ring
WP0: Electron Gun and injector
WP1: Production Linac (PL1 to E1, PL2 to E2)
PL1: 2 electron bunches or 2 production bunches acceleration to E1
PL2: 2 electron bunches or 2 production bunches & 2 positron bunches (energy gain E2-E1 )
WP2: Positron production (E2)
Target design, - capture optimisation
Energy choice (E2), production bunch intensity versus production energy, etc.
WP3: Positron Capture Linac (CL, E1)
Pre acceleration of 2 positron bunches (before DR) and acceleration (after DR) of 2 e+ bunches (energy gain E1 per passage)
Acceleration of 2 electron bunches (energy gain E1)
WP4: Damping Ring (E1)
Choice of E1
Impedance, space charge, e+ emittances, etc.
WP5: High Energy Linacs (HEL1+2, acceleration from (E1+E2) to E3 or E4)
Choice of end energy kept flexible at the moment,
Optimisation with Full Energy Booster (FEB) or Pre-Booster Ring (PBR) design at later stage
WP6: Pre-Booster Ring (PBR)
Either SPS or new ring
Impact of injection energy E3
Full ring design
WP7: Full-Energy Booster (FEB)
Impact of injection energy E4
Full ring design
WP8: Beam transfer system design
Transfer line design (from High Energy Linac onwards)
Injection and extraction concepts, linked to ring designs
HW concepts

## Slide 15: FCC-ee Injector Collaboration
Proposed starting point is consolidation and analysis of present baseline scheme that matches exactly the bunch number and fill pattern requirements that came out of the collider luminosity optimization.
Should be good starting point for investigations of alternative designs and future optimization.
Current design provides 1 or 2 bunches per RF pulse for the collider, assembled in trains either in a pre-booster or full-energy booster, with a maximum charge of 2E10 particles per bunch.
Additional e- bunches (production bunches) are used to produce the e+ bunches of identical intensity. Presently the bunch pair distance is 60 ns.
The baseline design assumes S-band linac structures throughout.

## Slide 16: Next Steps
Assumption that general understanding is met with potential partners.
Development of brief descriptions of activities for each work package for first phase, i.e. review and optimisation of baseline: PBR vs HE linac (E3 and/or E4), e+ production energy, etc.
Design goals, key parameters, interfaces, time lines
Resources estimates.
Further common discussion of programme

## Slide 17: First Proposals Already Appeared
H. Braun
Yesterday
Recirculating linac from LHeC/FCC-eh
O. Brüning

## Slide 18: Reserve

## Slide 19: Positron Filling
Linac after the target should have large aperture for capture efficiency
In CLIC can tolerate production of 18 x 1011 positrons per pulse
Could consider splitting charge in several bunches with short spacing
Reasoning for 60 ns spacing in CDR not clear
  CDR refers to longitudinal wakes
  Referred paper mentions transverse wakes
  No damping used in accelerator, so no fundamental limit
1.54 GeV
1.54 GeV
2.92 GeV

## Slide 20: Positron Filling
Linac after the target should have large aperture for capture efficiency
In CLIC can tolerate production of 18 x 1011 positrons per pulse
Could consider splitting charge in several bunches with short spacing
Reasoning for 60 ns spacing in CDR not clear
  CDR refers to longitudinal wakes
  Referred paper mentions transverse wakes
  No damping used in accelerator, so no fundamental limit
1.54 GeV
1.54 GeV
2.92 GeV
Design not clear to me

## Slide 21: Impact on Specifications
Could be reduced to 1.6-1.7
Could be reduced to 1.41-1.52
Could be reduced to 200-216
Could be reduced to 780-830

## Slide 22: Impact on Specifications
Could be reduced to 1.6-1.7
Could be reduced to 1.41-1.52
Could be reduced to 200-216
Could be reduced to 780-830
Reduced RF in damping ring and linacs
Or decreased apertures for higher gradient and lower cost
Smaller top-up fluctuations

## Slide 23: More on Bunch Trains
To increase in bunch number per pulse allows to
Further reduce the bunch charge
  Can help for accelerating structure design, smaller apertures, higher gradient, higher efficiency, less wakefield effects, …
Increase the charge per pulse
  This requires slightly more RF but might increase the efficiency
  Would allow to lower the repetition rate
  Have to pay attention to charge in the damping ring to not require excessive RF
  E.g. doubling the number of bunches allows to half repetition rate but does not require twice the peak power
Can reduce the charge for H and t as well by considering to use more bunches in the booster than in the collider
Ramp up and stay for a short moment at top energy for beam transfer in stages
Could also accelerate a few bunches per pulse in this scenario to limit time for injection

## Slide 24: Booster Linac
Proposal in CDR
Charge seems high for C-band linac
8% losses seems very high, should aim for close to 0%
Why this large emittance growth in linac?
Try to reduce charge per bunch
But use more bunches
This allows to use smaller aperture and hence higher gradient
Could also enable higher frequency

## Slide 25: Low Charge Considerations
Required filling pattern in CDR not clear to me
Some study will be required
Conservatively assume equal spacing
But circumferences are different so could in principle use different patters

## Slide 26: Low Charge Considerations
For top and Higgs can reduce bunch charge if we use more bunches
For Higgs accelerating two bunches per pulse would be useful
Need to delay one by O(1000 ns) could be done in 50 turns of the booster

## Slide 27: Lower Charge Consideration
Lower charge for Z and WW more difficult, since many bunches are already used
Pessimistic assumption for Z: Accelerate bunches with 19.6 ns spacing
This allows 10 bunches in X-band train
Assume 100 Hz
Can fill booster ring in 16.64 s
With ramp need 18 s
Can have about three booster ramps instead of one
Can reduce bunch charge by factor 3 to about 0.7 x 1010
Similar at WW

## Slide 28: Linac Studies
Why not European S-band? (2.855 vs. 3 GHz)
Linac hardware in simulations are not quite clear
  Aperture of first S-band structures is 20 mm radius and they have the same 25 MV/m gradient as the later ones with 10 mm radius?
  Arrangement of BPMs not clear, seem to use accelerating structures for this
Bunch spacing in linac is set to 60 ns due to long-range longitudinal wakefields
  In SLC long-range transverse effects were observed for 60 ns (this is the referred paper)
  Damping of structures should avoid such effects
Extra drifts in 20 GeV linac to reduce impact of BPM misalignments seems not clear
  I suspect that the BPMs in front of the quadrupoles are missing
Transmission loss of 8% from 6 to 20 GeV seems a lot
  Should expect only small tail losses
  Large losses make operation hard

## Slide 29: Linac Studies
Trains
In CDR, bunch spacing in linac is set to 60 ns due to long-range longitudinal wakefields
  Now 50 ns is assumed
  In SLC long-range transverse effects were observed for 60 ns (this is the referred paper)
  Damping of structures should avoid such effects
Extra drifts in 20 GeV linac to reduce impact of BPM misalignments seems not clear
  I suspect that the BPMs in front of the quadrupoles are missing
Transmission loss of 8% from 6 to 20 GeV seems a lot
  Should expect only small tail losses
  Large losses make operation hard

## Slide 30: Conclusion
Too early to conclude
But should consider some points
  More electron bunches in the current baseline scenario
  Review of RF frequencies and apertures
    Will depend on other choices
  Powering scheme
    Not clear to me right now, would need to be understood
  Are bunch trains useful?
    Detailed look required
  Would a reduced bunch charge help for a linac to 20 GeV?
  Clarify the questions concerning the linac design
  Check if higher positron capture efficiency is possible
More points will come up

## Slide 31: CLIC Positron Production
Assumed positron yield is about 0.5 at 4.5 GeV
Positron yield of about 1 in CLIC for 5 GeV electrons
Should try to understand the difference in capture efficiency
Important implication for the linacs
5 GeV
2.86 GeV
9 GeV
0.2 GeV
2 GHz RF

## Slide 32: Some Questions
Damping ring final horizontal emittance 3.2 μm
High charge electron pulse and positron pulse in same linac?
Normalised emittance at 1.54 GeV is > 15 μm
  Should be no problem to provide better for electron source
Bunch spacing in linac is set to 60 ns due to long-range longitudinal wakefields
  In SLC long-range transverse effects were observed for 60 ns
  Damping the structures should avoid such effects
Extra drifts in 20 GeV linac to reduce impact of BPM misalignments seems not clear
Transmission loss of 8% from 6 to 20 GeV seems a lot
  Should expect only small tail losses
  Large losses make operation hard
Positron yield of about 1 in CLIC for 5 GeV electrons
Emittance extracted at 1.54 GeV is much larger than injected at 1.54 GeV

## Slide 33: Bunch Trains
Accelerating bunch trains allow to increase the RF-to-beam efficiency
typically requires increase of RF energy per pulse
but one accelerate much more charge per pulse
This allows a faster filling of the pre-booster or booster
Increase in bunch number per pulse beyond two allows to
Reduce the bunch charge
  Can help for accelerating structure design, smaller apertures, higher gradient, higher efficiency, less wakefield effects, …
Increase the charge per pulse
  This requires slightly more RF but might increase the efficiency
  Would allow to lower the repetition rate
  Have to pay attention to charge in the damping ring to not require excessive RF
  E.g. doubling the number of bunches allows to half repetition rate but does not require twice the peak power
Can reduce the charge for H and t as well by considering to use more bunches in the booster than in the collider
Ramp up and stay for a short moment at top energy for beam transfer in stages
Could also accelerate a few bunches per pulse in this scenario to limit time for injection