## Slide 1: FCC Main Quad Clément GENOT, Clément LORIN, Gilles MINIER, Tiina SALMI, Davide TOMMASINI Inputs from: D. Schoerling, E. Rochepault, H. Felice, I. Pong, J. Fleiter, M. Segreti, M. Prioli
27 june 2019

## Slide 2: “History”
1st FCC week
Baseline: 450 T/m × 6.0 m
4 layers graded design (2×Nb3Sn + 2×Nb-Ti) 407 T/m with 20% LL margin, no protection check
2nd FCC week
Baseline: 420 T/m × 6.5 m
3 layers design (3×Nb3Sn) 413 T/m with 20% LL margin [E. Todesco], 40 ms protection delay
3rd FCC week
Baseline: 381.2 T/m × 6.0 m
4 layers design (4 × Nb3Sn) 400 T/m with 14% LL margin, 40 ms protection delay
4th FCC week
Baseline: 360 T/m x 7.2 m
2 layers design (2×Nb3Sn) 353 T/m with 20% LL margin, 30 ms protection delay
LHC
MQ: 223 T/m x 3.2 m
2 layers design (Nb-Ti)

## Slide 3: Last FCC-hh MQ version
Magnet parameter | Units | LHC MQ | FCC-hh MQ
Gradient | T/m | 223 | 367.4
Nominal current | A | 11870 | 22500
Peak field | T | 7.0 | 10.52
Peak field / (Radius x Gradient) | - | 1.12 | 1.15
Loadline margin | % | 20.0 | 20.0
Temp magin | K | 2.0 | 4.6
Inductance (2 ap.) | mH | 11 | 14.4
Stored energy (2 ap.) | kJ | 800 | 3670
Azimuthal force (per ½ coil) (1st + 2nd layers) | MN | 2.6 | 12.3
Radial force (per ½ coil) | MN | 0.9 | 5.5
Fx (per ½ coil) | MN | 1.5 | 7.8
Fy (per ½ coil) | MN | 2.4 | 11.4
Midplane shim | µm | 137 | 330
Hotspot (total delay) | K | - | 350 (30 ms)
Nb of turns per layer | - | 10 + 14 = 24 | 8 + 10 = 18
Total weight of conductor | tonnes | - | 272
Magnetic length | m | 3.15 | 7.06
LHC MQ
FCC-hh MQ
56 mm
50 mm

## Slide 4: Harmonics contents 2D analysis
Chart: b6 and b10 from injection to nominal
| 1485 | 1735.3 | 1985.6 | 2235.9 | 2486.1999999999998 | 2736.6 | 2986.9 | 3237.2 | 3487.5 | 3737.8 | 3988.1 | 4238.3999999999996 | 4488.8 | 4739.1000000000004 | 4989.3999999999996 | 5239.7 | 5490 | 5740.3 | 5990.6 | 6240.9 | 6491.2 | 6741.6 | 6991.9 | 7242.2 | 7492.5 | 7742.8 | 7993.1 | 8243.4 | 8493.7999999999993 | 8744.1 | 8994.4 | 9244.7000000000007 | 9495 | 10495 | 11496 | 12496 | 13497 | 14497 | 15497 | 16498 | 17498 | 18498 | 19499 | 20499 | 21500 | 22500
b10 55 µm | -0.45804 | 0.46069 | 1.0235 | 1.3499 | 1.5127 | 1.5604 | 1.5273 | 1.4385 | 1.314 | 1.17 | 1.0206 | 0.8782 | 0.75358 | 0.65168 | 0.56958 | 0.50196 | 0.44429 | 0.39374 | 0.34867 | 0.30806 | 0.27123 | 0.23766 | 0.20697 | 0.17884 | 0.15299 | 0.12919 | 0.10722 | 0.086908 | 0.06809 | 0.050621 | 0.03438 | 0.019252 | 0.0051383 | -0.042754 | -0.080066 | -0.10969 | -0.1336 | -0.15316 | -0.16936 | -0.18292 | -0.19438 | -0.20415 | -0.21255 | -0.21984 | -0.22619 | -0.23177
b10 20 µm | 1.535 | 1.4056 | 1.1628 | 0.90145 | 0.6901 | 0.54528 | 0.44026 | 0.35688 | 0.28789 | 0.22972 | 0.1802 | 0.13764 | 0.10084 | 0.068768 | 0.040644 | 0.015863 | -0.0061079 | -0.025676 | -0.043196 | -0.058949 | -0.073139 | -0.086007 | -0.097693 | -0.10835 | -0.1181 | -0.12702 | -0.13522 | -0.14279 | -0.14976 | -0.15622 | -0.16221 | -0.16776 | -0.17296 | -0.19046 | -0.20403 | -0.21478 | -0.22341 | -0.23049 | -0.23639 | -0.24132 | -0.24551 | -0.24911 | -0.25221 | -0.25494 | -0.25731 | -0.25944
b6 55 µm | 9.7983 | -3.3662 | -11.898 | -17.333 | -20.608 | -22.332 | -22.923 | -22.688 | -21.86 | -20.621 | -19.124 | -17.499 | -15.86 | -14.315 | -12.935 | -11.733 | -10.691 | -9.7848 | -8.9933 | -8.2974 | -7.6819 | -7.1342 | -6.6441 | -6.2034 | -5.8052 | -5.4439 | -5.1148 | -4.814 | -4.5382 | -4.2844 | -4.0505 | -3.8341 | -3.6336 | -2.9615 | -2.4457 | -2.0399 | -1.7138 | -1.447 | -1.2251 | -1.0377 | -0.87779 | -0.74046 | -0.62191 | -0.51906 | -0.42946 | -0.35105
b6 20 µm | -22.311 | -22.303 | -20.361 | -17.564 | -14.68 | -12.259 | -10.39 | -8.9412 | -7.7956 | -6.8703 | -6.109 | -5.4729 | -4.9342 | -4.4731 | -4.0745 | -3.727 | -3.4219 | -3.1521 | -2.9123 | -2.6979 | -2.5053 | -2.3315 | -2.174 | -2.0308 | -1.9001 | -1.7804 | -1.6705 | -1.5692 | -1.4756 | -1.389 | -1.3086 | -1.2338 | -1.1642 | -0.92821 | -0.74425 | -0.59761 | -0.47839 | -0.37962 | -0.29628 | -0.22475 | -0.16272 | -0.10869 | -0.061609 | -0.020511 | 0.015397 | 0.046881
I = 1485 A; G = 24 T/m
I = 22500 A; G = 367 T/m
Filament diameter:
55 µm (RRP QXF state of the art*)
20 µm (FCC target**)
*QXF cable is made with a strand of 0.85 mm in diameter, too - Simon Hopkins et al., The FCC conductor development programme, 4th FCC week, Amsterdam 9th-13th April 2018
**Ballarino A., Bottura L., Targets for R&D on Nb3Sn conductor for High Energy Physics, IEEE TAS, 6000906, (2015)
Current ramp-up after preparation cycle from injection (3.3 TeV/beam) to nominal (50 TeV/beam)

## Slide 5: Mechanical model
Double pancake glued (dark area)
Sliding contact elsewhere (without separation)
*Tommasini D. et al. https://indico.cern.ch/event/556692/contributions/2591664/ 3rd FCC week Berlin, 2017 + EuroCirCol meeting
**Lanza C., Perini D., Characteristics of the austenitic steels used in the LHC main dipoles, MT17, 24-28 September 2001, Geneva
***Scheuerlein et al, Mechanical properties of the HL-LHC 11 T Nb3Sn magnet constituent materials, IEEE TAS, 4003007, (2017)
Mechanical properties:
Material | E [GPA] / 293 K | E [GPA] / 4.2 K | Pr | (L4.3K – L293K)/L293K
Nb3Sn | 30 | 33 | 0.3 | 3.4e-3*
Epoxy | 5 | 8 | 0.34 | 6.0e-3
13RM19 (steel) | 200** | 210* | 0.28* | 2.7e-3**
DISCUP (copper) | 96*** | 96 | 0.3 | 3.3e-3

## Slide 6: Peak stress in the coil
Collaring | Collaring - 10% creep* | Cold | Powering
peak / average | peak / average | peak / average | peak / average
-101.5 / -85.5 | -91.4 / -76.9 | -88.5 / -73.2 | -111.1 / -69.7
Goal:
good coil-pole contact at nominal (< -5 MPa)
Azimuthal stress in the Nb3Sn blocks of the coil
Insulated cable width
inner layer
outer layer
[MPa]
[mm]
The pole could be even more loaded
*Felix Wolf : “Strong creep behavior starting at 125 MPa” in Effect of transverse stress applied during reaction heat treatment on the stiffness of Nb3Sn Rutherford cable stacks, https://indico.cern.ch/event/743626/contributions/3154023

## Slide 7: Elasto-plastic model for collar
Collar steel: 13RM19 (LHC quad steel)
Yield strength of the collars σ0.2 = 440 MPa*
*Lanza C., Perini D., Characteristics of the austenitic steels used in the LHC main dipoles, MT17, 24-28 September 2001, Geneva
**Bertinelli F., et al., Production of austenitic steel for the LHC superconducting dipole magnets, IEEE TAS, vol 16, no 2, (2006)
(for information YUS130 S for LHC dipoles**)
440 MPa
200 GPa
Stress
Strain
conservative
Collaring Elasto Plastic model
peak / average
-111.6 / -86.5
Collaring Elastic model
peak / average
-101.5 / -85.5
Azimuthal stress in the Nb3Sn blocks of the coil

## Slide 8: CLIQ Protection
Quantities | Values | Unit
Capacitance CLIQ unit | 50 | mF
Voltage CLIQ unit | 500 | V
Detect. + val. + trig. times | 10+10+1 | ms
Hotspot temp. 100% Inom | 300 | K
Hotspot temp. 105% Inom (< 350 K) | 325 | K
Voltage to ground (<1.2 kV) | 250 | V
Energy deposition after 10 ms [mJ/cm3]
600
500
400
300
200
100
P1
P2
P3
P4
I
ICLIQ
I + ICLIQ
Current [A]
P1
P2
P4
P3
I
I
CLIQ
[T. Salmi, M. Prioli, E. Ravaioli]

## Slide 9: 3D emag analysis – OPERA/ROXIE
Coil end design via ROXIE
  Cable windability
  Harmonic optimization
Geometry ROXIE -> OPERA
  End collar via OPERA
  Peak field calculation (ongoing investigation)
Lead extra length = 5 cm
ROXIE

## Slide 10
3D emag analysis – OPERA/ROXIE
Chart: pseudo-harmoniques b_2, b_6 et b_10
Lead end
Layer jump
Return end

## Slide 11
Chart: pseudo-harmoniques b6 et b10
Chart: pseudo-harmoniques b6 et b10
//
Return end
Lead end
Straight section
3D integrated harmonics (Lmag = 7,06 m)

## Slide 12
Cable windability
Nb3Sn cable less compact than Nb-Ti: stability ↘
Nb3Sn interstrand resistance less control (steel core): stability ↘
Machine | LHC (Nb-Ti) | FCC-hh (Nb3Sn)
Aperture (mm) | 56 | 50
Strand size (mm) | 0.825 | 0.85
Cu/non-Cu | 1.95 | 1.65
Number of strand (-) | 36 | 35
Bare cable width (mm) | 15.1 | 15.956
Mid-thickness (mm) | 1.48 | 1.493
Keystone (°) | 0.9 | 0.4
Inuslation (µm) | 130 | 150

## Slide 13
Windings trials
Closest cable geometry available is MQXF one: 40 strands instead of 35
[mm]
[mm]
~2 mm
  Δthickness = 50 µm
Inner layer CAD with MQXF cable
Outer layer CAD with MQXF cable

## Slide 14
FCC quad end spacers extruded to the MQXF cable width
Inner layer
Outer layer
RE
RE
LE
LE
Some of the spacers 3D printed
Fused Deposition Modelling
Tolerance~ 0.2 mm
ABSpluS-P430

## Slide 15: Conclusion
Several designs investigated over the past 5 years
Gradient in the 360 T/m range looks feasible
Mechanic : < 150 MPa
Protection : < 350 K
NEVERTHELESS, to me:
  very challenging in terms of windability of two layers magnet to reach 360 T/m
    0.85 mm x 35 strands (or 0.7 mm x 43 strands) -> too unstable?
    Validation on going with winding trials
    -> Back-up plan : to go back to 4 layer designs to reach 360 T/m

## Slide 16: EXTRA SLIDES

## Slide 17: Cable position versus harmonic content
Random harmonics:
σn(d) = dαβn in units
d = 50 or 100 in µm
β = 0.58
α = 0.4
(for allowed harmonics α = 0.8, Ezio/Susana’s comment, nevertheless no statistics reported on quadrupole, only for dipoles)
Random positioning

## Slide 18
Bpeak | 10,54 | T
Lstraight section | 180 | mm
Liron | 392 | mm
Lcoil | 539 | mm
Lmag | 484 | mm
Lcoil end RE | 27,5 | mm
Lcoil end RE | 269,5 | mm
Liron
Lcoil
Lmag
Lcoil end RE
Lcoil end LE
+0.3 T in the RE head
~17% margin
367 T/m -> 360 T/m -> +19% margin
300 K@ Inom -> 350 K
Could recover the margin
OPERA (with iron) :
OPERA (with iron) :
OPERA (no iron) :
OPERA (no iron) :
Actually, Bphead could be reduced by 0.3 T by inserting a spacer between the first two turns of the inner layer / return side. Under investigation.

## Slide 19: MQXF vs FCC MQ cables
Cable Parameter | Units | MQXF | FCC quad (v12)
Strand diameter | mm | 0.85 | 0.85
Cu/NonCu | - | 1.2 ± 0.1 | 1.65
Nb of strands | - | 40 | 35
Cable bare width (before/after HT) | mm | 18.15/18.363 | 15.956/16.120
Cable bare mid-thick.(before/after HT) | mm | 1.525/1.594 | 1.493/1.538*
Cable bare thinness (before/after HT) | mm | 1.462/1.530 | 1.438/1.481* (15.4%)
Cable bare thickness (before/after HT) | mm | 1.588/1.658 | 1.549/1.596* (8.9%)
Cable width expansion | % | 1.2 | 1.0**
Cable thickness expansion | % | 4.5 | 3.0**
Keystone | ° | 0.40 | 0.40
Transposition pitch length | mm | 109 | 96
Insulation thickness per side (5 MPa) | µm | 145 ± 5 | 150

## Slide 20: Winding trials: Reconcile FCC quad geom. and QXF cable
  Red reacted FCC cable (0.4°)
  Blue reacted MQXF cable (0.4°)
  -> Δthickness = 50 µm
  Same insulation: 150 µm/side
  Inner radius: 25.00 mm
  Outer radius: 41.92 mm
  2 mandrels (no layer jump)
  FCC quad 2D optimization:
    Central post -> extrapolated to MQXF cable width
    Copper wedges -> extrapolated to MQXF cable width
  FCC quad 3D optimization:
    End spacers ->extrapolated to MQXF cable width
  MQXF cable
    Bearing in mind that the components are based on the reacted cable -> bare cable 70 µm thinner
25.00 mm
41.92 mm
[mm]
[mm]

## Slide 21
Strand diameter: 0.7 mm or 0.9 mm
Nb of strands: 40-51-60
Protection delay: 30 ms or 40 ms
60 strands
51 strands
40 strands
0.7 mm
0.9 mm
30 ms
40 ms
2D exploration of the parameter space
Protection: 40 to 30 ms (Hotspot = 350 K)
  + 20 T/m on the gradient (~5%)
2 layers efficiency:
  Lower than ~51 strands
Worry about windability (50 mm aperture)
  Windability test with MBH 11 T cable or MQXF cable would be welcome
MBH
11 T
~MQXF
Design selected for this study:
Most simple design in-line with the optics baseline of 360 T/m

## Slide 22: Layer jump impact on b6
Chart: 
| 300 | 400 | 500 | 575
b6 | 15.7492 | 18.1686 | 20.0915 | 21.3433
calcul b6 le long de l'aimant : |  | 
R [mm]= | b6= | L_saut
300 | 0,75 | 141
400 | 0,84 | 163
500 | 0,92 | 183
575 | 0,97 | 196

## Slide 23: 11 T HL-LHC coil versus FCC quad coil
FCC quad: Rmin ≈ 4.0 mm
11T MBH: Rmin ≈ 7.5 mm
Magnet summary 1st FCC week (2015) by E. Todesco

## Slide 24
FCC quad end spacers with FCC quad cable
« Top » view
From outside

## Slide 25
« Bottom » view
From the aperture

## Slide 26
Some out-of-tolerance tooling
2 central posts and all angular wedges sent back to the manufacturer