## Slide 1: Resolver issue mitigation
1) Analog signals filtering (Patrik) Provides stable position – tested in the PS Ready for motion with Dspace (during technical stop?)
2) RDC Phase lock and amplitude adaptation Implemented in the new electronics (VFC based) Provides very stable position when adjusted (see next slide) Requires modification of circuits – ready for starting new version
3) Influence of the membrane type (2D or 3D forged)
4) Installation of a PSB type resolver in the PS
Issue identified with larger resolver (PSB & PS type) and the vacuum barrel

## Slide 2: Admotec Precision AG report

## Slide 3: Phase alignment principle using FPGA
RDC stimulation (blue)
Reconstructed stimulation with defined phase
~ +111 deg
Primary to secondary phase seen by the RDC: -24 deg
Phase introduced by the resolver & cable
Primary (blue)
Secondary (red)
Phase +52 deg

## Slide 4: Measures in the PS with the resolver
WITHOUT PHASE ALIGNMENT 20k values (~every 2.5ms) 35750 – 35430 = 320 => 80 values (14 bits resolution) Effective resolution: ~8 bits
WITH PHASE ALIGNMENT 200k values (~every 2.5ms) Systematic small shit at defined USER (sychro with the machine) 2720-2688=32 (16 bits) => 8 bits shift (14 bits) Effective resolution (long term) 14-3 = 11 bits! (short term is 14 bits)
Transition between values (small shit) to be recorded with Firmware update

## Slide 5: Influence of the membrane type – 25.04.2018
Phase | Admotec (2D) | Production (3D) | difference [%]
min | 29.86 | 31 | -3.8
max | 32.45 | 36 | -10.9
Position | Admotec (2D) | Production (3D) | difference [%]
32784 | 0.463 | 0.482 | -4.1
16400 | 0.481 | 0.48 | 0.2
7810 | 0.789 | 0.595 | 24.6
0 | 0.569 | 0.437 | 23.2

## Slide 6: Compare resolvers in PS environments
PS type
PSB type

## Slide 7: Compare resolvers in PS environments 30.04.2018
PSB resolver Highest setting stimulation Noise: 114, 126, 135
With Lowest setting: 63, 48, 51 (230mV, 330mV)
PS resolver Lowest settings stimulation Noise: 33, 35, 56 (280mV, 1.2V)

## Slide 8: Conclusions for the resolver investigation
The type of membrane does not influence the signal significantly
The sensitivity to noise between the PS and PSB type is similar.
When phase and amplitude is adjusted and the RDC works in +_ 44 deg max, the position is very stable
Small shift observed, synchro with the machine (one particular user)
No evidence that PS resolver is worst that PSB type.
We can continue with PS resolver type, using the mitigation proposed
During the TS1 in June: test motion with Dspace & analog filtering
Start operating the PS scanner after TS1

## Slide 9: BWS Drive system - Bill of Material
01/ BWSIDC - Intelligent Drive Crate - EDA-03634 (Assembly)
02/ BWSMCU Motion Control Unit EDA-03697 (Assembly)
03/ BWSMIB Motor Inverter Board EDA-03519 (PCB)
09/ Firmware
(Production)
07/ VFC-HD - EDA-03133 (PU)
08/ BWSAIF Analog Interface FMC EDA-03096 (PCB)
12/ Optical parts & cablings
05/ BWSCPC Capacitor Power Charger EDA-03592 (PCB)
07/ Mechanics & connectors
OP 01
10/ BWSFHE FMC height extender EDA-03624 (PCB)
11/ BWSVPA VME Power Adapter EDA-03698 (PCB)
13/ Mechanics & connectors
04/ Firmware EDA-03519 (Production)
OP 02
06/ Electrical parts & cablings

## Slide 10: BWS PMT assembly - Bill of Material
01/ BWS PMT (Assembly)
02/ BWSPSA EDA-03764 (PCB)
04/ Mechanics
Filter wheel (assembly)
OP 01
OP 02
03/ Mechanics box & shielding (Produced)
05/ Scintillator
(PU)
06/ Mechanics box (Produced)
07/ filters (PU)
08/ Motor (PU)
09/ Cabling & connectors