## Slide 1
Muon Phase2 Upgrade
The upgrade of the CMS Muon Spectrometer for HL-LHC
Anna Colaleo - INFN-Bari
7th ENHEP School on High Energy Physics
26-31 January 2019
Ain Shams University

## Slide 2: CMS Upgrade towards HL-LHC
CMS Upgrades
New tracker (4 pixel layers +3 disks)
New trigger/DAQ:
  Track information at L1 with extended trigger latency (from 3.2 total of 12.5 μs)
  Increased L1 bandwidth from 100 kHz to 750 kHz
Calorimeters with higher granularity
Upgrade of Muon system
Goal: keep the same performance as in Phase-1
|η| < 3
PU ~200
LHC Phase-1
LS2: Upgrade injection to increase beam brightness
HL-LHC Phase-2
LS3: Upgrade int. Region to increase beam overplap

## Slide 3: Phase-2 Muon Upgrade overview
Upgrades of the existing muon detectors
  Assess longevity of current detectors/electronics to withstand at HL-LHC
  Upgrade electronics to ensure longevity, cope with trigger and readout requirements
Enhancement of the forward region 1.6<|h|<2.4:
Plan for operation in the future decades requires three elements in the Muon upgrade:
  Additional GEM and RPC layers with new technology for improved triggering, background rejection.
Extension of coverage to the very forward region 2.0<|h|<2.8:
  new ME0 detector using GEM technology for triggering and tagging: extra coverage and reduced physics backgrounds from “lost leptons”

## Slide 4
Upgrades of the existing muon detectors
  Assess longevity of current detectors/electronics to withstand at HL-LHC

## Slide 5: Radiation particles at LHC
Hadronic interactions lead to activation of materials and give rise to neutron backgrounds. Long living neutrons can interact with nuclei and produce photons which further decay to electrons/positrons with some possibility to generate fake signals.
very high flux low detector sensitivity to the neutron and photons required
Monte Carlo estimation of the flux of all particles at CMS using FLUKA. Inelastic collision cross section used for normalization is 80 mb. Used simulation cut offs: Hadrons 1 keV, Muons 1 keV, Neutrons 0.01 meV, Photons 3 keV, Electrons 30 keV. Photons and Electrons have significantly higher cut-offs in some regions (heavy parts). The plot shows the particle flux in the whole CMS cavern for nominal instantaneous luminosity, (L = 1034 cm-2 s-1) .

## Slide 6
Hadronic interactions lead to activation of materials and give rise to neutron backgrounds. Long living neutrons can interact with nuclei and produce photons which further decay to electrons/positrons with some possibility to generate fake signals.
very high flux low detector sensitivity to the neutron and photons required
Radiation particles at LHC

## Slide 7: Radiation particles
neutrons: originate as “fast”, O(100) MeV, (the end product of hadron showers) and then “thermalize” down to 0.025 eV via multiple nuclear scattering
photons: 0.1-10 MeV, from nuclear capture of thermal neutrons, followed by nuclear de-excitation
electrons/positrons: 0.1-10 MeV, from photon conversions and Compton scattering
minimum ionizing particle (MIPs): muons (prompt, π/K in-ﬂight decays ) and punch-through hadrons
neutrons
: photons
: e+/e–
: mips
Although absolute ﬂuxes change dramtically from place to place, the relative ﬂuxes of diﬀerent species are approximately the same (except for mips):
3 : 1 : 0.01 : 0.001-0.01
Probability (sensitivity) for diﬀerent particles to cause a “hit” is almost detector technology independent, approximately:
0.2% : 1% : 20% : 100%

## Slide 8: Energy spectra
The shapes of the energy spectra of neutrons, photons, e+/e– are about the same throughout the muon system
Plots from Muon TDR

## Slide 9: Flux: neutrons (Muon TDR)

## Slide 10: Flux: photons (Muon TDR)

## Slide 11
The degradation of operating conditions of wire chambers under sustained irradiation are the main limitation to the use of gas detector in high-energy physics.
‘Classical aging effects’ are deposits formed on electrode surfaces by chemical reactions in avalanche plasma near the anode.
During gas avalanches many molecules break up and form free radicals (unionized atomic or molecular particles with one or more unsatisfied valence bonds).
Free-radical polymerization is regarded at the dominating mechanism of wire chamber aging
Aging and Long Term Operation
The integrate charge (per unit area for parallel detector or for unit lenght of the anode wire for wire chambers) during radiation exposure is the relevant quantity Type equation here.

## Slide 12
• polymerization
– wires get eﬀectively thicker:
• smaller non-uniform gas gain
• loss of eﬃciency
– long whiskers:
• can cause spurious pulses
• and eventual HV breakdown
• oxidation under gold coating:
– wires swell:
• smaller non-uniform gas gain
• loss of eﬃciency
– gold coating cracks:
• sharp edges can cause spurious pulses
• and eventual HV breakdown
Aging and Long Term Operation: wires

## Slide 13
– increased conductivity:
• leak currents
• loss of the proper electric ﬁeld conﬁguration
• Polymerization on surfaces:
– decreased conductivity; insulating blemishes can charge up and cause:
• erratic changes of the proper electric ﬁeld conﬁguration (unstable operation)
self-sustained discharges (Malter currents)
initial (clean)
after irradiation
Aging and Long Term Operation: surface

## Slide 14: HL-LHC: Assess longevity of detectors/electronics longevity
Background – 5x rates and 6x total doses with respect to LHC
Exceed the design tolerances of several components of the muon system:
- new assessment of the chambers and electronics longevity and performance under accelerated aging tests.
Different Radiation Environment in different stations
14

## Slide 15: Background and longevity issues
High radiation affects both the detectors and electronics:
can decrease the gas gain and increase hit-efficiency losses
radiation damage of the silicon substrate in electronic chips can lead to noisier electronics performance and even fatal failures of entire electronic boards.
elements of current system date even before 2000, currently 15-20 years old, eventually may need to last 40 years
must re-certify existing equipment to HL-LHC for the expected integrated radiation doses and signal and background rates.
Very harsh conditions expected at HL-LHC with integral radiation dose parameters and hit rates at the instantaneous luminosity of 5 · 1034 cm−2s−1

## Slide 16: Muon longevity studies at GIF++
16
All detectors profit from the CERN gamma irradiation facility, GIF++: 662 keV photons emitted by an intense 14 TBq 137Cs source + high momentum particle beam
ME1/1
ME2/1
GE1/1
ME2/1
RPC
DT
16

## Slide 17: Muon longevity studies at GIF++
17
All detectors profit from the CERN gamma irradiation facility, GIF++: 662 keV photons emitted by an intense 14 TBq 137Cs source + high momentum particle beam
ME1/1
ME2/1
GE1/1
ME2/1
RPC
DT
CSC
Irradiate one ME1/1 (higher rate) and one ME2/1.
Monitoring of gas gain and current. Measure trigger rates at HL-LHC condition.
Monitor Malter effect.
RPC
RE2 and RE4 chambers and six spare gaps under test:
detector performance and dark current/noise will be monitored
DT
Study radiation effect on the material: small Drift-tubes are installed at Gif++
Operated one spare MB1
GEM
Test GE1/1 triple-GEM chamber at HL-LHC condition
Also accelerated test with X-ray
17

## Slide 18
Present Detector longevity status
• DTs (Ar : CO2)
about 15% of chambers, most exposed to background, could see noticeable gas gain loss but:
  muon reconstruction will remain high, thanks to multiple layers of DTs on the path of a muon
• CSCs (Ar : CO2 : CF4)
– longevity test with standard mixture completed: no gas gain loss up to 3 × HL-LHC
• RPCs (i-C4H10 : C2H2F4 : SF6)
– no detector degradation effect so far..test continuing
CSC at GIF++
#DTφ hits
#DTφ hits aged
#DTθ hits
#DTθ hits aged
All installed Muon detectors will be kept operational at HL-LHC
GEM (Ar : CO2 )
  – At GIF++: 30 x HL-LHC of the GE1/1 expected charge (0.6 of ME0) accumulated.
  – At B904: More than 1 C/cm2 has been accumulated with X-ray test.
Operation conditions are stable no gas gain change observed

## Slide 19
Upgrades of the existing muon detectors
  Upgrade electronics to ensure longevity, cope with trigger and readout requirements

## Slide 20
LHC cross section and trigger rates

## Slide 21
LHC cross section and trigger

## Slide 22: Level 1 muon trigger
Why high-momentum leptons?
  QCD (strong interaction) provides many jets and large energy deposition, but generally not signatures of electroweak processes
  So signatures with large energy deposition face large QCD backgrounds
  Electrons, muons, taus are signatures of W, Z bosons, top quarks, higgs bosons, SUSY decays, etc., but are rare from QCD.
Muons especially:
  Excellent background reduction possible.
  Excellent momentum resolution for invariant masses etc.
Muon triggering:
  Typical Wμν muon transverse momentum <40 GeV/c. Wish to trigger above 15 or 20 GeV/c, typically.

## Slide 23: Level 1 trigger
New trigger/DAQ:
  Track information at L1 with extended trigger latency (from 3.2 total of 12.5 μs)
  Increased L1 bandwidth from 100 kHz to 750 kHz
HL-LHC

## Slide 24: Level 1 trigger: where?

## Slide 25: Level 1 trigger LHC

## Slide 26
High level trigger (HLT)
1kHz

## Slide 27
High level trigger (HLT)
1kHz

## Slide 28: Muon Electronics Upgrade
28
DT and RPC in barrel
CSC & RPC
in the endcap
Phase-2 CMS Upgrade: replace on chamber electronics to cope with longevity and operational issues, high rate and latency requirements
After initial installation completed in 2009, the Muon system underwent many upgrades in order to recover the initial system descoping and to improve the functionality
+ GEM

## Slide 29: L1T Muon Trigger Architecture upgrade evolution after LS1

## Slide 30: CMS: Muon L1 trigger flow at Phase2

## Slide 31: DT electronics and trigger primitives generation
STEP 1
Signals from wires are processed by Bunch and Track Identiﬁer (BTI): Rough track finding within a Super Layer (SL)
STEP 3
Trigger Server (TS) performs a quality based selection on segments coming from TRACOs
STEP 4
Sector Collector (SC), on balcony, reﬁnes the sorting per sector and performs BX alignments before sending data to the track finder
STEP 2
TRAck COrrelators (TRACO) Put out two best muon segments from each chamber. Correlate inner and outer superlayers
Trigger boards housed in on-chamber MiniCrates for trigger primitive generation
•A single large synchronous 40 MHz digital system of 55000 ASICs
•Two best muon segments on output from each chamber:

## Slide 32
DT minicrates
BTI, TRACO, and TS trigger electronics, etc.
An average MC has ~17 boards:
6 ROB, 6 TRB, SB/CCB, LB

## Slide 33: DT Sector collector and readout server crates
TTC ck,LV1A,bgo
local-LV1A (veto)
fibers to DTTF
CMS trigger stream
Local DAQ
fibers to DDU
CMS DAQ stream
Tower Near
TTC fiber ck, LV1A, bgo
TDC data LVDS
DCS fibers
TRIG data LVDS
LV 5V;3.3V
local-LV1A (veto)

## Slide 34: DT electronics evolution
During LS1 Trigger Sector Collector and Read Out Server crates have been relocated by simple electronics converting copper signal to optical.
CuOF does a parallel conversion from copper to optical and OFCu reconverts the signal to copper
More powerful electronics based on μTCA has replaced the Trigger Sector Collector and the Read Out Server:
  Such electronics is needed to overcome the limitations from the increase of luminosity in terms of processing speed and trigger rates
  Optical decoupling facilitated the electronics improvement without interfering LHC schedule (optical splitting)
After LS1
Now

## Slide 35: Barrel electronics upgrade after LS1
  Readout (uROS):
    Same HW as TwinMux but different firmware
    Installalled in YETS 2017-2018, operating very well in 2018.
  Readout and trigger electronics moved from VME standard to uTCA standard
  Trigger (TwinMux): Build Superprimitives (SP) with DT+RPC information.

## Slide 36: The aging of the DT electronics
In “Minicrates”, located at the ends of DT chambers

## Slide 37: Overview of DT electronics upgrade in Phase-2
Electronics need to be upgraded
➡ Limited to L1 rate of 300 kHz
Need at least 500 kHz for the HL-LHC
➡ Designed for TIDs corresponding to 500 fb-1
➡ Buried in iron yoke → difficult maintenance
➡ Not robust against single-hit inefficiency
Due to trigger primitives generated locally
Aging of DTs could lead to significant chamber trigger inefficiency
Phase-2 electronics move complexity to USC
➡ Same analog front end
➡ New on-detector board: OBDT
➡ Trigger primitive generation in new back-end electronics in USC (underground control room
Current
Phase 2

## Slide 38: DT On detector electronics for Phase-2
DT chamber
Minicrate
TDC Trig
UXC
USC
to L1 MBTF
to FED/cDaq
@ 100kHz
CuOF
TwinMux
CuOF
DT chamber
Minicrate 2
TDC on FPGA
UXC
USC
to L1
~ lpGBT links
Goals:
Reduced power consumption
enhanced reliability,
address legacy electronics longevity issues,
L1/ReadOut performance requirements
Backend:
FPGA
L1 processors
Readout Pipeline
uROS
RPC
Current
Phase 2
3-5 OBDTs
per chamber
1 minicrate
per chamber
One single type of board
New MiC2 designed over one single type of board (OBDT) that contains:
  time digitization (required resolution achievable with FPGAs)
  optical transmission (profit from CERN developments)
  reduced slow control

## Slide 39: CSC electronics and trigger primitives generation
CFEB:
Serves 6 (planes) x 16 strips
Ampliﬁer ­‐shaper ( τ = 100 ns )
Precision charge information stored every 50 ns
Comparator ASIC finds half-strips hit
FPGA (programmable) finds 6-layer patterns
  Patterns are different, depending on Pt of the muon
  Pt threshold around 3 GeV/c
ALCT board:
FPGA looks for a pattern of hits every 25 ns
Anodes “non-bend plane”
Pattern the same for all muons from interaction point
Bunch ID
Fine delay adjustment (2.2ns steps) for times-of-flight
Time history (16 bx) recorded for each wire group
Wires spaced at 3.2mm, drift times 0-50 ns with small tail up to 75ns
6 layers of information for both anodes and cathodes

## Slide 40: CSC Trigger Mother Board

## Slide 41: CSC Upgrade in LS1: ME1/1 chamber
DCFEBs continuously digitize strip signals
➡ Signals stored in deep buffers inside powerful Virtex-6 FPGA
Trigger/readout data sent via 3.2 Gb/s links to OTMB/ODMB
ALCT mezzanine upgraded
➡Based on more powerful Spartan 6 FPGA (ALCT-LX150 (it has a Spartan-6 LX150 FPGA), capable of improved algorithms
New DMB is capable of handling 7 DCFEBs
➡ Data received via seven 3.2 Gb/s links
➡ Powerful Virtex-6 FPGAs stores data in internal FIFOs.
Same 1.6 Gb/s output link to DDU
TMB upgraded (OTMB) with much more powerful Virtex-6 PFGA
➡ Also increased bandwidth from DCFEBs with 3.2 Gb/s optical link

## Slide 42: CSC Electronics Upgrade for Phase-2
On chamber Electronics:
Cathode Front End Board (CFEB) will be update with Digital CFEB in all ME234/1 chambers
DCFEBv2 very similar to DCFEB (installed in 2013-14 in ME1/1 ring)
DCFEB will be updted to xDCFEB in ME1/1 chamber:
Main difference with respect to DCFEBv1 is increased radiation hardness
Anode local charged Track (ALCTs)
designs based on ALCT mezzanine boards installed in ME1/1 and ME4/2 during LS1
New ALCT with Optical link in ME1234/1 (LX100/LX150)
Current ALCT from ME1/1 to ME1/3
Low Voltage Distributor Boards will be update to provide power to new DCFEBs and ALCTs
Off chamber Electronics:
Trigger Motherboard (TMB): replaced with Optical TMB in order to receive DCFEB trigger data; increased algorithmic power
Data Mother Boards (DMB): replaced with Optical DMBs
based on new generation Artix-7 FPGAs
new optical fibers at 6.4 Gb/s

## Slide 43: RPC Link System Upgrade in Phase-2
43
Off-detector electronics: consists of Link and Control Boards ("Link System") and is located in crates on the balconies around CMS.
FEB
FEB
FEB
Resistive Plate Chambers
Up to 6 layers of detectors.
480 chambers in Barrel, 648 in Endcap
FEB
FEB
FEB
Control & diagnostic
Link Board
Link Board
Link Board
Synchronization Unit & LMUX
Optic Links
90 m @ 1.6 GHz
492 fibers
Cu-cables
1376 Link Boards
in 108 Crates,
Steered by 216 Control Boards
Control Board
Motivation for Upgrade:
Operation issues:
  the CBs are connected into ring configuration. If one CB fails then the entire ring does not work, leading to a loss of 6 % of the system.
Maintenance: Not enough spares available (rely on old ASICs)
Low speed data transmission links (1.6 Gbps)
Electronics will be replaced during Long Shutdown3.

## Slide 44: RPC New Link System Design
New LB and CB
Back compatible with the present Link Boxes. Signal cables from the chambers will be not removed.
Based on Xilinx 7 FPGAs (replace ASICs)
RPC signal sampling frequency will be 640 MHz clock from the present 40 MHz clock
  Time resolution will be improved: from 25 ns to 1.6 ns. Impact on muon trigger and offline reconstruction.
  Background hits out of time could be removed and synchronization facilitated
  More robust
  Higher bandwidth (10 Gbps output, lpGBT and VL+)
44

## Slide 45
2. Enhancement of the forward region 1.6<|h|<2.4:
  Additional GEM and RPC layers with new technology for improved triggering, background rejection.

## Slide 46: HL-LHC: Muon requirements in endcap region
Event reconstruction capabilities (trigger and offline) require, particularly in forward region:
to enhance redundancy, to increase # of measurements with good spatial and time resolution, to solve track reconstruction ambiguities.
Extended acceptance
to complement the wider tracking and calorimeter coverage and to reduce physics backgrounds from “lost leptons”
Very challenging region:
High rates: muons, background hits, punchthrough
Small bending of muons by magnetic ﬁeld
Currently only CSC chambers at high h

## Slide 47: Enhancement and extension of the forward region
UPGRADE: augment the system with new detectors.
improved RPC (iRPC)
GEM detectors

## Slide 48
RE3/1
RE4/1
New 72 chambers (RE3/1 and RE4/1), related electronics and services to extend the coverage in || to 1.8 < || < 2.4 using an improved design of RPCs (iRPCs) in order to:
handle the particle rates foreseen at HL-LHC (2 KHz/cm2 including safety factor 3)
restore redundancy L1 muon trigger.
Forward muon system enhancement: improved RPC in RE3/1 and RE4/1

## Slide 49: Requirements for the iRPC chambers
 | Present system | iRPC
¦h¦ coverage | 0 – 1.9 | 1.8 – 2.4
Max expected rate (Safety factor SF = 3 included) | 600 Hz/cm2 | 2 kHz/cm2
Max integrated charge at 3 ab-1 (SF = 3 included) | ~ 0.8 C/cm2 | ~ 1.0 C / cm2
f granularity | ~ 0.3 ˚ | ~ 0.2̊
h resolution | ~ 20 cm | ~ 2 cm
time resolution | 1.5 ns | < 1 ns

## Slide 50: Requirements for the iRPC chambers

## Slide 51: iRPC Electronics
Electronics scheme of the project with 2 sided readout: 2 cm resolution in |η| with limited number of channels.
Based on OMEGA ASIC in TSMC 130 nm (Petiroc) with 64 chan/chip.
TDC implemented in FPGA
Both sides are connected at the same PETIROC to reduce jitter
New power system, new services
FULL SIZE PROTOTYPE
51

## Slide 52: Validation of iRPC detector
No background, only muons: 98 % efficiency at Working Point (WP) ~ 7 kV.
Background of 2 kHz/cm2: 94% efficiency with WP + 300 V.
The average charge (or the gain) within the gap is constant at WP optimized for each rate. The iRPC charge is 3 times lower than for RPC.
WP ~ 6950 V
WP ~ 7250 V

## Slide 53
Forward muon system enhancement: GEM project
Trigger and reconstruction
1.5 < |η| < 2.2
36 staggered super-chambers (SC) per endcap, each Triple-GEM chamber spans 10° 144 chambers in total
Installation: LS2 (2019-21)
GE2/1:
Trigger and reconstruction
1.6 < |η| < 2.4
18 staggered SC per endcap, each Triple-GEM chamber spans 20° 72 chambers each divided in 4 modules: 288 chambers
Installation in YETS 2021/22, 2022/23
GE1/1:
1

## Slide 54: The background in forward region
GE2/1
ME0
54
GE2/1
GE1/1
ME0
GE1/1

## Slide 55: The background in forward region
GE2/1
GE1/1
ME0
GE2/1
GE1/1
ME0
Expected hit rate up to 100’s Hz – 100’s kHz/cm2
55

## Slide 56: The GE1/1 and GE2/1 detectors
Based on triple-GEM technology:
  high gas gain 104
  High spatial resolution O(100 mm)
  Rate capability to MHz/cm2
  very resistant to aging
Two layers of triple-GEM (super-chamber) to be installed in front of existing CSC chamber: signals to be used in conjunction with CSC trigger primitives
GE1/1 consists of 72 10° triple-GEM super-chambers
  Covers 1.6 < |η| < 2.2 and it would be installed already in LS2 (2019-2020)
  A slice of the system (5 superchambers installed since Spring 2017.
GE2/1 consists of 36 20° triple-GEM super-chambers
- Covers 1.6 < |η| < 2.4
to installed already in YETS (2021/2022) and YETS (2022/2023)
GE1/1
Two additional detectors with good spatial resolution for triggering and reconstruction purpose.

## Slide 57: The GEM working principle
50 μm thick kapton foil, copper clad on each side and perforated by an high surface-density of bi-conical channels;
  Kapton is a high-resistivity material
By applying a potential difference between the two copper sides an electric field as high as 100 kV/cm is produced in the holes acting as multiplication channels.
Potential difference ranging between 400 - 500 V
Copper etching by chemical solution
kapton etching using the copper mask

## Slide 58: The Single GEM working principle
Electrons are collected on patterned readout board.
All readout electrodes are at ground potential.
Positive ions partially collected on the GEM electrode
To study gain in GEM we have to analyze which are the mechanisms of charge amplification
We identify three electric fields: drift field, moltiplication field, induction field
Drift electrode

## Slide 59: Ion Backflow suppression
The electric fields (drift and induction) play a crucial role to define the so called Transparency
Another important parameter is the geometry of holes
Ion backflow=ratio of positive ions reaching the drift electrode to the electron charge detected at the anode
Ions are re-absorbed by the walls!!!
electrons are lost on the lower face of the GEM electrode,

## Slide 60: Gain Determination
Collection efficiency
Extraction efficiency
Effective gain
Intrinsic gain
Geff = Gintr* εcoll * εextr = Gintr * T
Since a field-dependent fraction of the multiplying electrons is lost on the lower face of the GEM electrode, the useful or effective gain, defined as ratio of the detected to the primary ionization charge, is always lower than the real gain of the multiplier.

## Slide 61: GEM detector parameters
Electron transparency of a standard GEM electrode (at 140 um pitch, 70 um holes ) as a function of drift field for fixed induction field, for several values of GEM voltage.
increade too much the hole diametr is not beneficial on the gain value
Electron transparency for different GEM geometry labeled as pitch/holes diameter.
Electron transparency dependence vs
Different drift and induction electric field

## Slide 62: Single vs Triple GEM
With an appropriate choice of the fields, the fraction of amplified electrons transferring to the gas gap following a first electrode can be injected and multiplied in a second foil, and yet again in a cascade of GEM electrodes
Discharge probability on exposures to α particles is strongly reduced
Multiple structures provides equal gain at lower voltage

## Slide 63: Signal in Triple-­‐GEM detectors
• understand the detector signal shape

## Slide 64: Signal in Triple-­‐GEM detectors

## Slide 65: Signal in GEM detector

## Slide 66: Signal in GEM detector
40

## Slide 67: Signal in GEM detector
the signal induction is caused by the motion of the electrons towards the electrode;

## Slide 68: Signal in GEM detector
the signal induction is caused by the motion of the electrons towards the electrode;

## Slide 69: Signal in Triple-­‐GEM detectors
3 mm
mm
mm
1 mm
Anode current produced by 1 muon
GARFIELD simulation including GEM ampliﬁcation
  signal length: ~60 ns
  detector capacitance: 10-­‐30 pF
  charge range (MIP): 4-­‐110 fC

## Slide 70: Rate capability
A systematic study of rate dependence of gain in multi-GEM devices in a range of operating conditions and geometry has shown the gas gain to keep constant wrt to the rate;
Gas gain is observed to be constant over four orders of magnitude of incident particle rate up to 100 MHz/cm2.
In HEP experiment a maximum rate on the order of 10 kHz/cm2 is expected

## Slide 71: CMS GEM-CSC bending requirements
Adding detector in front of CSC to measure the muon bending angle in magnetic field in the each station, keeps the rate under control and adds redundancy:
Requirement high rate capability
precise Df meas.spatial resolution

## Slide 72: CMS GEM-CSC bending: GEM requirements and performance
Adding detector in front of CSC to measure the muon bending angle in magnetic field in the each station, keeps the rate under control and adds redundancy:
Requirement high rate capability
precise Df meas.spatial resolution
X5 reduction
GEM detector main characteristics:
Excellent rate capability: up to 105/cm2
Gas mixture: Ar/CO2 – not flammable
Angular resolution 500 mrad or better
Time resolution 8-10 ns
Gain uniformity of 15% or better across the module
No gain loss due to aging effect after 10 years of operation at HL-LHC
Large areas ~1 m x 2m with industrial processes
Long-term operation in COMPASS, TOTEM and LHCb

## Slide 73: GEM GE1/1 Project Status
10o
superchambers
short
long
  GE1/1 in high-η region 1.5<|η|<2.2
  36 superchambers in each endcap (144 modules)
Muon
Endcap
Station 1
GE1/1
Foils
Chamber
Installation in LS2 (2019-2020)
Single-mask technology
1D radial strip read-out with
3  8  128 = 3,072 channels
40/47 HV sectors
3/1/2/1 mm gap sizes
No glue in the assembly
Gas mixtures:
  Ar/CO2 (70:30)
  Gas flow ≈ 5 l/h

## Slide 74: GE2/1 design
VFATs
M4
M3
M2
M1
GE2/1 back chamber
Triple-GEM Modules
Chamber frame with longitudinal
reinforcement bars & coupling bars
coupling bars
GE2/1 consists of 20° 36 triple-GEM super-chambers and covers 1.6 < |η| < 2.4
GE2/1 chambers made up of 4 modules
➡ Different shape but similar size to single ME0 chamber
➡ Modules have different lengths → non-projective
GE2/1 superchambers made up of 2 chambers
M1
M2
M3
M4
Back Chamber
M5
M6
M7
M8
Front Chamber
I.P.
GE2/1 Superchamber
Front Chamber Back Chamber
35.5 mm
35.5 mm
35.5 mm
longer
shorter
M8/M4
M7/M3
M6/M2
M5/M1
GE2/1 Triple-GEM Modules
74

## Slide 75
ME0:
Triggering and reconstruction
2 < |η| < 2.8
36 wedges of 6 layers Triple-GEM
each chamber spans 20°
Installation: LS3 (2024-26)
Forward muon system enhancement: GEM project

## Slide 76
The ME0 Detector
High granularity and spatial segmentation for:
    Position and bending measurement of the muon stubs for efficient matching of the offline pixel tracks.
Multi-layered structure to:
  improve local muon track reconstruction
  discriminate muon (segment) against neutrons (uncorr hits).
New station to efficiently identifying and triggering muons, low in transverse momentum (but large in momentum) while maintaining a low rate of background in the harsh HL-LHC conditions up to h=2.8. Installation scheduled in LS3.
ME0 consists of 6 layers of triple-GEMs arranged in 200 super-module wedges: 216 chambers.
  Large lever arm between ME0 and CSC (ME1/1) up to h~2.4
    Allows large trigger rate reduction
ICHEP 2018 - A. COLALEO

## Slide 77: Muon trigger improvement
Very good separation between soft and hard muon
Schematic view of a muon trajectory from the collision point
CSC-GEM tandem improves trigger-level muon momentum measurement, by providing the local direction measurement
Background has steeply falling momentum spectrum
  Trigger rate reduction (otherwise raising trigger thresholds would harm physics acceptance)
x10 reduction in muon trigger rate

## Slide 78: Standalone L1 Trigger: efficiency
  iRPC additional hits recover the efficiency losses due to acceptance gaps in this region
   GEM and iRPC hits allows considerably higher efficiency in comparison to a L1 trigger based on CSC detectors alone.
Level-1 muon track finding efficiency in the endcap region benefits from the addition of GEM and iRPC in the high η region.

## Slide 79: Summary
The CMS Muon system is performing very well
  many upgrades have followed the initial installation made the system very robost
Some electronics need to be replaced to meet HL-LHC requirements.
The high η region to be enhanced with additional GEM and iRPC detectors.
Upgraded detector capabilities open windows for new physics opportunities.
Installation starts in the Long Shutdown2 (2019-2020); continues in Year-End-Techinical-Stops; and finishes in the Long Shutdown 3 (2024-mid 2026)
CMS Muon Upgrade TDR is published
For any question/information contact me at Anna.Colaleo@cern.ch

## Slide 81: New physics search: triggering on unconventional signals
up to a factor 4-5 improvement
factor of 50 improvement
Adding GEM makes it possible to build trigger- level muons without assuming muons come from the proton collision point
Trigger on highly displaced muons
The upgraded RPC link system fully exploits the RPC time resolution, enabling to identify patterns of delayed hits from one station to the next, with a precision of ~1 ns
Trigger on Heavy Stable Charge Particles

## Slide 82: Extended muon acceptance
Help in suppressing background such as WZ.
Ex. WZ→ µµµ decays signature, with two same-sign leptons and third non-reconstructed muon:
extended coverage up to 2.8 in η allows more efficient reconstruct and veto of WZ→ µµµ decays
D/Bàτ, τà3μ
CMS Signal acceptance
more than doubled
|η| of the most forward muon (p>2.5 GeV)
Many BSM searches and SM measurements beneﬁt from extended muon acceptance:
In WZ events
H → ZZ → 4µ: 17% more signal, with a very good background rejection
5s- observation limit on BR( τ3μ) = 1.1 x 10-8 @ 90% CL ( x2 Belle limit)

## Slide 83: Slow-moving muon-like particles
provide already at trigger level a mass resolution achieved only offline in Run2
with β < 0.5 can be triggered with nearly 90% efficiency for η < 1.4.
Search for heavy “colorless” charged particles (HSCP) with masses larger than O(1) TeV and very long lifetimes (β ∼ 0.3–0.5):
 slow muons emerging from IP.
Upgraded RPC electronics with precision timing allows to trigger on such slow “muons”
1.6 TeV stau: mass resolution

## Slide 84: Displaced signatures
Several new physics models predict long-lived particles would potentially lead to displaced signatures, decay outside the tracker volume
Trigger and tracking algorithms using position of the primary vertex not efficient in reconstructing tracks with such large impact parameters
Stand-alone capabilities of the muon system constitute the only possibility for detection of the signature:
  Additional GEM detectors in combination with CSC in improved algorithms permit to efficient triggering on displaced muon tracks and increase the physics sensitivity for many searches.
Ex. Improved upper limits on pair production of hypothetical particles, decaying in with lifetime distance cτ = 100 cm, as a function of the sparticle mass.

## Slide 85
GE1/1 Chamber construction
8
• GE1/1 chambers introduced a novel technique of GEM chambers construction, which avoid the usage of glue
• GE1/1 chambers are realizing using GEM foils stretched by means of moveable FR4 frame (internal). Cathode and Readout electrode made by standard single layer PCB. Electrical signal extracted by “vias” on PCB trough 130 pins Panasonic connectors
• The internal frames are controlled by “stretching screws”
• The tightness of the chambers is assured by an external FR4 frame sealed with o-­‐ring
• GE1/1 Mass producton started in April 2017. Production completed!
Chamber assembly have to be performed in clean room (at least class 1000) to avoid GEM foils contamination

## Slide 86: GEM Electronics
Feast DC-DC converter (designed by CERN)

## Slide 87: Time Resolution
The time resolution is dominated by fluctuations of the nearest distance of the primary ionisation processes to the region where the gain is acquired, dnear.
Defining N as the average number of primary clusters generated by an ionising particle inside the gas, this distance follows a classical exponential distribution
The contribution of the time resolution to the drift velocity is
Typical values for gases employed in MPGDs are N = 3(electrons-ion)/mm and vd ~ 0.12 mm/ns leading to few-10 ns time resolution with the best choice of gas mixtures and operating voltages
d= exp(-Nx)/N
st=1/N*vD

## Slide 88: Example: upgrade of the DT Readout for Phase-II
Local generation of trigger primitives from the DT- TDCs, implemented in ASICs, housed in the “minicrates”
BTI -Bunch & Track Identifier
TRACO TRAck COrrelator
Phase 0/1: Trigger primitives constructed locally from the TDC readings of the DTs
Phase-II: The bare TDC readings are sent via a “Patch Panel” to USC for processing
CuOF Copper to Opt. Fib. Translator
Current R/O
Phase-II R/O
TwinMux: Combines trigger primitives from DT and RPC and sends them to the Track Finder

## Slide 89: LHC trigger overview
Triggering takes much more time than the 25ns between crossings (bx)
  Speed of light c = 7.5 m / bx
  Calculations:
    Electrons, photons, and jets: energy clusters are calculated
    Missing-Et: all calorimeter energies are summed
    Muons: tracks are found and Pt calculated
  Path to electronics cavern is ~100 m (not straight-line)
Therefore, store temporary data while trigger does its calculations…
Detector n
front-end
100 bx
Local trigger electronics
Global trigger electronics
0 Time (bx) 128
New trigger/DAQ:
  Track information at L1 with extended trigger latency (from 3.2 total of 12.5 μs)
  Increased L1 bandwidth from 100 kHz to 750 kHz

## Slide 90: Barrel muon track finder
Accepts DT segments from 4 stations in a sector
+ neighbours
Accepts also CSC segments in “overlap” η region
Combines segments into full tracks
Assigns Pt,η,ϕ,quality to each muon track
Accepts DT segments from 4 stations in a sector
+ neighbours
Accepts also CSC segments in “overlap” η region
Combines segments into full tracks
Assigns Pt,η,ϕ,quality to each muon track
Sector Processor ( PHI Track Finder)
36

## Slide 91: Endcap Muon Track Finder(EMTF)