## Slide 1: High Power RF Processing of Couplers/Windows and Cavities for SNS Linac
Y. Kang
M. Crofford
T. Hardek
S. Kim
J. Mammosser
R. Peglow
C. Phibbs
A. Vassioutchenko
RAD/SNS/ORNL
6th CW and High Average Power RF Workshop
ALBA, Barcelona, Spain
May 4-7, 2010

## Slide 2: Machine layout
Presentation_name
H- stripped to p
Liquid Hg Target
Accumulator Ring;
Compress
1 ms long pulse
to 700 ns
Current
1ms
Injector
2.5
RFQ
DTL
86.8
CCL
402.5 MHz
805 MHz
SRF, b=0.61
SRF, b=0.81
186
387
1000 MeV
Linac; 1 GeV acceleration
945 ns
1 ms macro-pulse
Current
midi-pulse
Front-End: Produce
a 1-msec long, chopped, H-beam
Chopper system makes gaps
Notes: 2

## Slide 3
SNS RF Systems
HEBT
RFQ
DTL
CCL
805 MHz, 5.0 MW
4 x CCL
1 x HEBT
86.8 MeV
1000 MeV
Front End
402.5 MHz, 2.5 MW
1 x RFQ
6 x DTL
Linac
185 MeV
SCL
Ring
H - Injector
2.5 MeV
Ring
805 MHz, 550 kW
81 x SCL
1 MHz, 500 kW
4 x Ring
MEBT &
Chopper
402.5 MHz
20 kW
4 x MEBT
2 MHz
80 kW
1 x IS
All SNS linac RF systems are pulsed at 8% duty cycle (1.3 msec, 60 Hz)

## Slide 4: High Power Window/Couplers in SNS Linac
RFQ powered by one 2.5 MW Klystrons
  2 windows for 402.5 MHz Radio-frequency Quadrupole (RFQ)
6 DTL tanks powered by 2.5 MW Klystrons
  6 windows for 402.5 MHz Drift tube linac (DTL) cavities
4 CCL structures powered by 5 MW Klystrons
  Each CCL structure has 2 input ports
  Klystron output is divided with a quadrature hybrid
  8 windows for 805.0 MHz Coupled cavity linac (CCL) cavities
SCL cavities
  33 medium beta cavities in 11 cryomodules (with 0.55 MW Klystrons)
  48 high beta cavities in 12 cryomodules (with 0.55 MW Klystrons)
  81 windows for 805.0 MHz Superconducting linac (SCL) cavities
  36 high beta cavities will be added (9 cryomodules) in future power upgrade project

## Slide 5
RF Processing in SNS RF Test Facility
High power RF testing and processing can be performed at 8% duty (1.3 msec 60 Hz)
  805 MHz, up to 5 MW peak power
  402.5 MHz, 2.5 MW max. peak power
  Complete low-level RF control and monitoring for reliable processing and operation in EPICS environment
SCL cavities and cryomodules are prepared and processed
  Cryomodules high power RF tested in test cave after repairs
  New cryomodule is being assembled (Building a medium-beta cryomodule will start)
  SRF cavities are plasma processed
More than 60 windows/couplers including new spares have been conditioned for RFQ, DTL, CCL, and SCL
  42 of 81 power couplers of the SNS SRF cavities were RF processed in the RF Test Facility during construction of SNS cryomodules
  Several cavity window/couplers for RF frequencies different from SNS frequencies were processed

## Slide 6: SNS SCL Cryomodules
Fundamental power couplers
Return end can
Helium vessels
Space frame
Supply end can
Designed to operate at 2.1 K (superfluid helium)
Total 81 cavities in 23 Cryomodules
  med-β: 33 6-cell cavities in 11 cryomodules
  high-β: 48 6-cell cavities in 12 cryomodules
Medium Beta Cryomodule (=0.61)
High Beta Cryomodule (=0.81)

## Slide 7: SCL Present Status
Careful high power testing delivered practical operational limits of cavities (not fundamental limits) but to set a safe operating gradient (Sang-ho Kim)
SCL is providing a reliable operation for neutron production following SNS power ramp-up
930 MeV + 10 MeV (energy reserve)

## Slide 8: SCL Considerations (J. Mammosser, S-H. Kim)
For > 1GeV operation with high system availability
  high-beta gradients need to be improved
  Collective system performance with other improvement
In-situ plasma processing of cavities successfully tested with possibility of 2 - 3 MV improvement per cavity
  More poorly performing high-beta cavities will be processed
Chart: Eacc (MV/m)
| 5.7 | 6.5 | 7.5 | 8.5 | 9
baseline before processing | 0.0648 | 0.54 | 3.6 | 14.4 | 27
after processing | 0.0252 | 0.3132 | 1.512 | 3.6 | 7.2 | 13.32 | 23.4
Production of spare cryomodules with better performing cavities
  Building one high-beta cryomodule is under way and one medium-beta cryomodule will start
  Completion of SRF Facility (AIP Project)
Changes on the Cavities
  couplers are interlocked with e-current measurement (interlock using degrading CCGs abandoned)
  HOM feedthroughs will be taken out as needed
  Will not have HOM couplers for new cavities

## Slide 9: SCL Fundamental Power Coupler
GHe-cooled
outer conductor
Inner conductor
conduction cooled
Ceramic window
Door knob
Transition
Waveguide
Inner conductor
water cooled
6-cell cavity
Present coupler specifications:
  550 kW peak
50 kW average
  Qext ~ 7 x 105
Performance:
  Conditioned up to 650 kW power in traveling wave and 2.4 MW power in standing wave
  Over 500 kW peak power in linac cavity operation
Consideration
  Higher peak and average power capability for the future SNS power upgrade & more stable operation may require additional cooling at the antenna tip

## Slide 10: RF Processing Control Screen
Coupler RF Processing in EPICS

## Slide 11: SCL Coupler Conditioning Setup
Coupler conditioning processes:
  Baked up to 200 C with controlled slow ramp-up and cool down
  650 kW traveling wave to 6% duty cycle
  600 kW standing wave (2.4 MW peak) with variable waveguide short
  Use of DC biasing during conditioning

## Slide 12: RFQ Window/Coupler Construction
RFQ system was upgraded with two coupler configuration (from 8 coupler configuration)
  Use a magic-T hybrid power splitter with a water load on the isolation port
  Operate at ~ 800 kW (400 kW / coupler)
  Use coupler ports farther away from the H- ion-source for better vacuum condition
New couplers designed using SCL coupler window routinely conditioned to 600 kW peak power @ 6% duty in traveling wave
  6 new couplers manufactured and RF conditioned at SNS/RFTF
  RF conditioned up to 450 kW @ 1 msec, 30 Hz through bridge waveguide

## Slide 13: RFQ Coupler RF Conditioning
Return and insertion losses through bridge waveguide and couplers
402.5 MHz operating frequency
Rectangular re-entrant cavity type (or ridge waveguide) is used as the bridge waveguide
Used special vacuum ports to accommodate the coupler loop antenna tip design

## Slide 14: Upgraded RFQ Couplers

## Slide 15: SNS CCL Window/Coupler Preparation
Bridge waveguide is copper plated
Pumping ports are equipped with RF screen
Extra ports are for arc detectors and vacuum gauges
Insertion loss of two windows with the bridge waveguide is <-0.03 dB
Baked for 48 hrs at 150 C with 12 hrs ramp-up and 12 hrs cool down

## Slide 16: CCL Window RF Processing

## Slide 17: SNS DTL Window/Coupler Conditioning
Compact bridge waveguides have been built and copper plated
Spare windows for 402.5 MHz, 2.5 MW cavities have been conditioned
Conditioning setups for the DTL and CCL windows are similar except the waveguide dimensions

## Slide 18: RF Distribution Setup for Cryomodule Test (up to 4 cavities)
Vector
modulator

## Slide 19: Waveguide Feed Network for Four Cavity Conditioning
Feed four SCL cavities with one klystron (available 5 MW tubes)
Use waveguide vector modulator employing the mechanical phase shifters
Adjust the power of four outputs connected to cavities to 40% in amplitude and 30 in phase

## Slide 20: Summary
LINAC RF structures and their high power components are performing reliably with continuous improvements
RFTF completely equipped and operational:
  Two klystron tanks with complete waveguides in WR2100 (402.5 MHz) and WR1150 (805 MHz)
  One 11 MW peak power high voltage converter modulator (HVCM) for powering the klystrons up to 8% duty in 60 – 135 kV.
  Test cave measures 3.6 m x 8 m
  Clean room facility for SRF processing and other utilities for He cryo systems, vacuum, and water cooling
  Complete low-level RF control and monitoring for operation in EPICS environment
  Programmable bake out setup
Performed RF processing tasks successfully during construction, commissioning, and post-commissioning operation
  Conditioned new spare window/couplers have been conditioned for RFQ, DTL, CCL
  Conditioned more than 50 couplers for SCL
Ready for the upcoming power upgrade project (PUP) with assembling, testing, and conditioning of couplers and cavities