## Slide 1: A Metamaterial Structure for Wakefield Acceleration at the Argonne Wakefield Accelerator (AWA) Facility
John power (for Xueying lu now at SLAC)
ALEGRO WORKSHOP
26-29 March 2019, CERN
jp@anl.gov

## Slide 2: AWA facility
https://www.anl.gov/awa
Metamaterial experiment
John Power, Manoel Conde, Jiahang Shao, Eric E. Wisniewski
Argonne National Laboratory (ANL)
Chunguang Jing
Euclid Techlabs LLC
Xueying Lu, Michael A. Shapiro, Ivan Mastovsky, Richard J. Temkin
Massachusetts Institute of Technology (MIT)
outline
ALIC plans at AWA
(light version)

## Slide 3: Argonne national laboratory
30 minuets west of Chicago
APS (7GeV light source)
National User Facility
AWA (Advanced Accelerator)
Test Facility
ATLAS (Heavy Ion Accelerator)
National User Facility

## Slide 4: AWA Mission
Developing e- Beam-driven Wakefield Acceleration
- SWFA (Two Beam Acceleration (TBA) and Collinear Wakefield Acceleration (CWA) and Novel structure R&D and RF breakdown study)
- PWFA (High Transformer Ratio)
Advanced Acceleration Concepts
https://www.anl.gov/awa
- Longitudinal bunch shaping (EEX and Laser controlled)
- 6D emittance repartitioning (EEX + FBT)
- Diagnostics: Single shot & Non-destructive
Beam Physics
- Novel cathodes: field emission and photoemission
- High brightness beam generation (symmetrized)
- Bunch Shaping (both transversely and longitudinally)
Electron Sources
- TeV collider
- Compact X-ray source
- Tunable THz generation
- Electron cooling
- UED/UEM
Applications
https://www.anl.gov/awa
https://www.anl.gov/awa

## Slide 5: Awa Beamlines and test-stands
ACT
Cathode studies
Breakdown studies
Witness beamline
4 – 15 MeV
0.001 – 20 nC
20 MW RF power station
RF gun studies and conditioning
Drive beamline
8 – 70 MeV
0.001 – 100 nC (single bunch)
Bunch trains (up to 32 bunches with 600 nC total)
witness beam
drive beam
Unique capabilities of AWA:
Two independent linacs
6D: Emittance exchange and flat beam
Wide range of bunch charge (highest)
Flexible Test facility for beam driven wakefield studies
~40 m

## Slide 6: SWFA: Structure-based Wakefield Acceleration
drive beam
main beam
Several variations of scheme, geometry, frequency, material.
drive beam
main beam
Two-Beam Acceleration (TBA)
Collinear Wakefield Acceleration
(CWA)
Geometry: cylindrical, planar, or novel (PBG, metamaterial, etc)
Frequency: typically from 10 GHz to 1 THz
Material: metallic, dielectric, hybrid
Goals:
high efficiency
high gradient
beam quality
Advanced Acceleration Concepts

## Slide 7: TBA: metallic structures
11.7 GHz metallic iris loaded structure
300 MW
150 MeV/m
C. Jing et al., Nucl. Instr. Meth. in Phy. Res. A 898, 72-76 (2018)
Demonstrated: High Gradient in a Single Stage
Demonstrated: Staging
70 MeV/m
New Dielectric TBA results
(See Alexei Kanareykin next talk)
Advanced Acceleration Concepts

## Slide 8: Cwa: metallic STRUCTURES
High power, high gradient at 91 GHz with two halves structure
Corrugated waveguide structure for multi-beamline XFEL
G. Waldschmidt, et al, in Proceedings of IPAC2018 (2018)
Peak power ~5 MW peak gradient 85 MeV/m
D. Wang, et al, Phys. Rev. Lett., 116, 054801 (2016)
21 GHz prototype
First deceleration
91 GHz
220 GHz
Advanced Acceleration Concepts

## Slide 9: longitudinal shaping with EEX
5 nC / 48 MeV
Shaping with masks
Take final longitudinal current profile
Triangle
z
z
Train
Rectangle
z
Trapezoid
z
Train
y
Triangle
y
Rectangle
y
Trapezoid
y
*G. Ha et al., PRL 118, 104801 (2017)
*G. Ha et al., PRAB 19, 121301 (2016)
Beam Physics

## Slide 10: beam diagnostics development
The second new method since AWA made witness scan method in 80’s
Energy change follows wakefield
Single shot wakefield measurement
Transverse phase space measurement
x-y coupling
x-x’ coupling
Minimizing y-y’
This is new method introduced since 90’s
(x,x’) or (y,y’) can be projected in to (x,y) screen
A fast way to characterize the beam and beamline
Slit-scan result
Projection result
Getting image of each shots
10 spot ⨉100 shots ⨉ 2 Hz → 500 s for avg image
*G. Ha et al., submitted (2019)
Measured
phase space
w/o wake
*Q. Gao et al., PRAB 21, 062801 (2018)
Drive beam
Witness beam
Modulation from wakefield
Comparison between with and without wake provides actual shape of the wake
Beam Physics

## Slide 11: PWFA: Plasma wakefield acceleration
Advanced Acceleration Concepts
High R with EEX
Courtesy: R. Roussell,
J. Rosenzweig, G. Andonian
Emittance Exchange
Longitudinal Phase Space
(LPS) Diagnostic
Preliminary

## Slide 12: AWA Mission
Develop Science & Technology of e- Beam-driven Wakefield Acceleration
- SWFA: Two Beam Acceleration (TBA) and Collinear Wakefield Acceleration (CWA)
- Novel structure R&D
- Fundamental field emission and RF breakdown study
- BBU control in wakefield accelerators
- PWFA
Advanced Acceleration Concepts

## Slide 13: NOVEL structure R&D at the awa
Some of the structures that have been tested at the AWA facility
Iris loaded
Metallic (AWA)
Cylindrical dielectric (AWA)
Meta/left-handed (MIT)
Photonic band gap (LANL)
Planar dielectric (Euclid)
Coaxial dielectric (Omega-P)
Notes: AWA and collaborators have tight integration.

## Slide 14: Recent Publication

## Slide 15: Wagon Wheel Structure Unit Cell
Wagon wheel structure
  Periodic subwavelength structure
    Period: 2 mm
    Free wavelength at 11.42 GHz: 26 mm
  Negative group velocity
  Fundamental mode: TM mode
  Interaction frequency: 11.42 GHz
    Cutoff frequency of an empty waveguide: 14.2 GHz
Dispersion Curve
Stainless steel
Copper

## Slide 16: CST Simulation
CST Wakefield solver, single bunch
  45 nC, σz = 1.2 mm
26 MW steady state in the backward port
Much lower power in the forward port
  Reversed Cherenkov radiation
Analytical theory:
= 25 MW
Beam
Backward Port
Forward Port
Simulation

## Slide 17: Experimental Setup at AWA
Diagnostics:
ICT (Integrating current transformer): Bunch charge
YAG screen:
Bunch transverse size
RF probes:
Output microwave

## Slide 18: Installed Experiment at AWA

## Slide 19: Single Bunch Experiment
High RF power from a single 45 nC bunch
  Experiment: 25 MW
  Simulation: 26 MW (steady state)
  Analytical theory: 25 MW
Reversed Cherenkov radiation verified
  Coherent radiation at 11.4 GHz
  Backward port has much more power
100 GSa/s, 16 GHz BW scope

## Slide 20: Scaling with Charge
Good linear scaling of gradient vs. charge, good agreement with theory
  No breakdown events

## Slide 21: Two-Bunch Experiment
Single bunch
Two bunches with 0 deg phase difference
Two bunches with 180 deg phase difference

## Slide 22: Highest power shot
Two bunches with a total charge of 85 nC
80 MW extracted RF power
50 MV/m decelerating electric field
  75 MV/m available accelerating gradient for a possible witness bunch
~130 MV/m maximum surface field

## Slide 23: Next Experiment: Longer Structure
100-cell structure (20 cm long), 8 bunches, 40 nC/bunch
  0.9 GW peak power
  170 MV/m decelerating gradient
  250 MV/m available accelerating gradient for a witness bunch
CST simulation of
output power in the backward port
Bunch Train
To Output Ports

## Slide 24: Acknowledgement
Funding agency:
ANL: U.S. Department of Energy, Office of Science under Contract No. DE-AC02-06CH11357.
MIT: U.S. Department of Energy, Office of Science, Office of High Energy Physics under Award Number DE-SC0015566.
ANL-AWA
MIT