## Slide 1: CLIC: Main Linac Beam Dynamics
ALEGRO Workshop
CERN
March 2019
Daniel Schulte

## Slide 2: CLIC Introduction
2012 CDR:
Shows feasibility of 3 TeV design
CLIC: Compact LInear Collider
CLIC aims to provide multi-TeV electron-positron collisions with high luminosity at affordable cost and power consumption

## Slide 3: CLIC Staged Scenario
Plenty of physics at low centre-of-mass energies
Energy and luminosity targets from Physics Study Group
Implementation in stages
Study top at threshold
Top above threshold
Higgs via Zh and WW fusion
To be updated with more input from LHC and stage 1

## Slide 4: CLIC at 380 GeV
Developed optimised first energy stage
Upgrade to higher energies included

## Slide 5: Key Parameters
Parameter | Symbol [unit] | CLIC | CLIC
Centre of mass energy | Ecm [GeV] | 380 | 3000
Luminosity | L [1034cm-2s-1] | 1.5 | 6
Luminosity in peak | L0.01 [1034cm-2s-1] | 0.9 | 2
Gradient | G [MV/m] | 72 | 72 / 100
Particles per bunch | N [109] | 5.2 | 3.72
Bunch length | σz [μm] | 70 | 44
Collision beam size | σx,y [nm/nm] | 143 / 2.9 | 40 / 1
Emittance | εx,y [μm/nm] | 0.95 / 30 | 0.66 / 20
IP beta functions | βx,y [mm/mm] | 8 / 0.1 | 6 / 0.07
Bunches per pulse | nb | 352 | 312
Bunch distance | Δz [mm] | 0.5 | 0.5
Repetition rate | fr [Hz] | 50 | 50
Very small emittances required to achieve the luminosity
Bunch charge and length at IP determined by main linac

## Slide 6: Luminosity and Parameter Drivers
Beam Quality
(+bunch length)
Need to ensure that we can achieve each parameter
Can re-write normal luminosity formula
Luminosity
spectrum
Beam current

## Slide 7: Luminosity and Parameter Drivers
Beam Quality
(+bunch length)
Need to ensure that we can achieve each parameter
Can re-write normal luminosity formula
Luminosity
spectrum
Beam current
The limit is the beam stability in the main linac

## Slide 8: Luminosity Drivers at High Energy
In the classical regime
In the quantum regime (high energy)

## Slide 9: Luminosity and Beam Quality
Luminosity
spectrum
 | Δεx [nm] | Δεy [nm] |  | 
 | Total contribution | Design limits | Static imperf. | Dynamic imperf.
Damping ring exit | 700 | 5 | 0 | 0
End of RTML | 150 | 1 | 2 | 2
End of main linac | 50 | 0 | 5 | 5
Interaction point | 50 | 0 | 5 | 5
sum | 950 | 6 | 12 | 12
Imperfections are the main source of final vertical emittance
Require 90% likelihood to meet static emittance growth target
Damping ring main source of horizontal emittance
But value is OK, as we will see

## Slide 10: Main Linac: Low Emittance Preservation
Beam stability
incoming beam can jitter (have small offsets) and become unstable
lattice design, choice of beam parameters
Static imperfections
errors of reference line, elements to reference line, elements. . .
excellent pre-alignment, beam-based alignment, beam-based tuning
Dynamic imperfections
Ground motion, cooling water induced jitter, RF jitter, electronic noise,. . .
lattice design, BNS damping, component stabilisation, feedback, re-tuning, re-alignment
Combination of dynamic and static imperfections can be severe
Lattice design needs to balance dynamic and static effects

## Slide 11: Wakefields and Beam Current
2a
Two goals:
Maximise beam current
But maintain good beam quality
Maximise the current by
Maximising bunch charge
Minimising distance between bunches
Limit from main linac wakefields
Maximise beam quality
Main linac wakefields are important component
Will ignore multi-bunch wakefields solved by technical means in CLIC
RF team loves small a
Less power
easier to reach gradient
Beam team hates small a
More wakefields
Beam less stable

## Slide 12: Longitudinal Wakefield and Energy Spread
Z = time
Picture 1:
Particle extracts energy
Picture 2: Particle induces field
If a bunch extracts a large fraction of the energy in the structure the tail will gain much less energy
IP, i.e. focal point
Focusing lens
Actually a doublet of quadrupoles
Nominal particle
Lower energy particle
Limit arises from final focus system energy bandwidth
CLIC goal 0.35% RMS spread

## Slide 13: Energy Spread and Bunchlength
Energy spread can be reduced by passing beam off-crest of the RF
Reasonable limit 12°
2% gradient loss
1.3 MV/m
1.3 MV/m
1.5 MV/m
This ties the bunch length to the charge for a given structure design
More charge requires longer bunches
The transverse wakefield effect roughly increases as length x charge

## Slide 14: Transverse Wakefields
For short distances the wake-field rises linear
Coherent bunch offset (worst case)
The tail is deflected to the outside
Oscillation amplitude increases
Oscillation frequency decreases
First particle
Second particle
Example equation of motion second particle
Example equation of motion first particle

## Slide 15: Tricks of the Beam Physics
Make the focus strong again
Use O(10%) of the linac for magnets
Leads to small beta-function
Makes the beam stable (strong spring for an oscillator)
For single bunch use BNS damping (Balakin, Novokhatsky and Smirnov)
Introduce energy chirp that compensates transverse wakefields

## Slide 16: Beam Stability, With BNS
Direction of motion
Direction of motion
No BNS damping
With BNS damping
Offset beam centre at injection
Offset beam centre at injection

## Slide 17: Beam Stability, With BNS
Simple betatron oscillation
Tail still flaps a little bit
Centre of bunch is much more stable
Direction of motion
Direction of motion
No BNS damping
With BNS damping
Simple betatron oscillation
Tail and centre flap quite a lot

## Slide 18: Impact of Charge
If one increases the charge the beam stability will be compromised
30% more charge are still reasonable
But keep a bit away to as a margin
60% more charge leads to unstable beam

## Slide 19: Static Imperfections: Main Linac Alignment
The error for this is most critical misalignment of components is of the order O(10μm)
2) Establish reference system with overlapping wires, has some error but is not critical
3) Align modules remotely to the wires using their sensors and movers
1) Align components accurately on the supporting girders
4) Use sophisticated beam-based alignment such as dispersion free steering (DFS, i.e. different energy beams) to align components
In particular to align BPMs

## Slide 20: RF Alignment
Structures scattered on girder
Wakefield kick
5) Measure beam offset with wakefield monitor
Move girder to remove mean offset
No net wakefield kick
Limit mainly from
wakefield monitor accuracy (3.5 μm)
reproducibility of wakefield
tiny variation of betatron phase along girder
Wakefield monitor:
Measure wakefield in damping waveguide

## Slide 21: Main Linac Emittance Growth (3 TeV)
imperfection | with respect to | symbol | value | emitt. growth
BPM offset | wire reference | σBPM | 14 µm | 0.367 nm
BPM resolution |  | σres | 0.1 µm | 0.04 nm
accelerating structure offset | girder axis | σ4 | 10 µm | 0.03 nm
accelerating structure tilt | girder axis | σt | 200 µradian | 0.38 nm
articulation point offset | wire reference | σ5 | 12 µm | 0.1 nm
girder end point | articulation point | σ6 | 5 µm | 0.02 nm
wake monitor | structure centre | σ7 | 3.5 µm | 0.54 nm
quadrupole roll | longitudinal axis | σr | 100 µradian | ≈ 0.12 nm
Goal: less than 10% above Δεy = 5 nm
Further improvement using tuning bumps
Emittance growth for different imperfections
Using sophisticated beam-based methods
0 5 10
Δεy,0 [nm]
Note: The tight tolerances are the price for the strong focusing,
Which allowed high beam current

## Slide 22: CLIC Beam-Based Alignment Tests at FACET
DFS applied to 500 meters of SLC linac
System identification algorithms to construct model
DFS correction with GUI
Emittance growth is measured
System model
Emittance [10-5 m ]
Initial beam
After 1 iteration
After 3 iterations
iteration

## Slide 23: Dynamic Imperfection Example: Ground Motion
Beam-trajectory feedback corrects pulse-to-pulse (20 ms)
Cures low frequency ground motion
But not higher frequencies
Ground motion can impact beam trajectory
LEP tunnel
Want to be able to cope with this
(Model B10 similar to CMS hall)
Beam-trajectory feedback:
Example transfer curve (recursive filter)
Amplification/demagnification
Frequency [Hz]
25
0
5
10
20
15
demagnification

## Slide 24: Ground Motion

## Slide 25: Beam Motion with Beam Feedback Only

## Slide 26: Jitter at IP

## Slide 27: The Stabilisation System
K. Artoos et al.

## Slide 28: Beam Trajectory Jitter

## Slide 29: Beam Jitter at IP

## Slide 30: Beam Jitter at IP

## Slide 31: Conclusion
The main linac beam dynamics is a key parameter driver in CLIC
It defines the charge and collision bunch length and impacts the vertical emittance
For each accelerating structure design there is an optimum beam parameter set
The highest charge that is acceptable in each bunch
Strong focusing is used to mitigate transverse wakefield effects
Imperfections and their mitigation are critical for the emittance growth and luminosity

## Slide 32: Note: CLIC Optimisation
Scan 1.7 billion cases:
Fix structure design parameters: a1,a2,d1,d2,Nc,f,G
key beam parameters
Luminosity, cost and power (including other systems)
CERN-2016-004
Resulting designs:
Colors indicate luminosities
This is the one that we picked

## Slide 33: Reserve

## Slide 34
 | εx [nm] | εy [nm] | σz [μm] | N [109] | E [GeV]
Damping ring exit | 700 | 5 | 1600 | 5.2 | 2.86
End of RTML | 850 | 10 | 70 | 5.2 | 9.0
End of main linac | 920 | 20 | 70 | 5.2 | 190.0
Interaction point | 950 | 30 | 70 | 5.2 | 190.0
Damping ring makes flat beams
All systems contribute to vertical emittance
Final bunch length defined by main linac
Bunch charge defined by main linac
Bunch energy defined by main linac

## Slide 35: Main Linac: Dispersion-free Steering
Offset BPM produces bump
Off-energy beam has different bump
DFS finds new solution with smaller bump
Adjust BPM reference to be on new trajectory
Method reduces dispersion
Use beams of different energy to identify offset BPMs
Compromise between offset and difference
Dispersion:
Different energy particles take different trajectories

## Slide 36: Pre-alignment Wavelength
Reference line error with given wavelength
Betatron wavelengths of the different sectors

## Slide 37: Ground Motion Summary
 | B10
No stab. | 53%/68%
Current stab. | 108%/13%
Future stab. | 118%/3%
Luminosity achieved/lost [%]
Code
Close to/better than target
Machine model
Beam-based feedback