## Slide 1
Simulations for EuPRAXIA Accelerator Design
Phu Anh Phi NGHIEM (CEA-IRFU)

## Slide 2
16 Participants
25 Associated Partners
Private companies
EuPRAXIA Consortium

## Slide 3
EuPRAXIA scope
Mission: Produce a Conceptual Design Report for the world's first
- high energy 1-5 GeV plasma-based electron accelerator
driven by laser or electron beam
- with “industrial quality”
24/7 user operation
high reliability, reproducibility
high repetition rate ≥ 10 Hz toward 100 Hz
- with high beam quality and high beam charge
- with user areas: FEL & HOPA
From Acceleration to Accelerator
From Proof of principle to User’s Facility
Simultaneously !
Simultaneously !

## Slide 4
EuPRAXIA requirements
Critical parameters of the electron beam
required at Injection or Acceleration stages
OBJECTIVE:
- Providing beam at 5 GeV
meeting 'perfectly'
FEL and HOPA requirements
- Providing also beam at 1 GeV
'usable' for FEL and HOPA
as a 'commissioning' step
at the applications!

## Slide 5
Beam parameters at 5 GeV
at the user's doorstep
Required value

## Slide 6
"Accelerator" approach
"Physics experiment " approach : often built around a laser facility
"Accelerator" approach : like for a conventional accelerator
1. Definition of the desired beam parameters (TLR)
2. Large exploration (simulations) of inject./accelerat. configurations
3. Selection of the appropriate configurations
4. Determination of specifications for the laser and plasma systems
Issues : in plasma-based accelerator
- Simulations are very time consuming
- Many simulation codes  reliability, robustness ?

## Slide 7
PPAS
5 GeV
4B
500 MeV
RFI
L
W
F
A
PWFA
PPAS
1 GeV
4A
500 MeV
RFI
LPI
LPAS
1 GeV
5 GeV
1A
LPI
5 GeV
1B
LPAS
LPAS
1 GeV
5 GeV
2A
RFI
500 MeV
LPAS
5 GeV
2B
RFI
500 MeV
LPAS
LPAS
1 GeV
5 GeV
3A
150 MeV
LPI
LPAS
5 GeV
3B
150 MeV
LPI
Inj. / Accel. schemes considered

## Slide 8
L
W
F
A
PWFA
LPI
5 GeV
(1 GeV)
HETL
LPAS
5 GeV
(1 GeV)
150 MeV
LPI
LETL
HETL
PPAS
1 GeV
500 MeV
RFI
HETL
PPAS
5 GeV
(1 GeV)
HETL
LPAS
HYBRID
LPAS
5 GeV
(1 GeV)
RFI
HETL
250-500 MeV
LPAS
LPAS
2.5 GeV
RFI
240 MeV
HETL
5 GeV
(1 GeV)
3 GeV
Inj. / Accel. schemes studied

## Slide 9
L
W
F
A
PWFA
LPI
5 GeV
(1 GeV)
HETL
LPAS
5 GeV
(1 GeV)
150 MeV
LPI
HETL
PPAS
1 GeV
500 MeV
RFI
HETL
PPAS
5 GeV
(1 GeV)
HETL
LPAS
HYBRID
LPAS
5 GeV
(1 GeV)
RFI
HETL
250-500 MeV
LPAS
LPAS
2.5 GeV
RFI
240 MeV
HETL
5 GeV
(1 GeV)
3.5 GeV
CNR
CEA
DESY
INFN
CEA
DESY LNF
DESY
IST, LLR
LPGP, CNR
CEA
CEA LETL
CEA
Strathclyde, DESY
LNF
LNF LNF
CEA
A. Beck
A. Chancé
E. Chiadroni
A. Ferran Pousa
A. Giribono
B. Hidding
P. Lee
X. Li
A. Marocchino
A. Martinez de la Ossa
F. Massimo
G. Maynard
A. Mosnier
P.A.P. Nghiem
A.R. Rossi
T. Silva
E. Svystun
P. Tomassini
C. Vaccareza
J. Vieira
J. Zhu
11 European institutes
21 contributors
Inj. / Accel. schemes studied

## Slide 10
RFI 240 MeV S-band, RF & Magn.compression
RFI 500 MeV S-band & X-band, Comb technique
LPI 150 MeV Wave-breaking injection and nonlinear regime
Shock-front injection and blow-out regime
Ionization injection and quasi-linear regime
Downramp injection and blow-out regime
Resonant Multiple Ionization Injection (ReMPI)
LPAS 5 GeV Quasi-linear regime, 1 LPAS
Blow-out regime, 2 LPAS + chicane
PPAS 1 GeV Weakly-nonlinear regime
LPAS-PPAS Trojan Horse Injection and blow-out regime
Wakefield Induced Ionization Injection and blow-out regime
Inj. / Accel. techniques studied

## Slide 11
RFI 240 MeV S-band, RF & Magn.compression ASTRA
RFI 500 MeV S-band & X-band, Comb technique Tstep, Elegant
LPI 150 MeV Wave-breaking injection and nonlinear regime SMILEI
Shock-front injection and blow-out regime CALDER-C
Ionization injection and quasi-linear regime Warp
Downramp injection and blow-out regime OSIRIS
Resonant Multiple Ionization Injection (ReMPI) ALaDYN, QFluid
LPAS 5 GeV Quasi-linear regime, 1 LPAS FBPIC, QFluid, Warp
Blow-out regime, 2 LPAS + chicane FBPIC, ASTRA, CSRtrack
PPAS 1 GeV Weakly-nonlinear regime Architect
LPAS-PPAS Trojan Horse Injection and blow-out regime VSim
Wakefield Induce Ionization and blow-out regime OSIRIS
Inj. / Accel. techniques studied

## Slide 12
The resonant multi-pulse ionization injection, P. Tomassini, S. De Nicola, L. Labate, P. Londrillo, R. Fedele, D. Terzani, L. A. Gizzi, Physics of Plasmas, 24 , 10, 103120, doi: 10.1063/1.5000696 (2017).
Single-stage plasma-based correlated energy spread compensation for ultrahigh 6D brightness electron beams,
G.G. Manahan, A.F. Habib et al., Nat. Commun. 8, 15705 doi: 10.1038/ncomms15705 (2017).
Electron beam transfer line design for plasma driven Free Electron Lasers, M. Rossetti Conti, A. Bacci, A. Giribono, V. Petrillo, A.R. Rossi, L. Serafini, C. Vaccarezza, Nuclear Inst. and Methods in Physics Research A 909, 84-89 (2018).
Design of a 5 GeV Laser Plasma Accelerating Module in the Quasi-linear Regime, X. Li, A. Mosnier, P. A. P. Nghiem, Nuclear Inst. and Methods in Physics Research A 909, 49-53 (2018).
Toward Low Energy Spread in Plasma Accelerators in Quasi-linear Regime, X. Li, P. A. P. Nghiem, A. Mosnier, Phys. Rev. Accel. Beams, 21, 111301 (2018).
Plasma boosted electron beams for driving Free Electron Lasers, A. R. Rossi et al., Nuclear Inst. and Methods in Physics Research, A 909, 54 (2018).
Optimization of laser-plasma injector via beam loading effects using ionization-induced injection, P. Lee, G. Maynard, T. L. Audet, B. Cros, R. Lehe and J.-L. Vay, Phys. Rev. Accel. Beams, 21, 052802 (2018).
Preserving emittance by matching out and matching in plasma wakefield acceleration stage, X. Li, A. Chancé, P. A. P. Nghiem, Phys. Rev. Accel. Beams, 22, 021304 (2019).
Etc…………………………..
Published results

## Slide 13
Beam parameters obtained at 150 MeV
Required value
All the configurations

## Slide 14
Required value
Configurations closest to the requirements
Selected for start-to-end simulations
Beam parameters obtained at 150 MeV

## Slide 15
Beam parameters obtained at 1 GeV
All the configurations
Required value

## Slide 16
Required value
Configurations closest to requirements
Selected for start-to-end simulations
Beam parameters obtained at 1 GeV

## Slide 17
Beam parameters obtained at 5 GeV
Required value
All the configurations

## Slide 18
Configurations closest to the requirements
Required value
Beam parameters obtained at 5 GeV

## Slide 19
2-LPAS configuration selected for S2E
Required value
Beam parameters obtained at 5 GeV

## Slide 20
1-LPAS configurations closest to the requirements
Required value
Three experts
Three institutes
Three codes used:
- Warp 3D
- QFluid ~3D
- FBPIC 3D
Three injectors:
LPI 150 MeV
RFI 240 MeV
RFI 540 MeV
Quasi linear regime
Close plasma,
laser parameters
⇒
Close results
Quasilinear regime with external injection: very robust !!!
Beam parameters obtained at 5 GeV

## Slide 21
Beam Injection, Extraction & Transport
To minimize emittance growth, it is imperative to:
1
Tune the density ramp length, at entrance and exit (whatever its shape!)
2
Design transport lines where
number of quadrupoles = number of constraints (6, no more!)
LETL: 0.7 m, HETL: 4 m  20% emittance growth throughout a plasma stage

## Slide 22
Selected Inj./Acc. Configurations
L
W
F
A
PWFA
LPI
5 GeV
(1 GeV)
HETL
LPAS
5 GeV
(1 GeV)
150 MeV
LPI
LETL
HETL
PPAS
1 GeV
500 MeV
RFI
HETL
PPAS
5 GeV
(1 GeV)
HETL
LPAS
HYBRID
LPAS
5 GeV
(1 GeV)
RFI
HETL
250-500 MeV
LPAS
LPAS
2.5 GeV
RFI
240 MeV
HETL
5 GeV
(1 GeV)
3.5 GeV
RFI 250-500MeV +
LPAS (quasilinear regime)
LPI 150 MeV (REMPI) + LPAS (quasilinear regime)
RFI 500 MeV +
PPAS (weakly-nonlinear regime)
RFI 240MeV +
2 LPAS (blow-out regime) +
CHICANE
Notice: a certain level of sophistication is necessary!!
Decouple injection from acceleration: two stages!
and also in the injection stage itself again!

## Slide 23
Specifications for laser & plasma at 150 MeV
Laser: 35 TW, 1.05 J, w0 = 18 mm (a0= 1.8, tFWHM = 30 fs)
(a0 will be x 2 by self focusing)
Plasma: radially uniform, ~3.5 mm long
~1 mm upramp, ~0.1 mmm plateau at n0 = 6 1018 cm-3
~0.15 mm downramp, 1.8 mm accelerating plateau at n0 = 4 1018 cm-3
Exit ramp exponential Lexp=0.1 mm
+ passive plasma lens ~4mm at n0 = 1 1016 cm-3
Driving laser: decomposed in 4 subpulses, delay 160 fs
120 TW, 4 J, w0 = 30 mm (a0 = 1, tFWHM = 30 fs)
Ionizing laser: 3rd harmonic
1.0 TW, 0.07 J, w0 = 3.8 mm (a0 = 0.53, tFWHM = 45 fs)
Symmetrization laser: 3rd harmonic, delay 40 fs
0.7 TW, 0.02 J, w0 = 11 mm (a0 = 0.14, tFWHM = 25 fs)
Plasma: radially uniform, length 3.5 mm + 1 mm ramp
N preionized up to 5+, density n0 = 5 1017 cm-3
+ 3 mm passive plasma lens, n0 = 1.4 1016 cm-3
"ReMPI"
OR ELSE
"Downramp Injection"

## Slide 24
Spécifications for laser & plasma at 1 & 5 GeV
Laser: P = 200 TW, E = 30 J, w0 = 30 mm ( a0 = 2.57, tFWHM = 141 fs)
Bi gaussian
Plasma: parabolic in r, Dn/nc = 1 to 0.6
unniform in z, 5 to 7 cm long, n0 = 1 to 2 1017 cm-3
entrance and exit ramps ~2 cm
Laser: P = 400 TW, E = 60 J, w0 = 45 mm ( a0 = 2.42, tFWHM = 141 fs)
Bi gaussian
Plasma: parabolic in r, Dn/nc = 1 to 0.3
unniform in z, 30 to 50 cm long, n0 = 1 to 2 1017 cm-3
entrance and exit ramps ~2 cm
1 GeV
5 GeV

## Slide 25
Tremendous simulations and optimizations have been performed by many contributors
 Many results obtained on different injection/acceleration schemes and techniques
 First down selection performed for S2E simulations
Issues of emittance growth addressed and solved
Thorough S2E simulations done
 Beam parameters at user's doorstep very close to all the requirements
A certain level of sophistication is necessary
Solutions do exist, at least one is robust
Other schemes or techniques remain promising
Further progress is still possible
Next step: Errors and Tolerances studies
Summary

## Slide 26
RESERVE

## Slide 27
In the presence of significant beam loading
Optimizing energy spread
by optimizing the beam length
Optimizing slice energy spread
by optimizing jointly
the plasma density
and the laser rtength