## Slide 1
WP3: C-BAND INJECTOR
D. Alesini
on behalf of the WP3 C-band injector working team*
* F. Cardelli, M. Diomede, G. Castorina, B. Spataro, M. Croia, M. Ferrario, A. Mostacci, C. Kourkoutis, N. Gazis

## Slide 2
ORGANIZATION OF THE ACTIVITY ON C-BAND INJECTOR
1) C-Band gun design to reach the 240 MV/m peak field level
      1a) Optimum 2D profile to minimize mod. Poy. Vector, peak field etc… and to increase the gun mode separation for short RF pulses (F. Cardelli, D. Alesini, G. Castorina)
      1b) Powering schemes with RF pulse compressors and optimum coupling coefficient (D. Alesini, F. Cardelli)
      1c) Coupler design options:
      magnetic (F. Cardelli, D. Alesini)
      mode launcher (G. Castorina, B. Spataro)
      alternative schemes (F. Cardelli, D. Alesini)
2) C-Band TW accelerating structures design for the velocity bunching and acceleration: optimum irises tapering, structure length,… (M. Diomede, D. Alesini)
3) Beam dynamics simulations of the injector to reach the XLS requirements: gun gradient, TW structures accelerating field, solenoids strength, half cell length optimization…(M. Croia, M. Ferrario,…)
4) Solenoids design (C. Kourkoutis, N. Gazis)
5) Mechanical drawings of the injector module (N. Gazis)

## Slide 3
1) C-Band gun design to reach the 240 MV/m peak field level
      1a) Optimum 2D profile to minimize mod. Poy. Vector, peak field etc… and to increase the gun mode separation for short RF pulses (F. Cardelli, D. Alesini, G. Castorina)
      1b) Powering schemes with RF pulse compressors and optimum coupling coefficient (D. Alesini, F. Cardelli)
      1c) Coupler design options:
      magnetic (F. Cardelli, D. Alesini)
      mode launcher (G. Castorina, B. Spataro)
      alternative schemes (F. Cardelli, D. Alesini)
2) C-Band TW accelerating structures design for the velocity bunching and acceleration: optimum irises tapering, structure length,… (M. Diomede, D. Alesini)
3) Beam dynamics simulations of the injector to reach the XLS requirements: gun gradient, TW structures accelerating field, solenoids strength, half cell length optimization…(M. Croia, M. Ferrario,…)
4) Solenoids design (C. Kourkoutis, N. Gazis)
5) Mechanical drawings of the injector module (N. Gazis)
ORGANIZATION OF THE ACTIVITY ON C-BAND INJECTOR

## Slide 4
C-band gun design: general considerations
State of the art:
in X band (CERN/SLAC) with 180ns input pulse Esurf@irises240 MV/m BDR10-6
C Band klystrons with solid state modulators (Toshiba+Scandinova) are working up to 100 Hz with 3s, 50 MW peak power available
Circulator (CML) available: 50 MW, 2.5 s, 100 Hz
SLED/BOC C-band compressors available (PSI) with amplification factors >4 @ 200 ns flat top pulses
Consequences:
A C-Band gun filled in 180ns and working at 240 MV/m with BDR10-6 can work if properly designed;
Circulator can be used up to the 50 MW peak power level
SLED/BOC C-band compressors can be used (if necessary)
ULTRA FAST GUN

## Slide 5
thalf
tfull
ahalf
afull
dhalf
dfull
bfull
bhalf
Ellfull
Ellhalf
Three main parameters are used for the gun profile optimization: ellipse aspect ratio.
Iris profile with an elliptical shape and a large aperture to:
      increase the peak field at the cathode and reduce the peak surface electric field;
      increase the pumping speed on the half-cell;
      increase the frequency separation between the two gun RF modes: it has to work in pulsed regime with very short RF pulses (<200 ns)
      An optimization of the half cell length has to be done according to BD simulations
Ellipse aspect ratio =
C-Band gun 2D DESIGN: mode separation, QUALITY FACTOR

## Slide 6
[Grudiev et al. PRST-AB 12, 102001 (2009)]
Cahode
first iris
second iris
C-Band gun 2D DESIGN: MODIFIED POYNTING VECTOR
Sc<4 W/µm2 is the specified value for 10-6 BDR/m @ 200 ns RF pulse length. Expected BDR @ Sc=12 W/µm2 100-150 ns SW structures have to be evaluated/tested.

## Slide 7
C-Band gun design: optimum coupling coefficient CALCULATION
fπ | 5.712 GHz
Q0 | 10450
τF | 140 ns
Ecath | 240 MV/m
Pdiss @Ecath=240MV/m | 15.5 MW
Av. Pdiss @100Hz, 200ns | <300 W
Considered C-Band gun parameters (2D and preliminary 3D calculations)
Pin
Prefl
Pdiss
We calculated the required input power (and reflected power) to reach 240 MV/m cathode peak field
A coupling coefficient equal to 3 allows keeping under control the required input power necessary to reach the 240MV/m on the cathode.
With =3 we can also keep at a reasonable value the reflected power

## Slide 8
-Klystron connected to the cavity through one circulator
-RF pulse length 180 ns
KLY
0.180 s 40 MW
circ
GUN
=3
240 MV/m cathode peak field
C-Band gun design: POWERING SCHEME CASE 1

## Slide 9
KLY
1-1.5 s, 40 MW
P.C.
X2.1
GUN
Incident, reflected dissipated power from the gun
=3
100 ns, 85 MW
circ
circ
Short kly pulses
Small amplification factor
This scheme is flexible (we can detune the P.C. and go to the case 1) and allows exploring RF pulses even shorter than 100 ns
-Klystron connected to the cavity through one RF compressor (P.C.) and two circulators
-RF pulse length 100 ns
C-Band gun design: POWERING SCHEME CASE 2

## Slide 10
KLY
2.5 s, 40 MW
circ
BOC
X4.2
LOAD
POWER
DIVIDER
GUN
1/2
Reflected power to the circulator
Incident, reflected dissipated power from the gun
1/2
=3
0.1 s, 170 MW
-Klystron connected to the cavity through one circulator, one RF compressor and a power divider
-RF pulse length 100 ns
C-Band gun design: POWERING SCHEME CASE 3

## Slide 11
Input waveguide
Coupling apertures
cathode
Quadrupole field compensating hole and pumping port
Input waveguide
Magnetic Field Distorsion compensation:
Symmetric feeding with two input waveguides and two symmetric holes for quadrupole field compensation
Pulsed heating:
The coupling window strongly rounded to reduce the peak surface magnetic field and, as a consequence, the pulsed heating.
C-Band gun design: MAGNETIC COUPLING (1/2)
Pumping ports:
The holes for quadrupole compensation can be used for pumping
Laser injection:
On axis
Solenoid:
Can be put immediately after the gun and installed separately. Bore of the solenoid relatively small (no cathode compensation solenoids required, in principle)
Power splitter

## Slide 12
fπ | 5.712 GHz
Δf0- | ≈ 100 MHz
Q0 | 10450
β | 3.08
τF | 143 ns
Ecath | 240 MV/m
Pin @240MV/m | 20.8 MW
Average Pdiss @100Hz, 100ns | 150 W
S11 @res | -5.86 dB
Esurf/Ecathode | 0.92
Sc max on surface @ 240MV/m | 10.63 W/µm2
Field flatness | <1%
Tpulsed @ 100 ns (square pulse) @ 200 ns (square pulse) | 47°C 66°C
Electric field amplitude
Power splitter
Vacuum pumping port
Beam tube
cathode
1
2
3
d
a
Power
Splitter
Pin ≈ 21 MW
C-Band gun design: MAGNETIC COUPLING (2/2)
Parameters

## Slide 13
C-Band gun design: MODE LAUNCHER
Input waveguide
Gun
Mode launcher
fπ | 5.712 GHz
Δf0- | ≈ 100 MHz
Q0 | 11100
β | 3
τF | 150 ns
Ecath | 240 MV/m
Pin @240MV/m | 16 MW
Average Pdiss @100Hz, 200ns | 240 W
 | 66781
Esurf/Ecathode | 0.92
Field flatness | <1%
Tpulsed @ 200 ns (square pulse) | --
fπ | 5.712 GHz
Δf0- | ≈ 100 MHz
Q0 | 11100
β | 3
τF | 150 ns
Ecath | 240 MV/m
Pin @240MV/m | 16 MW
Average Pdiss @100Hz, 200ns | 240 W
 | 66781
Esurf/Ecathode | 0.92
Field flatness | <1%
Tpulsed @ 200 ns (square pulse) | --
Magnetic Field Distorsion compensation:
Perfect 2D profile: no multipole components
Pulsed heating:
No pulsed heating on the input coupler
Pumping ports:
To be studied. Pumping from waveguides could be too far form the accelerating cells
Laser injection:
To be studied. On axis injection after the mode launcher is probably too far from the cathode
Solenoid:
To be studied. The solenoid bore has to be increased with respect to the other cases and a compensating solenoid for the reduction of the magnetic field on the cathode has to be designed

## Slide 14
C-Band gun design: ELECTRIC COUPLING ON FULL CELL WORKING ON TM020 MODE (1/2)
Short circuit plane
TM010 like
Half cell
TM020 like
Full cell
Input port
Short circuit plane
TM010 like
Half cell
TM020 like
Full cell
Need to have a compact coupler with low pulsed heating
Electric coupling on TM020 mode on the full cell
Coupling hole
J-type feeding

## Slide 15
fπ | 5.712 GHz |  |  | 
Δf0- | ≈ 80 MHz |  |  | 
Q0 | 14126 | 14327 | 14350 | 
β | ≈3 |  |  | 
QL | 3181 | 3458 | 3416 | 
τF | ≈190 |  |  | 
Ecath | 240 MV/m |  |  | 
Pin @240MV/m | 25 MW |  |  | 
Average Pdiss @100Hz, 200ns | 330 W | 360 W |  | 360 W
Tpulsed @ 200 ns | 19°C | 21°C |  | 14°C
 | 59200 | 56000 |  | 55777
fπ | 5.712 GHz |  |  | 
Δf0- | ≈ 80 MHz |  |  | 
Q0 | 14126 | 14327 | 14350 | 
β | ≈3 |  |  | 
QL | 3181 | 3458 | 3416 | 
τF | ≈190 |  |  | 
Ecath | 240 MV/m |  |  | 
Pin @240MV/m | 25 MW |  |  | 
Average Pdiss @100Hz, 200ns | 330 W | 360 W |  | 360 W
Tpulsed @ 200 ns | 19°C | 21°C |  | 14°C
 | 59200 | 56000 |  | 55777
Magnetic Field Distorsion compensation:
Symmetric feeding with two input waveguides and two symmetric holes for quadrupole field compensation
Pulsed heating:
Reduced because of the electric coupling
Pumping ports:
From waveguides
C-Band gun design: ELECTRIC COUPLING ON FULL CELL WORKING ON TM020 MODE (2/2)
A
B
C
Laser injection:
On axis
Solenoid:
After the gun OK

## Slide 16
TW STRUCTURES FOR VELOCITY BUNCHING
BD simulations have to be done
In the meanwhile a scan of possible C-band structures geometries (irises apertures, tapering, powering schemes…) is under investigation
f | 5.712 GHz
d cell | 17.496 mm
t_k | 3 us
Q_0 of BOC | 216000
<a>=6.3 mm, Ls=1.2 m,
Referred to 65 MV/m