## Slide 1: Towards HL-LHCV1.4
R. De Maria
WP2 meeting 12/6/2018

## Slide 2: Changes HLLHC1.3 → 1.4
Layout:
2+2 crab cavities → 2 crab cavities only
Q4: 4xMCBY+MQY 1.9K → 3xMCBY+MQY 4.5 K
Q5: 3xMCBY+MQY 1.9K → 1xMCBC+MQML 4.5
Remote alignment system (i.e. machine can be realigned during beam commissioning)
Extended D1 beam-screen
New specification for TCTPV-TCTPH-TCLX stroke and apertures
Increased distance D2-CRAB
Changes in the triplet corrector package
Optics:
Crossing bumps re-optimized thanks to remote alignment system
Decision on crossing plane for Point 1/5
New aperture estimates thanks to remote alignment system
IR4 optimized for instrumentation and e-lens
IR6 reviewed and re-optimized for TCDQ gaps, Q5 strengths
Dedicated optics for 7TeV (using 7.5TeV equivalent currents where needed)

## Slide 3: Table of content
TCTPH-TCLX
Aperture outlook and iteration with vacuum
Next steps

## Slide 4: Layout changes
HLLHCV1.3
H
V
Q5
MQY
B1(E)
B2(I)
V
H
H
V
V
H
Q4
MQY
H
V
V
H
H
V
C
C
C
C
V
H
H
V
D2
MBRD
Q1
Q2a
HV
Q3
Q2b
HV
CP
HV
D1
1.9K
1.9 K
1.9 K
1.9 K
MCBXFB
MCBXFB
MCBXFA
MCBRD
MCBY
MCBY
IP
HLLHCV1.4
H
V
Q5
MQML
B1(E)
B2(I)
H
V
Q4
MQY
V
H
H
V
C
C
C
C
V
H
H
V
D2
MBRD
Q1
Q2a
HV
Q3
Q2b
HV
CP
HV
D1
1.9K
1.9 K
4.5 K
4.5 K
MCBXFB
MCBXFB
MCBXFA
MCBRD
MCBY
MCBC
IP
Changes with respect to the baseline:
Q4: reusing existing cold mass (3 correctors instead of 4), no need of 1.9 K.
Q5: reusing existing Q5 cold mass (1 corrector instead of 3), no need of 1.9 K.
Full deployment of remote alignment system to be used with safe beam.

## Slide 5: Orbit corrector strength budget
Q1 Q2 Q3 D2
Triplets
Q4 Q5 Q6-8
Matching section
IP
HLLHCV1.4
Q1 Q2 Q3 D2
Triplets
Q4 Q5 Q6-8
Matching section
IP
HLLHCV1.3
Right Point 5, H crossing.
The following symmetries apply:
Left B1 -> Right B2,
Left B2 -> Right B1
H Point 5 -> V Point 1
HLLHCV1.4:
orbit bumps reduced at the crab cavities
IP offset performed by remote alignment
Limited crab beam adjustment still possible
Crossing: ±295 μrad
Separation: ±0.75 mm
IP Offset: ±2.0 mm with re-alignment
Luminosity scan: ±100 μm
Crab knobs: ± 0.5 mm (baseline only)
Imperfection (2σ): from uniform distribution of mainly ±0.5 mm quad. alignment and 0.5 mrad / 20 units dipole errors.

## Slide 6: TCLX – TCPH issues in HLLHC
Beam size in between TAXN – D2 is much larger than LHC due to lower β* and D2 closer to the triplet, beam separation smaller than LHC because D1 – D2 distance is shorter.
TCLX needs thicker internal jaw to provide dose protection to D2
-> Larger stroke in less space.
  TCTPV
  TCLX
  TCTPH
  TAXN
  D2

## Slide 7: TCLX – TCPH issues in HLLHC
 | TCTPV | TCTPH | TCLX
Orientation | Vertical | Horizontal | Horizontal
Absorber Cross-section | 34 x 20 mm2 | 34 x 20 mm2 | 70 x 40 mm2
Jaw Stroke | 40 (+5) mm | 30 (+5) mm | 30 (+5) mm
Half Beam Separation | 80.4-81.9 mm | 83.4-84.9 mm | 86-87.5 mm
Interference* with present layout | 11.3 mm | 43 mm | 58.1 mm
* Interference calculated assuming a standard collimator tank and including baking equipment thicknesses (tank jacket thickness 25 mm and/or vacuum chamber wrapping 5 mm) and a new ID/OD 91/95 mm vacuum chamber.
TCLX and TCPH required maximum gap >80 mm: https://edms.cern.ch/file/1561432/1.0/CERN-ACC-2015-0129.pdf
ColUSM #67, 5/2/2016 https://indico.cern.ch/event/493012/
Further discussed at ColUSM #93 (22/9/2017) and integration meeting 12/1/2017:
Interference solved but still with stroke limited to 30 mm.

## Slide 8: TCL-TCT Aperture specifications
Offset (X,Y) | Baseline | Remote alignment
Ground Motion + Fiduc. | ~2 mm | ~0.5 mm
Orbit Error + crab adj. | 2.5 mm | 2.5 mm
Collimator stroke | 15 σ + 10 % (β-beat) | 15 σ + 10 % (β-beat)
Protected aperture | 12 σ + 10 % (β-beat) | 12 σ + 10 % (β-beat)
2 mm IP shift | With orbit correctors | With re-alignment
Round 15 cm | Ax [mm] | Ay [mm] | Ax [mm] | Ay [mm] | Sep. [mm]
TCLX | 36.4 | 27.9 | 31.9 | 26.1 | 86.0-87.5
VTCLX | 28.0 | 36.4 | 26.1 | 31.9 | 86.0-87.5
TCTPH | 28.5 | 37.1 | 26.5 | 32.7 | 83.4-84.9
VTCTPH | 37.0 | 28.1 | 32.5 | 26.4 | 83.4-84.9
TCTPV | 28.9 | 38.0 | 26.9 | 33.7 | 80.4-81.9
VTCTPV | 38.1 | 28.7 | 33.7 | 26.9 | 80.4-81.9
Flat 7.5/18 cm | Ax [mm] | Ay [mm] | Ax [mm] | Ay [mm] | Sep. [mm]
TCLX | 42.8 | 33.8 | 38.3 | 32.0 | 86.0-87.5
VTCLX | 33.9 | 42.9 | 32.1 | 38.4 | 86.0-87.5
TCTPH | 34.2 | 43.5 | 32.3 | 39.1 | 83.4-84.9
VTCPTH | 43.3 | 34.0 | 38.8 | 32.2 | 83.4-84.9
TCTPV | 34.5 | 44.3 | 32.6 | 39.9 | 80.4-81.9
VTCTPV | 44.2 | 34.5 | 39.8 | 32.5 | 80.4-81.9
Ax
Ay
Sep.
ColUSM, 23/2/2018

## Slide 9: New design proposal
Remote alignment meeting, L. Gentini, 31/5/2018
TCLX - 4 mm gap
TCTPH
TCTPV
 | Stroke | Chamber
TCLX | 40 mm | 65/80 mm
TCTPH | 32.5 mm | 80/65 mm
TCTPV | 40 mm | n/a

## Slide 10: Aperture update
Intermediate results: HLLHCV1.3 Optics without IP shift.
HL1.3 | 15 cm 500 μrad | 7.5/18 480 μrad
TAXS | 18.5 | 15.9
Triplet best case | 16.5 | 15.5
Triplet with tolerances1 | 13.2 | 12.7
TAXN | 17.5 | 14.0
D2 | 19.0 | 15.0
Q4 | 18.8 | 13.4
Q5 | 28.3 | 20.0
Q6 | 29.9 | 19.9
Possible improvements:
Shorter crossing angle bump will improve TAXN, D2 apertures (and slightly Q4).
Remote alignment expected to reduce ground motion and fiducialization tolerances (2 mm -> 0.5 mm).
Detailed orbit error model from D. Gamba (expected 2 mm -> 1 mm).
Round optics
Triplets aperture bottleneck for all scenarios
Flat optics
Q4, TAXN, D2 may become aperture bottleneck, but not limiting.
1 R. Bruce et al. CERN-ACC-2017-0051 + J. Jeanneret, LHC rep 1007

## Slide 11: Aperture for vacuum layout
WP12 asked beam envelope without mechanical, alignment and fiducialization tolerances to specify vacuum apertures.
The request inverts the typical work flow because mechanical, alignment and fiducialization are not finalized.
Beam stay clear =
1.1 nσ σnominal + 2 mm
where:
nσ = 13.25 up to D1
nσ = 15 TAXN-Q5
nσ = 20 sigma Q6 to Q7.
In addition, new vacuum aperture should always have larger margins than those found in the triplet.
Table available here.
Recipe given:
Consistent with present hardware and avoid additional aperture bottleneck.

## Slide 12: Next steps
To release version 1.4:
Decision or study new position for Q4/Q5 for cryogenic integration.
Decision on how to gain 30 cm in between D2/crab cavities.
Consistency check between drawings and optics model.
Optimization crossing schemes and other orbit bumps.
Finalization IR6 optics and IR4 optics.
Freeze mechanical, ground motion, fiduc. tolerences.
Computation aperture margins and phase advance tunability.
Evaluation/choice of crossing planes.
Studies in parallel:
Study optics at 7 TeV with ultimate currents in Q7 (more urgent if we want to ask for an hardware test at the end of the run).
Update MS10 branch and follow-up of the DA studies.
Optics optimization for forward physics.