## Slide 1: SEMGRID acquisition with present electronics
Profile signal sampling every 4µs (raw data with 30 wires each)
Trigger adjustable with 0.1µs
Needs to be carefully set for full integration of the bunch signal (like middle plot)
Possible to adjust such that all grids have correct signal
Clear slow exponential decay
=> subtract extrapolated signal of previous turn(s) in multi-turn measurement

## Slide 2: Turn-by-turn reconstruction
Time constants from exponential fit
Good fits with very similar decay
Very good subtraction of previous turn profile possible
Change sampling to 4.6µs (2 turns)
Measure 2 shots with 1 turn trigger difference
=> should allow to reconstruct data turn by turn (if shot reproducibility OK – otherwise larger statistics needed)