## Slide 2: 3rd ALICE & VSC LS2 preparation meeting Update on production and preparation works
Josef Sestak, Giuseppe Bregliozzi, Chiara di Paolo, Jerome Gilles Chaure
on behalf of TE – VSC – BVO

## Slide 3: Annular ion pump in RB24

## Slide 4: Annular ion pump in RB24
Two ion pumps are installed in A1L2.X (RB24)
Annular ion pump VPIXB (RED ARROW)
  Pumping speed for CH4 ≈ 5 l.s-1 (at 1e-9 mbar)
Standard LHC VPIA ion pump (GREEN ARROW)
  Pumping speed for CH4 ≈ 30 l.s-1 (at 1e-10 mbar)
These pumps were developed for ATLAS where the space constraints does not allow to install standard ion pump (first are +/- 18m from IP).

## Slide 5: Pumping speed measurements

## Slide 6: Vacuum simulation of A1L2 & IP2
Pressure after LS2 is higher due to reduced aperture in IP2 - validated

## Slide 7: Vacuum simulation of A1L2 & IP2

## Slide 8: Vacuum simulation of A1L2 & IP2
Absence of the annular ion pump has negligible effect on the critical current

## Slide 9: Annular ion pump in RB24
Purpose of annular ion pump close to IP is to pump CH4 (non-gatherable gas) if the space constraints does not allows to install standard ion pump.
Annular ion pumps has very limited pumping speed and for the pressure < 1e-10 mbar is negligible.
In ATLAS it stays in place as a preventive measure device in case of sudden CH4 pressure rise (as there are no other pumps close to IP.
In ALICE we have standard 30l.s-1 ion pump 9m from IP2.
ALICE requests to minimize the background due to vacuum equipment in RB24.