## Slide 1: Optimization algorithms for PyHEADTAIL Multibunch simulations
J. Komppula
Acknowledgements: K. Li

## Slide 2: Outline
Background
Wake algorithms
Benchmarking
Performance
Applications

## Slide 3: Background
Motivation: FCC-hh transverse feedback studies
Significant code development needed:
April 2016
Beta version of the FB module (single bunch, distributed systems)
September 2016
1st stable version of the FB module
December 2016
1st multibunch version of the FB module
May 2017
Wakes optimized for 1000 bunches
May 2017
Point bunch code for
CBI damping
October 2017
Tracking optimized for full beams
July 2017
Full beam wakes
(10 000 bunches)
November 2017
Parallelization for hundreds of cores
March 2018
Multi location wakes,
more benchmarking
Wake calculations ∝ Nbunches²
New algorithms ∝ Ntot log Ntot

## Slide 4: Background
Challenge arose from the unclear picture, which of the results from different theories/codes is correct and what are tolerable deviations.
I tried my best, the approach was valid, but there was still a problem:
)
)
should have been
PyHEADTAIL meeting #16
Because of the different ways to implement multibunch wakes, it wasn’t even clear to me if the original implementation was fully correct (but it is!).
In order to avoid this in future, I’ll explain why.

## Slide 5: PyHEADTAIL tracking, single bunch
There are two ways to think tracking
What is the difference?
There is no difference
1) Bunch goes physically through all the one turn map elements
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation
2) One turn map elements operate the bunch object on each turn
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation

## Slide 6: PyHEADTAIL tracking, beam
There are two ways to think tracking
1) Bunches go physically through all the one turn map elements
2) One turn map elements operate the beam object on each turn
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation

## Slide 7: PyHEADTAIL tracking, beam
There are two ways to think tracking
1) Bunches go physically through all the one turn map elements (linear convolution wakes)
2) One turn map elements operate the beam object on each turn (circular convolution wakes)
Because of the (wake) causality in z-direction, bunches can be tracked as a compressed train (no low beta multibunch wakes!).
What is the difference?
The only difference is the wake implementation!
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation
Transverse
tracking
Longitudinal
tracking
Wakes
Transverse
feedback
Synchrotron
radiation
Linear convolution wakes allow proper beam passing through the elements
Circular convolution wakes allow more flexible bunch interactions, but beam is handled as a circular object.

## Slide 8: What is the difference between tracking?
Linear convolution wakes
Circular convolution wakes
Wake kick:
Coupled bunch mode wavelength:
Turn by turn data
(mode -1):
j: target bunch index
k: source bunch index
m: turn index
next k:th bunch which is m turns behind
j: target bunch index
k: source bunch index
m: turn index
k:th bunch of the m:th turn
Reference frame:
Beam position monitor signal,
convenient for the wakes kicks
Snapshot picture of a beam,
convenient for the CBI modes
Transformation between the reference frames

## Slide 9: Where is the correction term coming from?
Linear convolution wakes
Circular convolution wakes
No discrete transitions in the beam between the turns
Discrete betatron transition between the turns
-> smooth betatron motion with
Code for transverse tracking is same for both convolutions
Only difference is the definition of the index
  The reference frame differences arise self consistently from the properties of the convolutions
  Linear convolution: turn by turn tracking of independent bunches, BPM monitor reference frame
  Circular convolution: turn by turn tracking of the entire beam, as a snapshot photo without betatron motion

## Slide 10: Positive outcomes from the journey with the circular wakes
Naturally led to explore circular convolution for the PyHEADTAIL wake kick computations -> all the optimizations
Leads naturally to complementary theory to the Sacherer approach can be used when only wake field is at hand
Allows treatment of wakefields which extend far ahead of bunches
Automatically comes with complementary numerical implementation which can be used for benchmarking, cross checking, etc
Faster algorithm

## Slide 11: Outline
Background
Wake algorithms
Benchmarking
Performance
Applications

## Slide 12: PyHEADTAIL wake algorithms
There are several different multibunch wake algorithms in PyHEADTAIL
  Differences in the algorithms do not change the results!
  Only difference is the reference framebetween the linear and circular convolution wakes
Linear convolution wakes:
  mpi=True
    The original algorithm
  mpi=“memory_optimized”
    Wake kicks are calculated for each tracked bunch
    Optimized for a few bunches, (up to 150-250 bunches with the LHC)
  mpi=“linear_full_ring_fft”
    Wake kicks are calculated for each bucket, even if empty, which allows “compressed convolution”
    Allows efficient use of the FFT convolution
    -> faster when filling factor >5-10%
Circular convolution wakes:
  mpi=“circular_full_ring_fft”
    Wake kicks are calculated for each bucket, even if empty
    Allows efficient use of the FFT convolution
    In theory 2x faster than “linear_full_ring_fft” because the FFT convolution is naturally circular
See more details from Nicolas’ presentation
I’ll focus
on this

## Slide 13: How compressed convolution works?
Full convolution between wake function and bunches without optimization

## Slide 14: How compressed convolution works?
1) Pick relevant periodic data from the moments and the wake function
These parts can be removed

## Slide 15: How compressed convolution works?
2) Compress data and calculate convolution

## Slide 16: How compressed convolution works?
The results from the full convolution and the compressed convolution are exactly same
See more detailes from the Nicolas’ presentation

## Slide 17: How efficient is it?
Benefits
  FFT convolution scales as Ntot log(Ntot)
  Wake field calculations can be efficiently parallelized to one turn length blocks
  Faster than N2 algorithms when filling factor >5-15%
Drawbacks
  Padding needed -> doubles the number of slices
  Includes all the buckets, even if they are empty
  Can be efficiently parallelized only to the total number of wake turns in the simulation (all wake kick objects in all planes)
  More data transfer between nodes, but reasonable
log-log scale
N2 algorithms
Ntot log(Ntot) algorithms

## Slide 18: Outline
Background
Wake algorithms
Benchmarking
Performance
Applications

## Slide 19: Benchmarking
004_test_split_slicing.py

## Slide 20: Benchmarking
003a_rigid_beam_test__linear_convolution.py
All the linear convolution wake implementations give exactly same traces
  mpi=‘linear_mpi_full_ring_fft’
  mpi=‘memory_optimized’
  mpi=True (original (py)HEADTAIL implementation)
  Independent minimalistic code with an uniformly sliced ring

## Slide 21: Benchmarking
005_compare_wake_implementations.py
Point like bunch beams are good tests for wake implementations
  Intra bunch motion does not affect results
  Simpler theories
Different wake approaches give exactly same growth rates
The results match excellently to the point like bunch theory from wake function

## Slide 22: PyHEADTAIL vs NHT
Results between the Nested Head-tail and PyHEADTAIL match well
  The error in the wake implementation had negligible effect because of the relatively short length of the wake function
1.97 GHz HL-LHC HOM
Solid lines: NHT
Dots: PyHT, 12/2017

## Slide 23: Outline
Background
Wake algorithms
Benchmarking
Performance
Applications

## Slide 24: Performance evolution
December 2017, batch-nodes
A factor of 2-3 better performance now
  Improved code and cluster performances, still room for code improvements
  Cluster optimization procedure is unclear, it might be possible to improve cluster/MPI efficiency at high number of cores
Perspective
  The HL-LHC 2GHz HOM test is easy: 3564 bunches, 20k mppb, 20 slices per bunch, 3 turns wake, chroma
    => 0.7 s per turn on 40 cores (2 nodes)
  One-tenth of the CERN HPC be-long queue: 8 nodes = 160 real cores / 320 ranks
    1 month = 2.6*106 seconds => 106 turns when tracking 2.6 s per turn
  => Full LHC beam can be simulated with chromaticity with 100k mppb and 100 slices per bunch
June 2018, be-nodes
3564 bunches, 20k mppb
20 slices per bunch
3 turns wake, chromaticity
mpi=‘circulat_full_ring_fft’

## Slide 25: Simulation performance
Wake calculations are parallelized to one turn segments
  Number of wake turns has minor effects
  Linearly proportionally to the total number of slices in the simulation
  Further improvements possible
    Direct convolution parallelization scales as 1/sqrt(N_cores/(all_wake_turns))
    Accumulated wake approach allows separate cores or node(s) for long range wakes
    etc.

## Slide 26: Outline
Background
Wake algorithms
Benchmarking
Performance
Applications

## Slide 27: Good enough for the FCC transverse feedback studies?
The goals were:
  Study CBI instability mitigation of the baseline damper
  Probe impedance/intensity margin given by the feedback system

## Slide 28: Good enough for the FCC transverse feedback studies?
The goal A: Stairgforward
  Full FCC-hh beam simulations including a filling pattern, multi-ten-turn-wakes and the detailed damper model
LHC ADT PyHEADTAIL model
FIR filters are the “soul” of the ADT. Exactly same filters can be used both in the simulations and the machine
(pyJapc interface).
Damper gain scans for different chromas and planes
for verification of the damper performance

## Slide 29: Good enough for the FCC transverse feedback studies?
The goal B: The code is sufficient, but the challenges arise from physics at very high intensities

## Slide 30: How feedback simulations could help beam dynamics and R&D studies?
Example: ongoing SPS tests of the FIR filter approach for betatron phase and close orbit offset corrections
  All steps can be simulated with the developed tools
  Same feedback model can be used in all simulations
RF engineer
Accelerator physicist
Emittance growth
Tune footprint at high gain values
Instabilities
Injection emittance growth
Damping performance
Noise performance
Signal response of the filter
(simulations + network analyzer)
Straightforwardly measurable
beam properties with amplified
beam/accelerator parameters
More precise simulations and experiments about the real effects
for daily operations
Operators
and users
Performance
Operational flexibility
Safety margins

## Slide 31: Summary
Several different implementations for multibunch wakes
  Linear and circular convolution wakes allow different multibunch reference frames
  Different optimization algorithms allow efficient wakes for different filling factors
  Full beam simulations are here!
Benchmarking
  All the wake implementations pass all the tests
  The tests are included into the multibunch PyHEADTAIL branch
  The validity of the ‘convolution compression’ mathematically proven by Nicolas
Simulation tools allow to fill the gaps between the ideal and real world as well as approaches and communication challenges between different expertises
Future studies would benefit from some basic studies of the collective effects and the feedback systems
  Shapes of wake functions at short time scales
  Transparent comparison of the different theories and codes and their limits (also control theory of the feedback systems)
  Well defined measurable, relevant, performance meters for the feedback systems
  Fundamental mechanisms and limitations for the feedback stabilization from the beam dynamics point of view

## Slide 32: Thank you!

## Slide 33: Spare slides

## Slide 34: What is the difference between trackings?
Linear convolution wakes
  Definition of the turn depends on the choice of the first bunch (smoot transition between the turns)
  Source bunches for the wake kick are all the previously tracked bunches
  Beam oscillation modes are self consistently continuous between the turns because of convolution properties
Circular convolution wakes
  Well defined turns for all bunches because of turn-by-turn tracking of the beam
  Source bunches are bunches from previous turns which location rotate (circular convolution)
  Beam oscillations are self consistently continuous inside the turn, but there is discontinuity between the turns
  => “helix” correction

## Slide 35: What is the difference between tracking?
Linear convolution wakes
  Definition of the turn depends on the choice of the first bunch (smoot transition between the turns)
  Source bunches for the wake kick are all the previously tracked bunches
  Beam oscillation modes are self consistently continuous between the turns because of convolution properties
Circular convolution wakes
  Well defined turns for all bunches because of turn-by-turn tracking of the beam
  Source bunches are bunches from previous turns which location rotate (circular convolution)
  Beam oscillations are self consistently continuous inside the turn, but there is discontinuity between the turns
  => “helix” correction

## Slide 36: Benchmarking
003b_rigid_beam_test__circular_convolution.py
Comparison of different linear convolution wake implementations
  mpi=‘circular_mpi_full_ring_fft’
  Independent minimalistic code with an uniformly sliced ring
Relative differences in the slice or bunch positions < 10-12 after the tracking

## Slide 37: Performance of the different algorithms
N2 algorithms are efficient when filling factor is low
Ntot log(Ntot) algorithms faster when over 2-15% filling factor
  Circular convolution wake algorithm is the fastest
Note the log-log scale!
N2 algorithms
Ntot log(Ntot) algorithms