## Slide 1: Inner detectors @CPPM
Eric Vigeolas 18/07/2018

## Slide 2: Long history @ CPPM
For the first time hybrids pixel sensors was used in a collider with Delphi experiment @ LEP (1994)  CPPM had an important role in the mechanic, services, electronic design and integration
Atlas Pixel detector (2006)
IBL 4th layer (2014)
Involvement in the ITK/Pixel detector (2024)

## Slide 3: ITK Pixel detector
ITK pixel detector will the biggest detector we ever built  more than 8k modules ~10m^2 of Si
Assembly rules and technics will be adapted  lot of parallelization

## Slide 4: Mechanical design
Most of our detectors are driven by minimizing the radiation length, preventing thermal runaway, high level of coverage and stability
Cooling
Stability
Radiation length

## Slide 5: Material
Huge amount a carbon foam and composite material used
Thin structure (~0,15mm) with large opening for material saving
Thin services including cooling pipes

## Slide 6: Geometry
Modules overlap R/Phi and Z  Complex insertions and integration scheme
Recently we introduced truss beam inspired from Alice vertex detector

## Slide 7: Stability, Temperature
Large possibilities of measurements @ CPPM:
  Thermal conductivity
  CTE
  Metrology
  Thermo-mechanical stability
35µm/ΔT 15°C

## Slide 8: Thermo-mechanical measurements

## Slide 9: Complex assembly scheme
Required overlaps involve complex geometries and assembly processes
Attachment compound development involve frequently the need to find a way to rework (large number of module to assemble
With ITK new problem appear like assembling 8k modules in two year (parallelization, process control)

## Slide 10: Cooling Service design
Thin wall cooling pipes was designed @ CPPM, it include the development of bending technics and joining technics
Specific fittings was designed and qualified a high level of reliability have been reach on IBL
Welding
Brazing
Bending

## Slide 11: Mechanical Team: 20 people are involved in projects from sea to space
Project management
Design
Atlas
LSST
Km3Net
Imagerie
Euclid
Underwater telescope
Camera for Telescope
Space focal plane
TEP/CT
Pixel detector
WorkShop

## Slide 12: Thank you for your attention