## Slide 1: Update on K-modulation beta-beat measurements
Alexander Huschauer, Frank Tecker
with many thanks to the OP crew for the support!
Introduction
Measurement results
Comparison to MAD-X

## Slide 2: Introduction
Changing quadrupole gradient by ∆k
only depends on tune measurement precision and ∆kL model-independent!
transfer function must be well known – hysteresis!
PS low-energy quadrupoles (type 401/402) are coils only
harmonic quadrupole excitation => reduce errors
=> Tune change => Beta

## Slide 3: Approximation error
Difference depends on tune and excitation amplitude
Was in the range 0.2-2% for presented data from last year
F. Zimmermann

## Slide 4: Analysis
5-parameter fit:
Consistency checks (some acquisitions identical (?))
Average of several (4) measurements
Errors propagated from statistical fit error (for the approximative calculation)
Horizontal fit results
QF
QD

## Slide 5: Beta-beating measured (6.19/6.22)

## Slide 6: Beta-beating measured (6.19/6.22)
Some locations with large beating
Maybe off-centre in quad
=> orbit changes and sextupole feed-down also changes tune ?

## Slide 7: Beta-beating measured HOR (6.19/6.22)
amplitude X: 0.07

## Slide 8: Beta-beating measured VERT (6.19/6.22)
amplitude X: 0.08

## Slide 9: Beta-beating measured H/V (6.19/6.22)
meanX=0.9992 meanY=1.0005
=> Magnet calibration errors small
amplitude X/Y: 0.07/0.08

## Slide 10: Conclusion
analysis with approximation has 1-2% error
Residual beating of ~5% in both planes measured
Measured beating shows some outliers
orbit changes and sextupole feed-down also changes tune ?
Orbit measurement to be included
Interesting to measure: at 6.21/6.24 / bare machine / low chroma

## Slide 11: Spares

## Slide 12: Beta-beating measured HOR (6.19/6.22)
amplitude X: 0.04

## Slide 13: Beta-beating measured VERT (6.19/6.22)
amplitude X: 0.08

## Slide 14: First try
expected sine tune variation
cropped sine due to strong coupling
skew quads used to decouple the planes
good sensitivity for decoupling

## Slide 15: Uncoupled!
PR.QSKODD/EVEN 0.40 / -0.38 A
sinusoidal tune variation
excitation amplitude reduced
2 campaigns: QFN/QDN, QFW/QDW
Tunes H 6.21 / V 6.24

## Slide 16: Quadrupole excitation
cycle with long injection flat bottom
tunes flattened
sine function added to individual quadrupoles

## Slide 17: Beta-beating measured 2017 (vs. 6.21/6.24 nom.)