## Slide 1: TDAQ for the Deep Underground Neutrino Experiment (DUNE)
Giovanna Lehmann Miotto (CERN)

## Slide 2: Foreword
The DUNE TDAQ doesn’t exist…
... We are eagerly awaiting your ideas on how to design and implement it!

## Slide 3: Outline
Deep Underground Neutrino Experiment (DUNE) parameters and challenges
Conceptual design of DUNE data flow
  Front end
  Module level trigger
  Event building
  Event filter
Predesign prototyping studies:
  ProtoDUNE-SP
DUNE DAQ control & monitoring
  Challenges and ideas

## Slide 4: DUNE parameters and challenges
When designing a TDAQ system it’s essential to:
have a broad understanding of what the experiment wants to achieve;
understand the detection principles and front-end electronics;
understand the constraints in which the TDAQ will live.

## Slide 5: DUNE - Physics
http://dunescience.org

## Slide 6: DUNE - Facility
Accelerator generating intense neutrino beam
Near detector measuring neutrinos close to source
Far detector 1300 km away from source and 1.48 km underground
TDAQ: no quick access and no large host lab in the vicinity!

## Slide 7: DUNE – The far detector
4 modules, each 18mx66mx17m (17 kton Lar)
Detector: TPC (slow) + photon detectors (fast)
TDAQ: 4 independent instances, synchronized to a common clock, supporting potentially different detector technologies

## Slide 8: DUNE - Signatures
Neutrino beam -> external trigger possible
Very local, rare signature
Very distributed, rare signature
TDAQ: active at “all” times!

## Slide 9: A short digression on triggering…

## Slide 10: Nomenclature
Globally triggered
  An “external device” decides that data are interesting
  There is a coherent event ID throughout the readout
  Front-end data are organized into fragments associated to the event ID
Locally triggered
  A local trigger element fires when data should be readout (e.g. signal above threshold)
  The trigger is relative to individual or groups of channels, not to the full front-end
  The readout can process incoming data to create fragments corresponding to the trigger
  There is no concept of a global event ID at the readout level
Continuous readout
  The front-end sends data to the readout at a fixed rate, irrespective of the data content
  Data rate and data size (if there is no zero suppression) are constant in input
  There is no indication for the readout on how to group front-end data into fragments corresponding to a physics event

## Slide 11: Use cases for different readouts
Colliders
  Normally use global trigger: if something interesting has been seen somewhere, take all the data corresponding to that bunch crossing
Large distributed telescopes
  Often use local trigger: readout data for the portions of the detector that have seen something
Very slow detectors
  Sometimes use continuous readout: sample the analogue signals at a fixed rate and let the downstream DAQ decide whether there were any interesting signals

## Slide 12: Globally triggered
storage
Processing
Processing
Data Collection
ADC
ADC
ADC
Processing
Processing
ADC
ADC
ADC
ADC
ADC
ADC
TRIGGER
Front-End
Readout
Event Building
Event Filtering
Event Logging
N channels
N channels
N channels
data extraction
data formatting
data buffering
event assembly
event buffering
event rejection
event buffering
file storage
file buffering
data digitization
data buffering

## Slide 13: Globally triggered: ATLAS@LHC

## Slide 14: An event

## Slide 15: Locally triggered
storage
Processing
Processing
Data Collection
Processing
Processing
Front-End
Readout
Event Building
Event Filtering
Event Logging
N channels
data extraction
data formatting
data buffering
event assembly
event buffering
event rejection
event buffering
file storage
file buffering
data digitization
data buffering
ADC
ADC
ADC
TRG
ADC
ADC
ADC
TRG
ADC
ADC
ADC
TRG
N channels
N channels
???
???
???

## Slide 16: Locally triggered: Auger observatory

## Slide 17: Continuous
storage
Processing
Processing
Data Collection
ADC
ADC
ADC
Processing
Processing
ADC
ADC
ADC
ADC
ADC
ADC
CLOCK
Front-End
Readout
Event Building
Event Filtering
Event Logging
N channels
N channels
N channels
data extraction
data formatting
data buffering
event assembly
event buffering
event rejection
event buffering
file storage
file buffering
data digitization
data buffering
???
???
???
???

## Slide 18: Not events, but rather a movie
By Rick Harrison (license)

## Slide 19: … end of digression, back to DUNE

## Slide 20: TPC schematic
charged particle ionizes argon
ionization electrons move
under E–field to wire-planes
electron drift lines from cathode to wires
(field lines from wires (fill white bits) not shown)
E0
E1
E2
E2>E1>E0
drift-time
a = cross u
b = cross v
c = cross x
drift-time
a b c
u
v
x
p
d
p~d~3-5 mm
Bunneman, Cranshaw, Harvey, Can. J. Res. 27 (1949) 191
Gatti, Padovini, Quartapelle, Greenlaw, Radeka
IEEE Trans. NS-26 (2) (1979) 2910]
FADC
FADC
FADC
Slide from S. Pordes

## Slide 21
induction
plane
Signals
collection
plane
signals
What the raw signals look like (16 sequential wires)
Slide from S. Pordes

## Slide 22: DUNE Front-End readout
DUNE mixes continuous readout (TPC) and locally triggered readout (Photon detectors)
  TPC sampling rate = 2 MHz
  Photon detectors sampling rate = 150 MHz (but data only when there is a signal)
  TPC wires (single phase technology) = 384000 per cryostat
  384 k channels (12 bit ADC) @ 2 MHz = 9.2 Tb/s (dominates data size)
  Adding all up the TDAQ has to sustain a readout of ~5 TB/s
    Sounds very much like HL-LHC…

## Slide 23: DUNE post-readout data selection
It is responsibility of the post-readout system to combine data snippets into time windows of interesting detector regions
  In DUNE the ”window” can be anything from few ms to ~100s for the supernova core collapse
  The data corresponding to a trigger can have a size ranging from << 1 GB to ~100 TB!
The rate of events varies widely from few Hz to <<1/month
The data selection needs to accumulate a view on the activity of the detector over several seconds to identify some signatures (SNB)
  The readout needs to have very large buffers to accommodate for the decision latency

## Slide 24: Conceptual design of the DUNE data flow

## Slide 25: DUNE data flow

## Slide 26: Front end – data flow interfaces
Many similar modular elements (~100 / module)
Frontend
Detector electronics
Module level trigger
Event builder
Trigger primitives storage
data
Trigger candidates
data
Trigger primitives

## Slide 27: Front end - functional blocks
Data reception
Noise filtering
Hit finding & archiving
Trigger candidates
Data buffer (~0.5 TB)
Data EB output
Data store
(2 TB)
EB request
compress?

## Slide 28: DUNE data flow

## Slide 29: Module Level Trigger– data flow interfaces
1 per module
Module level trigger
Calibration systems
Front end
Event builder
timestamp
Trigger candidates
Trigger decision / inhibit
External Trigger
Trigger decision

## Slide 30: Module Level Trigger - functional blocks
Candidates reception
Time-space correlation
Calib signals reception
Trigger logics
Trigger decision
EB I/O
Trigger data buffer
Inhibit signals

## Slide 31: DUNE data flow

## Slide 32: Event builder – data flow interfaces
Trigger decision
Inhibit
One orchestrator, few similar building elements (~10 / module)
Event Builder
Module level trigger
Module level trigger
Front end
Data storage
data
data
data

## Slide 33: Event builder - functional blocks
Trigger reception
Trigger/EB assignment
EB book keeping
Event Building
Data reception
EB request handling
Trigger inhibit
Trigger assignment
Files handling
orchestrator
event builders

## Slide 34: DUNE data flow

## Slide 35: Filter – data flow interfaces
Several similar elements (~10 / module)
Filter
External trigger
Data storage
Get data
information
Put data

## Slide 36: Filter - functional blocks
Data retrieval
Data filtering
Data compression
Data output
Ext trigger logics

## Slide 37: Predesign prototyping studies
The ProtoDUNE Single Phase project

## Slide 38: ProtoDUNE Single Phase
Largest monolithic single phase LArTPC detector and test beam built to date:
Goal is to validate detector design, construction and data acquisition solutions for DUNE’s Single Phase Far Detectors
  10x10x10 LArTPC
  800 tonnes of LAr
  Located on surface → external trigger needed
Extreme schedule:
  Project launch: Q1 2016
  Data taking with beam: Q4 2018
DAQ approach: use ready-to-use solutions
  minimise development time

## Slide 39: Data flow and volume
LArTPC → ionisation tracks are collected by the wires of the Anode Plane Assemblies (APAs)
Cold electronics in the detector digitise signals recorded by wires at 2 MHz
Warm interface boards (WIBs) then group the resulting channels into frames, each of which consists of a single 500 ns time slice of the grouped channels (128 or 256)
Output via optical links to DAQ:
  2x 9.6 Gb/s or 4x 4.8 Gb/s supported, depending on readout solution
  Continuous timestamped data frame streams
Each APA (2560 channels) is read out by 5x WIBs for a total payload of about 74 Gb/s
APA
WIBs

## Slide 40
By M. Brice, CERN

## Slide 42: ProtoDUNE SP TDAQ
Readout with large buffers to allow exploiting the spill structure
Trigger logics implemented in a custom board
  Inputs from beam instrumentation, muon tagger, photon detectors
Data compression to reduce storage and network needs
An event is a 3 ms window of all data contained in the readout corresponding to the timestamp of a trigger
Trigger
Event Builder
Storage
ADC
ADC
ADC
ADC
ADC
ADC
Loc Trigger
Readout
Readout
Trigger signals
Readout
Readout
Ext info
Event Builder
APAs
Photon Detectors
~430 Gb/s
< 20 Gb/s

## Slide 43: TDAQ Hardware setup
Storage servers
Disk arrays
Disk arrays
Timing
RCE
Trigger
BI interface
VST
Network, files servers, run control, monitoring, FELIX, board readers
Safety, power control, UPS

## Slide 44: ProtoDUNE SP TDAQ
Not a small DUNE TDAQ but an excellent test bench for TDAQ technologies for DUNE
  Timing system prototype
    Global time via White Rabbit
  Readout system prototypes
    Buffering in FPGA or server
  Compression scenarios
    On FPGA or SW
  Hit finding
    SW or FW
  Buffering
    RAM + SSD or new approaches such as Intel Optane Memory+QLC 3D NAND storage

## Slide 45: An example: FELIX based readout
P-to-p link throughput ✓
10 links -> host memory over 1 FELIX card ✓
  Need to switch to PCIe4 or greater to do 20 links
HW aided data compression using Intel QAT technology ✓
FLX-712 card
Mellanox ConnectX-5
Full I/O over InfiniBand for ProtoDUNE ✓
  Need much less network I/O for DUNE
  Need longer and high throughput storage (but new technologies go in the right direction)
    Joint R&D with ATLAS, CMS, DUNE and Intel on DAQ DB

## Slide 46: SW triggering from FELIX readout
Get the complete stream of raw data
Reformat WIB frames to
  Expand 12 bit ADCs into 16 bits
  Reorder wires in order to select only collection plane
Identify each time a wire has a “hit”
Combine information of hits in order to form track candidates
Implement a sw based trigger logics
This work is ongoing now! (next few slides from P. Rodrigues)

## Slide 47: Data Reordering
1 WIB frame = 464 B => 256 ADCs + headers @ 2 MHz
Unpack collection channels with AVX2 code
Spoiler: this appears to be the biggest CPU consumer

## Slide 54: SW triggering next steps
Generate trigger candidates from hits
Form a module level trigger
Carry out data reformatting in FPGA
  Measure benefits
Move the complete hit finding into FPGA
  Measure benefits and assess any drawbacks

## Slide 55: DUNE DAQ Control & Monitoring

## Slide 56: What is special about DUNE?
Complexity and size of a large collider experiment
  Uptime <<30%
Uptime requirement of a “rare events” experiment (gravitational waves, supernovae detectors, double beta neutrino decays, etc
  Uptime “100%”
Accessibility of installation quite limited
The combination of those three doesn’t work well together…
The whole system must be conceived and setup in a different way
  Redundancy and fail over mechanisms
  Automated anomaly detection and recovery
  Remote monitoring and control
The control and monitoring system will have a predominant role for the success of the DUNE TDAQ (i.e. the experiment)

## Slide 57: Few guidelines
Components must be as loosely coupled as possible
  Allow for tolerance to and recovery of local problems without affecting the data taking
Single points of failure (module level trigger, EB orchestrator) must have a running backup in standby mode
Running conditions must be as stable as possible
  Forget about stopping runs and regular full reconfigurations of the system
Assessment of data quality must be immediate and continuous
  Automated correction for bad data
System administration (computers, networks, storage) and repair must happen on an active system, i.e. be staggered and non intrusive
All tools need to be thought from the start for remote operators
  Heavily rely on web, but still ensure security and safety

## Slide 58: Design of the Control and Monitoring for DUNE
Do we know how to do it?
  Not really…
  Ideas are mainly on paper and need to be tried out
  System and software engineering skills are essential to get this right
How would you go about designing and implementing such a system?

## Slide 59: Summary and Outlook
DUNE is a new giant experiment scheduled to start taking data in 2025
The TDAQ system is being designed now
  Challenging readout performance
  Very challenging operational requirements
Predesign prototyping allows us to identify suitable technologies and validate ideas
  Advancing well on the main data flow path
  Still embryonic stage for the control and configuration
If ISOTDAQ awoke your desire of becoming a TDAQ expert
  DUNE is surely an experiment where you will be able to challenge your skills!