## Slide 1: Design and Implementation of a Monitoring System
Serguei Kolos
(University of California, Irvine)

## Slide 2: The Outline
Introduction: The Key Principals of Online Monitoring
Monitoring in a DAQ system
Scaling up to the size of the HEP experiments
Summary & Final Remarks

## Slide 3: What Monitoring is used for?
A good Monitoring System should be capable to answer all possible questions about the system being monitored:
  What happened?
  Where that happened?
  When that happened?
There are some questions it is not competent to answer, e.g.:
  What to do next?
But it tries to provide all possible information to those who can answer such questions

## Slide 4: How a Monitoring System does its job?
All of us are equipped with a perfect monitoring system:
  We have 5 types of sensors for detecting events in the outside space
  The information is transferred via nerve fibers to our brains which initiates an appropriate reaction
  Some information is memorized for the future reference
Monitoring for a complex HW+SW system acts in a similar way:
  The HW and SW elements play a role of sensors by publishing their status to the Monitoring System
  The Monitoring System transports this information to the system “brains”:
    A Human operator
    An Expert system
  It also records the monitoring information for a later in depth analysis

## Slide 5: The Simplest Monitoring Code Sample
print(“Hello, World”)
This is a monitoring message
This is the monitoring API function

## Slide 6: Is the Hello.py application well designed?
print(“Hello, World”)
The issue is that the “print(…)” function provides both the API and the implementation, which are tightly bound together
The destination for the messages passed to “print(…)” is fixed
Can we do better?

## Slide 7: Logging Module to the rescue
2017-02-02 16:21:13,583 INFO [hello.py:4 - <module>()] Hello, World
import logging
logging.info(“Hello, World”)
Use the standard well-designed API
A lot of extra useful information is available for free
The message destination can be changed without
touching the application code
The output format can be easily changed
logging.basicConfig(format='%(asctime)s %(levelname)s [%(filename)s:%(lineno)s - %(funcName)s()] %(message)s', level=logging.INFO)

## Slide 8: The Key Principal: Separate API from Implementation
A Message Reporting API must not depend on a particular destination of messages
Multiple destinations can be supported by different implementations of the same API
Common properties will be automatically added to all messages by the API:
  Time, Process ID, User ID, etc.
Software Application
File
Database
Message Reporting API
Network

## Slide 9: Monitoring in a DAQ system

## Slide 10: What shall be monitored in a DAQ System
System incidents:
  Expected and especially Unexpected incidents shall be immediately reported in a form of a message
System status:
  Health of individual HW & SW components:
    Resources consumption, IO rates, etc.
  Surrounding environment:
    Temperature, humidity, etc.
  Operational statistics:
    Number of triggers, number of recorded events, etc.
Data Quality Monitoring:
  Recorded physics data shall be constantly monitored for sensibility

## Slide 11: DAQ Messaging Service
Logging API is a good candidate for the DAQ Messaging Service API
There are several important considerations to be taken into account about messages:
  Messages shall contain human readable (and understandable!) explanation of the corresponding incidents:
    A shifter calling you in the middle of a night can just read it
  Messages shall be ready for machine processing:
    Every message shall contain a unique ID which corresponds to the given incident
    Messages shall contain some common automatically generated parameters:
      Time stamp, application ID, computer name, etc.

## Slide 12: Some Remarks on Time Stamps
Time Stamp is a vital property of a message and of any monitoring information in general:
  Used for correlating messages from different sources
  Used for correlating monitoring information with real-life events
The time stamp guidelines:
  Use the best possible precision (nanoseconds)
  Use UTC time when reporting
  Conversion to the human readable local time shall be done by a message displaying applications with respect to its location

## Slide 13: Message Types
CRITICAL – severe error has been detected. It can lead to system damage or affect Data Quality. Immediate attention is required
ERROR – recoverable error happened. Check the consequences
WARNING – nothing is bad so far, but system may be operating dangerously close to a certain limit
INFO – an expected incident occurred
DEBUG – shall be disabled in production system

## Slide 14: CRITICAL Messages & Alarms
A DAQ system may produce a CRITICAL message when immediate shifter attention is required:
  Such a message can be used to trigger an Alarm:
    A dedicated message display application changes the color (and the shape – for color blind people) of an appropriate item
    It can also make a sound
Do not overuse alarms:
  ‘Cry-Wolf’ effect may result in a severe system damage or data corruption

## Slide 15: Do not neglect WARNINGs
Reporting a CRITICAL event is straightforward
Deciding when to report a WARNING is much more cumbersome:
  Nothing wrong happened so far, but the system is dangerously close to a certain limit
  Requires some extra health-checking code to verify operational conditions
Warnings shall not be neglected as sooner or later they become errors:
  They can be effectively used for the future error prevention

## Slide 16: When to issue a WARNING: A real life example
RUN X:
Everything goes well so far
Chart: Trigger Farm CPU usage
| 0.763888888888889 | 0.764583333333333 | 0.765277777777778 | 0.765972222222222 | 0.766666666666667 | 0.767361111111111 | 0.768055555555556 | 0.76875 | 0.769444444444445 | 0.770138888888889 | 0.770833333333333 | 0.771527777777778
Series 1 | 50 | 50 | 50 | 90 | 90 | 50 | 50 | 50 | 90 | 90 | 50 | 50
Column1
Column2
RUN X+1:
CPU shortage causes dead-time
Chart: Trigger Farm CPU usage
| 0.805555555555556 | 0.80625 | 0.806944444444445 | 0.807638888888889 | 0.808333333333333 | 0.809027777777778 | 0.809722222222222 | 0.810416666666667 | 0.811111111111111 | 0.811805555555556 | 0.8125 | 0.813194444444445
Series 1 | 70 | 70 | 70 | 100 | 100 | 70 | 70 | 70 | 100 | 100 | 70 | 70
Column1
Column2
CPU used for physics data processing
Extra CPU used periodically for histogram aggregation
Adding new Trigger algorithm increased the average CPU usage

## Slide 17: DAQ System Status Information
A DAQ system has many numeric parameters to be monitored:
  Logging API is not convenient for that
A simple status information item can be represented in a form of a <key:value> pair:
  “key” - a unique identity of a particular information
  “value” - information value for a given moment:
    This makes it obvious that every pair has to be time-stamped
A “value” can be a simple number as well as an object :
  The object represents a state of a DAQ SW or HW element with multiple properties
  The object has a number of attributes that contain the values of the corresponding properties for a given moment in time

## Slide 18: Information Sharing: A Simple Provider API
interface InfoRepository {
void registerInfo(String id, InfoObject obj);
void unregisterInfo(String id);
}
A SW Application can register any information object with a unique ID:
  Afterwards it simply keeps updating the attributes of the objects in a usual way to reflect the status of the corresponding SW or HW component
The Interface intentionally does no expose any details of how information will be handled:
  This will be defined by an implementation

## Slide 19: Information Sharing: A Simple Consumer API
interface InfoMonitor {
  Enumeration<String> getInfoList();
  InfoObject getInfo(String info);
}
A SW Application can use the InfoMonitor Interface:
  To get a list of available monitoring information
  To get a value of an information object
Implementation of this interface is bound to the one of the InfoRepository

## Slide 20: Information Sharing: A Possible Implementation
REST – Representational State Transfer
  Client-server HTTP-based stateless communication
  Fits very well to the Status Monitoring communication model
The Web Service implements InfoRepository Interface
The HTTP Client implements InfoMonitor Interface
BONUS:
  A standard Web Browser can be used to display monitoring information
Software Application
InfoMonitor
HTTP Client
InfoRepository
RESTful Web Service

## Slide 21: A DAQ specialty: Data Quality Monitoring

## Slide 22: Data Quality Monitoring
Watching out the behavior of the DAQ system itself is not sufficient:
  The DAQ may be functioning perfectly well but at the same time is taking meaningless data, for example, due to wrong calibration constants
A dedicated service is required for checking that:
  Detector readout provides meaningful data
  Trigger does reasonable selection

## Slide 23: Data Quality Monitoring: Input Data
There are two main types of information that can be used for DQ Monitoring:
  A picture of a reconstructed physics event
  Histograms that accumulate data from a statistical sample of raw physics events
Only eyes of a true Experts can make sense of such data

## Slide 24: Data Quality Monitoring Automated: Step 1
InfoRepository interface can be used to register histograms:
  Histogram is just an object with a number of specific attributes
Histogram Analyzer registers a DQ Status object per histogram:
  Periodically reads the corresponding histogram and executes DQ Algorithm that updates this DQ Status
Event Analyzer
InfoRepository
Histogram Analyzer
InfoRepository
DQ Status
DQ Algorithm
InfoMonitor

## Slide 25: Data Quality Monitoring Automated: Step 2
A DQ Display application can read and display both the histograms and the DQ Statuses using the InfoMonitor Interface
Event Analyzer
InfoRepository
Histogram Analyzer
InfoRepository
DQ Status
DQ Algorithm
InfoMonitor

## Slide 26: Scaling up the Monitoring System

## Slide 27: The HEP Experimental Realm
A DAQ system of a modern HEP experiment includes:
  O(1K) computers and network devices
  O(10K) SW applications
  O(100K) HW sensors
If Monitoring APIs were properly designed they will not be affected by the scalability requirements
However the implementations of the Monitoring APIs may need to be adjusted

## Slide 28: Managing Monitoring Information in a distributed system
There are two main parameters which can be tuned for addressing scalability requirements:
  The information access model:
    Pull data vs Subscribe/Callback
  The communication model:
    Peer-to-Peer vs Client-Server
The choice of a particular model will limit a set of technologies which can be used for the implementations

## Slide 29: Information Access Models
Pull Model (synchronous communication):
  An Information Consumer requests information whenever it is required
  RESTful Web Service is a good example of a technology which can be used to implement this access model
Subscribe/Callback model (asynchronous communication):
  An Information Consumer subscribes for the relevant subset of information to get notified when the information is updated
  RESTful architectur can not be used because a subscription changes the state of the Information Provider
  One can consider using one of the existing IPC systems:
    Low-level Libraries: ZeroMQ, Boost ASIO, etc.
    High-level communication brokers: Ice from ZeroC, CORBA: TAO, omniORB

## Slide 30: Communication Models
Peer-to-Peer:
  Information Providers announce available information
  Information Consumers connect to the Providers to read information or subscribe for updates
Client-Server:
  Information Providers send their information to the server periodically or on demand
  Information Consumers connect to the server to read information or subscribe for updates

## Slide 31: Which one is the best?
Peer-to-Peer
Has no single point of failure
Scales better
Uses more connections
Providers are exposed to Consumers due to the direct connections
More difficult to implement and maintain
Client-Server
Separates Providers from Consumers
Simplifies information access
Implementation and maintenance is simpler
Has a single point of failure
Scalability requires multiple servers and additional HW resources

## Slide 32: A Client-Server Implementation Example
InfoRepository Interface implementations periodically save monitoring information to a database
A Web Browser can be used to query the database via the RESTful Web Service service and display the information
Software Application
InfoRepository
Database
Web Browser
Software Application
InfoRepository
Software Application
InfoRepository
RESTful
Web Service

## Slide 33: Monitoring Information Aggregation
Monitoring information produced by individual DAQ Applications may need to be collected to provide high-level system status, e.g.:
  Aggregating counters produced by individual computers of the Trigger Computer Farm one can access a complete state of the Trigger system
  Aggregating histograms from all Trigger applications will give accumulated statistics for all processed events

## Slide 34: Information Aggregation Implementation Options
The way of aggregating information may depend on the data access and communication models used for the Monitoring system implementation
Per-to-Peer communication model is used:
  Information Aggregator will retrieve data from all Providers
Client-Server communication model is used:
  Information Aggregator will retrieve data from the central server
Subscribe/Callback mechanism is available:
  Information Aggregator will subscribe for the information changes and do the aggregation only when information is updated

## Slide 35: Archiving Monitoring Information
Ideally all monitoring information shall be archived to a permanent storage:
  Do post mortem analysis
    Special attention should be paid to WARNINGs
  Investigating problems
Conceptually Archiver is just a special type of the Information Consumer
In practice the task is non-trivial due to the huge amount of information
It might be feasible to have multiple Archivers for different information types:
  Histograms, errors, operational status

## Slide 36: Bringing These All Together
A Monitoring system should consist of a number of independent services:
  More convenient for handling different types of monitoring information:
    E.g. messaging system vs status monitoring
  More simple to address scalability requirements
  Easier for development and maintenance
Information
Archiving
DAQ System
Information Sharing
Data Quality
Assessment
Information
Aggregation
DAQ Messaging
Alarms Display

## Slide 37: Choosing Technologies for A Monitoring System Implementation

## Slide 38: Commercial Solutions: SCADA systems
Supervisory Control and Data Acquisition
  It is primarily dedicated for control but does the monitoring as well
  Modern implementations scale well for small and mid-size systems
A SCADA system can be implemented using LabView:
  Graphical programming language for the system design
  Powerful and configurable graphical interface
Is used mostly for HW control and monitoring
  May not fit well to the DAQ specific monitoring, i.e. Data Quality

## Slide 39: The spectrum of the IPC technologies
Ice from ZeroC
CORBA: TAO, omniORB, …
Messaging systems: Qpid, ActiveMQ, RabbitMQ, ...
RESTful Web Services
Libraries: Boost ASIO, ZeroMQ, ACE, …
Socket API, TCP, RDMA, …
Performance overhead
Development and maintenance cost
In realty situation is slightly more complicated:
  Maintenance cost and performance overhead very often depend on the implementation quality
A choice would depend on a particular system requirements:
  System size, Programming languages, available resources, implementation time scale, etc.

## Slide 40: Data format for network transfer
For HTTP communication Json is the natural format:
  { “CPU”: 90, “Memory”: 4.3, … }
Advantages of Json:
  Simple, Human readable, self-contained
However performance is the weak point:
  Parsing Json is CPU-hungry
  Transferring attributes names adds noticeable overhead to the amount of data passed over network
Compact protocol buffer format can be considered as an alternative:
  E.g. google/protobuf, binary Json, etc.

## Slide 41: Data Archiving Technologies
A choice strongly depends on the requirements of a particular experiment
Large HEP experiments generate O(1)TB of monitoring information per year
Traditional (SQL) databases are not good for storing and indexing such amount of data
Big Data approach is the new trend in this area
  Hadoop, Teradata, Cassandra and many others

## Slide 42: Visualization Technologies
GUI Frameworks/Libraries
Normally is bound to some specific programming languages:
  Qt – C++, Python
  Swing – Java
Has to be installed in a binary form:
  Platforms compatibility
  3rd party libraries
Very good performance
WEB Browsers
Visualization is easily customizable (javascript, CSS, etc.)
A lot of out-of-the-box graphical visualization libraries are available
No additional software required on a client computer
Available all over the globe
Performance may not be adequate for real-time systems

## Slide 43: Web-based ATLAS Online Monitoring Customizable Dashboard implemented using Grafana

## Slide 44: Web Browser Visualization Technologies: Physics Special
Physicist needs histograms, which limits a range of suitable visualization technologies
Starting from Version 6 ROOT contains JavaScript library for histograms visualization in Web browsers:
  JSROOT
  https://root.cern.ch/root/htmldoc/guides/JSROOT/JSROOT.html

## Slide 45: Summary & Final Remarks

## Slide 46: The Key Points to Keep in Mind
A well-designed and complete Online Monitoring API is a pre-requisite for implementing a DAQ system:
  Use standard Monitoring APIs as much as possible:
    e.g. Logging API
  Think carefully when designing a custom API:
    It shall not depend on a communication technology
    It shall not change when a data access or communication model would need to be changed
It is acceptable that final implementations of Monitoring APIs are not available at the very beginning:
  Any way they may need to be changed in the course of the DAQ system development

## Slide 47: Monitoring vs DAQ
A properly designed monitoring system will help to keep things under control even during the DAQ system development:
  Reduces time for testing and debugging of the DAQ system
  Feedback will help fixing issues in the Monitoring system itself
Monitoring is often considered as an ad hoc system, which can be developed at leisure when a system to be monitored (e.g. DAQ) is ready:
  Big mistake!