## Slide 1
photo: J. Wenninger
http://cern.ch/fcc
FCC
PS
SPS
LHC
photo: J. Wenninger
HE-LHC
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; ARIES, grant agreement 730871; and E-JADE, contract no. 645479
Future Circular Collider Study
Overview and Design Status
M. Benedikt
gratefully acknowledging input from FCC coordination group,
global FCC design study team and all other contributors

## Slide 2
Future Circular Collider Study - Scope:
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  long-term goal, defining infrastructure requirements
~100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
HE-LHC with FCC-hh technology
p-e (FCC-he) option, IP integration, e- from ERL
~16 T  100 TeV pp in 100 km
HE-LHC

## Slide 3
HE-LHC integration aspects
Integration and design strategy:
Development of optimized 16 T magnet, compatible with HE LHC requirements
New cryogenic layout to limit QRL dimension
  LHC tunnel diameter 3.8 m
  Working hypothesis for HE LHC design:
  No major CE modifications on tunnel and caverns
  Similar geometry and layout as LHC machine & experiments
  Maximum magnet cryostat diameter ~1200 mm
  Maximum QRL diameter ~830 mm

## Slide 4
16 T dipole design evolution
Cosine-theta (baseline)
Block-type coils
Common-coils
2015 2017
800 mm 600 mm
Coil optimization and margin 18  14%
Inter-beam distance 250  204 mm
Stray-field < 0.1 T at cryostat
Half-sector cooling instead of full sector (as for LHC)
to limit cross section of cryogenic distribution line
higher heat load and integration limitations:
8 additional 1.8 K refrigeration units wrt. LHC
8 new higher-power 4.5 K cryoplants

## Slide 5
Worldwide FCC Nb3Sn program
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduction of coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
After only one year development, prototype Nb3Sn wires from several new industrial FCC partners already achieve HL-LHC performance
Conductor activities for FCC started in 2017:
Bochvar Institute (production at TVEL), Russia
KEK (Jastec and Furukawa), Japan
KAT, Korea
Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy
University of Freiberg, Germany
  In addition, agreements under preparation:
  Bruker, Germany
  Luvata Pori, Finland
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 6
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built from 2018 – 2022
Russian 16 T magnet program launched by BINP recently.
Swiss contribution
CHART
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 7
15 T dipole demonstrator (US-MDP)
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin

## Slide 8
16 T ERMC construction at CERN
First ERMC coil winding
Coil Reaction Tool
Coil Impregnation Tool
Aluminum shell
Magnet yoke
Axial rods
Dummy coils
Coil fabrication
  Winding of the first coil has been completed
  Preparation for reaction on-going
  All tooling for coil production ready
Magnet assembly
  components and tooling ready
  Dummy assembly to characterize the structure behavior on-going.

## Slide 9
Technical Schedule for each of the 3 options
20
22
24
26
28
30
32
34
38
40
Civil Engineering FCC-hh ring
Dipole short models
16 T dipole indust. prototypes
16 T dipoles preseries
16 T series production
SC Magnets
CE FCC-ee ring + injector
FCC-hh
FCC-ee
HE-LHC
Strategy Update 2026 – assumed project decision
Installation HE-LHC
LHC Modification
42
Technical Design Phase
36
Installation + test FCC-ee
Installation + test FCC-hh
CE TL to LHC
LHC Removal
Dipole long models
Injector
schedule constrained by 16 T magnets & CE
→ earliest possible beam operation dates
FCC-ee: 2039
FCC-hh: 2043
HE-LHC: 2040 (with HL-LHC stop LS5 / 2034)
16 T magnets
FCC-hh
FCC-ee
HE-LHC

## Slide 10
Further Planning – CDR production
Compact summary CDRs 1, 2, 4, 6 ready by November 2018
CDR long technical volumes 3, 5, 7:
  Collection of input (from status June 2018) during July – October 2018.
  Overall volume editing November 2018 – January 2019
  Proof reading and approval February – March 2019