## Slide 1: Transverse Mode Coupling Instability in LHC and HL-LHC
D.Amorim, S.Antipov, N.Biancacci, X.Buffat, L.Carver, E.Métral
Work Package 2 meeting
24/07/2018
Many thanks to:
T.Levens, A.Mereghetti, B.Salvant, M.Soderen, D.Valuch, LHC and Injectors Operations

## Slide 2: Stability in the HL-LHC era
At top energy, the collimators are the main contributors to the impedance
  54 per beam, 11 in IR7 betatron cleaning region
  In IR7: made of resistive materials (Carbon Fiber Composite), tightest gaps (<2mm)
Low resistivity collimators will start to be implemented during LS2
LHC collimation system
HL-LHC impedance budget at top energy

## Slide 3: TMCI threshold in LHC / HL-LHC
Investigate the single bunch stability limits
  Transverse Mode Coupling Instability happens when two bunch oscillation modes couple at high intensity
  It could be a single bunch intensity limitation as HL-LHC will use brighter beams
Goal: measure the tune-shift as a function of intensity to assess it
  Simulations using the LHC and HL-LHC impedance models
  Measurement in the machine: need to work with LHC operational constraints
  Try to reproduce an equivalent HL-LHC impedance in the LHC
Showcase the benefits of the impedance reduction for HL-LHC

## Slide 4: Five impedance scenarios studied
‘LHC ft 2017’: 2017 LHC flat top nominal configuration
‘LHC ft 2017, TCSGs at 14’: 2017 LHC flat top with open TCSGs gaps
  Reproduce an equivalent HL-LHC impedance
‘HL-LHC 48cm LS2.2 2 TCPs’: LS2 collimators upgrade
  Mo coating of 4 TCSGs + MoGr upgrade of 2 TCPs
‘HL-LHC 48 cm MoGr IP7’: TCSGs in MoGr (without coating)
  TCPs stay in CFC
‘HL-LHC 48cm Baseline’: HL-LHC baseline scenario
  Mo coating of all IR7 TCSGs + MoGr upgrade of 2 TCPs
 | TCPs | TCSGs
LHC ft 2017 | - | -
LHC ft 2017, TCSGs at 14 | - | -
HL-LHC 48cm LS2.2 2 TCPs | 2 in MoGr | 4 in MoGr with Mo coating
HL-LHC48 cm MoGr IP7 | - | All in MoGr (no coating)
HL-LHC 48cm Baseline | 2 in MoGr | All in MoGr with Mo coating
 | TCPs | TCSGs
LHC ft 2017 | - | -
 | - | -
HL-LHC 48cm LS2.2 2 TCPs | 2 in MoGr | 4 in MoGr with Mo coating
HL-LHC48 cm MoGr IP7 | - | All in MoGr (no coating)
HL-LHC 48cm Baseline | 2 in MoGr | All in MoGr with Mo coating
Simulated + Measured
Simulated
Material | Resistivity [] | Purpose
CFC | 5000 | Present in LHC
MoGr | 1000 | Baseline bulk
Mo | 53 | Baseline coating
TiN | 400 | Alternative coating
Cu | 19 | Alternative coating
Material |  | Purpose
CFC | 5000 | Present in LHC
MoGr | 1000 | Baseline bulk
Mo | 53 | Baseline coating
TiN | 400 | Alternative coating
Cu | 19 | Alternative coating
Material and coatings resistivity
From N.Biancacci, IPAC18, WEYGBE4
Notes: HL-LHC48 cm MoC IP7 ???

## Slide 5: Impedance models for the five cases
‘LHC ft 2017 TCSGs@14’ is close to ‘HL-LHC 48cm LS2.2 2 TCPs’ and ‘HL-LHC 48cm MoGr IP7’
  Approximation valid in the low frequency domain and in the 10MHz – 10GHz range
Notes: Change plot to simplified one

## Slide 6: DELPHI simulations for TMCI
Single bunch stability simulations with the Vlasov solver DELPHI
Scan in bunch intensity to find the TMCI threshold for each impedance scenario
TMCI clearly appears at Q’=0, without damper
  It also affects the modes for low positive ()
Other chromaticities and damper gains were simulated
  For these cases, the tune-shift vs. intensity is a relevant observable
  For chromaticities , the tune-shifts vs. intensity are similar
Parameter | Value (LHC) | Value (HL-LHC)
Bunch intensity scan / p.p.b | 0…0.7e12 | 0…1e12
Qs | 2.1e-3 | 2.0e-3
Energy / TeV | 6.5 | 7
Q’ scan | -5…5 | 0…20
Damper gain scan | 0 / 0.01 | 0 / 0.01
DELPHI simulations parameters

## Slide 7: Scenario: LHC ft 2017
DELPHI Simulations
Mode 0
Mode -1
LHC flat top 2017 nominal settings
  TCPs at
  TCSGs at
TMCI threshold at
2.6
Notes: Show a first plot without HLLHC results

## Slide 8: Scenario: LHC ft 2017, TCSGs at 14
DELPHI Simulations
Mode 0
Mode -1
LHC flat top 2017 with retracted TCSGs
  TCPs at
  TCSGs at
TMCI threshold at
Retracted TCSGs clearly improve the TMCI threshold
5.0
Notes: Show a first plot without HLLHC results

## Slide 9: Scenario: HL-LHC 48cm LS2.2 2 TCPs
DELPHI Simulations
Planned post LS2 configuration
  2 TCPs in MoGr
  4 TCSGs in Mo coated MoGr
    The 4 TCSGs are the main impedance contributors
TMCI threshold at
Low resistivity materials and coatings clearly improve the TMCI threshold
6.4
Notes: TCPs and TCSGs sigmas ?

## Slide 10: Scenario: HL-LHC48 cm MoGr IP7
DELPHI Simulations
HL-LHC with all IR7 collimators in MoGr
TMCI threshold at
Lower TMCI threshold compared to previous case because of the absence of coatings on the TCSGs
6.0
Notes: TCPs and TCSGs sigmas ?

## Slide 11: Scenario: HL-LHC 48cm Baseline
DELPHI Simulations
HL-LHC baseline scenario
  2 IR7 TCPs in MoGr
  IR7 TCSGs in MoGr with Mo coating
TMCI threshold at
Largest increase of TMCI threshold thanks to coatings on all IR7 TCSGs
8.7
Notes: TCPs and TCSGs sigmas ?

## Slide 12: Summary of simulations results
Tune-shift vs. intensity also computed for the different scenarios
Clear TMCI threshold increase when moving the TCSGs out (LHC simulations) or coating them (HL-LHC simulations)
 | Tune-shift (DELPHI) | Tune-shift (Measured) | TMCI threshold (DELPHI) | TMCI threshold (inferred)
LHC ft 2017 | -0.32 |  | 2.6 | 
LHC ft 2017, TCSGs at 14 | -0.18 |  | 5.0 | 
HL-LHC 48cm LS2.2 2 TCPs | -0.14 | - | 6.4 | -
HL-LHC48 cm MoGr IP7 | -0.15 | - | 6.0 | -
HL-LHC 48cm Baseline | -0.11 | - | 8.7 | -
LHC ft 2017 | -0.32 |  | 2.6 | 
 | -0.18 |  | 5.0 | 
HL-LHC 48cm LS2.2 2 TCPs | -0.14 | - | 6.4 | -
HL-LHC48 cm MoGr IP7 | -0.15 | - | 6.0 | -
HL-LHC 48cm Baseline | -0.11 | - | 8.7 | -

## Slide 13: Measurement of the TMCI threshold
To ensure beam stability, measurements were done with
  Mixed mode coupling and head-tail regime as
  But tune-shift vs. intensity remains similar:
    Can compare DELPHI simulations and tune-shifts measurements
  Allows to infer the TMCI threshold
Measurement with 2 or 3 bunches per beam
  Number limited by machine protection constraints
Bunch-by-bunch tune measurement
  High precision measurement with the ADT excitation and pickup (tune resolution: )
Notes: Show a first plot without HLLHC results

## Slide 14: Measurement of the TMCI threshold, B2H
Simulations
Mode 0
Mode -1
Notes: Show a first plot without HLLHC results

## Slide 15: Measurement of the TMCI threshold, B2H
Mode 0
Mode -1
Notes: Show a first plot without HLLHC results

## Slide 16: Summary of simulations results
Measured tune-shift higher than simulated
But a clear reduction is observed when opening the TCSGs
  Confirms the critical role played by IR7 TCSGs on impedance
Inferred TMCI threshold is also increased
 | Tune-shift (DELPHI) | Tune-shift (Measured) | TMCI threshold (DELPHI) | TMCI threshold (inferred)
LHC ft 2017 | -0.32 |  | 2.6 | 2.7
LHC ft 2017, TCSGs at 14 | -0.18 |  | 5.0 | 4.5
HL-LHC 48cm LS2.2 2 TCPs | -0.14 | - | 6.4 | -
HL-LHC48 cm MoGr IP7 | -0.15 | - | 6.0 | -
HL-LHC 48cm Baseline | -0.11 | - | 8.7 | -
LHC ft 2017 | -0.32 |  | 2.6 | 2.7
 | -0.18 |  | 5.0 | 4.5
HL-LHC 48cm LS2.2 2 TCPs | -0.14 | - | 6.4 | -
HL-LHC48 cm MoGr IP7 | -0.15 | - | 6.0 | -
HL-LHC 48cm Baseline | -0.11 | - | 8.7 | -

## Slide 17: Conclusions
The LHC and HL-LHC TMCI thresholds were investigated with simulations and measurements
  Measurement useful to assess the LHC impedance and stability model at low chromaticities
  Probe the possible stability limitations for HL-LHC
Direct measurement in the machine is challenging because of operational and safety constraints
  The TMCI threshold can be inferred by measuring the tune-shift versus bunch intensity
  Higher than simulated tune-shifts vs. intensity were found
Highlighted the beneficial effect of low resistivity collimators for HL-LHC
  Reproduced a low impedance scenario by changing the IR7 TCSGs gaps
  Clear tune-shift reduction and inferred a TMCI threshold 70% higher than for LHC

## Slide 18
Backup
Notes: Add quadrupolar effect
Add V plane:
- V plane is less critical for LHC and HL
Add B1: difference between B1 and B2 for LHC case

## Slide 19: TMCI in the LHC: measurement procedure
Measurement goals
  Infer the TMCI threshold by measuring the tune-shift vs intensity
  Try to observe a mode coupling instability in the LHC
8h time slot on Sep. 15th to 16th 2017 night to perform the measurement
Machine safety: each beam can not contain more than
Measurement procedure:
  Inject 2/3 bunches of different intensities, and ramp to top energy
  Bunch-by-bunch tune measurement: high precision tune measurement with the transverse damper stripline pickup (tune resolution: )
  Close the collimators to increase the machine impedance and repeat the measurement
Tentative to observe mode coupling by closing further the collimators
Notes: State of the art measurement
10-5 precision
ADT stripline BPM
LHC BPMs not precise to reach this precision

## Slide 20: Comparison of B2H simulations without and with damper
Notes: Add quadrupolar effect
Add V plane:
- V plane is less critical for LHC and HL
Add B1: difference between B1 and B2 for LHC case

## Slide 21: Measurement of the TMCI threshold, B2H
Notes: Show a first plot without HLLHC results

## Slide 22: Measurement of the TMCI threshold, B2H
Notes: Show a first plot without HLLHC results

## Slide 23: Measurement of the TMCI threshold, B2H
Notes: Show a first plot without HLLHC results

## Slide 24: Measurement of the TMCI threshold, B2H
Notes: Show a first plot without HLLHC results

## Slide 25: Results for B2V
Notes: Add quadrupolar effect
Add V plane:
- V plane is less critical for LHC and HL
Add B1: difference between B1 and B2 for LHC case

## Slide 26: Impedance models for the five cases, B2V
‘LHC ft 2017 TCSGs@14’ is between ‘HL-LHC 48cm MoGr IP7’ and ‘HL-LHC 48cm Baseline’
  Approximation valid in the 10MHz – 10GHz range
Notes: Change plot to simplified one

## Slide 27: Scenario: LHC ft 2017
DELPHI Simulations
Vertical plane
LHC flat top 2017 nominal settings
  TCPs at
  TCSGs at
TMCI threshold at
Higher than the horizontal plane
3.5
Notes: Show a first plot without HLLHC results

## Slide 28: Scenario: LHC ft 2017, TCSGs at 14
DELPHI Simulations
Vertical plane
LHC flat top 2017 with retracted TCSGs
  TCPs at
  TCSGs at
TMCI threshold at
Retracted TCSGs clearly improve the TMCI threshold
7.0
Notes: Show a first plot without HLLHC results

## Slide 29: Measurement of the TMCI threshold, B2V
Notes: Show a first plot without HLLHC results

## Slide 30: Measurement of the TMCI threshold, B2V
Notes: Show a first plot without HLLHC results

## Slide 31: Results for B1H and B1V
Notes: Add quadrupolar effect
Add V plane:
- V plane is less critical for LHC and HL
Add B1: difference between B1 and B2 for LHC case

## Slide 32: Measurement of the TMCI threshold, B1H
Notes: Show a first plot without HLLHC results

## Slide 33: Measurement of the TMCI threshold, B1H
Notes: Show a first plot without HLLHC results

## Slide 34: Measurement of the TMCI threshold, B1V
Notes: Show a first plot without HLLHC results

## Slide 35: Measurement of the TMCI threshold, B1V
Notes: Show a first plot without HLLHC results