## Slide 1
1Beam Instrumentation Group,
GSI Helmholtz Centre for Heavy Ion Research
GSI, Darmstadt
2TEMF, TU, Darmstadt
Germany
Robustness considerations for a fast
orbit feedback at hadron synchrotrons
Sajjad Hussain Mirza1,2
Dr. Rahul Singh1
Dr. Peter Forck1

## Slide 2: Outline
GSI and FAIR project
Upgrade of SIS18
  Robustness requirements of SIS18 Closed orbit feedback (COFB) system
Global orbit correction methods
  Harmonic analysis of the perturbed orbit
  Singular value decomposition (SVD) of response matrix
  Missing connection between two methods
Exploitation of Circulant symmetry in response matrix
  Simple symmetry
  Nearest-Circulant approximation
    Application of symmetry exploitation for subtracting the dispersion-induced orbit shift
  Block-Circulant symmetry in response matrix
Characterizing the effect of model mismatch on orbit correction
  Demonstration in COSY synchrotron Julich
Summary

## Slide 3
GSI
UNILAC(2-11.4 MeV/u)
SIS18(0.010-2 GeV/u)
Experimental storage ring (ESR)
Fragment separator FRS
FAIR
GSI and SIS100
SIS100 (0.2- 2.7 GeV/u)
GSI and FAIR: brief introduction
SIS18
SIS100
Specialties
Large range of ions (p to U)
Variable charge states
Ramp rates more than 10 T/s
Variable ramps (0.1 to 1s)
Magnet power supplies start at 3% of full power at injection
Beam size few cm
Facility for Antiproton and Ion Research

## Slide 4
SIS18 upgrade (as booster ring for SIS100)
Parameter/Time | Today | FAIR Booster
Reference Ion | U73+ | U28+
Maximum Energy GeV/u | 1 | 0.2
Maximum Intensity (Ions per pulse) | 4×109 | 4×1011
Repetition Rate (Hz) | 0.3 – 1 | 2.7
Higher to lower charge state to avoid space charge effects at high intensities
Vacuum improvements to avoid beam losses due to residual gas pressures
180 mm
Linear Ampl.
70 mm
SIS18
BPM
SIS100
BPM
135 × 65 mm
More control on beam quality to deliver more intensity to SIS100 (Closed orbit care)

## Slide 5: Closed orbit perturbation (distortion)
θ is the kick provided by field error
β(s) is the beta function at kick location
is the phase advance
Q is the tune of the machine
R is called the orbit response matrix
‘m’ BPMs
‘n’ correctors
Perturbed orbit due to single error
Notes: Enough of 3D plots, lets come back to 2D, visualization easier

## Slide 6
Closed orbit perturbations in SIS18
0 2 4 6 8 10
Time (ms)
At injection
0 0.5 1 1.5 2 2.5 3 3.5
Frequency (kHz)
Fourier Transform
0
6
-6
-12
position [mm]
along synchrotron
horizontal
vertical
Static perturbation
0 50 100 150 200 250
Time (ms)
During ramp
Ramps of two cycles
0 0.2 0.4 0.6 0.8 1 1.2
Frequency (kHz)
Fourier Transform
Wall thickness = 300 μm
200mm
116 mm

## Slide 7: Features of planned SIS18 COFB system
model-variation over ramp
triplet
doublet
Bending magnets
Focusing magnets
defocusing magnets
triplet focusing magnet
SIS18 cell
On-ramp orbit correction is planned
Ions have no synchrotron damping to restore beam quality at high energy
R. Singh, PhD Thesis, TU Darmstadt 2014.
sinusoidal excitation on one corrector

## Slide 8: Features of planned SIS18 COFB system
Online updating of the machine model?
How many models required for a given ramp?
Do we really need to update the ORM?
What if we use wrong ORM for the orbit correction and what are boundaries?
Orbit correction methods
Uncertainty modeling
R. Singh, PhD Thesis, TU Darmstadt 2014.
model-variation over ramp
sinusoidal excitation on one corrector
200 116

## Slide 9: Outline
GSI and FAIR project
Upgrade of SIS18
  Robustness requirements of SIS18 Closed orbit feedback (COFB) system
Global orbit correction methods
  Harmonic analysis of the perturbed orbit
  Singular value decomposition (SVD) of response matrix
  Missing connection between two methods
Exploitation of Circulant symmetry in response matrix
  Simple symmetry
  Nearest-Circulant approximation
    Application of symmetry exploitation for subtracting the dispersion-induced orbit shift
  Block-Circulant symmetry in response matrix
Characterizing the effect of model mismatch on orbit correction
  Demonstration in COSY synchrotron Julich
Summary

## Slide 10: Harmonic analysis (global correction)
Modes to be removed (corrected) are selected before-hand
measured orbit is fitted over corresponding mode e.g. modes around tune frequency
Corrector strengths are proportional to the Fourier coefficients
Mathematically complicated procedure
L.H.Yu et al.“Real time harmonic closed orbit correction”, Nucl. Instr. Meth. A, vol. 284, pp. 268–285, 1989

## Slide 11: Singular Value Decomposition (SVD)
U and V are orthogonal matrices such that
and
Which helps to find inverse R-1 (if R is invertible) as
-1
=
T
=
T
William H. Press, Numerical recipes; The art of scientific computing (2007) Cambridge university press
where the columns of U and V are the eigenvectors of RRT and RTR
Pseudo-inverse
Notes: First characteristic of SVD to decompose any matrix
singular values are positive scalars
orthoganal matirx measn all the coloumns are othogonal to each other i.e.their dot product equals zero (necessary conditions)

## Slide 12
Features of SVD
U and V matrices form the BPM and corrector spaces.
SVD can decompose and invert (or pseudo-invert) “any” matrix
A robust algorithm for global orbit correction
Benefits of SVD over harmonic analysis
One needs not to select the modes to be corrected before correction: decompose in all possible modes
“simple” matrix inversion
Mode-by-mode correction is still possible through selecting certain eigenvalues
Columns of U:Black
Columns of V: Red
Singular Value Decomposition (SVD)

## Slide 13: Weaknesses of SVD
U and V are interconnected through a phase relation
Over the ramp, updating of all three matrices required
Uncertainty modeling is required in all three matrices
Time complexity of the order of n3 , n being dimension of matrix
Loss of physical meaning of modes (interpolation)
Columns of U:Black
Columns of V: Red
Fourier coefficients of harmonic analysis have been proposed for uncertainty modeling
Qy = 3.28
k=3
k=4
k=5
S. Gayadeen, “Synchrotron Electron Beam Control”, Ph.D. thesis, St. Hugh’s College, University of Oxford, UK, 2014.

## Slide 14: Outline
GSI and FAIR project
Upgrade of SIS18
  Robustness requirements of SIS18 Closed orbit feedback (COFB) system
Global orbit correction methods
  Harmonic analysis of the perturbed orbit
  Singular value decomposition (SVD) of response matrix
  Missing connection between two methods
Exploitation of Circulant symmetry in response matrix
  Simple symmetry
  Nearest-Circulant approximation
    Application of symmetry exploitation for subtracting the dispersion-induced orbit shift
  Block-Circulant symmetry in response matrix
Characterizing the effect of model mismatch on orbit correction
  Demonstration in COSY synchrotron Julich
Summary

## Slide 15: Symmetry exploitation in SIS 18 vertical ORM
Each row is cyclic shift of previous row
All diagonal elements are identical
Reference: Philips J.Davis, Circulant matrices, (1994), Chelsea
Such a square matrix is called
Circulant Matrix
SIS18 lattice
(out of scale schematics)

## Slide 16
Diagonalization of a Circulant matrix
Standard Fourier matrix
=diag() ,k=1...n
Inverse is straightforward

## Slide 17: Equivalence of DFT and SVD
DFT:
SVD:
=
= phase
Why to do SVD when Circulant symmetry exits?
Herbert Karner et al. Spectral decomposition of real Circulant matrices, Linear Algebra and its Applications,
Volume 367, 2003
Notes: whole information is the magnitude and phase of Fourier coefficinets differnetly distributed in case of SVD.
phase and magnitude of weighting factors is only in the middl matrix in case of DFT
in case of SVD the information is distributed which means finding U and V for each new values of R
DFT gives possibility of online calculation

## Slide 18
Nearest-Circulant symmetry
SIS18 horizontal plane
Condition number =12
Condition number =9
Frobenius product
Orbit correction in SIS18 (9 July 2018)

## Slide 19
Dispersion effect in closed orbit
A DC shift in
closed orbit
Mismatch between RF frequency and the dipole field
an attempt to correct it can saturate the corrector magnets.

## Slide 20
Induced dispersion and closed orbit in SIS18
x-plane

## Slide 21
Induced dispersion and closed orbit in x-plane
Experiment at SIS18

## Slide 22
Block Circulant symmetry
SIS100
Circulant Matrices by P. J. Davis

## Slide 23
Extension of Circulant symmetry exploitation
SIS100
Circulant Matrices by P. J. Davis

## Slide 24: Outline
GSI and FAIR project
Upgrade of SIS18
  Robustness requirements of SIS18 Closed orbit feedback (COFB) system
Global orbit correction methods
  Harmonic analysis of the perturbed orbit
  Singular value decomposition (SVD) of response matrix
  Missing connection between two methods
Exploitation of Circulant symmetry in response matrix
  Simple symmetry
  Nearest-Circulant approximation
    Application of symmetry exploitation for subtracting the dispersion-induced orbit shift
  Block-Circulant symmetry in response matrix
Characterizing the effect of model mismatch on orbit correction
  Demonstration in COSY synchrotron Julich
Summary

## Slide 25
Reference
orbit
Corrector
settings
Source of orbit perturbation
residual
Measured
orbit
C
Characterizing the effect of spatial model mismatch
concept of spatial bandwidth
SIS18 is a unique synchrotron in terms of flexibility of operational scenarios.
Variable optics
Orbit response matrix variations
How much ORM variation we can live with?
How to quantify the effect of “wrong” model on orbit correction?

## Slide 26
SIS18 is a unique synchrotron in terms of flexibility of operational scenarios.
Variable optics
Orbit response matrix variations
How much ORM variation we can live with?
How to quantify the effect of “wrong” model on orbit correction?
Reference
orbit
Corrector
settings
Source of orbit perturbation
residual
Measured orbit
Characterizing the effect of spatial model mismatch
concept of spatial bandwidth

## Slide 27
Let [k] is the controller output at kth iteration
where,
Reference
orbit
Corrector
settings
Source of orbit perturbation
residual
Measured orbit
Characterizing the effect of spatial model mismatch
Mathematical treatment

## Slide 28
Reference
orbit
Corrector
settings
Source of orbit perturbation
residual
Measured orbit
Corrector settings
First iteration residual
nth iteration residual (n costs the bandwidth)
Characterizing the effect of spatial model mismatch
Mathematical treatment

## Slide 29
Corrector settings
First iteration residual
nth iteration residual (n costs the bandwidth)
Spatial sensitivity function
Correctability
No correction
Instability
Characterizing the effect of spatial model mismatch
Mathematical treatment

## Slide 30
On-ramp model variation in SIS18
Simulations: Orbit correction using injection ORM
First iteration residual

## Slide 31
Effect of wrong model on the orbit correction
Experiment: y-plane of COSY synchrotron Julich (31 Oct 2018)
ORM was varied as a function of betatron tune (3.52 – 4.18)
Machine tune was 3.62
Ratio of the RMS of first iteration to that of the perturbed orbit is plotted below
Thanks to Lorentz Bernd and Christian Weidemann for helping in the experiment.

## Slide 32
Summary
On-ramp orbit correction is planned for SIS18 synchrotron of GSI
  Symmetry exploitation in the ORM can result into faster matrix inversion than SVD
  DFT based diagonalization also gives physical meaning to SVD modes
  DFT based diagonalization provides the missing connection between SVD and harmonic analysis
Nearest-Circulant approximation can be made for slightly broken symmetries
Block-wise Circulant symmetry can also be applied for larger lattices (more than one BPMs per cell)
Spatial sensitivity function is defined as tool for the quantification of the effect of model mismatch on the orbit correction
2 to 3 ORM will be required over the ramp orbit correction for SIS18
Application of spatial sensitivity function has been demonstrated in COSY synchrotron Julich
I would like to acknowledge Dr. Guenther Rehm for nice discussions during my visit to Diamond Light Source