## Slide 1
QM update
L.Millward@qmul.ac.uk

## Slide 2
Scattering / Transmission
Want to Find a Front Back asymettry
Dark Spots are caused when backlighting is scattered away from the lens.
HYPOTHESIS: Halo lighting on front surface holes will cause aditional illumination due to light scattering INTO th lens

## Slide 3
Front / Back comparison Study
Makrofol ‘Correct Alignment’ - (foil numbering up) Backlighting
Makrofol ‘Reverse-side-flipped’ Backlighting

## Slide 4
Front / Back comparison Study
Align Using Target and reference holes Define regions of interest / closer study

## Slide 5
Imaging Parameters
Backlighting = 60 Halo lighting = 150
Backlight + Halo
Lens Lighting = 15
Same approx light level In all cases but halo Zoom = 102x

## Slide 6
Top Right Corner

## Slide 7
TRC - Backlighting
No clear difference
Relative symettry between front and reverse.

## Slide 8
TRC – BackLight + halo
Bright spots in multiple holes, Bright spots on front largely correspond to Dark spots on reverse, Vice Versa Supports scattering and transmission hypothesis

## Slide 9
TRC – Halo
Red – Example of hole appearing Highlighted on both sides Blue – Example of two holes, one highlighted on one side only

## Slide 10
TRC – Through Lens
Brightness variation quite sensitive to focal plane
Brightly Illuminated pits under halo lighting, correspond to dark spots here.

## Slide 11
Top Left Corner

## Slide 12
Top Left Corner - B+H
Line – probably a scratch or common event, thus expect holes to appear on the same side.
Side reversal flips bright / dark features, supporting hypothesis

## Slide 13
Top Left Corner

## Slide 14
Triad region, 165x Zoom
Bl = 8, Hl = 100

## Slide 15
Laser resoloution
RHS, laser position resoloution x 10, not a major improvement Tracking path (x,y) shows it does not travel completely smoothly

## Slide 16
Next steps;
More work on Automation / routines
Fine-tune and understand laser more
Look adifferent halo / backlighting mixes
Collect some bulk data, try to train rudimentary pit-finder