## Slide 1
I.G. Bearden
Experimental Subatomic Physics
EPIC
Niels Bohr Institute
Low Cost Gamma Ray Detectors for Outreach and Education

## Slide 2: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  DAQ
  HOW TO BUILD A 100€ Gamma Spectrometer
  Mini PET Scanner
NEXT STEPS

## Slide 3: THE TEAM
IGB
Axel Boisen
Jo Verwohlt Damm
Marta Mrozowska

## Slide 4: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  DAQ
  HOW TO BUILD A 100€ Gamma Spectrometer
  Mini PET Scanner
NEXT STEPS

## Slide 5: What I will talk about:
Simple detectors for Nuclear and Particle physics
Designed and built in-house (collaboration* between IGB and Axel Boisen from NBI’s fantastic electronics shop)
Design goals:
  AS INEXPENSIVE AS POSSIBLE
  ROBUST (to be used in both our teaching and outreach labs)
  AS FEW ”black boxes” AS POSSIBLE
BASED on rather new tech (Silicon Photomultipliers) as well as old (GM tubes, PMTs) depending on the purpose.
*Typically: IGB : ”I wonder if we could find a way to…” Axel, next day: ”Yes, like this. I made it for you”
Not all heroes wear capes, you know,

## Slide 6: Why this?
I am an experimental physicist.
PhD & first post-doc: high-spin gamma spectroscopy
Since then: Ultrarelativistic Heavy Ion Physics (presently: ALICE@LHC)
Teaching: I want to give students ”real” experimental experience as early as possible
Outreach: I want to finds ways to make the words ”nuclear” and ”radiation” less mysterious and frightening.

## Slide 7: Context

## Slide 8: Denmark
5.6 Mpeople
1/2 the size of Austria
  (unless we count Greenland)
No tuition (also for EU residents)
State stipend of 5500DKK

## Slide 9: University of Copenhagen
Roughly 40 kStudents
7000 faculty & staff

## Slide 10: Niels Bohr Institutet
Physics department of KU
~85(?) tenured faculty
~115 PhD students
~120 Post Docs
~600 students BSc&MSc students
155±10 new students/year. All physics majors (various ”specializations” bio, astro,geo…)

## Slide 11: Aside
Colliderscope: available from iTunes
Data from ATLAS inner tracker

## Slide 12: Curriculum
Bologna 3+2 (+3)
In DK secondary shools
3 levels (A,B,C)
Our students have had
Math: A
Phys: A or B**
Chem: A or B
At least 2 of these A
**quite a bit of laboratory work. In principle, well prepared for uni lab work.

## Slide 13: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  DAQ
  HOW TO BUILD A 100€ Gamma Spectrometer
  Mini PET Scanner
NEXT STEPS

## Slide 14: MARKET ”SURVEY”:commercial
Many commercially available nuclear/particle physics detector systems.
Both ”research” and ”educational” solutions.
Many of these are very good…BUT
Typically,* ”educational” solutions are expensive and not terribly flexible systems, often dependent on proprietary software.
*there may be some that are reasonably priced and open source that I have not found.

## Slide 15: MARKET ”SURVEY”:commercial
CAEN offers several nice packages, but 5-8k€/setup.
Canberra offers good NaI+Integrated base, 4k€+closed software.
”legacy” research equipment often requires expensive HV, DAQ, etc.
Difficult to have large scale lab teaching based on these

## Slide 16: MARKET ”SURVEY”:Open Source
$100* Cosmic ray detector ”Cosmic Watch” MIT (SiPM coupled to plastic scintillator) NEW: SensL offers $60 SiPM for students
MUON HUNTER based on inexpensive commercial electronics and 2 GM tubes in coincidence. Working system for ≈150€, depending on availability GM tubes, etc.
A number of web resources explaining how to build various detectors…(probably more applicable to hobbyists than to large scale lab teaching)
*$100 if you don’t have to buy scintillator

## Slide 17: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  HOW TO BUILD A 500€ PET SCANNER
NEXT STEPS

## Slide 18: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  DAQ
  HOW TO BUILD A 100€ Gamma Spectrometer
  Mini PET Scanner
NEXT STEPS

## Slide 19: IN-HOUSE Detectors for N&P Phys.
Generous support from NICE* and the Experimental SubAtomic Physics group at NBI
Support from NBI (technical infrastructure)
Fantastic students
ALLOW:
  NBI BiGS (BILLIGE GAMMA SPECTROMETER)
  Muon telescopes based on both SiPM+Scint & GM-tubes
  Alpha and beta spectroscopy (in development)
*Denmark’s National Instrument Center for CERN Experiments

## Slide 20: DAQ
Connects via USB
Works on Mac, Windows, Linux
Scripting language, allows for some real time signal processing
$279 ($179 academic) +$15 BNC breakout
100MS/s USB Oscilloscope, Logic Analyzer and Variable Power Supply

## Slide 21: The 100€ g spectrometer (BiGS)
PCB
SiPM
LYSO
3D printed cover
Optical
Grease

## Slide 22: The 100€ g spectrometer (BiGS)
Singles spectrum 22Na:
PCB
SiPM
LYSO
22Na source
3D printed cover
Optical
Grease

## Slide 23: The 100€ g spectrometer (BiGS)
Singles spectrum 137Cs:
PCB
SiPM
LYSO
137Cs source
3D printed cover
Optical
Grease

## Slide 24: The 100€ g spectrometer (BiGS)
Good resolution:
PCB
SiPM
LYSO
137Cs source
3D printed cover
DE/E≈10%
Optical
Grease

## Slide 25: The 100€ g spectrometer (BiGS)
Singles spectrum:
PCB
SiPM
LYSO
137Cs source
3D printed cover
DE/E≈10%
Optical
Grease

## Slide 26: LYSO scintillator
4x4x22mm (fra PET Scanner)
PCB
SiPM
LYSO
3D printed cover
Lutetium-yttrium oxyorthosilicate
Charge (au)
Optical
Grease

## Slide 27: LYSO scintillator
4x4x22mm (fra PET Scanner)
PCB
SiPM
LYSO
3D printed cover
Lutetium-yttrium oxyorthosilicate
g
g
g
g
g
g
Charge (au)
Optical
Grease

## Slide 28: Why is this interesting for Teaching/Outreach?
Inexpensive detectors (<10% cost of commercial alternatives)
Don’t require high voltage (SiPMs 25-30V, compared to ≈1kV for PMTs)
  Less expensive, more safe
Simple system that can be put together by students
Highly transportable:
  Detectors small and light, DAQ powered by USB
  Detector can be powered by batteries

## Slide 29: Not perfect, though, because
Small scintillators, poor efficiency for higher gamma energy
LYSO is radioactive, can make it difficult to measure low activity souces below ≈600keV
Steeply falling background makes peaks non-gaussian (so more difficult for novices to fit
Poor efficiency->low count rates, challenging for impatient researchers
511keV
1274 keV
4x4x22mm
6x6x40mm

## Slide 30: Intro course @NBI: Mechanics & Special Relativity
How to do good SR experiments in under 3 hours?
Need 10+ setups (30 students/section, 6 sections)
Needs to be simple enough that students don’t drown in technical details

## Slide 31: Intro course @NBI: Mechanics & Special Relativity
How to do good SR experiments in under 3 hours?
Need 10+ setups (30 students/section, 6 sections)
Needs to be simple enough that students don’t drown in technical details
Answer: measure gammas from e+ e- annihilation!

## Slide 32
Beta+ decay:

## Slide 33: PET Scanner
Fluorodeoxyglucose (18F)

## Slide 34: PET Scanner
Fluorodeoxyglucose (18F)
18O(p,n)18F

## Slide 35
Many per second

## Slide 36
Don’t ”see” gamma
NB: de kilder i bruger har
Ca. 37000 henfald/s

## Slide 37
”see” gamma
NB: de kilder i bruger har
Ca. 37000 henfald/s

## Slide 38
With 2 BiGS:miniPET Scanner
Det B
V (27-28V)
V (27-28V)
Oskop
PC
DetA
22Na
Notes: HUSK: forbind projekter med slogan!!

## Slide 39
no coincendence
Trigger detector

## Slide 40
Coincendence!

## Slide 41
In real life, it looks like this:

## Slide 42
Coincidence* spectrum
*Need to explicitly tell students the technical meaning of ”coincidence” as it is quite different from ordinary usage

## Slide 43: Two ways to do this:
Maximize trigger rate in Det A
Use DetB to measure at various angles
Find coincidence peak at 180°
Place DetA and Det B in same plane at 180°
Move source through scanner
When source exactly between A & B: Coincidence!

## Slide 44: Students ”see” that
The two coincident gammas are each 511keV
Aha! Rest mass of e is 511keV/c2
And gammas are always back to back!
So annihilation occurs at rest wrt lab and
Eg1+Eg2=me-c2+me+c2
That Einstein guy might have been onto something!

## Slide 45: Can be used with younger students
Demonstrate how PET scanners work
NB: this is one of S’cool labs cool labs!
Requires different scaffolding, fewer technical details

## Slide 46: PLAN
INTRODUCTION:
  What I will talk about
  Why I am talking about this
  Context in which this has been done
WHAT IS ”AVAILABLE”?
  A quick non-objective, non-exhaustive market ”survey”
THE NICE-NBI SOLUTION
  DAQ
  HOW TO BUILD A 100€ Gamma Spectrometer
  Mini PET Scanner
NEXT STEPS

## Slide 47: NEXT STEPS
Upper level labs: background subtraction:
Look at 176Hf gamma spectrum
g
g
g
g
g
g

## Slide 48: Normalize, subtract et voila!
176Hf g spectrum

## Slide 49: Environmental measurements
System extremely portable
Collect gamma spectra anywhere (you’re allowed to be with a computer)
November 2018: local school group to NBI to build and characterize BiGS (resolution, efficiency, P/T)
September 2019: Class to Fukushima.
  Can we measure residual 137Cs?

## Slide 50: TO DO!
EVALUATE
How can we prove that including such activities in outreach and education improve:
Interest in physics generally
Interest in Nuclear & particle physics

## Slide 51: TO DO!
For Physics students
How can we prove that including such activities in improve educational outcomes?
Increase interest in Nuclear & particle physics?
Increase technical skills?

## Slide 52: BASIC QUESTION:
HOW SHOULD WE MEASURE IMPACT OF INDIVIDUAL ACTIVITIES?

## Slide 53: SUMMARY
Possible to produce performant low cost detectors.
Consumer grade digital scopes work extremely well in teaching and outreach applications.
You can put together a (very small!) PET scanner demonstrator for roughly 500CHF.
Highly portable systems might give interesting possibilities for new activities.